PORTVIEW INFORMATION

                            Overview
     Portview was created to analyze the data flow between RS-232 
devices, and to allow limited simulation capability. The  program 
supports  sending  files and macro strings, and  saving  incoming 
data  to files. All strings and files are "binary", meaning  they 
may contain any characters including nulls. 
     Two  windows  are provided for incoming/outgoing  data.  The 
windows  are  not circumscribed by lines (boxed)  which  frees  4 
extra screen lines. A status line under each window provides port 
information. COM1 is ALWAYS assigned to the top window.
     Data  is shown in 3 formats. In the default "Analyzer  Mode" 
all  characters including space, tab, and hex ff  display  unique 
characters. Translated characters display in a "dim" attribute. 
The  second  or  Normal mode displays in the  usual  manner  with 
carriage-return/linefeed  causing a newline, and  tabs  expanded. 
Press  Alt-E  for Extended Hex mode. In this mode  incoming  text 
only is displayed in ascii followed by its hex equivalent. 

     example: a 61  . 2E  M 4D  y 79  J 4A  a 61  z 7A  z 7A

     The screen color scheme and display mode may be changed  and 
saved  to disk. Receive and send data are displayed in  different 
colors.

                            Hardware
     COM1  and  COM2  are supported. No  error  message  will  be 
returned for bad or missing adapter cards!

                          Key_Commands
     Most  commands  are assigned to function keys. For  a  quick 
reference guide to command keys press F10.

                             General
     F6  toggles between Port A and B. It affects all  data  sent 
from files, macros or typed from the keyboard.

     Alt-F6  allows entry of DOS commands. Most DOS commands  can 
be executed, including running programs and copying files.

     Ins  pauses the display and displays "Screen Paused" in  the 
message area of the status line. Press Ins again to restart  data 
flow.
.pa
     Shift-F8 sets up a Respond Mode command sequence (script).

                    Respond_Mode_Definitions

     Compare Element     = 1-8. There may be up to 8
                           compare strings.
     KEY of Match String = Key to access string to match 
                           against incoming data. I recommend
                           using Ctrl-A,Ctrl-B,Ctrl-C and Ctrl-D
                           corresponding to 1, 2, 3, 4, etc.
     COMMAND:            = Choose command from menu. Enter the 
                           number or letter preceeding your
                           selection. There may be up to 8
                           commands executed for each match.
     PARAMETER:          = Some commands need a parameter. In 
                           all cases, the parameter is a KEY
                           to a string. If no parameter is
                           needed, enter a Space.

     Alt-F8  sets  up binary strings. These can be used  for  any 
purpose. All strings can be sent as macros, can be filenames,  or 
be  used  as match strings. Enter an Access KEY, then  enter  the 
string.  Again, any character may be entered. To backup  use  the 
backarrow cursor key, NOT the backspace key.

To abort (not save) a string, press the PgUp key. When completed, 
a  string may be saved by pressing the PgDn key. All strings  may 
be  up to 32000 characters. The Home key moves the cursor to  the 
beginning of the string. The End key takes you to the end of  the 
string. When finished, the position of the cursor determines  the 
end of the string. If the cursor is located before the end of the 
string,  the  string  will  be  truncated  to  the  last  visible 
character.   Overtype  mode  allows  replacing  characters,   but 
deletion  by  collapse,  and  insertion  by  expansion  are   not 
supported.  To  move 30 characters in either direction,  use  the 
Ctrl- Arrow keys. To delete a string (make zero length) move  the 
cursor  with the Home key to the first position, then press  PgDn 
to end.

A  CRC  or LRC checksum can be calculated and  automatically  set 
into  the macro. To use LRC, press the F6 key. To  use  CRC-CCITT 
press Alt-F6. The checksum beginning offset default is zero,  but 
can be altered by use of the F5 key. Shift-F5 sets a 4 byte ASCII 
representation of a 2 byte Hex binary addition checksum into  the 
string. (used in Micros-4700 interface protocol)
.pa
                          Sound Macros

Sound macro strings can be created in the following form:

256,20  294,10  256,20  0,5  256,20  330,50
|  | ||                 | |
|  | ||                 | `Duration in hundredths of seconds
|  | ||                 `Zero freq for time delay only
|  | |`Space delimiter between pairs (any number of spaces)
|  | `Duration in hundredths of seconds
|  `Comma delimiter between freq and duration
`-- Frequency in Hz

The  pairs  may have any number of spaces between them,  but  the 
comma  delimiter  only must separate the frequency  and  duration 
fields as shown above.
.pa
     Alt-F7 Aborts a file send and clears the output buffers.
     Alt-F9 Clears the input buffers.

     Alt-F3/F4 keys allow named save files to be created for Port 
A or B respectively. The filenames must be unique. A previously
created  file cannot be overwritten with this function. To  close 
the files, press F3/F4 again.

     F3/F4 keys toggle capture mode. The files created have fixed 
filenames of "PORT1.SAV" and "PORT2.SAV". The files are opened in 
"append"  mode,  so  that  previous data is  added  to,  but  not 
destroyed.  These files should be deleted to clear them out.  Use 
the Alt-F6 DOS mode and the DOS delete command to erase them.
They will be automatically re-created by the next press of the F3 
or F4 keys.

     Alt-M  enables save of screen mode and colors. When  enabled 
the  screen  mode (analyzer or normal) will be saved to  disk  as 
well  as  the current color scheme. Extended  Hex  display  mode, 
Pause state, and the operating mode (Monitor, Terminal, Xover) is 
only saved when Alt-M is pressed. Toggling the Alt-E key does not 
interfere  with  the  current  screen mode  as  stored,  it  only 
temporarily overrides it.
     Alt-N  disables screen color/mode saving. While disabled the 
program  will  initially use the default color scheme,  begin  in 
analyzer screen mode, and use Monitor operating mode.

                          Monitor_Mode
     Use this mode with the special cable to monitor flow between 
RS-232  devices. The special cable allows communication  normally 
with  full  handshaking  without interfering  in  the  flow.  The 
different directions of flow appear in different windows,  making 
it easy to analyze or capture the data.

                           Xover_Mode
     This mode is useful for baud/protocol translation. With  the 
test  computer in line between the modem and the  host  computer, 
xover  mode allows checking out devices without having  to  setup 
internal  parameters. It is particularly handy for testing  Point 
Of Sale Terminals and Node Controllers.

                          Terminal_Mode
     In Terminal Mode the keyboard is active as well as macro and 
file   send  capabilities.  Split-screen   operation   eliminates 
confusion  from  intermixing  of xmit  and  receive  data.  Alt-L
adds  a  linefeed after each typed carriage return. It  does  NOT 
affect files or macros.
.pa
                          Testing_Hints
     Set  up data packets as binary macro strings. These  packets 
can  then  be  sent  to the connected  system  and  the  response 
analyzed.  A  match string can be set up to  respond  to  certain 
packets from the connected system. This allows simulation of most 
any communication packet protocol. Matches cannot be  overlapped. 
That is, if one match string is on the string "th" and another on 
"the",  the  second match will never occur, as the  counters  are 
reset  after  the first match.

To  be sure the PORTVIEW program and comm ports are  operational, 
connect  COM1 to COM2 via a null modem cable. In  Terminal  mode, 
any  data sent should echo back to the screen in the SAME  window 
as your typed text.

                             Errors
A  Program  Status Line occupies the center line of  the  display 
screen.  All  error messages display to the left of  the  current 
mode on this line. Hardware errors from a disk drive  (forgetting 
to  close the floppy drive door for example) display the  message 
"Device Error". When in the DOS Command mode, these errors  cause 
a message "Abort,Retry,Ignore" or "Abort,Retry,Fail" to  display. 
Choosing  Abort will not stop the program or cause loss of  data. 
It will only end the current DOS mode session inside PORTVIEW.
The  error  message  "Binary  Trunc  Err"  announces  failure  to 
eliminate the termination string from an automated file transfer. 
Usually  this  is caused by attempting to store a file  in  other 
than  the default directory. Remove the subdirectories  from  the 
"path" info in the filename and the error should not repeat.

                      Binary File Transfers
     Since  all  files  are binary, program  files  etc,  can  be 
transferred between systems using PORTVIEW on both computers.
Set  up the receive system using two compare elements. The  first 
should  be  set  up with "7" (close files) and  "5"  (named  file 
open/close for port A). This sequence assures proper open of  the 
file.  The second compare element should be set up with only  the 
"5"  (named  file open/close) command. This second  command  will 
be used to close the file. Set up key strings for open and close, 
and  enter  the  filename string. The filename  MUST  be  in  the 
current  default  directory.  It cannot contain  a  path  string, 
however  it may contain a drive specifier. i.e.  A:MYFILE.DOC  or 
MYFILE.DOC  are ok, but A:\STUFF\MYFILE.DOC or A:\MYFILE.DOC  are 
not. The backslash is not allowed.
.pa
For  example,  use  the Shift-F8 key to enter  the  Respond  Mode 
loader. press 1 to choose the first compare element. Next,  press 
Ctrl-A. This makes Ctrl-A the key to the "openfile" string.  Now, 
press  7  the  "close  all files"  command.  Since  there  is  no 
parameter with this command, press Enter. Assuming transfer  will 
be  from Port-A, press 5. This opens a named file. Press F.  This 
key  will  represent the filename string. To end, press  the  Esc 
key. Press any key to return to terminal mode.
The second step is to use Alt-F8 to enter the Macro String Loader 
function. Press F and enter the filename you want to use. In like 
manner  use  Alt-F8  again, with Ctrl-A as  the  key.  Enter  the 
openfile command string. I use open-transfer-file. It should be a 
string that would never be contained in normal text flow.
To complete the programming, use Alt-F8, this time with Ctrl-B as 
the key. Enter the close-file string. I use  close-transfer-file. 
It  is vital that this string be one that is NOT in the file  you 
are transferring. The string can be as complex or long as you like.
Activate the Alt-1 and Alt-2 compare elements.

On  the  transmit  system, set up macro  strings  containing  the 
openfile and closefile strings. These must be exactly the same as 
the ones used in the receive system. 
To  use the transfer now that it is programmed, simply  send  the 
openfile  macro from the transmit end. Next, send the file  using 
the F7 key. When transfer is complete, send the close-file macro. 
Do  not hit any other key before the close-file macro is sent  by 
mistake! If you do, that character will end up in the file.

                          Misc Commands

Alt-E  Toggles  the Extended Hex mode. This  displays  the  ascii 
character  followed  by  its hexadecimal equivalent.

Alt-D displays just the decimal character list.

Alt-H displays just the hexadecimal list.

End  displays both the hexadecimal and decimal character lists.

Alt-F  toggles  thru 3 options: 1. restore handshaking  state  on 
exit just as it was when the program started. 2. Inhibit flow  on 
exit. 3. Enable flow on exit.

Ins  toggles  display pause. Though data display is  halted,  the 
ports will still receive data into the buffers.