System Overview

      This  simulation  is  designed to show  the  complexity  of 
      operation  of  a  pressurized,  light water  nuclear  power 
      plant.   The key to this simulation is the  inter-relation-
      ships  between  the various systems  and  components.   The 
      information  and operating characteristics for this simula-
      tion  were taken from actual experience and from a  program 
      by Stephen R.   Berggren, titled APPLE NUCLEAR POWER PLANT, 
      which appeared in Creative Computing, December 1980, vol 6, 
      no 12.   The basic algorithms used in Reactor-150 are based 
      on  simplified  heat  transfer  equations  found  in  APPLE 
      NUCLEAR POWER PLANT.

                          System Design

      The reactor plant is constructed in two major sections: the 
      primary loop, and the secondary loop, each composed of many 
      subsystems.   Detailed information on these subsystems  can 
      be  requested  using the 'H' key,  or  by identifying  them 
      with the lightpen.

           Primary Loop:

           The  primary loop consists of the reactor and half  of 
           the heat exchanger {also called steam generator}.   In 
           this loop,  heat produced by the fission of uranium in 
           the reactor core is to the heat exchanger by  recircu-
           lating pressurized water.

           Secondary Loop:

           The  secondary  loop consists of  water  recirculating 
           through the remaining half of the heat exchanger,  the 
           turbine  and  the condenser.   Water is  converted  to 
           steam  in  the heat exchanger and then spins  the  tu-
           rbine,  and  the  steam exhausted by  the  turbine  is 
           condensed back to water in the condenser.

                        System Operation

      The  plant  is controlled by use of the function  keys  and 
      certain  keyboard keys.   The function key operations  take 
      place immediately, with the exception of 'ESC', which takes 
      place  at the beginning of the next update.   The  keyboard 
      keys  are acted on during each update.   Detailed  descrip-
      tions of the command keys are available by requesting 'H'.

                        Simulation Goals

      The operator is expected to operate the plant safely and to 
      produce  sufficient  power  above demand to  enable  excess 
      power to be sold to other power grids.   The operator  will 
      be scored on total production and total plant damage incur-
      red.   Safety and minimized plant damage are more important 
      than  production rate.   During each maintenance  shutdown, 
      production  levels and plant status will be displayed.   At 
      the end of the simulation,  the operator will be scored  on 
      how  safely and efficiently to plant was operated.   A  low 
      score indicates more proficient operations.

                           GOOD LUCK!