01
               RX TEMP - High Reactor Temperature

      This alarm indicates high reactor core temperature.   Imme-
      diate action should be taken to reduce core temperature  by 
      using Emergency SCRAM 'ESC', SCRAM 'F1', or Rod Height 'R0'.  
      Also consider using Emergency Cooling 'E100'.

      Warning  (Yellow)  Point:   Reactor core temperature  above 
      750F.

      Danger (Red) Point:  Reactor core temperature above 800F.

02
              RX PRESS - Low Reactor Pressurization

      This alarm indicates low reactor core pressurization, which 
      could result in localized boiling and fuel element failure.  
      Use Emergency SCRAM 'ESC'.

      Warning (Yellow) Point:  Reactor pressure below 2 X Reactor 
      temperature.

      Danger (Red) Point:   Reactor pressure below 1.8 X  Reactor 
      temperature.

03
                  RX Level - Low Reactor Level

      This  alarm  indicates a loss of reactor coolant such  that 
      the reactor core is in danger of becoming  uncovered.   Use 
      Emergency Cooling 'E100',  or Make-up Feed to Primary 'M100 
      DP'.

      Warning (Yellow) Point:  None.

      Danger (Red) Point:  Reactor coolant level below 100%.

04
               Rod Bottom - Rod Bottom Indication

      This indication indicates when the control rods are comple-
      tely inserted.

      Warning (Yellow) Point:  Control Rods on bottom, completely 
      inserted.

      Danger (Red) Point:  None

05
                 RAD HIGH - High Radiation Level

      This  alarm indicates above normal radiation levels in  the 
      containment building.  This may be due to normal continuous 
      high  power operation or to fuel element failure.   No  im-
      mediate action necessary.

      Warning  (Yellow) Point:   Radiation level above 200 Milli-
      rem/hour.

      Danger  (Red)  Point:   Radiation level  above  500  Milli-
      rem/hour.

06
                  Press Lvl - Pressurizer Level

      This  alarm indicates that the pressurizer level is out  of 
      specification.   A  level  too high will result in a  pres-
      surizer failure and primary coolant  leakage.   Pressurizer 
      level too low will result in pressurizer heater failure and 
      loss of pressurization to the reactor.   Control level with 
      Primary Drain Valve 'F2' and Make-up Feed 'DP'.

      Warning  (Yellow)  Point:   Pressurizer level above 85%  or 
      below 50%.

      Danger (Red) Point:   Pressurizer level above 90% or  below 
      45%.

07
              Pri Flow - Primary Coolant Flow Rate

      This  alarm indicates that the primary coolant flow rate is 
      out  of range.   If the flow is too low,  the reactor  core 
      receives inadequate cooling.  If too high, the primary pump 
      is overstressed and may fail prematurely.

      Warning (Yellow) Point:   Primary flow above 90%,  or below 
      .12 X Reactor temperature.

      Danger (Red) Point:  Primary flow 0.

08
             Emerg Low - Low Emergency Coolant Level

      This alarm indicates that the Emergency Coolant  reservoir 
      is below safe operating levels.

      Warning (Yellow) Point:  Emergency Coolant below 25%.

      Danger (Red) Point:  Emergency Coolant level below 10%.

09
           Xchg Temp - High Heat Exchanger Temperature

      This alarm indicates that the Heat Exchanger temperature is 
      exceeding design limits.   Action should be taken to reduce 
      Primary  temperature and to increase Secondary Coolant Flow 
      'S100'.

      Warning (Yellow) Point:   Heat Exchanger temperature  above 
      495F.

      Danger (Red) Point:  Heat Exchanger temperature above 500F.

10
               Sec Level - Secondary Coolant Level

      This alarm indicates low Secondary Coolant level.   Make-up 
      Feed 'DS' should be used to bring the level back to 100%.

      Warning (Yellow) Point:  Secondary Coolant level below 90%.

      Danger (Red) Point:  Secondary Coolant level below 50%

11
                Sec Flow - Secondary Coolant Flow

      This  alarm indicates that the Secondary Coolant flow  rate 
      is out of range.  Low Secondary Coolant flow can cause Heat 
      Exchanger  failure or Secondary Coolant pump damage.   High 
      flow can result in overstressing the pump.

      Warning (Yellow) Point:   Secondary Coolant Flow rate above 
      90%.

      Danger (Red) Point:  Secondary Coolant Flow rate 0.

12
         Cnd In Temp - High Condenser Inlet Temperature

      This  alarm  indicates high  condenser  inlet  temperature.  
      This can result in damage to the turbine, Secondary Coolant 
      pump and to the Condenser circulating pump.

      Warning (Yellow) Point:  Condenser inlet temperature  above 
      275F.

      Danger  (Red)  Point:   Condenser inlet  temperature  above 
      300F.

13
             Cnd Hi Press - High Condenser Pressure

      This  alarm  indicates high Condenser Pressure due to  high 
      condensate temperature or low Secondary Coolant flow.  High 
      Condensate  pressure  damages the Secondary  Coolant  pump.  
      Increase Secondary Coolant Flow 'S100'.
 

      Warning (Yellow) Point:  Condenser Pressure above 4 Psi.

      Danger (Red) Point:  Condenser Pressure above 10 Psi.

14
         Cnd Out Tmp - High Condenser Outlet Temperature

      This  alarm  indicates high Condenser  outlet  temperature.  
      High condensate temperature causes damage to the  Secondary 
      Coolant pump.   Increase Secondary Coolant flow 'S100',  or 
      decrease Heat Exchanger Temperature.

      Warning (Yellow) Point:  Condenser Outlet Temperature above 
      195F.

      Danger  (Red)  Point:   Condenser Outlet Temperature  above 
      212F.

15
               Turb Speed - Turbo-Generator Speed

      This alarm indicates that the Turbo-Generator system is not 
      on  design speed of 3,600 RPM.   Turbo-Generator  overspeed 
      damages  the turbine and generator.   Generator Trip  valve 
      'F3'  and Generator Field control 'F4' effect Turbo-Genera-
      tor speed.

      Warning (Yellow) Point:   Turbo-Generator speed other  than 
      3,600 RPM.

      Danger (Red) Point:  Turbo-Generator speed above 3,636 RPM.
 
16
          LOil Temp - High Lubricating Oil Temperature

      This  alarm  indicates High  Lubricating  Oil  temperature.  
      This  can  damage the Lubricating Oil pump and  the  Turbo-
      Generator.

      Warning (Yellow) Point:   Lubricating Oil Temperature above 
      200F.

      Danger  (Red)  Point:   Lubricating Oil  Temperature  above 
      212F.

17
               LOil Level - Lubricating Oil Level

      This alarm indicates low Lubricating Oil level.   Low level 
      can damage the Lubricating Oil Pump and Turbo-Generator.

      Warning (Yellow) Point:  Lube Oil Level below 35%.

      Danger (Red) Point:  Lube Oil Level below 15%.

18
              LOil Press - Lubricating Oil Pressure

      This alarm indicates unsafe Lubricating Oil Pressure.   Low 
      Lube Oil pressure can damage the Turbo-Generator.  Lube Oil 
      Pump control 'F8'.

      Warning  (Yellow)  Point:   Lube Oil pressure above 90  and 
      below 79.

      Danger (Red) Point:   Lube Oil pressure above 95 and  below 
      72.

19
              MkFeed Level - Low Make-up Feed Level 

      This  alarm indicates when Make-up Feed level is below safe 
      operating levels.   Make-up feed replenishment will  slowly 
      take place during normal operations; system refilled during 
      maintenance shutdowns.

      Warning (Yellow) Point:  Make-up Feed level below 40%.

      Danger (Red) Point:  Make-up Feed level below 5%.

20
                Pump Temp - High Pump Temperature 

      This  alarm indicates that one or more of the six pumps  is 
      overheating.   The  pumps  are Primary  Coolant,  Secondary 
      Coolant,  Condenser Circulation,  Lube Oil, Emergency Cool-
      ing, and Make-up Feed.

      Warning (Yellow) Point:  Pump temperature above 175F.

      Danger (Red) Point:  Pump temperature above 212F.

21
          Cntrl Warn - Control/Auxiliary Power Warning

      This  alarm indicates loss of auxiliary power or  an  error 
      detected  by  the automatic control system.   Loss of  aux-
      iliary  power results in failure of all pumps and  controls 
      if the generator is not producing power.

      Warning (Yellow) Point:   Automatic Control off above  600F 
      reactor temperature.

      Danger  (Red) Point:   Automatic Set-point off and  Control 
      set point above 494F.  Loss of Auxiliary Power.

22
               Turb Trip - Turbo-Generator Tripped

      This alarm indicates that the Turbo-Generator trip valve is 
      open,  and  that  the  secondary coolant  is  being  dumped 
      directly into the condenser.

      Warning (Yellow) Point:  Turbo-Generator Trip valve open.

      Danger  (Red) Point:   Turbo-Generator not tripped and Heat 
      exchanger temperature below 212F.

23
              Pri Drain - Primary Drain Valve Open

      This  alarm indicates that the Primary Drain Valve is  open 
      and allowing Primary Coolant to drain from the pressurizer.

      Warning (Yellow) Point:  Primary Drain Valve open.

      Danger (Red) Point:  None.

24
              Pr Htr OFF - Pressurizer Heaters Off

      This alarm indicates that the Pressurizer Heaters are  off.  
      The  Reactor  temperature should not exceed 212F  when  the 
      Pressurizer Heaters are off.

      Warning (Yellow) Point:  None

      Danger (Red) Point:  Pressurizer Heaters Off
99