Introduction
  CompuServe has implemented a version of the XMODEM protocol that
allows most XMODEM users to successfully transfer files securely between
their micros and CompuServe's hosts.  This implementation was not and
cannot be 100% faithful to the original XMODEM specification (see
reference [1]), and the differences between micro to micro XMODEM and
micro to host XMODEM has caused some people problems.  The purpose of
this short article is to describe, in detail, the most frequent problems
people have with micro to host XMODEM, and to offer some suggestions on
how to overcome these problems.
        XMODEM's origins
  The XMODEM (aka MODEM7) protocol was originally devised by Ward
Christensen as a protocol for communicatons between microcomputers.  As
it was originally devised, the user runs a program called "MODEM", and
dials up another computer. The user then instructs the remote computer
to run a program called "XMODEM".  XMODEM and MODEM then use the XMODEM
protocol to transfer files between the two computers.
  The XMODEM protocol has several assumptions implicit in its design,
and these assumptions are the source of the problems people have in
using XMODEM protocol on CompuServe.  Some of these assumptions are:
  o File lengths are exact multiples of 128 bytes.
  o Word size is 8 bits on both computers.
  o Data is transmitted 8 bits, no parity, one stop bit.
  o Both computers are dedicated (single user) microcomputers.
  o Both computers are talking to each other directly over a phone line.

      The XMODEM protocol
  The XMODEM protocol is a half duplex protocol -- infomation travels in
only one direction at once.  The basic protocol works something like
this:
     1.  When the receiver is
         ready to start
         receiving data, it
         transmits a <nak>
         (negative
         acknowledgment)
         character to the
         sender, and continues
         to do so every 10
         seconds until:
     2.  The sender sends a
         block.  Each block
         contains the block
         number (modulo 256),
         128 bytes of data, and
         a checksum.  Once the
         block is sent, the
         sender waits while:
     3.  The receiver verifies
         that he received the
         block correctly;  if
         the received checksum
         matches, then the
         receiver sends an <ack>
         character, and the
         sender sends the next
         128 bytes of the file
         (step 2).  If the block
         was not received
         correctly -- or if 10
         seconds expires before
         a complete block is
         received, the receiver
         sends a <nak> character
         to the sender.  When
         the sender receives a
         <nak>, it re-transmits
         the last block.
     4.  Steps 2 3 are repeated
         until the end of the
         file.  At the end of
         the file, the sender
         sends an <eot>
         character instead of a
         block of data.
     5.  When the receiver sees
         the <eot>, it sends an
         <ack> to the sender,
         and then the file
         transmission process is
         complete.
  There is a variant of the XMODEM protocol that CompuServe also
supports, called the CRC option.  In the original XMODEM protocol, the
checksum of each block was only one byte long. This small of a checksum
(along with the algorithm used to generate it) allows errors to easily
sneak into a supposedly error free protocol.
  The CRC option works roughly like this:  Instead of the receiver
sending out <nak>s at the very beginning, it sends out the letter "C".
If the sender has the CRC option, it treats this just like a <nak>, but
knows to compute the two-byte CCITT CRC-16 and add it to the end of all
blocks instead of the one byte checksum.  If the sender does not have
the CRC option, then the "C" character has no meaning to it and is
ignored.  The receiver may try about three "C"s before deciding that the
sender will not handle CRCs, and then the receiver transmits a <nak> to
start a checksum-XMODEM file transfer.
1.  XMODEM Problems on CompuServe
  Because of the assumptions made in the XMODEM protocol, various
difficulties arise in using XMODEM over CompuServe. Here are some major
classes of problems:
         XMODEM Timing
  Since XMODEM was originally devised for micro-to-micro communications,
it has some problems fitting into an environment where one of the
computers happens to be a mainframe and the two computers are not
connected over a simple phone line but via a packet switching network.
CompuServe's network can often introduce long delays in what should be
continuous communications, as can a very busy host.
  When these delays arise, the microcomputer running XMODEM may mistake
them for a breakdown in communications.  If a long delay occurs in the
middle of a packet -- in the middle of the data -- many XMODEM
implementations see that as meaning there has been data lost.  These
delays result in the following symptoms:
  o The receiver cannot successfully receive even the first block of
data.
  o The receiver consistently <nak>s blocks or <nak>s a majority of
blocks, although eventually receives the file.
  o The receiver just suddenly gives up in the middle of a seemingly
successful file transfer.
  o The receiver has great difficultly in receiving the file, and gives
up anywhere from 5 to 20 blocks through the transfer.
  o The file transfer proceeds very smoothly with several successfully
transfered blocks when all of a sudden every block transmitted is
rejected (<nak>ed) by the host.
  Note that all of these problems are indistinguishable from other
communications problems (e.g., noisy phone lines, bad parity settings).
A key question to ask people who are having XMODEM problems is "Have you
ever successfully done a XMODEM transfer to CompuServe?"  If the answer
is yes, then the following problems may be at fault.
      Delays within blocks
  The XMODEM documentation recomends that a gap of more than 1 second be
treated as a breakdown of communications.  On a microcomputer, this
makes sense -- there is no reason for a dedicated micro computer to
suddenly stop transmitting and then resume.  But on CompuServe's systems
and network, a 1 second delay is not only possible, but happens
frequently!
  If the microcomputer decides that this delay is a breakdown of some
sort, it will send a <nak> to CompuServe, requesting that the block be
retransmitted. Unfortunately, the rest of the first block is still "in
the pipe" -- and when the receiver gets this block the receiver may do
anything from abort the transfer to ignore it.  Assuming the receiver
handles the rest of the block gracefully (and the rest of the block
doesn't look like the start of another block), the host will see the
<nak> the receiver sent and retransmit the block.  If there's a delay in
the middle of that transmission, the receiver will <nak> it too, and so
on forever.
  Thus, when the receiver is too sensitive to delays in the middle of
transmissions, either the receiver gives up very quickly or the receiver
<nak>s every block transmitted.
     Delays between blocks
  Fortunately, most implementations of the XMODEM protocol aren't that
sensitive to delays in the middle of blocks.  But other delays can cause
problems too.  When a block is received by the microcomputer, for
example, the micro will almost immediately <ack> or <nak> the block and
wait for the next block to be sent.  The XMODEM specification [1] states
that if the next block does not arrive within 10 seconds, the receiver
should send its <ack> or <nak> again.
  Ten seconds is not a very long time, however, when the network and/or
mainframe is heavily loaded.  Often, what will happen is that the <ack>
or <nak> will arrive at the host, the host will begin transmission of
the next block, but the block won't make it to the micro in time. Then,
the micro transmits a <nak>, even though the host has correctly received
the first <ack>/<nak>.
  What happens, then, is that a <nak> enters the network, even though
the host has seen and responded to the first <ack> or <nak>.  After
that, things can easily degrade.  The host may find itself one block
ahead of the receiver, causing the receiver to give up on the spot. The
host may find itself stuck one <ack> or <nak> behind the receiver, which
could result in a successful, although very difficult, file transfer.
And the network problems could be severe enough -- or the micro
sensitive enough -- that the micro goes through about 6 or so blocks
(mostly <nak>s with a few <ack>s) and gives up.
      Network Flow Control
  When the user is sending data to CompuServe, the node will send an
XOFF (S) character to the micro if the micro is transmitting faster than
the node can send the data to the host.  This happens even during an
XMODEM transfer (although very infrequently).  If the micro
misinterprets the S as a <nak>, it will immediately retransmit the block
-- causing the network to send even more Ses and the micro to see even
more naks.  Usually what happens is that the micro thinks that every
block it transmits is being <nak>ed, and the micro gives up almost
immediately. This problem can strike anytime during an upload to the
host, and things can be proceeding very smoothly upto that point.
  Timing suggestions and hints
  To overcome and avoid these problems, an XMODEM protocol
implementation should wait 20 seconds before sending a <nak> on a lost
block, wait at least 10 seconds during delays in the middle of a block,
and honor (or at least ignore) flow control from the node during
uploading of files.
  Many programs which have timing problems with CompuServe can be
patched to relax their timing restrictions.  A typical place to look is
for calls to a "timed input" routine (where the routine will only wait
so long for a character to arrive). Either patching that routine (make
it wait twice as long, perhaps) or patching the code that calls the
routine (to use a longer time out value) would help to make the XMODEM
work on CompuServe.
   Host file Format Concerns
  While almost all microcomputers have an 8 bit word (or multiple of 8
bits), CompuServe has a 36 bit word. Text files are stored with 7 bit
bytes (5 of them per word). While this poses no problems for pure text
files (as the ASCII character set is defined for only 7 bits of data),
"binary" files cannot be stored as is on our host systems (an example of
binary data would be an executable program, or a WordStar file).  Files
in which 8 bits of data per byte must be preserved -- binary files --
are stored in a special file format (currently Intel hex format).
  Thus, when people upload or download to CompuServe using XMODEM, they
are asked:
 Transfer types available,
  1 - ASCII  (7 - bit)
  2 - Binary (8 - bit)
Please make a selection:
  People often pick the wrong answer, the results are either an
unsuccessful or useless upload or download.
      The correct approach
  For uploading, the choice of a transfer type can be as simple as:  "If
it's a text file, use ASCII.  If it's not, use binary."
  For downloading, the correct transfer type is the same one that was
used to upload the file, i.e., if the file was uploaded with an ASCII
transfer it must be downloaded with an ASCII transfer;  if the file was
uploaded with a binary transfer it must be downloaded with a binary
transfer.
  At the moment, it is a problem for users to determine which type the
file was uploaded in. Many SYSOPs have the file's description specify
the correct approach for downloading.  Other SYSOPs enforce the
convention that files with a ".BIN" extension should be downloaded with
the binary transfer while other files should use the ASCII transfer.  It
is best to ask what policy is in use if there is some doubt.
  In the future, the SIG program will be improved so that the choice of
which transfer type won't be asked during a download. bl
       What happens if...
  The user downloads a binary file with ASCII mode?
  The user gets the Intel hex format of the file.  The downloaded file
can be salvaged by use of a program to convert Intel hex format back to
binary. Currently, the IBM Novice forum (PCS-129) has such a program
available.
  The user downloads an ASCII file in binary mode?
  The user usually receives one or two blocks of garbage data, at best.
  The user uploads a binary file in ASCII mode?
  The file transfer will not succeed, and any files left over after the
upload will be useless.
  The user uploads an ASCII file in binary mode?
  The file transfer will succeed, but the uploaded file will be encoded
into Intel hex
format.  Thus, any people who downloaded the file in ASCII mode will
have the hex representation of the file.  People who download the file
in Binary mode, however will be able to receive the file correctly.
          PC-TALK III
  PC-Talk will work fine with CompuServe, so long as the user is running
PC-Talk in 8 bits / no parity mode.  The most recent version(s) of
PC-Talk are set up to switch to 8 bits / no parity automatically on an
XMODEM transfer, but these versions are still rare in the user
community.
  By default, CompuServe communicates in 7 bits, even parity.  Thus,
before PC-Talk can be thrown into 8 bits no partiy, the user must tell
CompuServe to talk 8 bits no parity.
  The steps involved in making this change are as follows:
     1.  The user must log into
         CompuServe as usual
         (i.e., 7 bits even
         parity).
     2.  The user must then run
         the Default program.
         This program can be
         reached either by
         typing "R DEFALT" from
         command mode in the
         personal file area (the
         "OK" prompt), or by
         typing "GO DEFALT" from
         any "!"  prompt.
     3.  In Default, the user
         should select option
          5, "View or Change
         current terminal
         parameters."  Then, he
         should select option
          8, "Parity is", change
         parity to ZERO, and
         then exit the default
         program, making all
         changes permanent.
     4.  At this point, PC-Talk
         can be switched into 8
         bits no parity.  On
         some modems (but not
         most of the Hayes line
         of modems), doing this
         switch will cause the
         modem to hang up.
         Thus, it may be
         advisible to log off
         CompuServe before
         switching to 8 bits no
         parity.
     5.  Once PC-Talk is running
         in 8 bit mode, it is
         possible to easily
         upload and download
         using XMODEM.
  The next time the user dials into CompuServe (with PC Talk set to 8
bits no parity) and types control-c to catch the system's attention, the
"User ID:"  prompt will be garbled. Once the system recognizes the User
ID, however, the password prompt will be presented in clear text.  Thus,
users should just muddle through the garbled User ID prompt and
everything will work well after that.
  If the user's modem does not hang up when the parity setting is
changed, it is also possible to change to 8 bits no parity just before
performing an XMODEM transfer, and change back to 7 bits even parity
when it completes.  This is a rather involved, manual process, though,
and is not recomended.
  Note:  Putting PC-Talk into 8 bits no parity is necessary even to
upload or download ASCII files.