==================================================================
       EEEEEEE  MM   MM  IIIIIII  L       Y     Y        5555555   22222
       E        M M M M     I     L        Y   Y         5        2     2
       E        M  M  M     I     L         Y Y          555555         2
       EEEE     M     M     I     L          Y     ---         5   22222
       E        M     M     I     L          Y                 5  2
       E        M     M     I     L          Y           5     5  2
       EEEEEEE  M     M  IIIIIII  LLLLLLL    Y            55555   2222222
       ==================================================================
    
    
    
    
    
                                       A
                               Simulator/Emulator
                                    for the
                                 8051 and 8052
    
    
    
    
    
                                  Release 1.3
    
                               Revised 04-Jan-94
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
                       Copyright 1991-1994 Dave Dunfield
                              All rights reserved

    EMILY: An 8051/52 simulator                                      Page: 1


    1. INTRODUCTION
    
          EMILY is a software simulator for the 8051 and  8052  families  of
       processors. It provides a powerful  debugging  environment,  offering
       many features:
    
       - Supports full 64K of PROGRAM and  64K  of  DATA  memory.  DATA  and
         PROGRAM memory may also be overlapped into  a  single  64K  address
         space.
    
       - Hardware emulation mode communciates with the  target  system,  and
         allows you to include the physical I/O lines, timers etc.  in  your
         simulation.
    
       - Single step, Multi Step, Animate and Full Speed execution modes.
    
       - Simultanious on-screen displays of  program  disassembly,  internal
         memory, CPU registers and simulation messages.
    
       - Full screen editors for CPU registers, Special  Function  Registers
         (SFR's), and each of the INTERNAL, EXTERNAL DATA and PROGRAM memory
         spaces. All of the above may be viewed/altered at any  time  during
         the debugging session.
    
       - Multiple breakpoints are transparent to the user program.
    
       - Supports the additional SFR's and internal RAM of the 8052 series.
    
       1.1 System Requirements
    
             EMILY will run on any IBM PC/AT/PS2 compatible  system  with  a
          MDA/CGA/EGA or VGA display, two COMM ports, and at least  192K  of
          free system RAM.
    
          - If hardware emulation or serial I/O are not used, only one  COMM
            port is required.
    
          - If Overlapped data/program memory is used, only 128K of free ram
            is required.
    
          - Some CGA displays may exibit "snow" or flicker during high speed
            screen updates. This effect will not occur with MDA, EGA or  VGA
            displays.

    EMILY: An 8051/52 simulator                                      Page: 2


    2. STARTING UP EMILY
    
          If you are using the optional hardware emulation mode, insure that
       the resident control software (supplied) is inserted into the  target
       system, and that the PC running EMILY  is  connected  to  the  target
       systems serial port  via  COM2.  Power  on  the  test  system  before
       starting EMILY. The resident control software  must  be  active  when
       EMILY "looks" for it.
    
          EMILY is invoked by typing her name at the DOS command  line.  You
       will be greeted with a "welcome" screen which displays a reminder  of
       the command line syntax and the copyright message. This  screen  will
       remain on the display for about 5 seconds (10  seconds  in  the  demo
       version). Pressing any key while this screen is visible  will  bypass
       this delay, and proceed directly to the main control panel.
    
          If EMILY is given a file name on the command line, she loads it in
       the same manner as if the 'L'oad command had been  used  from  within
       the main control panel.

    EMILY: An 8051/52 simulator                                      Page: 3


          EMILY also accepts several option switches on the command line:
    
            /Hardware[:n]  - Enables the hardware emulation feature to cause
                             EMILY to interact with the target  system  when
                             performing I/O accesses.  This  option  may  be
                             followed by a  ':'  and  a  numeric value which
                             defines the BAUD RATE to be used to communicate
                             with the target system. Default is 28800.
    
            /Mono *        - Inhibits the  color display, even  if  a  color
                             adapter is present. This option may  be  useful
                             if your monitor/adapter combination provides an
                             unpleasent or unusable display for EMILY.
    
            /Overlap       - Joins EXTERNAL DATA  and PROGRAM  memory into a
                             single 64K address space which can be  accessed
                             with either MOVX or MOVC. This is equivalent to
                             a hardware implementation in which the PSEN and
                             RD signals are ANDed together.
    
            /Reset         - Causes EMILY to de-assert the RTS line when she
                             initializes the serial port. This option may be
                             required when using  EMILY  with older versions
                             of our "BD52" single board computer.
    
            /Swapcom       - Exchanges the operation of the two serial ports
                             on the PC.  When this option is used, COM1 will
                             be used to communicate with the  target system,
                             and COM2 is used for serial I/O redirection.
    
        * Note: If some of the EMILY windows appear  to  be  an  un-readable
                washed-out yellow color, try adjusting the color contrast on
                your monitor. Those windows should be an easy to read brown.
    
          If you are using the '/Hardware' option, and EMILY  is  unable  to
       establish communication with the target system, you will see an error
       message flashing on the screen. EMILY will keep trying, allowing  you
       to debug the connection. You may also press the ESCAPE key to disable
       hardware emulation, and proceed with a software only simulation.

    EMILY: An 8051/52 simulator                                      Page: 4


    3. USING EMILY
    
       3.1 The Main Control Panel
    
             Once EMILY is up and running, you will be  presented  with  the
          "Main Control Panel", which consists of four "windows" displaying:
    
            - A disassembly of program memory       (Upper LEFT)
            - The contents of CPU registers         (Upper CENTER)
            - The contents of INTERNAL MEMORY       (Upper RIGHT)
            - Informational messages from EMILY     (Lower portion)
    
             All of EMILY'S functions are  accessed  by  command  characters
          entered from this screen:
    
          3.1.1 A - Animate execution
    
                This function begins execution of the user program (from the
             address in the PC register). As each instruction  is  executed,
             EMILY will display the  instruction  being  executed,  the  CPU
             registers, and the contents of internal RAM in the  appropriate
             windows.
    
                When you enter the 'A' command, EMILY will  prompt  you  for
             the number of instructions to animate. Pressing return (without
             entering  a  number)  will  cause  the  animation  to   proceed
             non-stop. Pressing <escape> will return you to the Main Control
             Panel.
    
             The animation will terminate when:
    
                - The requested number of instructions have been stepped.
                - A breakpoint is encountered.
                - The illegal opcode ($A5) is encountered.
                - The <escape> key is pressed on the PC console.
    
          3.1.2 B - set Breakpoint
    
                This command sets a breakpoint such that  program  execution
             under the 'A'nimate, or  'G'o,  commands  will  stop  when  the
             breakpoint address is encountered.
    
                Up to 10 breakpoints may be in effect at the same time.
    
                You will be prompted for  the  address  (in  HEX).  Pressing
             return (without entering an address) will cause the  breakpoint
             to be  set  at  the  current  program  counter  (PC)  location.
             Pressing <escape> will return you to the main control panel.
    
                EMILY stores the breakpoint addresses internally in a simple
             zero terminated list. This allows  her  to  avoid  searching  a
             fixed size table, and helps  speed  up  the  operation  of  the
             program, especially when there are few breakpoints.  This  does
             however cause the restriction that you cannot set a  breakpoint
             at address zero ($0000).

    EMILY: An 8051/52 simulator                                      Page: 5


          3.1.3 C - Change register
    
                You will be prompted for the CPU register to change. Enter a
             character from the following list, ESCAPE to abort, or F1 for a
             reminder:
    
                A   - A accumulator
                B   - B accumulator
                D   - Data pointer (DPTR)
                S   - Stack pointer
                P   - Program counter
                W   - processor status Word
                0-7 - general register 0-7
    
                After you have selected the register, you will  be  prompted
             for the new contents (in HEX).
    
          3.1.4 D - edit Data memory
    
                This command allows you to edit EXTERNAL DATA  memory  using
             EMILY's  built  in  memory  editor.  See  the  "Memory  Editor"
             section.
    
          3.1.5 F - display/edit special Function registers
    
                The names and contents of all SFR's are displayed in a menu.
             To change a register, enter the character preceeding  the  ':',
             immediately to the left of its name. You will be  prompted  for
             its new contents.
    
                If multiple columns of SFR's are  defined,  use  <space>  to
             select the column to edit.
    
                When debugging  with  the  hardware  emulation  option,  the
             values read/and written to the SFR's will  reflect  the  actual
             state of the hardware lines etc. on the  target  system  board.
             Pressing any key while in this menu will refresh  the  display,
             and make visible any changes which have occured on  the  target
             system I/O lines etc.
    
                When debugging without the hardware emulator  option,  SFR's
             are simply stored internaly within EMILY's memory.

    EMILY: An 8051/52 simulator                                      Page: 6


          3.1.6 G - Go: execute program
    
                This  function  begins  high-speed  execution  of  the  user
             program (from the address in the PC register).
    
                When you enter the 'G' command, EMILY will  prompt  you  for
             the number of instructions to execute. Pressing return (without
             entering a number) will cause the program to proceed  non-stop.
             Pressing <escape> will return you to the Main Control Panel.
    
             Program execution will terminate when:
    
                - The requested number of instructions have been executed.
                - A breakpoint is encountered.
                - The illegal opcode ($A5) is encountered.
                - The <escape> key is pressed on the PC console. *
    
             * NOTE: If you are using 'Local' serial I/O mode, ESCAPE offers
             you a menu of execution I/O functions. See the F3  command  for
             more information.
    
          3.1.7 I - edit Internal memory
    
                This command  allows  you  to  edit  INTERNAL  memory  using
             EMILY's  built  in  memory  editor.  See  the  "Memory  Editor"
             section.
    
          3.1.8 J - Jump to PC
    
                This command re-positions the disassembly display window (if
             necessary) to display the instruction addressed by the  current
             CPU Program Counter (PC).
    
          3.1.9 K - Kill all breakpoints
    
                Removes ALL breakpoints after prompting for permission to do
             so.
    
          3.1.10 L - Load program image
    
                Prompts for the name of a file, and loads  it  into  PROGRAM
             memory. The file must  be  in  either  INTEL  or  MOTOROLA  hex
             download format.
    
          3.1.11 N - Next disassembly window
    
                Advances the disassembler to display the  following  screen.
             Subsequent 'N' commands  will  proceed  to  disassemble  higher
             memory addresses.
    
          3.1.12 P - edit Program memory
    
                This command allows you to edit PROGRAM memory using EMILY's
             built in memory editor. See the "Memory Editor" section.

    EMILY: An 8051/52 simulator                                      Page: 7


          3.1.13 R - Remove a breakpoint
    
                Prompts for the address, and if a breakpoint is set at  that
             address, it is removed. Pressing return  (without  entering  an
             address) will remove the  breakpoint  at  the  current  program
             counter (PC) location.
    
          3.1.14 T - Traceback viewer
    
                In all execution modes, EMILY keeps track of the  last  4095
             instructions executed. By entering the  traceback  viewer,  you
             can examine this recording, and determine program  activity  up
             to 4095 instructions preceeding the one on which execution last
             stopped.
    
                The following command keys are available in the viewer:
    
                Up   - Backup the display 1 instruction.
                Down - Advance the display 1 instruction.
                PgUp - Backup the display 50 instructions.
                PgDn - Advance the display 50 instructions.
                Home - Position to the beginning of recording.
                End  - Position to the end of recording.
                F1   - Display a help summary.
                F2   - Prompt for position & move.
                F3   - Search backward (in time) for address. *
                F4   - Search forward  (in time) for address. *
                Esc  - Exit the Traceback viewer.
    
              * If you press <return> without entering an address, the search
                commands will look for the previous or next instance of the
                instruction at your current position in the traceback buffer.
    
                Only the instruction executed  is  saved  in  the  traceback
             viewer, the contents of registers, RAM etc. are not recorded.
    
                The instruction at position 0 in the traceback buffer is the
             one to which the current  PC  points,  and  has  not  yet  been
             executed.
    
          3.1.15 V - Vector to interrupt
    
                This function prompts you with a menu of the available  8052
             interrupts. Use the arrow keys to position the  cursor  bar  to
             the interrupt you desire to simulate, and press ENTER to select
             it. You may use ESCAPE to cancel the function and return to the
             Main Control Panel.
    
                EMILY will simulate a long call (LCALL) to the corresponding
             interrupt vector address by saving the current Program  Counter
             on the CPU stack, and reloading it with  the  vector.  Any  SFR
             bits normally set when the particular interrupt occurs will  be
             set at this time.

    EMILY: An 8051/52 simulator                                      Page: 8


          3.1.16 F1 - Help display
    
                Pressing this key displays a summary of the  EMILY  commands
             which are available from the Main Control Panel.
    
          3.1.17 F2 - Set Disassembler Address
    
                Prompts for  an  address  (in  HEX),  and  re-positions  the
             disassembler window to display instructions beginning  at  that
             address.
    
          3.1.18 F3 - Setup Serial Port
    
                Opens a window displaying the (B)audrate,  (P)arity,  (D)ata
             bits and (S)top bits which are  currently  configured  for  the
             PC's COM1 serial port.
    
                Press B, P, D or S to cycle to the next corresponding entry.
    
                When Baudrate is selected as 'Local', EMILY  will  re-direct
             the  programs  serial  accesses  to  the  message  window.  Any
             characters which are written to SBUF  will  be  output  in  the
             message window, and  any  character  which  are  typed  at  the
             keyboard will appear as incomming serial data. When  this  mode
             is active, Pressing ESCAPE in the 'G'o command brings up a menu
             of execution options:
    
                End simulation  - Stops the 'G'o command.
                Send ESCAPE     - Send ESCAPE through as a charcter.
                Zoom window     - Switch to full screen I/O window.
    
                If 'Local' is not selected, EMILY  re-directs  the  programs
             serial accesses to the PC's  COM1  serial  port,  however,  for
             maximum  flexibility,  the  actual  data  format  used  may  be
             configured by this menu.
    
                EMILY allows you to "fine tune" a baud rate,  by  using  the
             Up/Down keys. Note that the  available  baud  rate  values  are
             determined by the PC COMM  port  hardware,  and  may  not  fall
             exactly on the value you wish to use.
    
                Asynchronous communication is specified to work properly  as
             long as the device is operating within 5% of the intended  baud
             rate.
    
                For example:
    
                        Desired baud rate       : 1500
                        Allowable range (+/- 5%): 1425-1575
                        Closest PC baud rate    : 1496
    
                In the above example, the baud rate produced is within  0.3%
             of  the  desired  value,   and   is   therefore   well   within
             specifications.

    EMILY: An 8051/52 simulator                                      Page: 9


          3.1.19 <space> - Single step one instruction
    
                Every time you press the <space> bar, EMILY will execute one
             instruction, and update the on-screen displays.
    
          3.1.20 PgDn - Advance IRAM display page
    
                Pressing this  key  advances  the  internal  memory  display
             window by one page (64 bytes).
    
          3.1.21 PgUp - Backup IRAM display page
    
                Pressing this key  backs  up  the  internal  memory  display
             window by one page (64 bytes).
    
          3.1.22 Down - Advance IRAM display line
    
                Pressing the "down arrow" key advances the  internal  memory
             display window by one line (4 bytes).
    
          3.1.23 Up - Backup IRAM display line
    
                Pressing the "up arrow" key backs  up  the  internal  memory
             display window by one line (4 bytes).

    EMILY: An 8051/52 simulator                                      Page: 10


       3.2 The Memory Editor
    
             When you activate the 'D', 'I' or 'P' commands  from  the  main
          control panel, EMILY will invoke its internal "Memory  Editor"  to
          access the desired memory area. When you are within  this  editor,
          the following commands are available:
    
          3.2.1 F1 - Help display
    
                Pressing this key displays a summary of the  EMILY  commands
             which are available from within the Memory Editor.
    
          3.2.2 F2 - Set Edit Address
    
                Prompts for an address (in HEX), and re-positions the editor
             display and cursor to edit at that address.
    
          3.2.3 F3 - Toggle Edit Mode
    
                EMILY allows two edit modes, HEX  and  ASCII.  When  in  HEX
             mode, your cursor will be positioned in the hexidecimal display
             portion of the memory  memory  dump,  allowing  you  to  change
             memory by entering a new value as two  hexidecimal  characters.
             When in ASCII mode, your cursor will  be  positioned  over  the
             ASCII portion of the dump, and  you  can  replace  memory  with
             ASCII text typed at the keyboard.
    
                Pressing F3 will toggle between HEX and ASCII mode,  causing
             your cursor to switch between the corresponding portion of  the
             memory display.
    
          3.2.4 Up - Move up 1 line
    
                Pressing the UP ARROW causes the cursor to move  upwards  on
             the screen by one line. This reduces the memory edit address by
             16 bytes.
    
          3.2.5 Down - Move down 1 line
    
                Pressing the DOWN ARROW causes the cursor to move  downwards
             on the screen by one  line.  This  increases  the  memory  edit
             address by 16 bytes.
    
          3.2.6 Left - Move left 1 byte
    
                Pressing the LEFT ARROW causes the cursor  to  move  to  the
             left by one byte position. This reduces the memory edit address
             by 1 byte.
    
                If the cursor is already at the left hand  margin,  it  will
             wrap around to the rightmost position of the previous line.

    EMILY: An 8051/52 simulator                                      Page: 11


          3.2.7 Right - Move right 1 byte
    
                Pressing the RIGHT ARROW causes the cursor to  move  to  the
             right by one byte position. This in increases the  memory  edit
             address by 1 byte.
    
                If the cursor is already at the right hand margin,  it  will
             wrap around to the leftmost position of the following line.
    
          3.2.8 PgUp - Move back 1 page
    
                Pressing the PGUP key causes the editor  to  move  back  one
             display page. This reduces  the  memory  edit  address  by  256
             bytes.
    
          3.2.9 PgDn - Move forward 1 page
    
                Pressing the PGDN causes the  editor  to  move  forward  one
             display page. This increases the memory  edit  address  by  256
             bytes.
    
          3.2.10 Home - Move to start of line
    
                Pressing the HOME key causes  the  cursor  to  move  to  the
             leftmost position of the line it is currently on. If the cursor
             was already in the  leftmost  position,  it  is  moved  to  the
             leftmost position of the preceeding line.
    
          3.2.11 End - Move to end of line
    
                Pressing the END key  causes  the  cursor  to  move  to  the
             rightmost position of the line  it  is  currently  on.  If  the
             cursor was already in the rightmost position, it  is  moved  to
             the rightmost position of the following line.
    
          3.2.12 Ctrl-PgUp - Move to start of memory
    
                Pressing the CTRL and  PGUP  keys  re-positions  the  editor
             display and cursor to address $0000 at the start of the  memory
             block.
    
          3.2.13 Ctrl-PgDn - Move to end of memory
    
                Pressing the CTRL and  PGDN  keys  re=positions  the  editor
             display and cursor to the  highest  address  available  in  the
             memory block.

    EMILY: An 8051/52 simulator                                      Page: 12


       3.3 Hardware Emulation
    
             EMILY supports a hardware emulation mode, which provides access
          to most of the physical I/O ports, timers  etc.  from  the  target
          system in your simulation.
    
             The  target  system  must  be  running  the  supplied   control
          software, which interacts with EMILY, and perform the I/O accesses
          upon her commands. The serial port of the target  system  must  be
          connected to the COM2 serial port of the PC.
    
             There are a few restrictions which apply:
    
             - The target system must provide access to the CPU serial port.
    
             - There is an approximatly 0.7 MS delay when accessing the  I/O
               ports and other physical hardware. This  occurs  due  to  the
               serial activity required to communicate the data to and  from
               the target system.  For  most  applications,  this  delay  is
               acceptable, particularly in  the  stop/start  environment  of
               simulation and debugging. NOTE: If you are using  a  baudrate
               to communicate with the target system which is lower than the
               default (28800), this delay will be longer.
    
             - The control software uses TIMER1 internally to  generate  the
               baud rate clock for its serial port. This means  that  TIMER1
               is unavailable during the  simulation.  If  your  application
               uses the serial port, we recommend you also use TIMER1 as the
               baud rate generator. Since EMILY has a  separate  setup  memu
               for serial port speed, parity etc. It will  not  affect  your
               program that TIMER1 is disabled during the simulation. Simply
               press F3 at EMILY's main control panel, and select the serial
               parameters you desire.

    EMILY: An 8051/52 simulator                                      Page: 13


             When using this  (Hardware  Emulation)  feature,  the  Resident
          Control Firmware should be running in  the  target  system  BEFORE
          executing EMILY. Be sure to specify '/H:<speed>' parameter on  the
          command line when starting EMILY.
    
             The value of <speed> depends on the  target  systems  operating
          frequency. The following table shows the speeds which can be  used
          with several common  crystal  frequencies  without  modifying  the
          supplied Resident Control Firmware:
    
                    Freq (Mhz)          Speed -> Actual
                    ----------------------------------------
                    11.0592             28800 -> 28800  0.0%
                    11.0                28646 -> 28800  0.5%
                    9.0                 23438 -> 23040  1.7%
                    7.3728              19200 -> 19200  0.0%
                    5.0                 13020 -> 12800  1.7%
                    4.0                 10417 -> 10473  0.5%
                    3.68                9600  -> 9600   0.0%
                    3.59                9349  -> 9600   2.7%
                    3.0                 7813  -> 7680   1.7%
                    2.0                 5208  -> 5236   0.5%
                    1.84                4800  -> 4800   0.0%
                    1.0                 2604  -> 2618   0.5%
    
             At the beginning of the supplied KERNAL.ASM  file  is  a  large
          comment which describes how to change the baud  rate  constant  to
          obtain other serial port speeds. The following table shows  speeds
          which can  be  used  with  other  common  crystal  frequencies  by
          altering the "BAUD" value in the KERNAL.ASM file:
    
                Freq (Mhz)  BAUD Value      Speed -> PC Speed
                ------------------------------------------------
                12.0            3           10417 -> 10473  0.5%
                10.0            2           13020 -> 12800  1.7%
                8.0             2           10417 -> 10473  0.5%
                7.0             2           9116  -> 8862   2.8%
                6.0             2           7813  -> 7680   1.7%

    EMILY: An 8051/52 simulator                                      Page: 14


       3.4 Messages
    
             During the course of operation, EMILY may display the following
          messages in the message window located in the lower portion of the
          screen:
    
          3.4.1 All Used!
    
                You have tried to enter a  breakpoint,  when  all  available
             breakpoints are in use. EMILY allows up to 10 code  breakpoints
             to be active at any one time.
    
          3.4.2 Animating at XXXX
    
                Indicates that EMILY has  commenced  animated  execution  of
             your program, beginning at the address 'XXXX'.
    
          3.4.3 Already set!
    
                Issued to indicate that the address at which you have  tried
             to set a breakpoint is already active as a breakpoint.
    
                This message will also  result  of  you  attempt  to  set  a
             breakpoint at address zero ($0000).
    
          3.4.4 Breakpoints: [XXXX ...]
    
                This message shows the currently set  breakpoint  addresses,
             and is issued whenever any  command  involving  breakpoints  is
             performed.
    
          3.4.5 Executing at XXXX
    
                Indicates that EMILY has commenced full  speed  exection  of
             your program, beginning at the address 'XXXX'.
    
          3.4.6 Code and data are overlapped
    
                This message results from the use of the  '/Overlap'  switch
             on the EMILY command line, and indicates that the external CODE
             and DATA memory address  spaces  are  combined  into  a  single
             overlapping 64K segment.
    
          3.4.7 Code and data are separate
    
                Indicate that EMILY  has  established  separate  64K  memory
             address spaces for the code and data, resulting in  128K  total
             external memory.
    
          3.4.8 FILENAME: Bad checksum
    
                EMILY  has  encountered  a  record  containing  a  incorrect
             checksum value while attempting to 'L'oad the named file.

    EMILY: An 8051/52 simulator                                      Page: 15


          3.4.9 FILENAME: Demo limit exceeded!
    
                This message occurs only in the "Demonstration"  version  of
             EMILY, and indicates that you have  attempted  to  'L'oad  more
             than 500 bytes of code. The demonstration release  is  intended
             only to allow you to  check  out  EMILY's  features,  you  must
             purchase the "production" version if  you  intend  to  use  the
             program for serious development and debugging.
    
          3.4.10 FILENAME: Invalid HEX record
    
                EMILY  has  encountered  an  improperly  formatted  download
             record while attempting to 'L'oad the named file.
    
          3.4.11 FILENAME: N bytes loaded
    
                The  indicated  number  of  bytes  have  been   successfully
             'L'oaded from the named file.
    
          3.4.12 FILENAME: Unable to access
    
                EMILY was unable to open and read the named file.
    
          3.4.13 Hardware emulation is disabled
    
                Indicates that the EMILY  is  running  as  a  software  only
             simulator, and will emulate special  functions  registers  etc.
             using internal RAM memory.
    
          3.4.14 Hardware emulation is enabled
    
                Issued if the "/Hardware"  switch  was  used  on  the  EMILY
             command line, and the Resident Control Software in  the  target
             system has been detected. In this mode  of  operation,  special
             function register accesses  are  communicated  to  the  control
             software, and result in physical activity on the target system.
    
          3.4.15 Stopped at XXXX
    
                Indicates that EMILY has stopped execution of you program at
             the indicated address. This message is appended to the  initial
             message indicating that execution had commenced.
    
          3.4.16 Target system is not responding!!!
    
                Indicates that the "/Hardware" option switch was used on the
             EMILY command line, but EMILY  cannot  establish  communication
             with the target system. EMILY will keep trying, allowing you to
             attempt to debug the connection. You may also press the  ESCAPE
             key, to disable hardware emulation mode,  and  proceed  with  a
             software only simulation.

    EMILY: An 8051/52 simulator                                      Page: 16


          3.4.17 XXXX: Not found
    
                This message is issued while in the 'T'raceback  viewer,  to
             indicate that an address 'XXXX' you have searched for does  not
             occur between your current position, and the start/end  of  the
             traceback buffer.




                          EMILY: An 8051/52 simulator

                               TABLE OF CONTENTS


                                                                         Page

     1. INTRODUCTION                                                        1

        1.1 System Requirements                                             1

     2. STARTING UP EMILY                                                   2


     3. USING EMILY                                                         4

        3.1 The Main Control Panel                                          4
        3.2 The Memory Editor                                              10
        3.3 Hardware Emulation                                             12
        3.4 Messages                                                       14