In this reference, I try to follow the path you would
usually take when creating a Profile - starting with the
general and getting more specific.  However, the upper
layers constantly refer to the lower layers, so a solid
understanding of the guts of X-or is a prerequisite for
understanding the rest of it.  Suffice to say that no matter
how great your reading comprehension skills are, you'll have
to read this thing more than once.  The best way to learn is
by doing, so we've provided different tutorials at the end
to help you put your X-or knowledge into action.

X-or can be broken down into two areas: the Editor stuff and
the Librarian stuff.  The general practice for creating a
profile is to first decide on the file structure you want,
then deal with the System Exclusive protocol via X-or's
control language (XORCL).  When all the basic MIDI Librarian
tasks are working, one then proceeds to the Editor stuff.

Synths with only one type of data are a snap (relatively
speaking).  More than one data type requires more fore-
thought, although tools in E-or will allow you to re-arrange
quite easily.  Anyhow, on with the show...



I. DESIGNING A PROFILE

OVERALL ORGANIZATION

The first thing you will need to do is determine how to
organize the instrument's data.  What will the bank file
format be?  What parts of the instrument do you wish to
support in your Profile?  For simple devices, this is easy -
but for complex synthesizers, it can be challenging.

A General Rule: A Profile should group together all data
types for an instrument which share a bank file, and this
bank file should contain at least all the stored data for an
instrument (that is, data which isn't necessarily active).

The reason Profiles contain multiple data types is to make
it easier for X-or to do inter-module communication.
Otherwise, X-or would have a tough time finding the Profiles
it needs quickly.  Also, it simplifies the setup process,
since in general it's just one Profile per machine.
Furthermore, it allows all the data types to share XORCL
routines, which are located at the "Machine" level, and not
at the "Datatype" level.

Your basic complex synth has a bank of single sounds, a bank
of multi-timbral setups, a program change table, system
global parameters, one or more microtuning tables, etc.  The
questions you must ask about each type of data are:
     a) Does the data type exist in stored (non-running or
     bank) format?  Usually, this will apply to only single
     and multi-timbral patches.  These data types should
     always share a bank type and a Profile.

     b) Does the data type have a meaningful dependence on
     bank (stored, non-running) data?  This may include
     Program Change Tables (mapping program changes to
     specific patches in the bank), or a Rhythm Channel
     Setup (mapping keys to patches).  These data types
     should also be included in the Profile, so that the
     Profile can use special X-or parameter objects to show
     bank patch names on the edit screen, instead of
     numbers.

     c) Does the data type potentially affect the status of
     other areas of the instrument?  A good example is a
     "System Global" patch, which may include the current
     mode or receive channel of the instrument.  An
     intelligent X-or profile uses special XORCL functions
     to communicate this information between data types, but
     they must be in the same Profile.

There are many options for handling data types which don't
fall under any of the above catagories:

     a) Is the data type so unlikely to be changed that it
     should be optional?  If so, maybe it should be in its
     own Profile.  There aren't many good examples, because
     it seems that almost every data type in an instrument
     is in some way related the other data types.  For
     instance, global parameters may include the Basic
     Receive Channel, and Microtune tables may be changed by
     a parameter somewhere in the single or multi-timbral
     patches.  However, X-or currently is only able to
     switch individual instruments (entire Profiles) on or
     off, so it is better to have things which may need to
     be turned off in a separate Profile, for now at least.

     b) Another option is to include the data type in the
     Profile, but don't store it in the Profile's bank
     format.  To do this, set the "total names" parameter on
     the Data Type Master screen to zero.  This avoids
     redundancy when a Performance is loaded.  However,
     having no bank file takes away the Randomize and Blend
     / Mingle features.  Most data which only exists in
     "running" form in the instrument isn't the type of data
     you would need to randomize anyhow, but if you do...

     c) You could make up your own bank format, allowing the
     data type to use the Randomize, Blend, Mingle and other
     features.  This bank would merely consist of a number
     of single patches.  If you do this, make sure both Get
     Bank and Send Bank are void (-1), so that they are
     properly disabled in the menu.

     d) If necessary, you could make the bank file identical
     to the single file.  This works, but it doesn't seem to
     buy any additional functionality.

     NOTE: If for any reason you have more than one bank
     file type in a Profile, keep in mind that X-or assumes
     that the first bank file type is the only important one
     (the only one saved and restored with the Performance).
FILE FORMATS

I do have a general way of laying out file formats, which
has grown out of the many editors I have done.  If people
stick to these guidelines, we may be able to minimize
situations where two profiles for the same instrument are
incompatible.

     a) The data should be in its most compact form, not
     necessarily the way it is transmitted.  X-or is set up
     to handle this in the TXDATA and RXDATA instructions
     (see XORCL below).

     b) The data format should not include any header
     information.  Include the size of the data only if it
     is variable, in which case it should be stored as a 4-
     byte long value at the beginning of the file.  Do not
     include sumcheck or EOX.

     (The obvious exception to these rules is if you are
     developing a general SYS EX filer, in which case you
     need to store data exactly as it comes in.)

     c) Store single patches in the bank first, followed by
     multi-timbral combinations, followed by any other
     stored data.  Often manufacturers release new synths in
     which the single patches are compatible with older
     models, to which they may have added new multi-timbral
     patches.  If data is stored this way in the bank, a
     file extension change is all that's required for a
     quick and dirty bank conversion.

     d) Any extra names are generally 16 characters each (no
     terminating 0), and always follow the data.  In a bank,
     a name would follow each patch IF the data could be
     sent patch by patch, rather than as one big bulk dump.
     If sent and received as one big block of data, then the
     extra names should be stored after the bank (this
     complicates the Load and Store Routines, as data and
     name need to be separately copied).

     d) Unfortunately, file extensions are way up in what's
     left of the ozone.  Perhaps we can communicate our file
     types and extensions through Dr. T's bulletin board,
     and in this way avoid Tower-of-Babel-like consequences.
STARTING FROM SCRATCH

The first thing you need to do is to set up the quantity and
sizes for all the Patch areas (see Machine Structure and
Module Structure), and open up the Performance Window.  Make
sure all Routine pointers are set to -1 (E-or should do this
automatically).  If you need to change the size of a patch
area, you must close the Performance window first.  Once the
Performance window is open, the MIDI functions become
available in the menus.  Then, one generally gets the XORCL
MIDI routines and name display working before proceeding to
the Parameter definitions and objects.



II X-OR MACHINE STRUCTURE

The outermost structure in a profile is the Machine.  This
tells X-or about the overall architecture of the machine -
how many data types, how many patch buffers for each, etc.
The Machine includes text for the device's name (which will
appear in X-or's Performance and Setup windows), the profile
programmer's name, the X-or version it was created for, the
ROM version of the instrument used to test the profile, and
the date and time the profile was last modified (these
appear in X-or's Info menu).  Also, the minimum and maximum
system exclusive channels may be set, although this is
presently not used by X-or.  X-or calls a "Machine Init
Routine" for each instrument when the program is booted.
This generally sends or receives whatever MIDI information
or commands are appropriate for initializing X-or/Instrument
communication (e.g. Enable Sys Ex, turn off Memory Protect,
etc.).

The most important information here is a) the total number
of data types in the Profile, and b) the number of patch
areas for each data type.  E-or must have this information
before opening the Performance window.

NOTE: Whenever you see something called "Routine" or "Rout",
this refers to a line number in the XORCL program (see
below).  All these values should be set to minus one (-1)
until you've done the associated XORCL program.
III X-OR CONTROL LANGUAGE

The most important part of X-or is the simplified assembly
language-like interpreted language which has special
functions to handle MIDI as well as some other particularly
tricky chores.  This language was created because of the
need for very flexible logic in the MIDI routines.  It is
simply impossible to codify all the crazy things that
manufacturer's do, let alone work around the various System
Exclusive bugs which exist in almost every piece of MIDI
hardware.  You will find that bugs, oversight, and plain old
stupidity are the norm -- just be happy if the instrument
you're working on doesn't have a bug which renders it
completely useless.

Most synthesizers are vaguely similar as far as bank and
patch I/O goes.  However, some instruments lead me to
believe that almost any type of insane protocol is possible.
Real problems may occur when you send certain parameters:
these annoying quirks can only be resolved with logic.  For
example, the ESQ-1 sends parameters in the form of a
controller message for which the parameter value needs to be
re-scaled.  One then finds that this re-scaling doesn't work
with some parameters, so special cases are needed.

The Control language lets you program functions which are
called by the higher levels of X-or.  Before calling the
function, X-or sets two arrays of variables - the "int"
(integer) array and the "adr" (long or address) array.  All
the global variables you are likely to need are in preset
locations in the arrays.  These arrays can be freely used
without affecting X-or (like local variables in a "C"
function).  There are some exceptions, so read on!

Each machine has its own byte (character) size array - the
so-called "XORCL MIDI String."  Usually this array is used
to set up messages to be sent or received, but really it can
be used for many things (e.g. to store an initialized patch
used in the XORCL Patch Init Routine).  This array is part
of the Profile, and the Profile is completely responsible
for it (i.e. X-or doesn't ever modify this area directly).

Like any programming language, XORCL has operations related
to program control (subroutines, goto statements, branching,
etc.), and data manipulation (arithmetic and logical
functions).  XORCL also has some fairly high level MIDI-
specific functions, for example a function to transmit data,
using any one of a number of data packing algorithms.

The program consists of variable length instructions.  Each
instruction includes one "opcode," which defines its length
and the meaning of the other parts of the instruction (if
any).  To reiterate: a certain line of the XORCL program is
called by X-or, after it has put all the potentially useful
global and local variable values into the XORCL arrays.
These variables may be considered "local" to the XORCL
program, and may be changed.  However, at the same time, all
the variables are global as far as our "program within the
program" is concerned (i.e. there are no values passed to or
from an XORCL subroutine)

To the left of the screen is the instruction editor.  It
lets you select the instruction opcode and all the arguments
(and choose the argument type).  To enter the instruction
into the program, use Paste (Ctrl-V, which is actually
"Insert As" in this case), Add (Ctrl-A), or Insert (which
inserts before the current instruction).  To edit a
particular line in the listing, first click on the line,
which moves the pointer to that line.  Use Cut (Ctrl-X) or
Copy (Ctrl-C) to copy the line to the editing area.

X-orcist Note: Cumbersome, maybe, but I'm working on it.  I
will eventually have pop-up menus to select opcodes and
arguments - in time, I think XORCL will be faster and easier
than most other languages.  The advantage is that you don't
need to type in text and have it interpreted.  The line
numbers are "word numbers," which I one day hope to replace
with some sort of titles.  They currently show the word
number at which the instruction begins (the XORCL program is
just a big bunch 'o' integers).  I also plan to add comments
for every line A.S.A.P.

Whenever you insert or delete an instruction, E-or tries to
keep track of all "referenced" instructions.  It goes
through the entire program, and modifies all higher numbered
references.  It also checks all the places in all the data
types where XORCL routines are called and modifies them as
well.  This works well, except when you insert or delete at
the exact instruction someone else is pointing to, in which
case E-or may not be able determine your intent.  E-or's
Insert function assumes that you are inserting before the
instruction, so it modifies any references.  The Paste
(Ctrl-V) insert does not modify references - instead, the
inserted line becomes the referenced line.  Use Paste if you
want to insert instructions at the beginning of a
subroutine.  Always be careful when you modify within a
branching "if-then-else" sort of structure.

Particularly tricky is the programming of forward logical
branching, since you may not know the number of the
instruction you're branching to.  I would suggest Inserting
the Branch instruction with the current line as the line
number for the "true" branch, then use Insert to insert the
code for the "false" branch, and then Paste to begin the
"true" branch.  I should point out that the tradeoff for the
inconvenience is that XORCL requires no interpretation or
compiling -- it's always ready to run, and runs exactly as
it will in X-or.
XORCL ARGUMENT TYPES

The language is pretty flexible about what type of argument
an instruction takes; most conversions between long, int,
and char are automatic and pretty transparent.  The argument
types are as follows:

     STR: a location in the Profile's MIDI string area (a
     table of bytes, stored with and used exclusively by the
     Profile).

     VAR: an integer variable.  There are 32 of these
     available.  Many are preset to certain global values
     before the XORCL function is called (such as
     SysExChnl), and are intended to be used as such. Use
     the Temp#x variables for passing values to subroutines,
     or for temporary computations.

     ADR: a long variable.  There are 16 of these available,
     some preset to global addresses which the XORCL
     function may need to know (e.g. PatchAdr).  These can
     also be used for long-sized variables, if need be.  Use
     the TempAdr#x addresses for passing addresses to
     subroutines, or for long variables.

     CON: an integer constant.

     &STR: the address of (i.e. pointer to) a specific
     location in the Profile's MIDI string area.  This form
     is to be used in instructions which require an address
     (TXSTRG, RXSTRG, TXDATA, RXDATA, BCOPY).

     *ADR: the contents of the location pointed to by the
     specified address (byte-sized).  Note that "indirect"
     addressing of data is limited -- to get the contents of
     the 12th byte of a patch, one would first have to add
     12 to the patch address.

     *ADRW, *ADRL: same as *ADR, but the data is either word
     or long-sized (68000 format, must be on even address).

X-orcist Note: Indirect addressing is not XORCL's forte, but
at least there is a way to do it.  If anyone has any
brilliant ideas about XORCL, leave an E-MAIL message for me
on the BBS.
XORCL INSTRUCTIONS

Here are the XORCL instructions, with a brief description of
the arguments each takes:

     RETURN: needs no argument, returns from a subroutine,
     or to the main program when done.

     GOSUB,GOTO: The argument is the word# to transfer
     control to. GOSUB transfers control to a subroutine,
     and when RETURN is encountered, control returns to the
     next instruction after the GOSUB instruction.  The GOTO
     instruction is useful both as an alternative to using
     subroutines, and as part of an "if-then-else" type
     statement.

     EXIT: (VERS 1.1) Exit pops you out of XORCL
     immediately.  Arg. 1 is an error message number: 0
     means no error, -1 through -6 are:

          -1: Nobody Answers

          -2: You Canceled?

          -3: Bad Header Recvd

          -4: Deviant Data

          -5: Bad Sumcheck

          -6: Receive Time-out

          other: (?)

     WAIT: Arg.A is the amount (in tenths of a millisecond,
     well really 12ths of a millisecond) to wait.

     BEQ, BNE, BLT, BGT: Conditional statements in which
     Arg.A is compared to Arg.B (equal, not equal, less
     than, greater than).  If the statement is true, control
     is passed to the word# defined in Arg.C.

     EQU: The variable defined by Arg.A is set to the value
     of Arg.B. (A=B).

     INC,DEC: Arg.A is either incremented or decremented.
     (A++, A--).

     ADD,SUB,MULT,DIV: Arg 1 equals Arg.A plus, minus,
     multiplied by, or divided by the value of Arg.B.
     (A+=B, A-=B, A*=B, A/=B).

     AND,OR: Arg.A equals Arg.A AND'd or OR'd with Arg.B.
     (A&=B, A|=B).  If a constant, Arg.B is shown in hex.
     SHFTR,SHFTL: Arg.A equals Arg.A shifted right or left
     by Arg.B.  (A>>=B, A<<=B).

     2SCOMP: Arg.A equals the 2's complement of Arg.A.
     (A=(-A)).

     LWM: This instruction speeds up data extraction by
     doing the equivalent of an EQU, AND, and SHFT in one
     instruction.  Arg.A is the destination variable, Arg.B
     is the source.  Currently, the last argument (Arg.C) is
     a little tricky: The low byte is the mask value.  The
     high byte is the shift value (positive = right shift,
     negative = left shift). C equivalent: A=(B & Cl)>>Ch,
     where Ch is the high nybble of C, and Cl is the low
     nybble.

     SWM: This instruction replaces an operation which would
     otherwise take a SHFT, MASK, MASK, and OR to complete.
     It stores data from Arg.B into Arg.A at specific bit
     locations. Argument definitions are the same as LWM,
     except that definitions of Arg.C are reversed so that
     using the same Arg.C value would result in undoing a
     LWM instruction.  C equivalent: A=(A&~Cl)|((B<<Ch)&Cl).

     SWITCH: In some cases, you may need to have the
     instrument bi-directionally connected.  This is
     automatic for all Receive Routines, but not for Bank,
     Patch, or Parameter Transmit.  Use this instruction -
     X-or will either switch the switcher or ask the user
     to.  For advanced Profiles, you could use the
     "SwitchPgm" variable (see next section) to determine if
     the current instrument may be switched, in order to do
     fancy stuff (e.g. send multi patch, and get the single
     patches).

     RXANY: Receive the number of MIDI bytes defined by
     Arg.A (just throw them away).  Useful for skipping non-
     critical data (like sumchecks and F7's).  This function
     currently only aborts on Keyboard input (no timer).

     NOTE NOTE NOTE Don't use RXCMP, it may be axed.  Use
     the more generic EXIT function, which will allow you to
     terminate the function with the error code of your
     choice.  RXCMP: Receive one byte, which must be the
     same as the byte in Arg.A, or the XORCL function is
     terminated and sumcheck error is issued.

     TXBYTE: Transmit one byte defined by Arg.A.

     RXBYTE: Receive one byte and put it in the variable
     defined by Arg.A.

     * other functions and options may be implemented in the
     future, like setting size to -1 in RXDATA or RXANY
     means receive until F7 or other status.  These will be
     useful for generic Profiles and non-fixed length
     messages.  For now, this can be done with a simple loop
     and RXBYTE operation.

     TXSTRG: Transmit a MIDI message (no sumchecking or
     packing).  Arg.A is a pointer to the string I/O area,
     or to data to be transmitted (must be of type "adr" or
     "&str").  Arg.B is the number of bytes to send (not
     bytes-1, as with the ST's Midiws function).

     RXSTRG: Get a specific message via MIDI.  This uses the
     same arguments as TXSTRING.  The expected message is
     first set up in the string I/O area.  This instruction
     waits for this string to be received.  The whole XORCL
     routine is aborted if the user presses the computer
     keys, or if there is no response in a certain amount of
     time, or if there is a string which starts off the
     same, and then deviates from the specified string.

     RXSTRE: This is an extended form of RXSTRG. Arg.C sets
     the error return flags.  Bit 0 of Arg.C is the Timer:
     if set to zero, this function will wait indefinitely
     for the string to be received.  Bit 1 is the String
     compare error: if set to zero this function will wait
     until it receives the correct string, and will ignore
     all incorrect strings.  Note that the Keyboard input
     cancel can't be turned off (too dangerous).  Also note
     that RXSTRG is equivalent to RXSTRE with Arg.C = 3.

     TXDATA: Transmit MIDI data.  Unlike the string
     transmit, the data transmit keeps track of a sumcheck
     value, and allows different preset packing schemes.
     The first argument is the variable in which this
     function will store the sumcheck value.  IMPORTANT: The
     sumcheck value is added to the current value of the
     sumcheck variable, so if you start a new transmission,
     be sure to clear the sumcheck variable (it is initially
     cleared by X-or before calling XORCL routines).  Arg.B
     is a pointer to the data to be transmitted (must be of
     type "adr" or "&str".  Arg.C is the number of bytes to
     be transmitted (counted as they exist in the computer,
     NOT in the unpacked, or transmitted form).  The last
     argument is the data packing format (see Data Packing
     Formats, below).

     RXDATA: Receive MIDI data.  The data receive
     instruction stores received data in memory rather than
     comparing it to a string.  The Arguments are the same
     as with TXDATA: Arg.A is storage for the value returned
     from the routine, which may be the number of bytes
     received, a sumcheck, or an error code.  Sumchecking
     isn't implemented, so you can use the Sumcheck variable
     as you'd like.  Arg.B is a pointer to the area where
     the data is to be stored as it is received.   Arg.C is
     the size of stored data.  The last argument is the data
     packing format (see Data Packing Formats, below).  NEW
     NEW NEW - If size is set to -1, X-or will receive until
     an F7 (EOX) or other status is received - the number of
     bytes received will be stored in Arg.A.

     Data Packing Formats:

          standard: No fancy packing - just send them as
          they are stored.

          nybl l-h: For each stored byte, transmit two
          bytes.  Send the low nybble (least significant
          four bits) first, followed by the high nybble.

          nybl h-l: For each stored byte, transmit two
          bytes.  Send the high nybble (most significant
          four bits) first, followed by the low nybble.

          korg 7/8: (Also used by Lexicon) For each 7 stored
          bytes, transmit 8 bytes.  First transmit the high
          bits of all 7 stored bytes, then transmit the
          least significant 7 bits of each of the 7 bytes.

          ales 7/8: (Only used by Alesis) For each 7 stored
          bytes, transmit 8 bytes.  As if the 7 bytes were
          one huge 56-bit value, transmit 7 bits at a time,
          from the highest 7 bits (of the first byte) to the
          lowest 7 bits (of the 7th byte).

          veryfast: Occasionally, you may have need to
          receive data at a faster clip than the computer
          can handle.  Usually, RXDATA has several checks;
          for keyboard input, for time-out, and for unwanted
          status bytes.  Without this error checking, X-or
          can process incoming MIDI with slightly improved
          speed.

          msb/ls7b: For each stored byte, transmit two
          bytes.  Send the most significant bit, and then
          the 7 least significant bits.

          ls7b/msb: For each stored byte, transmit two
          bytes.  First send the 7 least significant bits,
          and then the most significant bit.

          asciinyb: Yamaha uses this format in some
          instruments - its just like nybl h-l, but each
          nybble is made into hex ASCII code before
          transmitting (kind of silly, when you think about
          it).
     TALLOC: (VERS 1.1-untested as of 12/13/89) Allocates
     Arg.B bytes of temporary memory (use a long variable to
     allocate more than 32767 bytes).  Returns a pointer to
     this memory in Arg.A.  This will be useful for
     unsupported data encoding schemes, when the instrument
     sends too much data too fast for XORCL to process it.
     The area is automatically de-allocated at the end of
     the routine.

     ZERO: (VERS 1.1) Stores Arg.B bytes of zeros in an area
     pointed to by Arg.A.  This is useful for patch
     initialization.

     BCOPY: This instruction is usually used in Patch Load
     and Store routines, or in a Patch Init routine.  It
     copies data from an area pointed to be Arg.A to an area
     pointed to by Arg.B.  The number of bytes is in Arg.C.

     PROMPT: Arg.A is the prompt # you wish to display.
     Prompts are:

          0: "Initiate Bank Dump"

          1: "Initiate Patch Dump"

          2: "Initiate Bank Load"

          3: "Initiate Patch Load"

     Only one of prompts 0-1 may be used in a function call,
     or there may be a problem.  Control returns immediately
     to the XORCL program.  Use these prompts for those
     (!@#$%^&) synths which have no request message.
     Prompts 2-3 are for the even more insane synthesizers,
     which need to be in a special mode to receive a Bank or
     Patch Dump.  These prompts use alert boxes and wait for
     confirmation(OK) or Cancel.  If Cancelled, the function
     terminates with a User Cancel error code.

     GETVAR: (VERS 1.1) This one re-sets all the XORCL
     variables and pointers for the buffer number defined by
     Arg.A.  XORCL uses the absolute buffer number within
     the same instrument (in E-or, this is equivalent to the
     line number of the buffer's display in the Performance
     window - starting at zero).  All pointers and variables
     which have to do with patch-level information, as
     opposed to instrument-level information, are changed.
     Be sure to save anything important in one of the Temp
     pointers or variables before using this command.  This
     instruction is part of a typical multi-timbral support
     routine.

     SETVAR: (VERS 1.1) A companion for GETVAR, this
     instruction sets all the patch-related variables for
     the buffer# defined in the BuffNo variable.  All
     necessary screen updating is handled automatically.

     SET-IN: (VERS 1.1) This command sets instrument-related
     variables which may be changed in XORCL - SysXChnl,
     CurrBank, and InstMode, for example.  If any values
     have changed, the screen will be updated accordingly.

     NOTE: IF AN INSTRUCTION RETURNS AN ARGUMENT, IT ALWAYS
     RETURNS IT IN THE ARG.A VARIABLE.  NONE OF THE OTHER
     VARIABLES ARE EVER ALTERED BY AN INSTRUCTION.
XORCL VARIABLES AND ADDRESSES

Many of the available address and integer variables are set
to certain values before certain XORCL routines are called.

Advanced Profiles may also obtain or change these variables
for other patch areas within the instrument (e.g. to deal
with multi-timbral synths).  The Addresses and Variables
marked with an (I) are instrument-related, and are updated
by the SET-IN command.  Those marked (P) pertain to a patch,
and can be loaded for any patch buffer with the GETVAR
command. If marked (PS), the SETVAR command will also work,
storing (PS) variables and updating X-or's display as
necessary.

First, the addresses:

     CurBnkAdr (I): The address of a bank which is supposed
     to be identical in content to the data within the
     instrument.  It is the last bank received from, or
     transmitted to the instrument.  This may or may not be
     the same as "SrcBank."  If no such bank exists, the
     address will be zero.

     SrcBnkAdr (P): The address of the bank from which the
     current patch was last loaded or stored.  In the load
     and store routines, the bank which is currently being
     loaded from or stored to.  For many routines, it is
     possible for this bank to be undefined, in which case
     it is zero.

     PatchAdr (P): (All Routines) The address of the current
     patch's data.

     ParamAdr: (Parm Send Only) The address of the current
     parameter's raw data (Patch + Offset).

     SrcPchAdr (P): The address of the current patch in the
     bank from which it came, as computed by the standard
     formula, if such a bank exists.  In the Bank->Patch or
     Patch->Bank routines, this is the source or destination
     address, respectively.

     XORPatch (P): This is the address of a structure which
     exists for each patch area in X-or.  Addresses of
     Machine, Module and Instrument structures may be found
     from this structure, as well as lots of patch-related
     information.  This is only for the very advanced users,
     and requires special information not included with this
     manual.

The Variables:
     SysXChnl (I): The System Exclusive Channel for the
     current instrument.

     InstMode (I): The PLAY and/or PANEL mode of the current
     instrument.

     CurBankNo (I): The reference number of the Current Bank
     (see above).  One current bank is stored per
     instrument.

     Buffno (P): The buffer number of the current patch area
     within the instrument (counting all buffers for all
     data types).

     DataType (P): The data type number of the current patch
     area.

     Areano (P): The number of the current patch area within
     its own data type (= -1 if there is only one area for
     this data type).

     VoiceChnl (PS): Each patch area has it's own channel,
     which automatically becomes the Solo/Rech/Mouse Channel
     when the patch area is selected.

     SrcBnkNo (PS): The reference number of the bank from
     which the current patch came, if any (otherwise -1).

     SrcPtchNo (PS): The number of the patch in the bank
     from which the patch originally comes.

     Patchsize (PS): The size of the patch in the current
     patch area.

     EditFlag (PS): This variable is One if a patch has been
     edited, and not yet stored into a bank or saved to
     disk, otherwise it is zero.

     GreyFlag (PS): If a patch is not contributing to the
     sound of an instrument, for whatever reason, the
     GreyFlag should be set to one, otherwise it is zero.
     When the GreyFlag is set, "xx" will appear to the left
     of the Instrument name instead of the channel.  This
     can be used for multi-timbral single patch areas which
     aren't contributing to the sound, or for patches which
     aren't available in a certain Instrument mode.

     TotPatch: The number of patches in a bank (typically) -
     this value isn't generally very useful, but it was in
     Version 1.0 and some Profiles used it, so I won't get
     rid of it for now.

     Offset, ParamNo, ParamMin, and ParamMax are the values
     for the current parameter as set on the Parameter Page.
     ParamVal is the displayed parameter value (not the
     stored parameter value).  These are only valid for the
     Parameter Transmit and XORCL Loader Routines.

     Sumcheck: Generally used for sumcheck output from the
     TXDATA routine - always set to zero each time XORCL is
     called.

     SwitchPgm: This simply tells the XORCL routine if a
     MIDI switcher program is available for the current
     instrument, so that it may decide to go to a fancy bi-
     directional protocol or not.


XORCL RECOMMENDED PROGRAMMING TECHNIQUES

To repeat a bit, our standard practice for file formats is
to use the most compact format available (i.e. NOT
nybblized), and to strip away the System Exclusive header,
and the sumcheck (if any) and EOX at the end.  Obviously, if
you are dealing with certain types of generic data, you may
want to ignore this protocol.  Generally, you use TXSTRG and
RXSTRG to handle the headers, with TXDATA and RXDATA to
handle the data.  One exception is in the case when part of
a header is included in a sumcheck, in which case you should
use TXDATA when sending that part of the header.

One possible method of programming uses the MIDI String
extensively.  By putting all the required message strings
into the MIDI string area, some work can be saved, possibly
at the expense of efficiency and flexibility.  With more
complicated protocols, you are better off using a central
core of routines with one string.  I tend to use the one-
string method most of the time.

Loop variables can be integers, or, if a value is being
incremented in a string somewhere, off two pigeons with one
stone by using the string value as a loop variable.

Sumchecking is done automatically by the TXDATA routine, and
the result is left in the location of your choice (byte,
word or long).  We usually use the Variable "Sumcheck."
This result is just a straight sum, which you will need to
modify before you send.  You may need to do a two's
complement (2SCOMP) and/or a mask (AND), or you may need to
add a certain value, etc.  Use TXBYTE or TXSTRG to send the
sumcheck and F7 (EOX) bytes.

If the sumcheck is done on stored data, rather than the
transmitted bytes, you will need to do it yourself, since X-
or always sums the transmitted bytes.  The time to do it is
probably before you start sending, if possible.

Currently, receive sumchecking doesn't exist, so just ignore
sumchecks on the receive end.  In general, I try to receive
EOX bytes, but I don't usually bother to check them.

X-or (ST Version) has an 8K MIDI buffer, which is big enough
for most bulk dumps.  The only time we've encountered a
problem is with a larger dump that used an unsupported data
compression algorithm.  Trying to decode it on the fly
proved to be too slow.  If this happens (and you've tried
everything else), use the TALLOC command to get a dump's
worth of memory, and receive it all before decoding.
DEBUGGING WITH THE MONITOR WINDOW

Show MIDI Sent and Show MIDI Received:  These are very
useful for debugging any XORCL MIDI routine.  The MIDI
communication occurring during the last routine called is
shown in the window.  When first encountering an instrument,
I often just program a XORCL routine which just waits a
certain amount of time (WAIT), or receives some number of
bytes (RXANY less than 8K).  I then call the routine, and
use the synth to send Sys Ex stuff, after which I inspect
the MIDI Received window (X-orcist note: I may put in a
"Free-run" Show MIDI Received Monitor mode for this
purpose).  Show MIDI sent is usually the mode in which I
detect my XORCL errors.

Show Patch Data and Show Bank Data displays:  Show Patch
Data shows the data for the current patch area, while Show
Bank Data shows the data in the first bank window (not
necessarily the front window).  These displays can be useful
when it comes to parameter load/store problems, and
particularly for debugging XORCL Patch Load, Store or Init
routines.

X-orcist Note: I hope to eventually have a single step
animation of the program and all its variables and I/O.
PART IV: E-OR DATA TYPE MASTER SCREEN

The DataType structure gives X-or tabular information for a
certain type of data.  All offsets and sizes are given in
bytes.  All routines are in terms of word# (as described
above).

     Data Type Name: An 8-letter name which describes the
     type of data  using the manufacturer's
     terminology.(e.g. Patch, Combi, Perform., Voice)

     Data Type Code: This currently isn't used.  Set it to
     the code the manufacturer uses to signify data of this
     type (if any single, consistent code exists).

     Bank File Suffix: Please don't use any existing
     suffixes that you know of, if possible, unless you
     don't plan to release the profile to anyone else.

     Bank File Size (Hex): The entire size of one bank file.
     One bank file may include data of more than data type.

     Bank Init Routine: The word# of a XORCL routine which
     initializes bank data for this data type only (this
     routine should not do MIDI).  If set to -1, X-or will
     use the Patch Init Routine (see below), and then the
     Store Routine (see below) to store patches into the
     bank - it does this for all data types in the bank.
     Bank Init is much faster if there is a complicated
     Load/Store conversion.

     Patch File Suffix: The warning above (Bank File Suffix)
     applies doubly, because the patch file suffix is also
     used as the name of the library file.

     Patch File Size (Hex): The patch area for a certain
     data type must be a constant size.  If the data is
     variable size, you must specify a maximum size here.
     Note that the Patch File Size and Bank Patch Size
     (below) may be different (a good example in which they
     are different is a DX-7).

     Patch Init Routine: The word# of a XORCL routine which
     initializes patch data (this routine should do nothing
     MIDI-wise).

     Offset to 1st Patch and Bank Patch Size: Together,
     these two values are used to determine the default
     address for a patch in a bank.  The formula is Offset +
     patch# * Size.  If a bank includes more than one data
     type, the Offset may be non-zero.  If the instrument is
     "well behaved," all Patch Loading and Storing can be
     automatic, but for more complex bank structures, you'll
     need to use custom Patch Load and Store Routines.
     Patch Load Routine, Patch Store Routine: These Routines
     may be used either to locate individual patches in a
     bank before copying data and/or to translate between
     bank patch format, and running patch format.  Often,
     especially with Yamaha gear, the bank format packs data
     as tightly as possible, while the "running" format
     separates all parameters, so, instead of difficult
     parameter extractors (see Parameter Extract, below),
     you have these two difficult routines to figure out.
     Both routines are called with pointers to the start of
     the bank, the default bank patch location as computed
     by the standard formula, and the patch location.  Also,
     included in the variables is the source/destination
     patch number in case you need to re-figure the bank
     patch address.  You'll be using mainly BCOPY, LWM, SWM,
     and EQU, along with a lot of pointer arithmetic.  NOTE:
     Do not do anything with MIDI in these routines - they
     should be strictly limited to getting data from point A
     to point B.

     Patches per Bank: The number of Patches of this data
     type in a bank is defined by this constant.  This is a
     fixed value, so if you have a variable # of patches,
     you'll need to set this to the maximum, and kludge
     something together with the XORCL routines.  This has
     not been attempted as of December, 1989.

     Offset to 1st Name, Offset between Names: The standard
     way of locating and copying names is to use the
     formula: bank address + 1st Name Offset + (Patch Number
     * Between Name Offset).  Patch Number is the internal
     patch number (0 through Patches per Bank-1).

     Name Locate Rout.: As with patches, the names in a bank
     occasionally wont be found via the standard formula.
     Or, the number of names in a bank wont be constant.  In
     these cases, this routine can be used to circumvent the
     usual X-or procedure.  This is similar the Load Routine
     described above, except that only the name is loaded.
     If unused, Name Locate Rout must be set to -1.

     Offset to Name in Patch: The offset to the name in the
     Patch Edit buffer MUST be a constant - so far this has
     never been a limitation, but if you run into an
     instrument which doesn't behave, you'll have to make it
     behave by tacking a name on at the beginning, and using
     the Load and Store routines to make it work.

     Numbering Style and Number Start/Base: Unfortunately,
     nobody ever standardized the way patches are numbered.
     In many cases, this is because of front panel design -
     only eight switches forces you into a octal numbering
     scheme.  Also, many people start counting with 1
     instead of 0, or 11 instead of 00.  This is an age old
     problem for most of mankind, particularly with
     marketing people - the concept of zero meaning
     something other than nothing.  For this reason, Number
     Start can be set to any value, the only restriction is
     that numbers can't use more than three digits.  With
     the octal style, numbers either start at 00 or 11.
     There are many different formats supported - detailed
     elsewhere in this document.

     Name Characters: The number of characters in a name
     (always a constant).

     Add-on Name?: For data types with no built in name, you
     must tack on your own name.  If this is on, X-or will
     automatically rename patches it gets from the
     instrument, and Re-naming will not cause the patch to
     be transmitted.  Every type of patch must have a name
     in X-or - if not, you'll need to tack on this extra
     name.

     Allow Uppercase Only?: If the instrument only supports
     Uppercase letters (common ailment amongst certain types
     of displays), set this switch to on.  In all name input
     functions, lowercase characters will be converted to
     uppercase automatically by X-or.

     Integer Characters?: In one machine that we know of,
     everything is in integer format, even the name
     characters.  Sure, this wastes space...sure, the
     designers must have access to powerful hallucinogens,
     but hey, it's a free country, whether you're burning
     memory or flags, right?  This is almost definitely off.

     Pre-convert Mask, Pre-convert Adjust (use only if
     necessary): Characters must be converted to standard
     ASCII before they can be displayed.  These two values
     are used to condition the raw name data by first
     stripping off unwanted bits (unwanted bits should be
     set to one in the Mask), and then adding the Adjust
     value.  If the instrument uses standard ASCII, these
     values should both be zero.

     Convert Text Table (use only if necessary):  Another
     thing designers do, to save space or to deal with
     limited displays, is to mangle the ASCII codes to fit
     their needs.  The Character Convert Table will convert
     any such format to standard ASCII.  The raw data is
     first conditioned (if necessary) via the Pre-convert
     Mask and Adjust (see above).  This value is then used
     to index into a table which has been entered in E-or's
     Text Tables Screen.  The result is a standard ASCII
     character.  Un-defined character codes should be given
     the same character as the first code in the table, and
     the Text Table should be terminated with a zero.  The
     Convert Text Table value on the Data Type Master screen
     is set to the starting byte number of the table.  If no
     table is needed, it is set to -1.

     Total Edit Pages, Edit Page Width, Edit Page Height:
     The basic size of the edit screen is declared here.
     Edit screens are broken into quantized pages.  Page
     Height is used in Parameter Object Editing.  It also
     determines the amount of vertical distance X-or will
     jump when you click in the Vertical Slider's control
     areas.  By experiment, I have settled on a 620w by 170h
     page.  this allows two full pages to be shown in full
     screen mode.  The width can be as wide as you need it.
     The Total Edit Pages * Edit Page Height determines the
     total height of the edit page.  If you are writing or
     editing a Profile for a different size screen, you may
     want to experiment with these values.

     MIDI ROUTINES: These are pretty self explanatory.  They
     all point to routines in the XORCL program.  Anything
     which is not available should be set to -1.  It's
     certainly OK to use the Patch Tx Routine as the Param
     Tx Routine, but don't try to use a Bank Routine in
     place of a Patch Routine, or heavy bombing may result.
     Lots of tricks are possible here - see the examples to
     gain a better understanding.

     Mode Switch Routine (VERS 1.1): called when a patch is
     selected in the Performance Window, or when a patch is
     loaded and sent as part of a Performance.  This usually
     checks the InstMode variable, and changes the mode if
     necessary to communicate with the selected patch area.

     Send to Bank Routine (VERS 1.1): called when the
     current patch edit buffer is stored into the Internal
     instrument bank.  The Profile should update the bank in
     the instrument, if such a message is available, and/or
     do any number of possibly convenient things (automatic
     multi-timbral patch edit, for example).

     TX Slowdown Amount: I haven't ever personally
     experienced this phenomena, but certain early MIDI
     machines can't take data at the full MIDI baud rate.
     Hopefully, none of these exist in your studio, but just
     in case they do, this parameter (if non-zero) slows the
     rate of transmission (only when talking to this synth
     however).

     Between Txmit Wait: Currently, any desired wait must be
     programmed into XORCL.  In the future, X-or will be
     smart enough to keep routines from being called before
     it is safe to do so, without unnecessarily slowing down
     the user interface operation.  This is in 10ths (O.K.
     actually 12ths) of a millisecond.

     Fast Param Send?: This should probably be set to off,
     unless you are dealing with a synthesizer that can
     accept parameter changes at full speed without
     glitching or choking.  Certainly, for this to work, the
     machine's System Exclusive implementation must include
     parameter change messages, and it must react quickly
     and smoothly enough to make it worthwhile.  Once you've
     got things working, you can test your machine by
     turning this parameter on, and trying a slider.  If it
     works without a hitch, you're lucky.

     Receive Channel Follows: For the current data type, if
     the channel on which the unit receives system exclusive
     data is also the channel on which it receives voice
     data (key on/off, etc.), set this to "SysX."  If there
     is an separate receive channel (e.g. Basic Channel), or
     no defined channel, set it to "User."  If the channel
     is under XORCL control, set it to "data".  This
     information is used to set the receive channel default
     for each patch area, and when SysX Chnl or Recv channel
     are changed on X-or's Instrument Setup screen.

How to Handle Situations in Which Bi-directional
Transmission is Required:

Some machines require a bi-directional connection to receive
system exclusive data.  This is so "handshaking" techniques
may be used, which theoretically should take care of any
timing problems that would otherwise result in lost data.
Some engineers think that this is a good idea, but in the
real world, because of the way MIDI is designed, it is
usually just a pain in the butt.  If you have a programmable
switcher and X-or, however, its absolutely painless.  In the
XORCL routine, you should use the SWITCH command, which
either switches in the instrument, or asks the user to do it
manually.  If you'd like to make it optional, the SwitchOK
variable tells you if the user has a switcher program change
defined for the instrument.
V. PATCH SECTIONS

This quick and painless screen lets you program the sections
to be used in all the Transplant operations.  Up to 16
sections may be defined.  Each section has a 12-character
name.  These sections are either Master Sections or Sub-
sections.

     Master Sections: A master section is any section which
     is defined to have a possible destination.  The start
     and end offsets are the offsets into the Patch of the
     first and last bytes of the section.  The Subsection/
     Destination Matrix lets you program which of the other
     sections this section may be copied to ('D' for
     destination) - you should always allow a Master Section
     to be copied to itself.  Also, the matrix flag may be
     set to 'S', which stands for Subsection.  This
     designates a section as a legal Subsection for this
     Master section.

     Subsections: The start and end offset of a Subsection
     are relative to the start offset of the associated
     Master Section(s).  Note: "all" is an automatic choice
     in X-or's Subsection box: you don't need to program it.
     None of the Subsection/ Destination flags should be set
     for a Subsection.

     The Copy Ct. and Skip Ct. are for non-contiguous
     sections, for example these can be used to program the
     section to be every 4th byte.  Copy Ct. = 1 byte and
     Skip Ct. = 3 bytes in this example.  If Skip count is
     zero, no data is skipped.



PART VI: PARAMETER EDITING

The screens Word Tables, Byte Tables, Param Extract,
Parameters, Text tables, and Screen Layout all have to do
with displaying and editing parameters in X-or's Patch Edit
Window.

Let's skip Word Tables and Byte Tables for now, since they
are best covered in the context in which they are used.
Moving right along, we now get into the guts of parameter
editing.

The low level parameter structures, "Loaders" and
"Parameters" define the technical aspects of a parameter
enough for it to be edited.  These structures are
responsible for locating and conditioning a parameter, and
making sure it stays in bounds.  The Parameter objects
("Parmobs," edited on the Screen Layout screen) take care of
display type, location, etc.
A. PARAMETER EXTRACTION (i.e. "LOADERS")

A loader structure (one line on E-or's Parameter Extract
screen), or a group of loaders linked together define a
"load sequence," which extracts a parameter from the raw
(bulk) data, and conditions it to be displayed and/or
edited.  The "store sequence" uses the exact same settings
to store the edited parameter back into the raw data format.
Each loader structure therefore defines a reversible
process.

The object of the game is to get all parameters into "NICE"
(Normal Integer Continuous Editing) format.  X-or doesn't
take kindly to discontinuous parameters (e.g. a parameter
which can be 0, 1, or 3, but not 2).  Don't worry about the
displayed value of the parameter for the time being, we can
attempt to deal with that later.

The way X-or works, the same load sequence may be used for
any number of parameters.  If a machine is particularly well
behaved, it may need only a few simple load sequences.
However, if the data format contains a lot of packed
parameters, or discontinuous parameters, you may need a
different one for every parameter.

Individual loaders either extract data or modify it.  They
are strung together in a sequence to handle more complex
situations.  Every loader has:

     loader type: determines the action of the loader

     flags: further refinement - link, invert, sign extend,
     global offset, and storage only.

     two general purpose word-sized arguments: These have
     different uses depending on the type (see below).

     adjust: an amount to add or subtract from the loaders
     value (post-loader when loading, pre-loader when
     storing).  Given in terms of the amount to be added
     when loading (neg value means subtract).

Here are the loader types defined, extractors first:

     Single, Dbl-HiLo, Dbl-LoHi: Extracts and OR's together
     bits of data bytes.  Single handles one group of bits,
     while the Dbl's handle the more specialized (but quite
     common) case in which there are parameter bits in two
     successive bytes.

     For each byte there is a bit mask and a bit shift
     value, which are combined into one hex word in E-or
     (this inconvenient situation may soon change).  The
     mask/shift format is the same as with LWM and SWM in
     XORCL.  The high byte is the shift, and the low byte is
     the mask.  When loading, the raw data byte is first
     AND'd with the mask, and then shifted right by the
     shift value.  A negative shift value means left shift.

     In a Single loader, the second argument is the
     additional offset, if any, to be added to the base
     offset (defined by the parameter structure- see below).
     Both of the Dbl loaders use two mask-shift words, and
     assume that the first loads from the data byte at the
     base offset, and the second loads from the base offset
     + 1.  The only difference between the two is which byte
     gets sign extended if the sign extension flag is on.
     If the flag is set, sign extension occurs from the
     highest bit which is set in the mask.

     Single loaders may be linked together in a sequence. If
     the link flag of a loader is set, the next loader
     becomes part of the load sequence.  The Single and
     Double loaders OR their result with the running loaded
     value.  Using this feature, parameters with bits spread
     all over the place can still be assembled into a
     coherent value.

     Sign Bit: Added in version 1.1 of X-or, this loader
     extracts a sign bit only.  This loader MUST be linked
     after whatever loaders are needed to extract the
     magnitude (otherwise it does nothing).  The arguments
     are the same as a Single loader (except there is no
     need for a shift value).  Before X-or 1.1, you would
     need a table to deal with most sign-magnitude
     situations...clearly a problem when the range of values
     is large.

     NOTE: DON'T USE RADIOBIT, I'm retiring it A.S.A.P.!

     Radiobit: A real special case, this one extracts data
     from "Radio-bit" bit flags in separate, evenly spaced
     bytes.  A prime example is a flag marking a particular
     step of an envelope.  This loader also assumes that
     only one of these flags may be set (otherwise, you
     would make them all separate parameters). There are
     other ways to do this using single loaders with a table
     modifier (see below), so don't despair if the bit flags
     aren't evenly spaced. 1st word high byte is the mask
     used to test a byte, low byte is the spacing.  2nd word
     high byte is the number of bytes to test, and the low
     byte is the default value if no bit flag is on.

     Internal: This is used for special cases in which the
     module needs to store its own internal data (not part
     of the patch).  The prime example is a global offset
     (see the discussion of Global Offsets).  It also could
     be a mode, if somebody wants to get fancy and have
     different ways of entering the same data (i.e. the mode
     is part of the module, not a patch param).  For
     example, you could have a DX-7 Profile where an
     Internal parameter could switch between displaying
     operator parameters by operator, or by parameter.  The
     first word of the Internal loader is its value, and the
     second is not used (but should be set to zero or one).

Now the modifiers....

     Modulo, Quotient: This is used to separate combined
     data, when the divisor is NOT a power of two (in which
     case it can be handled by masking and shifting.  A good
     example is the separation of semitone data into octave
     and step (divide by 12).  The result of this modifier
     when loading is either the quotient or remainder
     (Modulo) of the input value divided by the specified
     divisor.  On the store side, this is tricky: the loader
     sequence is re-traced up to the Quotient or Modulo
     loader, and part of the stored data is combined with
     the data presently being stored to give the value to be
     stored.

     Multiply, Divide: SEE THE BUG NOTE BELOW!  These are
     basically used to scale the input value, by multiplying
     and dividing it by specified amounts.  Round-off values
     are required for loading and storing (otherwise the
     equation is not reversible, due to the nature of
     integer division).  Therefore the second word of these
     loaders is the "round-off" value.  For a Divide loader
     the round-off is added before dividing during the load
     sequence, and ignored during the store sequence - and
     vice versa for the Multiply loader.  Example: to
     imitate a synthesizer's display, you may need to use
     these loader types to make 0-63 data into 0-99 data by
     multiplying by 100 and dividing by 64 (or by 99/63,
     depending on how the machine does it).

     BUG NOTE: Multiply/Divide scaling works poorly with the
     slider increment/decrement feature if the parameter is
     scaled UP (i.e. intermediate displayed values don't
     really exist - implied resolution is greater than
     actual resolution).  The displayed value may change,
     but the stored value doesn't change, and it is re-
     loaded back to the old displayed value, so the
     parameter gets "stuck."  There is no known fix for this
     at this time, but XORCL may provide an answer soon.

     Byte Tbl and Word Tbl: Even the ugliest parameters can
     be put into "NICE" format with a table transformation.
     Byte Tbl is for byte-size raw data, Word Tbl is for
     integer-size.  Both take the current value in the load
     sequence and compare it to all the entries in the table
     until a match is found.  The table index then becomes
     the value which is returned.  When storing, the input
     is the index, and the output is the table entry.  The
     tables are entered on the Byte Table and Word Table
     screens (strangely enough), and they both have a
     similar format:  The first argument of the Table loader
     points to a table.  The 1st entry in the table is the
     number of entries in the table, followed by the table
     values.  The 2nd argument of the loader is the default
     value to be returned if no match is found during the
     load.

     Mask/Sft: NOTE: This has yet to be used (any masking or
     shifting can usually be done in the Single or Double
     loader).  Please let me know if you intend to use it,
     as I may choose to discontinue it!  This is designed
     for applying an integer sized mask and/or shifting the
     current value of a load sequence. 1st word is mask, 2nd
     word is shift - with the same conventions as usual.

XORCL LOADER: The most flexible of all loaders is the XORCL
loader, which simply patches the parameter loader system
into XORCL, where you can do a multitude of unusual,
creative or simply necessary things.  All the parameter
variables (and only a few others) are set before calling.
The first argument of the loader is the load sequence
routine.  The second argument is the store sequence routine.
When the XORCL routine returns, the ParamVal variable is
returned as the result of the loader.  It is up to the
programmer to insure that manipulations of the parameter
value in the load and store sequence work together
correctly.

This loader may be used as either an extractor, or as a
modifier.  It is slower than the other loaders, so use the
standard ones if possible.  It should be used:

     a) When the necessary load sequence is too complex for
     standard loaders to handle.

     b) When changing a parameter that affects other
     parameter values (it may necessary to do this before
     the param txmit routine if corrections are not also
     handled in the patch transmit routine, due to the
     randomize function's operation).

NOTE: DO NOT attempt to use the XORCL loader to affect
anything outside of the patch data itself (no banks, no
MIDI, no external flags, channels, etc.)  These tasks must
be done during the parameter transmit routine.  Many of the
variables and pointers are invalid when the XORCL Loader is
called.
GROUP MAXIMUMS: The way to handle the problem of "Group
Maximums" or any parameters which have changing minimums or
maximums is with a XORCL loader.  For example, groups of
parameters which have a collective maximum value are quite
often used in multi-timbral note allocation.  The XORCL
loader (linked onto the normal load sequence) should compute
and check the parameter limits when the parameter is stored,
and change the value being stored if necessary.  If the
XORCL loader changes the value being stored, it should
return with an EXIT -1 command.  This lets the upper levels
of X-or know that something unusual has happened.

LOADER LIMITATIONS: The Extracting Loaders (Single, Double,
Radiobit, Internal) must be OR'd together so that they may
be separated when storing, without any confusion.  If they
are added (to something other than a constant), the process
can become irreversible.  If the load/store sequence
requires logic or becomes too complex the only remedy is the
XORCL loader.  For example, the waveforms in a CZ-101 are
such a tangled web that they require both tables and logic
to be done correctly.  The CZ is probably the worst case
anyone will encounter - unless the government starts
designing synthesizers.

Here are the loader flags currently defined:

     lnk (link): Defined above.

     se (sign extend): This flag may be used on any Single
     or Double byte extractor to extend the highest bit.
     The highest bit set in the mask is defined as the sign
     bit, which is then extended.

     iv (invert): When this flag is set, the final operation
     during a load is to subtract the current value from the
     "adjust" value (rather than adding the adjust).  This
     makes it possible to invert a parameters range if
     necessary, while also adjusting it.

     go (global offset): This flag notifies the program that
     the parameter value being loaded or stored by this
     loader is either the global offset value, or it uses
     the global offset value.  The global offset is stored
     in an "Internal" loader.  See the discussion of Global
     Offsets ("Special Situation #3") for more info.

     so (store only): This allows an extra, completely
     separate branch of the sequence to be programmed, which
     is used only during a store sequence.  This is here
     mainly for the CZ series, which brilliantly stores the
     same data in two formats - displayed and actual -
     within the patch, both of which must be set when a
     parameter is changed.  Are there any other S.O.B.s out
     there who do this?
B. PARAMETER STRUCTURES

A Parameter Structure corresponds to a single parameter,
unlike loaders, which may be re-used, and Parmobs such as
the Envelope Parmob, which may correspond to a whole group
of parameters.  Parameters consist of:

     parmno: the identifying parameter number (for param
     transmit routine on certain synths).

     offset: the offset in bytes from the start of the data
     buffer to the primary data byte.

     min,max: the minimum and maximum value of a parameter,
     in terms of its displayed value.

     loader #: the number of the first loader structure in
     the load sequence used for loading and storing the
     parameter's value.





C. PARAMETER OBJECT STRUCTURES

"Parmobs" are higher level parameter editing objects, which
determine the type of input for each parameter.  These
objects usually point to one or more PARAMETER structures.
Ideally, more than one object could point to the same
PARAMETER, and the system would know to update all displayed
objects that point to a given PARAMETER when a new value is
stored.  This, however, is not the way it's implemented.
What we do have is a system for forcing updates to occur
down a linked path of objects (see "Special Situation" #1).

     1. SLIDER TYPE

     A normal slider needs only a parameter and text to put
     above the slider.  The slider includes a numeric
     display of the value, or optionally a key name display
     (set the "op 1" flag to 'Y' - key numbers start at C-
     2).  Slider values can be incremented or decremented by
     one by clicking briefly above or below the slider.  The
     object name consists of two lines separated by a '\'.
     The data field is used by the program to store the
     current y value of the slider (this may cause streaks
     in E-or when the slider is moved).
     2. BUTTON TYPE (Version 1.?, maybe)

     This is for binary parameters.  All that's needed is
     the Parameter number.  The name goes in the button,
     which is either highlighted (on) or not (off).  This is
     not implemented in Version 1.1.

     3. TEXTBOX TYPE

     Some parameters demand a more descriptive display (
     e.g. for a waveform display, "hammer" is better than
     "83").  The data field of a Textbox object points to a
     position in the Text Tables where all the parameter
     value names are listed (with a '\' after each entry.
     In X-or only, if you click on the text data, X-or will
     display the entire list of possibilities, and let you
     choose the value by clicking on it.  Be sure your text
     box is wide enough to contain the longest parameter
     text (the text box width also affects the Pop-up window
     width).

     4. INFOBOX TYPE

     This is just a TEXTBOX which can't be edited - no
     arrows appear, nothing happens when you click on it.
     It's useful for parameters which can't be changed, like
     the effect type in the PCM-70.  Also, for general
     information. (the PCM-70 uses it to show row names).
     Note that a parameter must be defined, even if it's not
     needed - use a dummy parameter with an Internal loader.

     5. PATCHBOX TYPE (Version 1.1)

     The data area of this object is a buffer# within the
     same Profile whose bank patch names correspond to the
     parameter's value.  It will appear just like a TEXTBOX,
     but the names and numbers will be the patch names from
     the last bank sent or received from the instrument if
     it is open (the Internal Bank).  Otherwise, it just
     displays a number.

     6. MODESW TYPE

     This is not an object which appears on the screen, but
     it controls which objects will appear.  It is fully
     discussed below in "Special Situations - Display Mode
     Change."
     7. ENVELOPE TYPE

     This is a very flexible envelope entry structure.  It
     can be used to edit virtually anything that can be
     visualized as an envelope - which may also include
     keyboard scaling, graphic eq's, etc.  The object name
     is printed to the upper left of a shadowed box
     containing the envelope.  This box is set according to
     the object's x, y, w & h dimensions.  All coordinates
     of the envelope are measured relative to the lower left
     corner of the object's box.  The data field of the
     object points to an arbitrarily large integer array
     (Word Tables screen), which contains the following
     information:

          [0]= x_adjust: Usually, x=val+x_adjust

          [1]= x_invert flag: If set, x=x_adjust-val

          [2]= x_scale: x=val*x_scale/100

          [3]= note_off: x coordinate of dotted "key off"
          line.  Set this to a high value if you don't want
          it (e.g. the envelope never has a sustain point).

          [4]= y_adjust: y=val+y_adjust.

          [5]= y_scale: y=val*y_scale/100.

          [6]= y coordinate of optional dotted horizontal
          line.  Any non-zero value causes the line to be
          drawn.

          [7]-[9]= future expansion.

          [10]=end step param/constant.

          [11]=sus step param/constant.

          [12]-...= time0, level0, time1 ...etc.

          x and y adjust and x invert values: You can modify
          a parameter pretty extensively with loaders, so
          these adjustments may seem superfluous.  But
          ideally, the loaders should be used to condition
          the parameters as if they were to be displayed,
          for printing purposes.  The envelope wants to see
          all positive values.  Also, a rate parameter needs
          to be inverted to have the proper relationship
          with time (x).  Time values of zero are generally
          not pretty, because the envelope can be drawn on
          top of itself and thus disappear (it is drawn in
          X-or mode, no relation to the program).
          x and y scale are the amount/100 to scale envelope
          by in x and y directions.  Currently, only linear
          adjustments are available.  If I were to get
          fancy, I would have equations which could cover
          rate type or logarithmic envelopes - but that's a
          huge pain, so I'll just leave room for a pointer
          to equations, perhaps to be added at a later date.
          This would also require some kind of panning or
          zooming control.

          Parameter/Constants: If the high bit is set, the
          value is assumed to be a constant.  E-or currently
          is dumb in this regard, so you have to figure out
          what value you want, and subtract 32768 from it.

          End point param #/constant: This defines the
          number of the last step of the envelope.  Usually,
          but not necessarily, an end point is fixed
          (constant).  However, for CZ-type envelopes, it
          can also be a parameter.

          sus point: same as above, but for the sustain
          step.  No provision is made for repeating
          envelopes (as in K5), because that would make the
          envelope display too difficult to show and edit.
          For ADR (no sustain) envelopes, set the sus point
          higher than the end point.

          times and levels: Starting with the T0 and L0
          params/constants, up to Tn and Ln (where n is the
          end step).  Each may be a constant or a parameter.

Example: an ADSR would have END=3, SUS=2, T0 = L0 = L3 = 0,
L1 = (maximum level), and T1, T2, L2 and T3 would be the A,
D, S, and R parameters respectively.
D. THE PARMOB LIST

Parameter objects are organized in a list.  This is a simple
single linked list - each object contains the number of the
next object.  Control just passes along the chain starting
with the first object, until it reaches a dead end (-1).  A
special MODESW object is self-modifying: it specifies a
parameter which modifies its own "next" field, allowing
control to branch in different directions, as necessary.  A
practical example would be the "effects algorithm" on almost
any multi-effect device.  MODESW objects could also be used
with INTERNAL parameters to provide alternate views of the
data.  When a parameter object is "switched out" it will not
appear in the Patch Edit Window or the Randomization Mask,
so don't worry about duplicate objects.

SPECIAL SITUATIONS

     1. Parameters that affect other Parameters:

     Sometimes two parameters overlap, or in some way one
     parameter causes the display for another parameter to
     change.  X-or parameter objects with their "rdo mst"
     (redo master) flag set generate a re-draw when they are
     changed.  The redraw starts with the next object, and
     continues as long as the "rdo flg" (redo flag) is set.
     If this flag is not set for an object, the re-draw
     terminates.  This is admittedly not flexible enough,
     since it doesn't provide a way for two parameters to
     redraw each other - a limitation I will deal with
     somehow in version 1.1.  Also, you may want a parameter
     to alter the min or max value of another parameter -
     another problem yet to be solved.

     2. Display Mode Change:

     There are some situations in which changing a parameter
     should cause other parameters to appear or disappear.
     X-or's MODESW object can change the entire Patch Edit
     Screen if necessary.  For example, you could use this
     feature to substitute certain sliders for other sliders
     under certain conditions, or you could create an
     alternate display for the same parameters.

     The MODESW object consists of a name which isn't used
     (so you should treat it as a comment), and a rectangle
     which currently isn't used, but which should contain
     the area of the screen to be modified, or all zeros to
     modify the whole screen.  The "parm no" field should
     point to a parameter (for display modes of your own
     invention, you would use an Internal parameter).  The
     "data field" is an index into the Word Table.  The
     parameter is evaluated, and its value is added to the
     index.  The value taken from the table is the "next
     object" for the MODESW object.  Therefore, the MODESW
     object works by changing the path of the linked list.
     Currently, X-or erases and redraws the entire screen
     (if and only if the "next" value changes).  In the
     future X-or may only re-draw the area within the MODESW
     rectangle, if I can figure out a way of doing this
     without upsetting other things.

     Normally, the parameter pointed to by the MODESW object
     will also be associated with another object "upstream."
     Otherwise, there would be no user control (nor any
     indication) of the mode.  Any parameter which may
     affect a MODESW object should have its "mode master"
     flag set.  This tells X-or to re-evaluate all MODESW
     objects downstream from the object being changed.  If
     this flag isn't set, the MODESW object isn't re-
     evaluated until the next window redraw.

     3. Repeating Parameter Data Structures:

     (Global Offsets)

     Many Data Types include repeating data structures, like
     operators on an FM synth, or Partials on an L/A synth,
     etc.  To make the Patch Edit Screen easier to get
     around, it is often useful to set up the screen to edit
     only one of these structures, and provide a parameter
     to select the "current" structure.  This could be done
     with the MODESW system described above, but there is
     another way... The Global Offset system provides many
     advantages: less work for you, a smaller Profile,
     faster operation, etc.  To be able to use it, the data
     must be organized such that the only difference between
     the data structures is the offset byte number at which
     they start.  Instrument designers generally structure
     their data this way, unless they are masochistic.

     A Global Offset is always an Internal parameter (see
     Internal Loaders above) which has its "go" option flag
     set.  There can only be one Global Offset per Data
     Type.  Usually, the Internal Loader is linked to a
     Divide Loader, in which the divisor is the space
     between data structures.  The Global Offset parameter
     object is generally a redo master, and all objects
     which are subject to change are downstream, with their
     redo flags set.

     NOTE: Be sure to set the "go" flags in all the loaders
     which pertain to parameters affected by the global
     offset.  Use separate loaders for any parameters not
     affected by the global offset.  This restriction is
     really for my convenience, and may be lifted by version
     1.1.
Other Info Regarding Objects:

The current standard page height is 170, although this
creates a slight problem with the color screen (it can't
quite fit two pages on the screen).  The standard slider
height is 128.  Sliders should have at least 24 pixels
clearance at the top, and 12 pixels clearance at the bottom.
This is all to insure color compatibility.  Sliders are
always 19 pixels wide, and Text Boxes are always 36 pixels
high.  Coordinates are always given in hi-res values.

NOTE: Byte Tables are used for Byte Tbl Loaders only.  Word
Tables may be used for Word Tbl Loaders, ENVELOPE
structures, or MODESW "next" object lists, so be careful
when you insert or delete from the Word Tables!!! -- make
sure E-or followed your changes correctly.
Example #1 - A Simple Profile - The Prophet V.

Step 1 - Enter information on Machine Screen:

     Model Name......... Seq.ProphetV
     ROM Version................10.00
     X-or Version............... 1.10
     Perpetrator.............YourName
     Last Modified.....mm/dd/yy hh:mm

     This information is used in X-or's Info Menu - the
     model name is used in the Performance window, among
     other places.  If you can find out the ROM version of
     the synthesizer which you are using, enter it -
     otherwise, enter 0.00.  Enter the number of the latest
     X-or version that you have.

     Minimum SysX Channel...........0
     Maximum SysX Channel..........15

     X-or's setup screen may check for correct SysX Channel
     settings in the future.  Normally, the SysX Channel
     (which may be called Basic Channel in your synth
     documentation) goes from 0 to 15, unless your
     instrument has a "unit number," which is a special
     SysX-only channel (newer Roland instruments, for
     example).

     Machine Init Routine........  -1

     This routine is used to send a start-up SysX Message to
     the instrument.  Set it to -1 until you're ready for
     some advanced tinkering.

     Total Data Types...............1
     Type #1 Areas..................1
     Type #2 Areas..................0
     (the rest are all 0)

     This represents the simplest possible architecture -
     typical of a mono-timbral synth or effects device.  A
     multi-timbral synth like the FB-01 would have at least
     two data types - the "single" and the "multi."  The
     single data type may have more than one area (more on
     that in the advanced section - coming soon).
Step 2 - Enter information on the Data Type Screen:

     We first decide to make the patch size 40 bytes: 24
     bytes of patch data and, since the Prophet V has no
     name in it's patch format, we need to add a 16
     character name (24 + 16 = 40 bytes).

     Data Type Name.............Voice
     Data Type Code................00      (Not used)

     Bank File Size..............4800
     Bank File Extension..........PR5
     Patch File Size...............40
     Patch File Extension.........P5V
     Patches in a Bank............120

     There are 120 patches in a bank, so the bank file size
     is 120 x 40 = 4800 bytes.  To be safe, always attempt
     to use unique Extension names.

     Offset to 1st Patch.............0
     Bank Patch Size................40
     Patch Load Routine.............-1
     Patch Store Routine............-1

     Since the Prophet V doesn't have its own bank dump
     format (it only transmits and receives single patches),
     we were free to make up our own format - this is a good
     model if you encounter a similar situation.  In our
     bank format, the Bank Patch Size is the same as the
     Patch File Size (this is true with the majority of
     instruments).  There is no "Offset to First Patch" data
     because the bank format contains no header or other
     data ahead of the voice data.

     This format fits the standard equation for loading and
     storing patches, which is to copy "Bank Patch Size"
     bytes from the address computed by the formula: Offset
     to 1st Patch + (patch# * Bank Patch Size).  If this
     formula works, the Load & Store Routines may be set to
     their default values of -1.

     Offset to 1st Name..............24
     Offset Between Names............40
     Name Locate Routine.............-1
     Offset to Name in Patch.........24

     These settings give X-or the location of a patch name
     to be displayed.  In this case, the name is our
     additional name, which we put after the patch data, at
     byte #24.  Therefore, the "Offset to Name in Patch" is
     24.  The "Offset to 1st Name in Bank" is generally the
     same number.  The "Offset Between Names" is usually the
     same as the Bank Patch Size (40).  You don't need to
     use the Name Locate Routine unless the bank patch names
     are unevenly spaced, so set it to -1.

     SPECIAL CASE: BANK HEADER OR MORE THAN ONE DATA TYPE:
     If the data for this data type doesn't begin at the 1st
     byte of the bank, the "Offset to 1st Patch" and "Offset
     to 1st name" values will both include the additional
     offset. Example: see the Profile for any multi-timbral
     instrument.

     SPECIAL CASE: NAMES SEPARATE FROM PATCH DATA:
     Sometimes it is necessary to add names at the end of a
     bank of patches.  For example, if an instrument
     supports a bulk dump format, but includes no names in
     the data.  Let's take the Prophet V example and do it
     another way - suppose each patch is 24 bytes long, and
     there are 120 of them.  The offset to the 1st Name is
     then 2880.  Our names are 16 characters long, so the
     Offset between names is 16.  This would require a
     separate Load and Store Routine, since all the data
     isn't lumped together in one spot - see the CZ-101
     Profile for an example showing how to do this.