!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
HELPFUL HINT #1: Don't erase your old Profile!!! If there is a format
change in a new Profile, the best way to convert to the new format is
to create a temporary setup with both Profiles in it. Download data
to the instrument using the old Profile, and upload it using the
new Profile.  Use the new Profile to save the data to disk (but
keep a copy of the old data files, just in case).  
!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!

There are several versions of DX and TX profiles.  I'll attempt to
outline the differences and compatibility here.  

DX7ORIG.XOR:
This Profile is your basic DX-7 voice, with old DX-type Function data.
The original DX-7 does not remember Function data for each voice, so
this profile dosn't either.  You can edit the Function data from the
Patch Edit screen. However, it is not a reliable display, since 
it dosn't necessarily reflect the correct value until you've 
changed it (we could make a Profile that kludges TX-like Function
storage for every patch, if so desired). Also, the "range" parameters
go from 0-15 instead of 0-99, so that they will be compatible with 
TX function parameters.  The original DX had no "request" message,
so we've automated the Get Bank process by simulating button pushes
on the DX.  Make sure that SYS INFO is ON on your DX, or this profile 
will not work at all (at least not until XOR is updated to send 
initialization messages).  The Get Patch process is not automated -
you need to select a patch on the front panel in response to the
"Initiate Bulk Dump" prompt.  NOTE: the DX only sends System Exclusive
on Channel 1.  ALSO NOTE: Turn Memory Protect OFF if you wish to 
send a bank of patches to the DX.

DX7NEWER.XOR:
This Profile deals with newer version DX-7s (we hope, although we 
don't have one to test it with at this time).  The newer DX-7's are
able to accept TX function data for one patch.  This Profile always 
sends one voice function data when it sends a voice.  We think that 
the newer DX-7's also respond to request messages, but we're not
positive.  

TX7.XOR:
Use this Profile for either a TX-7, a TF-1 module (TX-216/816) or
a DX-7 with an E! card.  It uses TX-style function data (bank and
single format), so that each voice has its own function data. TX 
Function data also includes the extra "Attenuation" parameter. 
This is a fairly prototypical XOR Profile, with very few surprises.

NOTE for multiple DX/TX or TX-216/816 users:
If there is any chance that you'll be using two or more DX/TX units 
on the same channel, you may want to connect them separately through
your programmable MIDI switcher, and turn "Sw. to Send" ON in XOR's
Instrument Setup screen for those instruments.  This is the best way
to address each instrument separately, while also keeping them on
the same MIDI channel.  A better System Exclusive implementation would
include a Unit, or Device Number, separate from the Receive Channel(s),
in which case you wouldn't need to switch when sending data.

DX7II.XOR:
NOTE: The original version of this profile had a bank format which
only stored 32 voices.  The format has been re-vamped to store 64
voices.  

This Profile handles the different areas of the DX-7II (FD or no FD).
The DX-7 type voice parameters are joined with the DX-7II additional
parameters (this includes the stuff which used to be call functions).
The Profile also handles DX-7II Performances, albeit no too well.
There is a major problem with the DX-7II's MIDI implementation we
haven't been able to work around yet - that is, how to definitely
know which edit buffer (A or B) we are addressing.  We can toggle
between them, but we never really know which one is selected.  Also,
Performances are a problem - when a Performance is sent, the voices
are not changed (as they are in almost every other synth I can think
of).  As the Profile is currently programmed, you need to manually
load the individual voices.  The next version of XOR (1.1) contains
much more powerful internal capabilities, which will allow us to
get around both these problems, so please bear with us.

TX802.XOR:
This Profile is similar to the DX-7II Profile, except for the Per-
formance data, which is completely different in the TX-802.

COMPATIBILITY:
Patch files are semi-compatible throughout the DX/TX line.  All are
saved in the same Library and single patch file format.  However,
there are incompatibilities between patches created with the DX-7II
or TX-802 and all earlier DX/TX formats.  The DX-7II "additional" data
isn't compatible with the DX/TX "function" data.  If you upgrade 
instruments at some point, you'll need to edit the "additional" data 
in your entire Library, at which time you may want to obtain a 
conversion program to automate this otherwise grueling task.

NOTE: Profiles for older DX/TX models which are patch-compatible with
the newer DX-7II and TX-802 models have been developed by James Cox,
and are now available.  These Profiles use the later style format as
a standard, and convert to the older format "on the fly," whenever
necessary - a great example of creative Profile programming.  For
people with instruments from both DX/TX generations, this is a must.

Bank Files are not compatible between generations. All older DX/TX 
Profiles use the .TX7 file format - 32 Voices followed by 32 TX-style
Function data.  The DX7II has its own bank format, with 64 voices,plus
additional and Performance data, and the TX-802 has yet another bank 
format similar to the DX7II, but with its own style of Performances.  
If you upgrade instruments, a simple name change (from .TX7 to .D72) 
will suffice for a quick and dirty conversion - but you'll need to 
remove a bit of garbage from the higher numbered patches. 
Transplant->Bank can be used to copy additional data into each patch 
in the bank, which speeds the conversion process.

OTHER Profiles may be crafted for the DX-7 with E!, the DX-7II with E!,
the DX-9 and DX-5 (don't hold your breath on that one).  Until these
exist, use one of the existing Profiles.