In brief, here are a few things you SHOULD know about this
software: 

o    This current release includes full software support for the
Supercharger PC emulator.  You MUST determine the SCSI ID of your
Supercharger.  They are shipped as ID 3.  After setting up your
hard drive to Auto boot with HDUTIL, go to the Config option of
that program.  Near the bottom of the screen you will see a line
that says 'Skip SCSI ID's:'.  Normally only ID 6 is skipped; this
is the ICD real time clock.  You MUST also set the ID of your
Supercharger here, then save.  This means that all ICD programs
will not do any SCSI commands on this ID.  (This means that you
need no longer hold down the reset button when booting the computer
with the Supercharger attached).

You must also disable write cacheing when running the Supercharger,
otherwise you will never write to your hard disk.  This can be
accomplished in several ways.  First, you can set up your booter to
disable write cacheing.  Second, you can permanently enable write
cacheing and turn it off temporarily with the DESKTOP.ACC or with
the CACHEOFF.PRG.  There is also a CACHEON.PRG to turn the cacheing
back on.  See below for a more complete explanation.

Please note that the Supercharger is fully compatible with OLD
ICD Host Adapters.  It is NOT compatible with early release versions
of the ICD Advantage and Advantage Plus host adapters.  In addition
to the software you will need a hardware upgrade kit which replaces
one of the GAL chips on the Advantage and Advantage Plus boards. The
cost for this upgrade kit is $15.00.  

           Address:  ICD Advantage ST Upgrade Offer
                     1220 Rock St.
                     Rockford, IL 61101

Note that Advantage and Advantage Plus host adapters shipped from ICD
after the date of this file will have hardware upgrades in place to be
compatible with the Supercharger.