REPLAY PROFESSIONAL DEMO
                           by 2-Bit Systems

                 SEE REVIEW IN THIS MONTH'S ST FORMAT

         FOR FURTHER DETAILS CONTACT MICRODEAL ON 0726 68020
        OR WRITE TO: PO BOX 68, ST AUSTELL, CORNWALL, PL25 4YB

Note: only part of the Replay Professional Editor is present. Neither
Drumbeat, MIDIplay or the sampling/playback cartridge are present with
this demo.

Note: if you have the Replay 4 cartridge, you will be able to sample
software with this demo version of the Replay Professional Editor.

REPLAY CARTRIDGE SPECIFICATIONS

Anti-aliasing filters              -    2:  1 each on I/P & O/P

Signal to noise ratio    (input)   -    48 dBs Best case

Max. sample frequency              -    100 kHz (not guaranteed)

Frequency selection                -    software controlled

Resolution     (input)             -    8  BITS
              (output)                  12 BITS

Linearity      (input)             -    Within 1 LSB

Max. input / output signal         -    2 V (P-P) / 0.7 V (R.M.S)


REPLAY PROFESSIONAL EDITOR

Sample frequencies                 -    5.5,8,11,16,22,32 Khz
                                        (Through Monitor/HI-FI)

                                   -    Plus  44 and 48 Khz
                                        (Through HI-FI mode only)

Max. sample buffer size            -    UP TO 4 MEGA BYTES
                                        (On 4 'MEGA ST')

Max. sample magnification          _    to 600 sample BYTES

Sample display modes               -    Filled,Outline & Envelope

Sample editing facilities          -    Reverse, Fade in/out, Overlay,
                                        Insert, Delete, Copy, Clear,
Fill,
                                        Shrink, Load, Save, Filter,
Echo,
                                        Flange and up to 10 sample
preset
                                        function keys.

MIDI facilities                    -    Mono channel (MIDI 1 to 16)
                                        10 note assignable samples
                                        Loop points with full A/S/R
                                        (Attack, Sustain, Release)
                                        Real time pitch shift
                                        MIDI trigger/shift
                                        Store MIDI sets to disc

Total free memory   520  ST        -    better than 230 kBytes
(inc paste buffer)                      ( > 10 secs @ 22 kHz)
                    1040 ST             better than 750 kBytes
                                        ( > 34 secs @ 22 kHz)

DRUMBEAT PROFESSIONAL

Play back frequency                -    22 kHz

Max. kit size                      -    15 SAMPLES

Max. sample size                   -    10 kBytes (half second
samples)

Max. patterns                      -    50

Max. pattern steps per song        -    100

Tempo                              -    40 to 239 beats per minute

Beat registration                  -    1/8, 1/16, 1/32 and triplets
                                        (2,4,8,3,6,9 Beats/quarter
note)

Synchronisation                    -    INTERNAL TEMPO or EXTERNAL
MIDI


MIDIPLAY

Max. number of samples             -    128 (Memory permitting)

RAM control                        -    Dynamic allocation of space

Polophony                          -    UP TO 4 VOICE / NOTE POLY

Keyboard range                     -    C2 to G7 (9 octave)

Features                           -    Pitch bend, A/S/R looping,
                                        MONO/POLY operation.
                                        4 separate keyboards at once
                                        each with its own channel.

Free RAM                 520  ST   -    Better than 280 kBytes
                         1040 ST   -    Better than 820 kBytes





REPLAY PROFESSIONAL EDITOR.

When the EDITOR is first run, it automatically splits the computers
memory into TWO large chunks, one of these is visible as the SAMPLE
DISPLAY, the other is invisible and is called the PASTE BUFFER. This
buffer is used for the temporary storage of samples during editing
operations. Obviously, the larger the PASTE BUFFER, the smaller the
SAMPLE memory is. For this reason it is possible to make the PASTE
BUFFER smaller or even to remove it entirely. This means that larger
sample times can be achieved though it does have the nasty side effect
of restricting the size of the temporary sample which can be held or
restricting the number of edit functions which are available at any
one time.

The MENU bar

DESK
Selecting Desk will allow you to see the REPLAY program credits and
version number only. Any desk accessories loaded will be displayed in
grey lettering, indicating that it has been disabled and is not
available for use within the REPLAY software. Desk accessories are
disabled because of their ability to indiscriminately corrupt samples
held in memory.

FILE
The FILE title will reveal options for loading and saving individual
samples to and from disc, loading and saving SETs of samples complete
with PRESET and MIDI data and finally, the option to leave the program
and return to the desktop. For more information on the LOAD, SAVE and
SET facilities.

FREQUENCY
Selection of the sample and play back speed is achieved by clicking on
the desired value and is put into effect immediately. The 22 KHz value
is the default speed. Roughly speaking, the faster the sample speed,
the higher the sound quality but the shorter the sample time.

OUTPUT
The default output mode is MONITOR but selecting HI-FI will cause all
future output to be heard via an amplifier connected to the REPLAY
cartridge output socket. All output can be heard via HI-FI but certain
restrictions are placed upon the MONITOR mode. For example, an attempt
to select a frequency above 32 KHz in monitor mode will not be
allowed. Similarly, an attempt to return to MONITOR whilst FREQUENCY
is at say, 44 KHz, will be prevented.

DISPLAY
The options shown here will select the mode used to display the sample
in the edit window. The different modes are available to enhance
particular detail in a sample. The general purpose selection, FILLED,
is the default, but OUTLINE would usually be fine. The main use of
outline is for revealing the true shape of a waveform under high
MAGNIFICATION where the true wave shape is displayed. The ENVELOPE
option will display the full wave envelope reflected along the central
axis. This display mode is useful for showing bursts of speech or
drums (for example) in amongst a lot of otherwise confusing data.

The sample display
You will notice a Black line to the left of the display. This is the
LOWER edit cursor. To the right you will notice a Black and White
dashed line. This is the UPPER edit cursor but it is covered by
another cursor called the GHOST cursor.

UPPER & LOWER cursors

The UPPER and LOWER edit cursors are the key to the operation of the
whole EDITOR because it is between these two points that ALL
operations are performed. To be useful, it must be possible to move
these two pointers. This can be achieved in two ways. One is to use
the cursor movement buttons found on the cursor control panel (section
4.5), the other is to use the mouse directly within the sample
display. First, Move the mouse 'ARROW' pointer over the dashed line to
the right of the sample display, press the left mouse button and keep
it pressed. If you are over the cursor line, the ARROW should change
into a POINTING FINGER. This means that you have found the cursor and
are ready to move it. Now, keeping your finger on the left mouse
button, move the mouse to the left, a black line should follow. Move
the cursor to the centre of the screen and release the mouse button.
The POINTING FINGER should revert back to an ARROW. There should now
be three vertical lines on the screen, two black and one dashed. The
same operation can be performed on the LOWER cursor to the left of the
screen, try it now. You will find that it is not possible to move a
cursor further than the position of its opposite number.

Both of the UPPER and LOWER cursors will be visible AT ALL TIMES in
the SAMPLE display while the GHOST cursor (the dashed line) may
disappear from view from time to time.

The GHOST cursor
Quite simply, the GHOST cursor is a position marker. For example, when
a sample is played back and stopped early by pressing the escape key,
the GHOST will mark the position at which the sample play back was
stopped allowing easy location of parts of a sample of interest. The
GHOST may appear to do strange things. If, for example, a sample is
loaded from Disc, the UPPER cursor is automatically placed at the end
of the new sample on screen and the GHOST will mark the position of
the UPPER cursor BEFORE it was moved to the end of the newly loaded
sample. This is because the EDITOR will perform an operation by
default, but might do something that the user did not want or expect
it to do. Therefore the user can correct the mistake by moving the
UPPER cursor back to the position marked by the GHOST cursor. The
GHOST cursor has a special function assigned to it called the SWAP
button located on the PASTE BUFFER control panel. Pressing this button
(or the space bar) will cause the EDITOR to swap the locations of the
UPPER and GHOST cursors instantly, thus enabling fast and accurate
relocation of the UPPER cursor to its old position. A little
experimentation with the EDITOR will show the exact nature of this
very useful facility.

ZOOM (magnify)
The ZOOM button will cause the display to magnify in upon the data
currently displayed between the cursors. Magnification can be
performed as much as desired, but magnification beyond 600 sample
values between the cursors has no effect.

SAMPLE SIZE DISPLAY / SET
This box displays the size of the sample currently displayed between
the UPPER and LOWER cursors. However, this box also has the hidden
ability to set the size of the sample. This is achieved by clicking
the mouse inside the sample display, upon which the numbers in the box
will be replaced with '________'. This indicates that the computer is
waiting for the user to type in a number and press the RETURN key when
finished. If the RETURN button is pressed without entering a number,
then the old size is retained by default. Any valid number is one
between the values of 2 (minimum size) and the present size of the
SAMPLE buffer. If a value that is too great is entered, then the
previous size is returned to. Please note that as an alternative to
terminating the number with RETURN, the letters 'K' and 'S' may be
substituted. The significance of these is to set the size to kbytes or
seconds respectively. Hence entering 10K will set the size to 10,000
bytes. Entering 10S will attempt to set the size to that equivalent to
10 seconds of sampling. Only integer values are permitted, decimal
points are not allowed.

RESET magnification
The RESET key has the effect of un magnifying back up to maximum
screen size. The UPPER and LOWER cursors will remain at their previous
positions. If the cursors are too close together, then they may
disappear from the display. This is because they are virtually on top
of one another. Simply use MAGNIFY again to relocate them, or move one
or the other cursor, one position either way via its key on the cursor
control line. Pressing RESET when no magnification is in effect will
cause the cursors to return to their respective extremes on either
side of the edit window. All cursor position data will be lost. If the
positions were accurately located and were important, then they could
have been stored in one of the 10 PRESET memories in case of mishap.

SAMPLING / PLAY BACK control

SAMPLE
Clicking on this button will cause the program to start sampling the
sound currently being played on the input of the REPLAY cartridge. The
sound will be heard simultaneously via the Monitor speaker or
Amplifier, depending upon the current setting of the MENU bar OUTPUT
control. Sampling will stop automatically when the sample space is
used up, or when the the sampling has been terminated prematurely by
pressing the ESCape key. The sample display will be redrawn to reflect
the changes within the SAMPLE buffer.

PRE-SAMPLE
This very useful feature samples continuously. The only way to exit
PRE-SAMPLE is to use the ESCape key, after which the sample will be
drawn on the screen. There may be a small delay between halting the
function and control being returned to the editor, especially when
using very large sample areas. When using the straight SAMPLE button,
TRIGGER can be used to actually start the sampling but does not
guarantee to catch the end of the desired sample. PRE-SAMPLE allows
continuous monitoring of the sound and may be terminated upon
completion of the sample. Of course, we can not guarantee to have
captured the start of the sample in memory, but with use of the set
sample size facility we can set the size of the record buffer to any
size we choose. The best option however is probably to use the entire
sample memory to be quite confident of catching the sample required.

TRIGGER ON / OFF
With TRIGGER selected, selecting SAMPLE has no immediate effect.
Sampling is suspended until the incoming sample volume exceeds the
value displayed in the box to the right of the TRIGGER button. As soon
as SAMPLE is selected, the MOUSE pointer will turn into a BEE to
indicate that it is waiting to start sampling. As soon as the sample
volume exceeds the preset value the sample button will then turn
black. Sampling may be terminated BEFORE the TRIGGER occurs by
pressing the ESCape key. No sample operation will take place under
these circumstances.

TRIGGER sensitivity
The box to the right of the TRIGGER button displays the trigger
sensitivity. The smaller the value, the more sensitive, the larger the
value, the less sensitive the TRIGGER is. The two arrows on either
side of this display are used to adjust this threshold value up and
down. Sensitivity is incremented in steps of two. When related to the
SCOPE display, a value of 1 represents a small movement of the scope
display, where as a value of 127 requires the signal in the SCOPE
display to touch either the top or bottom of the display to cause a
sample TRIGGER to occur.

HEAR (audio monitor)
Upon selecting HEAR, audio input to the REPLAY cartridge may be
monitored in real time. It is possible to start sampling at any time
by pressing the 'S' key, otherwise selecting ESCape will halt the
function in the normal fashion.

LOOP ON / OFF
With LOOP selected, forward or backward play back of a sample will
continue looping from start to end and back again, until the ESCape
key is pressed.

PASTE BUFFER control
As has previously been explained, the PASTE BUFFER is an area of the
computers memory which is automatically set aside by the EDITOR for
the temporary storage of samples or parts of samples. The paste buffer
can only hold one sample at a time and may occasionally be required
for other uses by the EDITOR, the SPECIAL EFFECTS for example.
Whenever an operation to clear or overwrite the contents of the buffer
is required, the EDITOR will always request permission to destroy the
contents of this otherwise hidden sample. On occasions, the EDITOR may
throw up the strange message 'CURSOR GAP TOO SMALL' and give the
option to 'OVERFLOW', 'CLIP' or 'CANCEL'. This is trying to say that
the sample in the BUFFER at present is larger than the size of the gap
between the UPPER and LOWER cursors. You are given the opportunity to
cancel the function, to just take sufficient of the sample from the
BUFFER to fit the cursor gap or simply to take the entire sample from
the BUFFER and ignore the size of the cursor gap entirely.

STORE sample
Selecting STORE will copy the current sample between the UPPER and
LOWER cursors into the PASTE BUFFER. It will remain there until it is
erased by another sample or when cleared out for use by another
function, such as reducing the size of the BUFFER itself.

INSert sample
The LOWER cursor position is taken as the start of this operation. The
EDITOR will move the entire contents of the sample space, starting
from the lower cursor position, towards the right of the screen by
just enough space to fit the sample in the PASTE BUFFER into the new
space created. The sample in the PASTE area is then copied into the
sample edit area. Any sample that used to exist at the very end of the
sample buffer will be lost forever. To clarify exactly what the
function does, a little demonstration is required. Suppose that we had
just sampled the word 'HELLO' into the computers memory. We now move
the UPPER cursor down towards the start of the sample until we only
have the letter 'H' surrounded by the cursors. Now press the STORE
button. Next, press the INSert button twice, allowing time for the
operation to complete between presses. Now move the UPPER cursor back
to the end of the sample and press PLAY. The computer will now say 'H-
H-HELLO'.

REPeat sample
REPeat performs a similar function to insert. It will copy the entire
contents of the sample edit area from the LOWER cursor position and
place the copy at the position pointed to by the UPPER cursor. Again,
any sample at the end of the sample area will be lost. Again, a simple
explanation will clarify the exact function of this useful feature.
Suppose that we had just sampled the 'HELLO' into the computers
memory, as before. Again we surround the 'H' with both cursors. Now
press the REPEAT button twice, allowing time for the operation to
complete between presses. Now move the UPPER cursor back to the end of
the sample and press PLAY, it should now say 'H-H-HELLO'. Notice that
we have created EXACTLY the same effect as before, but we did not have
to use the PASTE BUFFER directly as before.

Create a GAP
GAP inserts a blank space between the cursors. The whole sample,
starting from the lower cursor running right up to the end of memory,
will be shifted up to the UPPER cursor leaving the space between both
cursors. This space may now be recorded into or have something PASTED
or loaded into it.

PASTE sample
The contents of the PASTE BUFFER are copied from the buffer into the
sample area overwriting what ever was in the sample space before the
operation. The copy is placed at the start of the area marked by the
LOWER cursor position.

CUT sample
The sample between the cursors is removed and the contents of the
sample edit area, starting from the UPPER cursor, are copied down to
the LOWER cursor. Any trace of the old sample is lost unless it was
first saved with a STORE operation. This function DOES NOT work in the
manner that some WORD PROCESSOR users might imagine. The choice of the
words in the EDITOR for CUT, PASTE and STORE are more logical and
describe EXACTLY what they do.

CLR
Selecting CLR will erase the sample between the UPPER and LOWER
cursors. Again, the action of this button is NOT reversible unless
preceded by a STORE operation.

SWP
SWP causes the editor to SWAP the positions of the UPPER and GHOST
cursors. Whilst not sampling, pressing the space bar performs the same
function.

BUFFER size display
The value shown in this box shows the size of the current PASTE BUFFER
and therefore the largest sample size that can be held in the buffer.
However, in the same way that the sample size display can be used to
set the cursor width, clicking in this box with the mouse will again
display '________'. The size of the PASTE BUFFER can not be larger
than the sample edit work space.

PASTE BUFFER status
Finally a little box is located to the right of the BUFFER size
display. The contents of the display are either E for Empty or F for
Full. If the user clicks on the button when 'Full' the contents of the
buffer are played out through the currently selected output channel.


EDITOR FUNCTIONS

FADE IN / OUT
Selecting either of the Fade options will cause the sample to fade in
from zero to maximum volume or fade out from maximum volume to zero.
As with ALL of the edit functions, the area between the UPPER and
LOWER cursors is the area faded in or out.

FILL
The area between the cursors is filled with as many repetitions of the
sample presently held in the PASTE BUFFER as can be fitted in. Please
note that this may include a copy of the sample at the end of the FILL
area which is INCOMPLETE ! (I.E. two and a half copies of the PASTE
sample).

VOLUME
Upon selecting VOLUME, the computer will ask you to select volume up
or down. Select the desired direction and the EDITOR will increase or
decrease the sample between the sample cursors by about 12%. Please
note that repeated use of VOLUME increase will result in a
proportional increase in any noise present in the sample !

FIND
FIND will locate the occurrences of a sample segment held in the PASTE
BUFFER. Upon selecting FIND, the EDITOR will ask were to start
searching from. The search will either look from the very START of the
sample buffer to find the FIRST occurrence of the sample in the sample
buffer, or start searching from the LOWER cursor position (the NEXT
occurrence). Please note that FIND may take some while to search a
very large sample buffer. Also, to make a match, the sample being
searched for must be an EXACT copy of that held in the PASTE BUFFER.
It is therefore a waste of time to search for a sample which has had
its volume adjusted !

REVERSE
This function reverses the sample in memory and has the same effect in
RAM as having played the sample backwards using the BACK option from
the sample play control panel.

FINE
FINE allows accurate positioning of the UPPER and LOWER cursor
positions. The EDITOR will give the user the option of which cursor to
adjust. Upon selecting a cursor, the sample display window will be
replaced with a magnified display of the sample surrounding the
selected cursor. Moving the mouse pointer into the display area and
pressing the LEFT mouse button will cause the cursor to be moved to
that position. Pressing the RIGHT mouse button in the display area
will cause the cursor to be positioned back at the exact same location
found upon entry into the display mode. To exit from this mode of
operation, move the mouse pointer outside of display area and press
the RIGHT mouse button. The display will be returned to that relevant
at the time before entry into the FINE mode with the selected cursor
at its new position. This mode of location is useful for accurately
identifying the start and end of sample segments, or for locating the
cursors in an attempt to remove MIDI looping clicks.

SHRINK
SHRINK compresses a sample to be half of its original size. As a
result, the speed of the sample will now be double its original value,
so to correct for this, it will be necessary to select a new sample
frequency from the FREQUENCY menu on the MENU bar. For example, assume
that a sample was made at 22 kHz and then shrunk, then a new value of
11 kHz will need to be selected to make the sample sound correct. It
is advisable to sample sounds at the highest possible speed and then
shrink them down to the desired speed. This will normally result in a
higher quality sound than if it had simply been sampled at a lower
speed since the sample will have been made at a speed many times
faster than the filtering threshold of the REPLAY cartridge and will,
therefore, be subject to much less ALIASING than at lower speeds.

JOIN
The controls now in the centre of the screen, effectively allow fine
positioning of both of the UPPER and LOWER cursors by selecting the
appropriate buttons. Alternatively, the user can actually draw, on the
screen, the waveform between the sample start and end points.
Provision is made for testing the sample from within this mode of
operation. On leaving the JOIN mode, the EDITOR central control panel
will be redrawn and the sample display will also be redrawn with the
cursors at their new locations.

Micro adjust.
Selecting the double arrows located either side of the legends
marked LEFT and RIGHT will increment the cursor positions in steps of
10 samples at a time where as the single arrow keys will move 1 sample
at a time. The display is redrawn after each selection to display the
latest cursor position.

Screen draw.
Selecting screen draw will enable the user to place the mouse
pointer any where within the sample display and hand draw the
waveform by pressing the LEFT mouse button and moving the mouse
pointer slowly around the screen. To exit draw mode, move the mouse
pointer to some point OUTSIDE of the sample display area and press the
RIGHT mouse button, upon which the editor will return to normal loop
edit mode. Screen draw should only be used where the cursors represent
the START AND END of the sample and not where the cursors represent
loop pointers located somewhere inside a MIDI looping sample.

OVERLAY
The sample in the PASTE BUFFER is superimposed on top of the sample
between the current cursor positions. Please note that there will be a
resulting reduction in the overall sample volumes after the operation
has been performed. Crude ECHO effects can be created by overlaying
samples on top of themselves but displaced by a small amount.

PRESET
To assign a sample or memorise the cursor positions at any time,
select the PRESET key, it should turn black. The EDITOR is now waiting
for the user to select the function key to which the assignment should
be made. Select an unused key from f1 to f10. Once this is done, the
user will be requested to enter a name for the sample. The name can
consist of up to 8 valid printable characters, and should be typed in
from the computer keyboard. Press RETURN when finished. If a key
already has a name, then just pressing the RETURN key will keep the
old name. The name of the current sample is displayed in the edit
window after selecting or naming a function key.

F1 to F10
The function keys can be used on their own or jointly with the PRESET
key. When the PRESET key is selected, pressing a function key will
cause the EDITOR to assign a sample or memorise the positions of the
cursors within the sample edit display window. Pressing a function key
while the PRESET key is NOT selected, will cause the EDITOR to
relocate the screen to the exact position that it was in when the
definition was last set. The entire contents of the screen are
remembered including the state of magnification.

SPECIAL EFFECTS (S.F.X)
***NOT IMPLEMENTED IN DEMO***

DIGITAL FILTERING
***NOT IMPLEMENTED IN DEMO***

MIDI

Within the EDITOR, it is possible to play samples under the control of
an external MIDI keyboard. While the facilities offered here are some
what more restrictive than within the MIDIPLAY software, the user has
the chance at least to try out samples under MIDI KEYBOARD control and
test the loop points accurately using the TEST function.

MIDI looping
Throughout the use of the EDITOR, it is made clear that performing an
operation upon a sample is always relevant to the sample or part
sample held between the LOWER and UPPER cursors, until now ! Because
of the fact that REPLAY PROFESSIONAL can now perform MIDI LOOPING, the
cursors now perform a slightly different function. It is always
assumed that the extreme Left of the display is the start of the
sample and the the extreme right of the display is the end of the
sample to be played REGARDLESS of the present setting of the cursors.
The cursors now form the body of the sample to be looped. The LOWER
cursor defines the start of the loop and the UPPER cursor, the end.
But what is MIDI looping ? Well, consider an instrument such as a
guitar. When the guitarist strums a note, the note plays, loud at
first and decays away until it can no longer be heard. In this case
the sample plays once and decays away naturally. Now consider an
instrument such as a violin. As the violinist draws the bow across the
violin, the instrument makes a noise. The violinist can make the
instrument play a short or a long note depending on how far the bow is
pulled across the strings, the violinist can SUSTAIN the note for a
longer period. As soon as the bow is removed, the note will decay to
nothing. By carefully defining loop points in some samples we can add
our own SUSTAIN period. We do this by surrounding the loop point by
the cursors. REPLAY PROFESSIONAL supports a form of A.S.R. looping
(Attack, Sustain, Release) which can be individually selected to be on
or off for each sample.

The attack is the first and often loudest part of a sample and is
defined as the part of the sample between the Left of the display and
the Left cursor. The Sustain period is the 'Flat' part between the
cursors. The Release phase of the sample is defined as the point
between the Right cursor and the Right hand side of the display. When
a looped sample is played, the sample is played from the far left of
the screen through the Left cursor to the Right cursor. If the MIDI
key is still pressed then the sample goes BACK to the Left cursor
again and plays to the right cursor. If the MIDI key is now released,
then the sample will continue to play until the end, upon which it
will stop.

Sample data box
In the centre of the display, the editor shows data on the PRESETS. It
shows the sample PRESET number and the name of the sample assigned to
it, if any. Next the MIDI note assignment, if valid followed by an 'L'
if the sample is defined to be a looping sample.

Sample selection
To select a sample, simply click the Mouse on the relevant function
key legend on the screen.

The SCREEN pointer
At the end of the row of Function buttons is a large button called
SCREEN. This button is a button which will allow the user to
experiment with looping pointers without having to go through the
rather tedious business of setting up a PRESET every time a change is
to be tested.

Assigning to a MIDI note or KEY
To assign a PRESET to a MIDI note for the TRIGGER mode, select the
button called NOTE. Now click on the legend of the function key that
you wish to assign the NOTE to. The Mouse pointer should now change to
the small image of a MIDI keyboard. The computer is now waiting to
receive a note on the MIDI input, simply press a key on the MIDI
keyboard or press the ESCape key. The mouse pointer should now return
to its Arrow shape.

MIDI CHANNEL selection
For the TRIGGER, KEYBOARD and TEST modes to work, the MIDI channel
must be set up to be the same as that of the MIDI keyboard in use. The
MIDI channel number can be selected by clicking on the arrows
surrounding the MIDI channel display.

TRIGGER performance mode
Upon selecting TRIGGER, the computer will wait for a key on the MIDI
keyboard to be played that matches on of those in the sample data
display. As soon as a selected key is pressed, then the sound assigned
to that key will be played. To exit trigger mode press the ESCape key.

KEYBOARD performance mode
As soon as keyboard mode is selected, the the computer is waiting for
a note on the MIDI keyboard to be played. When a key is pressed, then
the current sample will be played in that KEY. To change the sample,
simply press the associated FUNCTION key on the COMPUTERS keyboard.
The new sample will become the active one straight away. To exit the
KEYBOARD mode simply press the ESCape key.

TEST mode
TEST mode is identical to the KEYBOARD mode with the exception that on
entry, its default sample is whatever is setup on the SCREEN button.
The other point of interest is that setting the LOOP button before
selecting TEST will cause the sample to adopt A.S.R. loop mode.

SAMPLE change in KEYBOARD mode
While in KEYBOARD mode, the simple method of changing the 'ACTIVE'
sample is by pressing a Function key on the computer keyboard. An
alternative exists if the MIDI keyboard in use is equipped with voice
change buttons which are MIDI controllable. By pressing the voice
button which issues the MIDI data 'VOICE 1' will cause the computer to
select that sample number.

LOOP CLICKS
Loop clicks are probably the biggest enemy of the musician wanting to
use samplers as serious alternatives to REAL instruments. Use of the
FINE and JOIN modes in the editor are highly recommended to try and
help this often arduous and thankless task. Remember the famous saying
'Patience is a virtue' ! Perseverance really is the name of the game
here.

FILE handling

LOAD sample
Clicking on LOAD SAMPLE will cause the EDITOR to place the computers
file requester on the screen. The default file type to load will be
.SPL It may be necessary to change the extension to .AVR depending on
the type of sample to load (see APPENDIX iii for further details).

SAVE sample
***NOT IMPLEMENTED IN DEMO***

SETS
A SET is a disc file which contains a number of samples (between 1 &
10) which are used in conjunction with the EDITORS MIDI facilities
(section 4.13).

LOAD SET
Selecting LOAD set will cause the file selector to appear. Upon
selecting the desired SET, the computer will proceed to load all of
the samples into memory and assign them to the Function keys
accordingly. MIDI key assignment and looping data is also
automatically loaded in along with the cursor positions. The samples
are all loaded in as one block and it is up to the user to ensure that
sufficient space is available to load the SET into memory since, with
all other operations, the samples are loaded into the memory space
starting from the LOWER cursor position. If prior to loading a SET
into memory, some function keys are already defined, then these
definitions will be wiped. All samples are assumed to have been made
at the same sample speed. After loading, the computer will attempt to
set the system play back speed to be that relevant at the time of
saving the SET to disc.

SAVE SET
***NOT IMPLEMENTED IN DEMO***

ADD SET
After selecting ADD SET and choosing the set to load from disc, the
computer will start to load the samples into memory. The new sample(s)
will again be loaded into the sample edit area starting from the LOWER
cursor position so great care must be taken to ensure that the new
sample data does not overwrite the sample space of existing PRESETS !
When assigning the key definitions, the computer will start to assign
sample from the lowest available spare function key and will only
assign the new samples to empty keys. If in the process of allocating
the definitions, the computer runs out of spare function keys, then a
warning will appear on the screen. All sample will be loaded (space
permitting) but some samples may NOT be assigned to a key if none are
available.

WIPE SET
Upon selecting WIPE set, the central control panel will be replaced
with a new control panel. The top line of control buttons represent
the Ten function keys. It will now be possible to select a function
key or series of keys to de-allocate. Upon selecting ERASE, the
definitions highlighted in black will be made empty. Only the Function
key definition is removed, the sample in memory is left intact ! This
must be cleared out separately if required.