BMODEM for the Atari ST Computers
                                  Version 2.3a

                     A Public Domain Communications Program
                                  by David Betz





       Permission  is  granted for the non-commercial use and distribution
       of  this  software  and documentation, provided only that credit be
       duly  given.   Suggestions  for improvement, or reports of problems
       regarding this software should be made to the author:


                                   David Betz
                               114 Davenport Ave.
                              Manchester, NH 03103

                              (603) 625-4691 (home)















                     Manual Revision 1.1 - December 2, 1986

                 Questions or suggestions regarding this manual
                             should be addressed to:

                                  Ron Sprunger
                                 74-285 Primrose
                              Palm Desert, CA 92260
                               Tel (619) 341-0109





















                               -TABLE OF CONTENTS-


                       Manual Conventions..............  1
                       Purpose of BMODEM...............  1
                       Program Setup...................  1
                       Usage...........................  2
                       Terminal Mode...................  2
                       Command Mode....................  2
                       Commands........................  3
                           TYPE........................  3
                           EXPECT......................  3
                           SEND........................  4
                           RECEIVE.....................  4
                           CAPTURE.....................  4
                           CLOSE.......................  4
                           ASEND.......................  4
                           XMODEM/YMODEM...............  5
                           CHECKSUM/CRC................  5
                           VERIFY/NOVERIFY.............  5
                           WATCH/NOWATCH...............  5
                           FULL-DUPLEX/HALF-DUPLEX.....  5
                           BAUD-RATE...................  6
                           DTR/NODTR...................  6
                           ESCAPE......................  6
                           CALL........................  6
                           EXIT........................  7
                           ABORT.......................  7
                           HELP........................  7
                           PROMPT......................  7
                           DELAY.......................  7
                           MKEY........................  8
                           STATUS......................  8
                           SYSTEM......................  9
                           SET.........................  9
                       Script Files.................... 10
                       BMODEM.INI...................... 11
                       Command Summary................. 12
                       Macro Binding Summary........... 12
                       Version History................. 13
                       Known Bugs/Problems............. 13
                       Under Consideration............. 13




















       BMODEM for the Atari ST                                 Page 1
       Reference Guide


                              -MANUAL CONVENTIONS-

       In  this  manual,  the  characters  "<"  and ">" are used to denote
       specific  keys  to be pressed.  For instance <Return> refers to the
       key marked "Return" on the keyboard.

       The  caret  ("^")  is  used to signify a "control key".  This means
       that a particular key is to be struck while <Control> is depressed.
       In  the  case  of  scripts,  the  caret is also used to signify the
       character  which would be produced by pressing a particular control
       key.   "^M",  for instance, is the ASCII carriage return character,
       which may be produced from the keyboard by striking <Return>, or by
       pressing <m> while holding down <Control>.

       Parentheses ("()") are used to indicate required parameters.

       Square brackets ("[]") are used to indicate optional parameters.

       "/"  is  used  to indicate that either of two choices is possible.
       For instance CRC/CHECKSUM means that either "CRC" or "CHECKSUM" may
       be given as the command, depending on which is desired.


                                    -PURPOSE-

       BMODEM   is   a   terminal   emulator/file-transfer   program.   It
       facilitates  communications  with  remote computers by allowing the
       use  of  the Atari ST as a terminal via modem or direct hookup, and
       allows   inter-computer  transfer  of  files,  using  file-transfer
       protocols commonly available on remote bulletin board services.  It
       was  specifically  designed to make life easier when using the Byte
       Information Exchange, or BIX.

       A  "protocol"  is  simply a way for two computers to transfer files
       between  themselves  with verified accuracy of the transfer by some
       means.   BMODEM  allows capturing or sending ASCII text files using
       no protocol, as well as receiving and sending binary files with the
       popular  xmodem  and  ymodem  protocols.   An  ASCII  file  is  one
       containing  text;  that  is, readable characters.  A binary file is
       one  which might have meaning to a computer, such as a program, but
       which  might  contain  some  characters which people, printers, and
       terminals can't handle.

       In  addition,  BMODEM  has  the  ability  to  perform  sequences of
       commands automatically, according to information in "script" files,
       as  well  as  to  expand  specific  function  keys to user-selected
       commands (macros).


                                     -SETUP-

       BMODEM  may  be installed on any Atari ST computer.  If the program
       is  to  be  invoked  from  the  desktop  with specific script files
       specified,  it should be renamed to BMODEM.ttp, or installed on the
       desktop  as  a  "TOS  Takes Parameters" program.  Otherwise, it may
       simply be installed as BMODEM.tos.






       BMODEM for the Atari ST                                 Page 2
       Reference Guide


                                     -USAGE-

       BMODEM  is  invoked from the desktop by double-clicking on its icon
       or  filename,  or  from  a  shell  by  invoking  according to shell
       conventions.   If  BMODEM  is  installed  as a Tos-Takes-Parameters
       program, the user will be prompted for parameters to pass on to the
       program.  The only valid parameter is a filename, which BMODEM will
       interpret  as  a  script  file  (q.v.).  When first started, BMODEM
       looks  for  a  file called BMODEM.ini, and uses that as the default
       script.   If  BMODEM.ini  exists, all commands in that file will be
       interpreted and executed first, then if a script file was specified
       in  the  program invocation, that script will be read and acted on.
       In the absence of other specifications, BMODEM will default to 1200
       baud, half-duplex operation, with default file-transfer protocol of
       xmodem/crc.

       When  BMODEM starts, a one-line version identification message will
       be displayed, after which BMODEM will first interpret and implement
       BMODEM.ini,  then whatever script file is pending, then immediately
       go  into  terminal  mode.   BMODEM  operates  in either terminal or
       command mode, both of which are explained below.


                                 -TERMINAL MODE-

       When  BMODEM is in terminal mode, whatever is typed at the keyboard
       will  be delivered to the serial communications port.  Commands may
       be  given  to  the  modem attached to the serial port to initiate a
       call, or if a connection already exists, what is typed will be sent
       on to the remote computer.

       BMODEM  commands  may  not be given in terminal mode, since what is
       typed  at  the  keyboard  is  not  interpreted by BMODEM.  While in
       terminal  mode,  you  may  use BMODEM's "macro" capability to issue
       commands by pressing certain "function keys".  See "MACROS".

       Pressing  <^\> (hold down <Control> while pressing <\>) will switch
       to command mode, signified by the "CMD>" prompt appearing.  <^\> is
       the  "escape"  key,  and may be changed with the "ESCAPE" command.
       See "COMMANDS".


                                 -COMMAND MODE-

       Except for macros, BMODEM commands must be given from command mode.
       You are in command mode when you see the "CMD>" prompt.  In command
       mode,  you  are  talking  to  BMODEM,  and  may  change  any of the
       user-controllable  parameters  of  the  program, such as baud rate,
       communications  protocol,  or  the  escape key.  You may also begin
       file transfers, issue system commands, and close files.

       To exit command mode, just press <Return>.










       BMODEM for the Atari ST                                 Page 3
       Reference Guide


                                   -COMMANDS-

       BMODEM  commands  may  be  given  in  upper  or  lower-case, or any
       combination  of  the  two.  Some commands are self-sufficient; that
       is,  merely  typing  in  the  command,  followed  by  <Return>,  is
       sufficient  to  bring  about  the  desired  effect.  Other commands
       require additional information, such as a file name to act upon, or
       a  character  or  string  of  characters to associate with a key or
       action.    If  the  command  requires  additional  information,  or
       "parameters", type in the command, followed by a space, followed by
       the parameter.

       More  than  one  command  may be given on a line, provided that the
       commands are separated by a space.

       All BMODEM commands are explained below.  The commands are given in
       upper case, though they may be entered lower case as well.  A brief
       description  of each command is given, along with an example of its
       use.  The examples are preceded by "CMD>", indicating that they are
       to  be  typed  in  from  command mode.  All commands may be used in
       script  files as well.  Valid commands for BMODEM, along with their
       usage, are:


         TYPE (character-string)

         Send  a character, or string of characters, to the communications
         port.  If the string contains spaces or certain other characters,
         it  MUST  be  enclosed  in  quotes, so quoting a string is a good
         idea.   If the string contains control-characters (ASCII values 0
         through  31  decimal), they may be signified with the caret ("^")
         followed  by  the  character having an ASCII value 64 higher than
         the  ASCII  value  desired.  For example, to send "myname" to the
         port, followed by a carriage return, you would give the command:

         CMD> type "myname^M"


         EXPECT (character-string)

         The  program  awaits  character-string before proceeding with the
         script.  While it waits, BMODEM returns to terminal mode, so that
         normal  communications occur until the expected string is sent by
         the remote system, at which time the script will be resumed.

         CMD> expect "login:"
















       BMODEM for the Atari ST                                 Page 4
       Reference Guide


                              -COMMANDS (Continued)-

         SEND (filename)

         Begin  sending the specified file using the current file-transfer
         protocol.   The  remote  system  must be set up to receive a file
         using  the  same  protocol prior to invoking the "SEND" command.
         The filename does not need to be quoted.

         CMD> send test.prg


         RECEIVE (filename)

         Begin  receiving  the  specified file using the currently-defined
         file-transfer  protocol.   The remote system must be commanded to
         send  a  file  using  the  same  protocol  prior  to invoking the
         "RECEIVE"  command.   The  file  is automatically closed when the
         transfer is complete.

         CMD> receive test.prg


         CAPTURE (filename)

         Begin capturing ASCII text, to be put into the specified file.

         CMD> capture test.txt


         CLOSE

         "Close"  requires  no  parameters,  and closes the currently-open
         ASCII  capture  file.   No  on-screen  indication is given of its
         action,  and  the  only  indication  the  user  might have of its
         efficacy  is  some  activity on the disk drive.  BMODEM closes an
         open capture file automatically on EXIT.

         CMD> close


         ASEND (filename)

         Send  the specified ASCII text file over the port.  The user must
         prepare  the  remote  system  in advance for receiving the text.
         Usually, this means invoking an editor on the remote system, then
         giving  the  asend  command.   When  ASEND  opens  the file to be
         transferred,  it  reports the file name and number of bytes to be
         sent.   As  the  transfer  takes place, a status line continually
         reports the line being sent and the cumulative bytes transferred.
         At  the  end of the transfer, the message [ ASCII send complete ]
         is  displayed.   While  the  transfer  is  in progress, it may be
         terminated at any time by pressing the <Esc> key.

         CMD> asend test.txt







       BMODEM for the Atari ST                                 Page 5
       Reference Guide


                              -COMMANDS (Continued)-

         XMODEM/YMODEM

         These are the two protocols currently supported by BMODEM for the
         transfer  of binary files.  Xmodem is the popular Modem7 protocol
         of Ward Christensen, supported by almost all bulletin boards.  It
         involves  the  transfer of files in 128-byte chunks, or packets.
         Ymodem  is  a  similar  protocol, but uses 1024-byte packets, and
         thus  works  more  rapidly,  if  the  remote  system supports the
         protocol.   In  either case, each packet is checked at both ends,
         and the verifying information compared.  The checking can be done
         by  either  CRC or CHECKSUM, which will not be further explained,
         other  than  to  say  that  they  are  two  different  methods of
         verifying the content of a packet.

         CMD> xmodem


         CHECKSUM/CRC

         The  user  may  specify one of these two verification methods for
         use in file transfers.

         CMD> checksum


         VERIFY/NOVERIFY

         Signals  whether  script  commands  are  to be echoed on the host
         screen or not.

         CMD> verify


         WATCH/NOWATCH

         Indicates whether BMODEM should show the results of script dialog
         on the screen or not.

         CMD> watch


         FULL-DUPLEX/HALF-DUPLEX

         In  full-duplex,  BMODEM  expects  the remote system to echo back
         everything  the  host  sends it.  In half-duplex, BMODEM does the
         echoing,  saving transmission time.  If the remote system assumes
         full-duplex,  and  the  user selects half-duplex, every character
         typed  at the keyboard will appear twice on the screen; once from
         BMODEM, and once from the remote system.

         CMD> full-duplex









       BMODEM for the Atari ST                                 Page 6
       Reference Guide


                              -COMMANDS (Continued)-

         BAUD-RATE (rate)

         Most  modem  communication  is  done at either 300 or 1200 baud.
         Baud  refers to the speed with which data is transferred.  Direct
         connection  of two computers usually allows faster rates, such as
         2400,  4800,  or  even  9600 to be used.  The "baud-rate" command
         sets  the Atari's serial port to the specified speed.  The remote
         computer  must  be communicating at the same speed, and the modem
         (if any) must also support the speed.

         CMD> baud-rate 1200


         DTR/NODTR

         When  two  computers  are  communicating, it is necessary to have
         some  form  of flow control, so that information is not sent over
         the  line  faster  than  the  recipient  can  accept it.  This is
         typically done with a protocol called XON/XOFF, meaning that when
         the recipient needs to stop the flow, it sends the XOFF character
         (usually ^S), and when it again is ready to receive, it sends the
         XON  character (usually ^Q).  Another method is DTR, meaning Data
         Terminal  Ready.   This  requires  at  least one more line in the
         communications  line,  usually  connected to pin 20 on the serial
         port.  Whether DTR is being used is controlled by this command.

         CMD> nodtr


         ESCAPE [modifier-](named key)

         BMODEM by default recognizes <^\> as the command to transfer from
         terminal  to command mode.  The user may change this to any named
         key  with  the  "ESCAPE"  command.  After entering "escape ", the
         user  may  enter  any  or  all  of  the  modifiers 's', 'c', 'a',
         specifying  that  the  named  key  must  be entered with <Shift>,
         <Control>,  or <Alternate> depressed, or any combination thereof.
         For  more  information  on named keys and modifiers, see MKEY and
         "Command Summary".

         CMD> escape s-undo


         CALL (filename)

         In  addition  to  allowing  a  script file name as a parameter on
         invocation,  BMODEM  will open and use a named script at any time
         by  use  of the "call" command.  The filename does not need to be
         quoted.

         CMD> call myini.fil









       BMODEM for the Atari ST                                 Page 7
       Reference Guide


                              -COMMANDS (Continued)-

         EXIT

         Leaves  BMODEM  and  returns  to the calling program (usually the
         desktop or a shell).

         CMD> exit


         ABORT

         Ceases  execution  of  the  current  script  file.  This might be
         necessary  if  the  script  gets  out of synch, or if there is no
         answer on the number being called from within a script.

         CMD> abort


         HELP [more]

         The  "Help" command produces a screen listing of the valid BMODEM
         commands.   The  same  listing may be seen by pressing the <Help>
         key from terminal mode.  If "help more" is entered, a list of the
         default  function  key  macros is shown, along with the rules for
         defining macros.

         CMD> help more


         PROMPT [prompt string] (command)

         Used  in  scripts to display a message on the screen.  The PROMPT
         command  might  be  used  to  explain  usage  prior  to issuing a
         command.   The prompt string will be shown on the screen, but NOT
         sent to the serial port.

         CMD> prompt "Enter the name of the program to run:^M^J" system


         DELAY (nn)

         If a pause in a script is needed, for instance to allow the modem
         time  to  dial,  or because a telephone dialing sequence requires
         it,  this  is  the  way  to introduce the pause.  The delay is in
         tenths of a second.

         CMD> delay 5














       BMODEM for the Atari ST                                 Page 8
       Reference Guide


                              -COMMANDS (Continued)-

         MKEY [modifier-](named key) (macro character string)

         Associates  a  character  string  (which  would  be a command, or
         series  of commands) with a particular named key.  The assignment
         remains  in effect for the duration of the work session, or until
         changed  with  another mkey command.  The modifiers are 's', 'c',
         and  'a',  for <Shift>, <Control>, and <Alternate>, respectively.
         If  a modifier is specified, it means that the named modifier key
         must  be held down while the named key is pressed.  More than one
         modifier  may  be  specified, separated from one another and from
         the key name by '-' (dash).

         A  complete  list  of  the  function  keys  available  for  macro
         assignment  with  the  mkey  command,  as well as all the default
         macro  bindings  can  be  obtained by typing "help more" from the
         CMD>  prompt.   In  addition,  the  Command  Summary page in this
         manual  lists  all the named keys.  Keys without a specified name
         may  be  used as named keys by using their "scan codes", preceded
         by  "$".  A key's scan code may be obtained by running the public
         domain program SHOWCHAR.TOS, which is distributed with BMODEM.

         CMD> mkey F9 "prompt \"Aborting Script\" abort"
         CMD> mkey INSERT "help more"
         CMD> mkey s-c-INSERT "prompt \"Shift-Control-Insert^M^J\""
         CMD> mkey c-$1E "prompt \"This is Control-A^M^J\""

         Note in three of the examples that the backslash ("\") is used to
         allow  quotes  for  the  prompt command within the quotes for the
         mkey  character  string.   Each  of  the  internal quotes must be
         backslashed in order for this to work.  Also note that two BMODEM
         commands are included in the character string now associated with
         <F9>.   The  second  example  binds  the default macro definition
         screen to the <Insert> key.


         STATUS

         This  command  produces  a  screen  display of the current BMODEM
         settings.    It   includes  protocols,  display  parameters,  and
         environment variables.

         CMD> status


















       BMODEM for the Atari ST                                 Page 9
       Reference Guide


                              -COMMANDS (Continued)-

         SYSTEM [progname] [program parameters]

         External  programs  can  be  run  on the computer without leaving
         BMODEM.   The  SYSTEM  command  can  be invoked without a program
         name,  in  which case the prompt "System?" will be displayed, and
         the  user  can  type  in the name of the program to be run, along
         with  any  parameters which that program might need.  The program
         name can lack the file suffix (.tos, .ttp, .prg), and BMODEM will
         look  under  all  three  common  program  suffixes.   If  only  a
         particular  suffix  is  to  be looked for, or a particular search
         order  is  desired,  the  user can specify the suffix in the SUFF
         variable,  explained  below  under "SET".  The directory in which
         the  program  resides must be specified, unless it is the current
         directory, or is specified in the PATH variable.

         CMD> system a:\bin\me.ttp test.fil
         CMD> system me test.fil


         SET [variable name] [character string]

         BMODEM  has three "environment variables" which may be controlled
         with the SET command.  They are:

           PATH     The path to search for external programs (SYSTEM)
           SUFF     The program suffix search order
           BMODEM   The path to search for BMODEM scripts

         Each  variable  accepts more than one parameter.  If program code
         is  commonly  kept  in directories other than the work directory,
         those paths may be set into the PATH variable, obviating the need
         to  specify  the  path  to search when running a program with the
         SYSTEM  command.   The  SUFF  variable  must  be  given  complete
         suffixes,  including ".".  Use of the BMODEM variable facilitates
         keeping  all script files in one place on the system, even though
         BMODEM itself might be run from another directory.  Note that the
         BMODEM.INI  file  must  be  in the directory from which BMODEM is
         invoked.   Backslash characters within paths must be escaped with
         a second backslash.

         CMD> set path "a:\\bin,b:\\"
         CMD> set suff ".ttp,.tos,.prg"
         CMD> set bmodem ".,b:\\scripts"

















       BMODEM for the Atari ST                                 Page 10
       Reference Guide


                                 -SCRIPT FILES-

       Often, upon entering BMODEM, or during a communications session, it
       is  desirable  to  execute a sequence of BMODEM commands.  The user
       might  want  to  log  onto a bulletin board automatically, or use a
       special  script  to  handle  a file transfer.  All this can be done
       with script files.

       When  executed,  BMODEM looks for the script file "BMODEM.INI".  By
       creating  a  script  file  with this name, the user can assure that
       BMODEM  will  be  configured  according to his needs.  Since BMODEM
       defaults  to  1200  baud, half-duplex, xmodem-crc operation, a user
       with  other requirements might use the BMODEM.ini file to start out
       at  2400 baud, full-duplex, ymodem protocol, and to define <F9> for
       aborting script files:

       VERIFY NOWATCH
       BAUD-RATE 2400
       FULL-DUPLEX
       YMODEM CRC
       MKEY F9 "ABORT"

       In  order to log onto a bulletin board, a user might need to have a
       more  complex  script file, using many of the BMODEM commands.  The
       script  file  needs  to  send  commands  over the modem, as well as
       respond  to  the  prompts  issued  by the bulletin board.  Here's a
       sample  file, using the Hayes modem commands to log onto a bulletin
       board,  allow  the user to work on the board, and hang up the phone
       and exit BMODEM when the session is done.  At one point this script
       issues  the  full-duplex  command  in order to avoid echoing of the
       password  on the screen - in cases where people other than the user
       have  access  to  the  machine,  it  might  not be desirable to put
       passwords in script files at all.

       TYPE "ATD 555-9999^M"
       EXPECT "Login:"
       TYPE "MyLoginName^M"
       EXPECT "Password:"
       FULL-DUPLEX
       TYPE "MyPassWord^M"
       HALF-DUPLEX
       EXPECT "Topic?"
       TYPE "MyTopic^M"
       EXPECT "Goodbye"
       TYPE "ATH^M"
       EXIT
















       BMODEM for the Atari ST                                 Page 11
       Reference Guide


                           -SCRIPT FILES (Continued)-

       This  script  is  purely  hypothetical.  By logging onto a bulletin
       board  for which you want to create a script, carefully noting each
       step  in  the  procedure, including prompts issued by the board and
       your responses, you can build a list of the actual prompts received
       and  commands  issued  to get you onto the board.  Special commands
       might  be  needed at some point to set up the proper communications
       with  the  board; for instance, to tell the board that you're using
       half-duplex,  or what baud-rate you're using (some boards determine
       baud-rate by receiving one or more ^M characters).

       When  communicating with BIX via TYMNET, some commands can be given
       at  the  TYMNET login to control full/half-duplex and flow control.
       In  order  to  set  these  up  properly,  a line like this might be
       needed:

       EXPECT "Login:"
       TYPE "^H^X^RMyLogin^M"

       ^H  tells  TYMNET to use half-duplex, ^X and ^R tell it you want to
       be  able  to  control information flow with ^S and ^Q, and, as with
       other  examples,  ^M sends the carriage return needed to signal the
       end of your input.


                                  -BMODEM.INI-

       This  special script file must, if present, reside in the directory
       from which BMODEM is invoked in order to be found.  If found, it is
       read in and acted on first thing when BMODEM is run.  This file may
       be  used to define macros, set environment variables and protocols,
       and  in  general  to configure BMODEM always to start up in the way
       most convenient for the user.  A sample follows:

       verify
       baud-rate 1200
       half-duplex
       noverify watch
       set path "a:\\bin,a:\\"
       set bmodem ".,b:\\scripts"
       set suff ".prg,.ttp,.tos"
       mkey F9 abort
       mkey INSERT "help more"


















       BMODEM for the Atari ST                                 Page 12
       Reference Guide


                            -BMODEM COMMAND SUMMARY-

           TYPE (character string)    -- To Port
           EXPECT (character string)  -- From Port
           SEND (character string)    -- Use current protocol
           RECEIVE (filename)         -- Use current Protocol
           CAPTURE (ASCII file name)  -- Open for Capture
           CLOSE                      -- Capture File
           ASEND (filename)           -- Send ASCII
           XMODEM/YMODEM              -- Transfer Protocol
           CHECKSUM/CRC               -- Error Checking
           VERIFY/NOVERIFY            -- Echo Script Cmds
           WATCH/NOWATCH              -- Modem Script Data
           FULL-DUPLEX/HALF-DUPLEX    -- Remote/Local Echo
           BAUD-RATE (rate)           -- Port Speed
           DTR/NODTR                  -- Hardware Handshake
           ESCAPE [a/s/c-](named key) -- Terminal to Command Mode
           CALL (script filename)     -- Start Script
           EXIT                       -- Leave BMODEM
           ABORT                      -- Terminate Script
           HELP [more]                -- Show Commands [Macros]
           PROMPT (character string)  -- Display on screen
           MKEY [a/s/c-](key) (macro) -- Bind Macro to Key
           SYSTEM (program) [params]  -- Run External Program (! also)
           SET (VAR name) (value)     -- Set Environmt Variable
           STATUS                     -- Show Current Settings
           DELAY (nn)                 -- Pause nn tenths of second

                          -MACRO KEY BINDINGS SUMMARY-

       These are the default macro key bindings for BMODEM:

           F1       HALF-DUPLEX
           F2       FULL-DUPLEX
           F3       SEND
           F4       RECEIVE
           F5       ASEND
           F6       CAPTURE
           F7       CLOSE
           F8       SYSTEM
           F10      EXIT
           HELP     HELP

       Named  keys  are:   F1 F2 F3 F4 F5 F6 F7 F8 F9 F10 HELP UNDO INSERT
       CLR-HOME UP DOWN LEFT RIGHT

       Any  Key  may  be used if the key's scan code is known.  Scan codes
       are  specified with $hh, where 'hh' is the hexadecimal code for the
       key.   For  example,  the  numeric  keys on the top row of the main
       keyboard  have  scan codes of 120-129, when used with  <Alternate>,
       which  translates to hexadecimal values $78-$81.  A key's scan code
       may  be  determined  by using SHOWCHAR.TOS, a public domain program
       distributed  with BMODEM.  Shift-Alt-0 is named s-a-$81.  Note that
       the  top  row  keys  from <1> to <=> are unique in having different
       scan  codes  when  used with <Alternate>. 'a-' must be used to name
       these keys with <Alt>.






       BMODEM for the Atari ST                                 Page 13
       Reference Guide


                                -VERSION HISTORY-

       VERSION 1.0
           Original port of BMODEM from UNIX
           XMODEM/YMODEM protocols for Atari ST

       VERSION 2.0
           ASEND command added
           MKEY command and Macro key bindings added
           HELP MORE for macro key bindings
           ESCAPE command added
           PROMPT command added
           BMODEM.INI initialization
           SYSTEM command added

       VERSION 2.1 : 11/16/86
           SET command added
           STATUS command added
           Environment Variables PATH, SUFF, BMODEM added
           Report on Progress added to ASEND command

       VERSION 2.3 : 11/22/86
           Pass existing environment to SYSTEM-called programs
           Ability to bind ESCAPE command to function key
           Ability to specify Shift/Control/Alt combinations

       VERSION 2.3a : 12/02/86
           8K capture buffer
           Key binding to scan code fixed
           DELAY nn (sec/10) implemented


                              -KNOWN BUGS/PROBLEMS-

           ABORT command does not work
           SUFF variable requires ".sfx" - will not supply "."


                              -UNDER CONSIDERATION-

           User-selectable buffer size for capture
           Command language implementation