------------  DOCUMENTATION FOR BOINK.PRG / BOINK.ACC  ----------

	Boink is yet another bouncing ball program with a few extra
features added in as an attempt to justify its existence. The
program works as either a program or a desk accessory just by
changing its name. In addition to bouncing a ball in a Gem window,
the Boink window displays the current time, amount of free memory
in the system, and whether or not the blitter chip (if present) is
activated. Also, the scroll bars allow you to activate or deactivate
the blitter chip or reverse the screen colors.

------------------------  Boring Stuff  -------------------------

	When boink is run (or loaded as a desk accessory) it looks for
two files, its background picture (a standard DEGAS uncompressed
picture) and the image of the rotating ball. If run on a
monochrome monitor the files it looks for are:

		boink.pi3	(degas background picture)
		boink.im3	(high res ball image)

If run on a color monitor, the files are:

		boink.pi2	(degas background picture)
		boink.im2	(medium res ball image)

The program does not do anything if run in low resolution. It looks
for its two files first in the current directory (the directory you
ran boink from, usually) and if not found there, it looks for the
files in the "\BOINK" folder.

	If you wish to use a different picture for the background
image, simply rename it to "BOINK.PI2" or "BOINK.PI3" and this
will become the default picture.

	If boink is run as a desk accessory, you can get a dialog box
by holding the left shift key down as you click on the "boink"
entry in the desk accessory menu. This will enable you to load a
different background picture.


-------------------  More Interesting Stuff  --------------------

	Boink was written in Megamax C with a few assembly routines
thrown in to keep things interesting. I have modified it to
compile with Laser C or Mark Williams, but I still use Megamax for
this one because it gives me the smallest code (due to the way it
accesses global variables, mostly...)

	The ball bounces smoothly because a double buffered animation
technique is used: The image of the rotating ball is constructed
in a background buffer, and the modified area of the background
buffer is transferred to the visible screen. The animation would
be faster if the image were only drawn to the foreground window,
but the user would observe the ball flickering, which is a nasty
effect. Paged animation is out for a program which must share its
logical screen with other programs' windows.

	Boink can be used to show the multi tasking aspect of Gem's
event handler - The ball will continue to bounce as you type in
your word processor.

	Since this program does a lot of block data transfers, it is a
good demonstration of Atari's blitter chip at work. Some of the
effect of the blitter chip is lost if the program is run as a desk
accessory, since boink is not running all the time and therefore
does not call the blitter as fast as possible. If you run boink as
a program, however, the menu has a "fast mode" which runs the
blitter at full speed and gives a true demonstration of the
blitter speedup.

	For what it is worth: Boink blits by going straight to the
line-a blit routines. If you use the AES function vro_copyfm() the
event handler may be invoked, which is not necessarily bad but
slows you down slightly. The aes call will just set up the line-a
variables anyway, and I can set them up 3 times as fast by
avoiding the AES trap call and using a custom assembly language
binding. (Once the variables are set up, however, the blits take
the same amount of time, of course).

	Other interesting speed related stuff (which is more noticable
if you have a blitter chip): If installed, GDOS kills the bouncing
speed of boink. G+Plus has no effect. (What did you expect?) The
AES keeps a keyboard buffer of about 8 characters. If that buffer
is not full, the AES checks CConis() or Bconstat() continuously to
see if the keyboard has a character that it can buffer, and this
slows down the event handler and thus boink. If you hold down a
key for a short while that key will fill the AES buffer and it
will stop looking for keypresses and boink will speed up.

	I consider the boink sound marginally acceptible, but if
someone sends me sound chip parameters for a nice thundering
	BBBBOOOOOOOOOOMMMMMMMMMM!!!!!!!
I would probably use it!

	Boink should work nicely on a large screen monitor. Thanks to
Julian F. Reschke for his large screen simulator!

	Boink is copyrighted by me (Samuel Streeper) but is freely
redistributable. So long as you keep the program or accessory
together with the 2 ball images and this document, feel free to
change the background picture and pass it around. If you include
boink with a commercial release or use it to advertise your
product it would be nice if you sent me a copy of the finished
thing...


My address:
Samuel G. Streeper
1333 Wenatchee Ave
El Cajon, CA 92021 USA


Coming Soon:

SGSnet
	A fault tolerant network for Atari ST's. Connect up to 32
Atari's together through the midi port. Uses standard coax cable.

Available: When it's done, not before.
	(I bet every software developer wants to say that!) But people
living in the real world love dates... I'm running it on this
computer right now, so end of July should be realistic. Murphy
says August. Who do you believe, me or Murphy?

SGSnet distributed by:

Paradise Computer Systems
3485 B Sacramento St.
San Luis Obispo, CA 93401 USA
(805) 544-7127