06601030301800
6L....T....T....T....T....T....T....T....T....T....T....T....T....R
€

Why-RISC?



     
     Instruction-sets-for-general-purpose-processors-are-fairly-

complex-and-powerful.-For-example,-the-68000,-a-sixteen-bit-

microprocessor-made-by-Motorola-can-multiply-or-divide-two-numbers-

with-a-single-instruction.-However,-approximately-160-clock-cycles-

are-needed-for-such-powerful-instructions.-A-RISC-processor-can-

usually-execute,-with-its-much-simpler-instruction-set,-one-

instruction-per-second.-The-RISC-processor-would-have-to-use-a-

whole-subroutine-to-accomplish-one-multiply-or-divide-instruction,-

however-as-long-as-the-subroutine-was-less-than-160-instructions-

long,-the-RISC-processor-would-out-perform-the-68000.-The-

increased-speed-obtained-by-implementing-a-simpler,-and-smaller-

instruction-set-is-the-main-reason-for-RISC.



The-History-of-RISC




     IBM-started-working-with-RISC-in-1975.-Originally-it-was-

thought-that-a-faster-controller-being-designed-for-a-telephone-

switching-system-could-be-obtained-by-reducing-the-instruction-

set.-Much-later-after-the-telephone-controller-project-had-been-

abandoned,-members-of-the-team-working-on-the-telephone-switching-

project-decided-to-use-the-controller-itself-as-a-computer.-The-

resulting-computer-developed-by-this-team-at-IBM,-had-a-very-fast-

memory,-fixed-format-instructions-and-could-execute-a-single-

instruction-in-one-clock-cycle.-This-new-computer-never-made-it-to-

the-market,-however-ideas-from-it-were-implemented-in-the-IBM-RT-

PC-workstation.

     The-IBM-RT-PC-had-a-118-instruction-micorprocessor,-an-

instruction-set-half-the-size-of-existing-CISC-machines.-Although-

the-RT-PC-wasn't-a-true-RISC-machine,-it-was-one-of-the-first-to-

use-RISC-ideas-that-was-marketed.-A-diagram-of-the-IBM-RT-PC-

processor-can-be-found-at-the-end-of-this-paper.



What-exactly-is-RISC?--




     According-to-Professor-David-Patterson-of-the-University-of-

California,-Berkeley,-one-of-the-first-to-work-on-RISC,-a-RISC-

processor-must-have-the-following-attributes;-It-must-execute-one-

instruction-each-clock-cycle.-A-RISC-processor-must-use-a-fixed-

format-for-the-instructions-in-order-to-simplify-and-therefore-

speed-up-decoding-and-also-reduce-the-amount-of-control-logic-on-

the-chip.-A-RISC-processor-must-only-use-simple-load/store-

instructions-when-dealing-with-main-memory.-This-reduces-the-speed-

killing-effects-of-too-many-main-memory-operations.-Increased-

numbers-of-registers-on-a-RISC-chip-allow-many-of-the-operations-

that-require-main-memory-accesses-with-Complex-Instruction-Set-

Computer-architecture,(CISC),-to-be-done-with-registers.-Its-

interesting-to-note-that-research-by-a-team-headed-by-Prof-

Patterson-of-U.C.-Berkeley-discovered-that-one-of-the-most-time-

consuming-operations-in-a-computer-was-the-loading-of-the-stack,-

an-operation-required-when-making-a-subroutine-call.-A-RISC-chip-

puts-its-extra-registers-to-use-by-loading-them-with-the-necessary-

numbers-required-by-the-subroutine-then-shifts-to-the-new-

registers-rather-than-pushing-everything-in-the-currently-utilized-

registers-onto-the-stack-and-popping-them-off-again-at-the-end-of-

the-subroutine.-




Processors-using-RISC-architecture




     Different-research-teams-across-the-country-and-in-Great-

Britain-are-currently-working-on-RISC-technology.-A-team-headed-by-

professor-Hennessy-of-Stanford-University--is-working-on-a-project-

whose-goal-is-maximum-speed.-They-have-produced-a-functional-32-

bit-microprocessor-chip-that-has-parts-that-work-at-17-million-

instructions-per-second,(MIPS).

     At-U.C.-Berkeley-a-team-finished-a-project-whose-goal-was-to-

implement-Smalltalk-On-A-Risc,-(SOAR).-After-succeeding-they-went-

on-to-work-on-SPUR,(symbolic-processing-using-RISC's),(see-diagram-

at-end-of-paper).-The-SPUR-project-implements-6-to-12-CMOS-

processors.-The-processors-support-Common-LISP-and-IEEE-floating-

point-processing.

     Advanced-Micro-Devices-also-has-two-families-of-VLSI-chips-

using-RISC-technology,(see-diagram-at-end-of-paper).-The-AMD-chips-

can-support-80ns-cycle-times.-The-AMD-chips-also-use-overlapping-

register-windows-to-improve-context-switching-speed,(referred-to-

previously-in-brief-discussion-of-subroutine-time-saving-by-use-of-

extra-registers).

     Acorn,-a-British-subsidiary-of-Olivetti-developed-the-Acorn-

RISC-machine,-ARM.-A-32-bit-processor-that-runs-at-4-MIPS-

originally-intended-for-Artificial-Intelligence-applications-but-

mostly-used-in-microcomputers.-A-block-diagram-of-this-processor-

can-be-found-at-the-end-of-this-paper.

     In-1984-DARPA,(Defense-Advanced-Research-Projects-Agency)-

began-funding-research-in-Gallium-Arsenide-RISC-development.-

Control-Data-Corp.-and-Texas-Instruments-have-since-designed-a-CPU-

that-should-at-close-to-200-MIPS,-(see-figure-at-end-of-paper).--