D110 PATCH EIDTOR INSTRUCTIONS

SETTING UP

1.CONNECT THE MIDI OUT PORT OF YOUR ST TO THE MIDI IN OF THE D110 AND THE MIDI
IN OF THE ST TO THE MIDI OUT OF THE D110,USING STANDARD MIDI CABLES.

2.SWITCH ON THE D110 AND CHECK THAT THE EXCLUSIVE UNIT NUMBER OF YOUR D110 IS
SET TO 17(THE DEFAULT).DO THIS BY PRESSING THE SYSTEM BUTTON ONCE AND THE
PARAMETER/GROUP " ^ " BUTTON THREE TIMES.THE D110 DISPLAY SHOULD THEN SHOW:
"Exclu Unit#=  17".IF THE NUMBER IS DIFFERENT CHANGE IT TO 17 USING THE VALUE
/NUMBER BUTTONS.ONCE THIS HAS BEEN SET THERE IS NO FURTHER NEED TO TOUCH THE
D110.

3.RUN THE PROGRAM BY DOUBLE CLICKING ON THE D110ED.PRG ICON.THE PROGRAM WILL
START BY LOADING TONE NAMES AND PATCH DATA FROM THE D110 VIA MIDI.IF YOU GET A
"D110 IS NOT RESPONDING MESSAGE" THEN CHECK THE CONNECTIONS MADE IN STEP 1.IF
YOU CHOOSE TO CONTINUE THE PROGRAM WILL LOAD DEFAULT.DTN AND DEFAULT.D11 FILES
WHICH SHOULD BE PRESENT ON THE DISC.IF THEY ARE NOT THE EDITOR WILL INDICATE
THIS AND GIVE YOU THE CHOICE TO RETRY OR TO CONTINUE.

EDITTING

ONCE THE MAIN SCREEN COMES UP PATCH NO.1 (I-11 IN ROLAND SPEAK) IS SELECTED
THE "EDITTABLE" PARAMETERS ARE HIGHLIGHTED BY MOVING THE MOUSE POINTER OVER
THEM.BY PRESSING THE RIGHT MOUSE BUTTON THE PARAMETER VALUE IS INCREASED
PRESSING THE LEFT MOUSE BUTTON DECREASES THE PARAMETER VALUE.

SELECT A PATCH TO EDIT IN THE PATCH DIRECTORY BY CLICKING ON IT.THE PARAMETERS
OF THIS PATCH ARE DISPLAYED IN THE PATCH PARAMETER AND PART PARAMETER SCREEN
AREAS AND EDITTING CAN TAKE PLACE.

IN EDITTING ONLY THE TEMPORARY PATCH MEMORY AREA OF THE D110 IS CHANGED ALTHOUGH
ALL EDITTED PATCHES ARE RETAINED IN THE EDITOR.TO UPDATE THE D110 PATCH MEMORY
CLICK ON THE SEND PATCH BOX IN THE FUNCTION AREA AND CHOOSE WHETHER TO SEND
EITHER THE SELECTED PATCH OR ALL PATCHES(64) TO THE D110 PATCH MEMORY.

THE OTHER FUNCTIONS ARE EXPLAINED IN THE DOCS FILE.

TO USE THE MIDI THRU' FUNCTION DISCONNECT THE MIDI LEAD FROM THE D110 MIDI OUT
PORT AND PLUG IT INTO A MIDI KEYBOARD MIDI OUT.CLICK THE MIDI THRU' FUNCTION BOX
WHEN IT TURNS BLACK IT IS ACTIVE AND NOTES PLAYED ON THE KEYBOARD WILL BE
TRANSMITTED TO THE D110 SO THAT YOU CAN HEAR THE EDITS AS YOU MAKE THEM.THE MIDI
THRU ONLY WORKS WHEN A PART IS INDICATED BY THE MOUSE POINTER.WHEN USING THE
MIDI THRU' NOTE THAT IT WILL NOT BE POSSIBLE TO GET DATA FROM THE D110 SINCE THE
ST MIDI IN IS NOW CONNECTED TO YOUR MIDI KEYBOARD.