TABLE OF CONTENTS

powerpc.library/AllocVec32
powerpc.library/AllocXMsg
powerpc.library/FreeVec32
powerpc.library/FreeXMsg
powerpc.library/GetCPU
powerpc.library/PowerDebugMode
powerpc.library/PutXMsg
powerpc.library/RunPPC
powerpc.library/SPrintF68K
powerpc.library/WaitForPPC

powerpc.library/AddHeadPPC
powerpc.library/AddPortPPC
powerpc.library/AddSemaphorePPC
powerpc.library/AddTailPPC
powerpc.library/AddTimePPC
powerpc.library/AllocSignalPPC
powerpc.library/AllocVecPPC
powerpc.library/AllocXMsgPPC
powerpc.library/AttemptSemaphorePPC
powerpc.library/ChangeMMU
powerpc.library/CmpTimePPC
powerpc.library/CopyMemPPC
powerpc.library/CreateMsgPortPPC
powerpc.library/CreateTaskPPC
powerpc.library/DeleteMsgPortPPC
powerpc.library/DeleteTaskPPC
powerpc.library/EnqueuePPC
powerpc.library/FindNamePPC
powerpc.library/FindPortPPC
powerpc.library/FindSemaphorePPC
powerpc.library/FindTagItemPPC
powerpc.library/FindTaskPPC
powerpc.library/FreeAllMem
powerpc.library/FreeSemaphorePPC
powerpc.library/FreeSignalPPC
powerpc.library/FreeVecPPC
powerpc.library/FreeXMsgPPC
powerpc.library/GetInfo
powerpc.library/GetMsgPPC
powerpc.library/GetSysTimePPC
powerpc.library/GetTagDataPPC
powerpc.library/InitSemaphorePPC
powerpc.library/InsertPPC
powerpc.library/LockTaskList
powerpc.library/ModifyFPExc
powerpc.library/NextTagItemPPC
powerpc.library/ObtainSemaphorePPC
powerpc.library/PutMsgPPC
powerpc.library/PutXMsgPPC
powerpc.library/ReleaseSemaphorePPC
powerpc.library/RemExcHandler
powerpc.library/RemHeadPPC
powerpc.library/RemovePPC
powerpc.library/RemPortPPC
powerpc.library/RemTailPPC
powerpc.library/RemSemaphorePPC
powerpc.library/ReplyMsgPPC
powerpc.library/Run68K
powerpc.library/SetCache
powerpc.library/SetExcHandler
powerpc.library/SetHardware
powerpc.library/SetSignalPPC
powerpc.library/SetTaskPriPPC
powerpc.library/Signal68K
powerpc.library/SignalPPC
powerpc.library/SPrintF
powerpc.library/SubTimePPC
powerpc.library/Super
powerpc.library/UnLockTaskList
powerpc.library/User
powerpc.library/WaitFor68K
powerpc.library/WaitPortPPC
powerpc.library/WaitPPC
powerpc.library/WaitTime


powerpc.library/AllocVec32                          powerpc.library/AllocVec32

    NAME
	AllocVec32 - allocates memory which is correctly aligned (V7)

    CPU
	680x0

    SYNOPSIS
	memblock = AllocVec32(memsize, attributes)
	d0                    d0       d1

	void *AllocVec32(ULONG, ULONG);

    FUNCTION
	This function allocates memory via exec/AllocVec and aligns the
	memory block properly, so that this memory block can be shared
	with PPC tasks. The minimal alignment of the memory block is 32.

    INPUTS
	memsize - size of memory to be allocated
	attributes - the desired memory attributes (see exec/AllocMem for
		     a description of these attributes)

    RESULT
	memblock - The address of the allocated memory block

    NOTES
	Memory blocks allocated with 'AllocVec32' must be freed using
	'FreeVec32'.

    SEE ALSO
	FreeVec32, exec/AllocMem


powerpc.library/AllocXMsg                            powerpc.library/AllocXMsg

    NAME
	AllocXMsg - allocates a message for Inter-CPU communication (V12)

    CPU
	680x0

    SYNOPSIS
	message = AllocXMsg(bodysize, replyport)
	d0                  d0        a0

	struct Message *AllocXMsg(ULONG, struct MsgPort *);

    FUNCTION
	This function allocates memory for a message which can be used
	for Inter-CPU communication. Some fields of the message are
	initialized.
	After this function was called, the message body must be
	created before sending this message.

    INPUTS
	bodysize - the size of the message body (max. 65535-MN_SIZE)
	replyport - the reply port

    RESULT
	message - The address of an initialized message (except for
		  the message body, which must be initialized by the
		  programmer).

    NOTES
	Calling this function is the only way allowed to create a
	message which can be sent to a PPC task.

	A message allocated with 'AllocXMsg' should be freed using
	'FreeXMsg' if it is not used anymore.

	An Inter-CPU message must be sent with 'PutXMsg' to a PPC
	task.

	A replyport should always be specified. Inter-CPU messages
	should always be replied and the reply should be read.

    SEE ALSO
	FreeXMsg, PutXMsg


powerpc.library/FreeVec32                            powerpc.library/FreeVec32

    NAME
	FreeVec32 - frees memory allocated with 'AllocVec32' (V7)

    CPU
	680x0

    SYNOPSIS
	FreeVec32(memblock)
		  a1

	void FreeVec32(void *);

    FUNCTION
	This function frees a memory block which was allocated using
	'AllocVec32'.

    INPUTS
	memblock - The address of the allocated memory block

    SEE ALSO
	AllocVec32


powerpc.library/FreeXMsg                              powerpc.library/FreeXMsg

    NAME
	FreeXMsg - frees a message allocated with 'AllocXMsg' (V12)

    CPU
	680x0

    SYNOPSIS
	FreeXMsg(message)
		 a1

	void FreeXMsg(struct Message *);

    FUNCTION
	This function frees a memory allocated using 'AllocXMsg'.

    INPUTS
	message - a message allocated by 'AllocXMsg'.

    NOTES
	An Inter-CPU message must not be freed, if it was sent to
	a PPC task and the reply has not yet arrived back.

    SEE ALSO
	AllocXMsg, PutXMsg


powerpc.library/GetCPU                                  powerpc.library/GetCPU

    NAME
	GetCPU - gets the PowerPC CPU type (V7)

    CPU
	680x0

    SYNOPSIS
	CPUType = GetCPU
	d0

	ULONG GetCPU (void);

    FUNCTION
	This function reads the PowerPC CPU type. A longword is returned with
	one specific bit set (see the include file 'powerpc/powerpc.i' for a
	description of the different CPU types)

    RESULT
	CPUType - A longword with one specific bit set.


powerpc.library/PowerDebugMode                  powerpc.library/PowerDebugMode

    NAME
	PowerDebugMode - sets the level of debugging output (V7)

    CPU
	680x0

    SYNOPSIS
	PowerDebugMode (debuglevel)
			d0

	void PowerDebugMode (ULONG);

    FUNCTION
	The powerpc.library has a built-in debugging system which prints out
	many informations to the serial port. The main purpose of this
	function is to improve the maintenance of this library. If problems
	occur with the powerpc.library then it will help the author of this
	library a lot to fix the problems. Try to reproduce the problems with
	debugging output enabled and send the debugging output to the author.
	Use a program which captures the data transferred to the serial port
	(for example Sushi) to save the debugging output.

    INPUTS
	debuglevel - Debugging level (0-3). All other values are ignored.
		     The higher the debugging level, the larger the debugging
		     output. 0 means no debugging output.

    NOTES
	The powerpc.library operates with debugging level 0 by default (no
	debugging output). You can change the default value with the
	environment variable 'powerpc/debug' (set values from 0 to 3).


powerpc.library/PutXMsg                                powerpc.library/PutXMsg

    NAME
	PutXMsg - sends an Inter-CPU message to a PPC task (V12)

    CPU
	680x0

    SYNOPSIS
	PutXMsg(MsgPortPPC, message)
		a0          a1

	void PutXMsg(struct MsgPortPPC *, struct Message *);

    FUNCTION
	This function sends an Inter-CPU message allocated by 'AllocXMsg'
	to a PPC task.

    INPUTS
	MsgPortPPC - a PPC message port
	message - a message allocated by 'AllocXMsg'.

    NOTES
	Inter-CPU messages get a different node type, if they are
	sent. If you want to filter out Reply-Messages from standard
	or Inter-CPU messages, compare the LN_TYPE field to NT_REPLYMSG.
	Replied Inter-CPU messages still get the same node type
	(NT_REPLYMSG). Any assumptions about the value of the new
	node type are ILLEGAL!!

	As soon as an Inter-CPU message is sent, the 68K looses ownership
	over the message. No access to the message is allowed until the
	reply has been arrived.

	Inter-CPU messages can be reused if they have been replied.

	Inter-CPU messages are read and replied using the standard
	message handling mechanisms (exec/WaitPort,exec/GetMsg,exec/ReplyMsg
	for 68K, powerpc/WaitPortPPC, powerpc/GetMsgPPC, powerpc/ReplyMsgPPC
	for PPC).

	The receiving task must NOT access message data, which are not
	explicitely located in the message body (for example data which is
	referenced by a pointer) unless both tasks care for the cache
	consistency. Only the message itself is flushed/invalidated
	automatically by the system.

	The receiving task may write to the message body of an Inter-CPU
	message.

	Inter-CPU messages should always be replied and the reply should
	be read and filtered out.

    SEE ALSO
	AllocXMsg, FreeXMsg


powerpc.library/RunPPC                                  powerpc.library/RunPPC

    NAME
	RunPPC - runs a PowerPC function (V7)

    CPU
	680x0

    SYNOPSIS
	status = RunPPC(PPStruct)
	d0              a0

	LONG RunPPC (struct PowerPC *);

    FUNCTION
	Runs a PowerPC function. A mirror PPC process is created. All
	registers can be transferred to PPC as well as parameters on
	stack. All cache management actions are handled automatically.

	All registers are transferred back from PPC after the PPC call
	is completed. They are stored in the PowerPC structure.

	The register assignment is as follows:

	d0      <->     r3              fp0     <->     f1
	d1      <->     r4              fp1     <->     f2
	d2      <->     r22             fp2     <->     f3
	d3      <->     r23             fp3     <->     f4
	d4      <->     r24             fp4     <->     f5
	d5      <->     r25             fp5     <->     f6
	d6      <->     r26             fp6     <->     f7
	d7      <->     r27             fp7     <->     f8
	a0      <->     r5
	a1      <->     r6
	a2      <->     r28
	a3      <->     r29
	a4      <->     r2
	a5      <->     r30
	a6      <->     r31

INPUTS
	PPStruct - Pointer to an initialized PowerPC Structure

	  PP_CODE       : Pointer to the PowerPC code
	  PP_OFFSET     : Not used by RunPPC (set to zero)
	  PP_FLAGS      : Flags which can be ore'd together
	  - PP[F/B]_ASYNC   : Call PPC function asynchronely (68K process
			      returns immediately)
	  PP_STACKPTR   : Pointer to the arguments on the stack to be
			  transferred. The pointer must point directly
			  to the first argument, not to the return address!
			  If no arguments on stack should be transferred,
			  set this to zero.
	  PP_STACKSIZE  : Size of the stack area to be transferred. If no
			  stack parameters should be transferred, set this
			  to zero.
	  PP_REGS       : Array of longwords where the registers to be
			  transferred can be stored (d0-a6)
	  PP_FREGS      : Array of quadwords (8 bytes) where the FP-registers
			  to be transferred can be stored (fp0-fp7)

    RESULT
	status - PPERR_SUCCESS if the call was successfully
		 PPERR_ASYNCERR if a synchrone PPC call was made after an
				asynchrone PPC call

    NOTES
	Calling a PPC function asynchronely is dangerous. Take care of
	possible cache conflicts. Avoid calling system functions as much
	as possible.

	If an asynchrone PPC call is done, the function WaitForPPC MUST be
	called ONCE after the call was done. No other PPC call is allowed
	for this 68K process after an asynchrone PPC call and before a call
	to WaitForPPC.

	If an asynchronely called PPC function performs a 68K call, the call
	is only performed when WaitForPPC is called by the 68K process. Note
	that the PPC mirror process is still connected to the calling 68K
	process.

	DON'T pass arguments on stack when calling a PPC function asynchronely.
	The stack is most likely to be trashed before it is copied to the PPC
	stack.

	Assembler programmers should use the macros RUNPOWERPC and
	RUNPOWERPC_XL located in the include file 'powerpc/powerpc.i'

    SEE ALSO
	WaitForPPC,powerpc/powerpc.i


powerpc.library/SPrintF68K                          powerpc.library/SPrintF68K

    NAME
	SPrintF68K - prints a formatted string to the serial port (V7)

    CPU
	680x0

    SYNOPSIS
	SPrintF68K (Formatstring, values )
		    a0            a1

	void SPrintF68K (STRPTR, APTR);

    FUNCTION
	Prints a formatted string to the serial port using the AMIGA-OS
	functions 'exec/RawPutChar' and 'exec/RawDoFmt'. Can be used to add
	debugging features and to improve the maintenance of software.

    INPUTS
	Formatstring - A C style string with % commands to indicate where
		       parameters have to be inserted (see 'exec/RawDoFmt'
		       for a detailed description of these commands).
	values - A pointer to an array of parameters to be inserted into
		 specified places in the string.

    SEE ALSO
	exec/RawDoFmt


powerpc.library/WaitForPPC                          powerpc.library/WaitForPPC

    NAME
	WaitForPPC - waits for the completion of an asynchrone PPC call (V7)

    CPU
	680x0

    SYNOPSIS
	status = WaitForPPC(PPStruct)
	d0                  a0

	LONG WaitForPPC (struct PowerPC *);

    FUNCTION
	After an asynchrone PPC call was done (see RunPPC) this function must
	be called to wait for the completion of the PowerPC function. All
	registers transferred to the PowerPC with RunPPC are returned into the
	PowerPC Structure.

    INPUTS
	PPStruct - Pointer to a PowerPC Structure (see RunPPC for a description
		   of the elements). The structure has not to be initialized.
		   The structure must be transferred to hold the returned
		   registers by the PPC function.

    RESULT
	status - PPERR_SUCCESS if the call was successfully
		 PPERR_WAITERR if WaitForPPC is called after a synchrone PPC
			       call.

    NOTES
	Assembler programmers should use the macros WAITFORPPC and
	WAITFORPPC_XL located in the include file 'powerpc/powerpc.i'

    SEE ALSO
	RunPPC,powerpc/powerpc.i


powerpc.library/AddHeadPPC                          powerpc.library/AddHeadPPC

    NAME
	AddHeadPPC - insert a node at the head of a list (V8)

    CPU
	PowerPC

    SYNOPSIS
	AddHeadPPC(_PowerPCBase, list, node)
		   r3            r4    r5

	void AddHeadPPC(struct Library *, struct List*, struct Node*);

    FUNCTION
	Insert a node to the head of a standard exec list. This is the
	mirror function of exec/AddHead.

    INPUTS
	_PowerPCBase - base of powerpc.library (can be omitted)
	list - a pointer to the target list
	node - the node to insert

    NOTES
	This function is guaranteed to work correctly, if the PowerPCBase
	is not passed in r3.

	Assembler programmers may use the macro _ADDHEAD located in
	'powerpc/listsPPC.i'

	This function is safe to call from exception handlers.

    SEE ALSO
	InsertPPC, AddTailPPC, RemovePPC, RemHeadPPC, RemTailPPC,
	EnqueuePPC, FindNamePPC, powerpc/listsPPC.i


powerpc.library/AddPortPPC                          powerpc.library/AddPortPPC

    NAME
	AddPortPPC - adds a public PPC message port to the system (V11)

    CPU
	PowerPC

    SYNOPSIS
	AddPortPPC(_PowerPCBase, MsgPortPPC)
		   r3            r4

	void AddPortPPC(struct Library *, struct MsgPortPPC *);

    FUNCTION
	This function adds a PPC message port to a public list of ports.
	The message port should be named and the priority field should
	be set. A public message port can be found by name using
	'FindPortPPC'. This is the mirror function of exec/AddPort.

    INPUTS
	_PowerPCBase - base of powerpc.library
	MsgPortPPC - pointer to a PPC message port. It's safe to pass a
		     NULL parameter.

    SEE ALSO
	CreateMsgPortPPC,DeleteMsgPortPPC,FindPortPPC,RemPortPPC
	powerpc/portsPPC.i


powerpc.library/AddSemaphorePPC                powerpc.library/AddSemaphorePPC

    NAME
	AddSemaphorePPC - initializes a global signal semaphore (V8)

    CPU
	PowerPC

    SYNOPSIS
	status = AddSemaphorePPC(_PowerPCBase, SignalSemaphorePPC)
	r3                        r3            r4

	LONG AddSemaphorePPC(struct Library *, struct SignalSemaphorePPC *);

    FUNCTION
	Initializes a signal semaphore and adds it to the public semaphore
	list. This is the mirror function of exec/AddSemaphore.

    INPUTS
	_PowerPCBase - base of powerpc.library
	SignalSemaphorePPC - pointer to a signalsemaphorePPC structure
			     (a semaphore name should be specified)

    RESULT
	status - status value:
	    SSPPC_SUCCESS: function was successful
	    SSPPC_NOMEM: function failed due to lack of memory

    SEE ALSO
	InitSemaphorePPC, FreeSemaphorePPC, ObtainSemaphorePPC,
	AttemptSemaphorePPC, ReleaseSemaphorePPC, RemSemaphorePPC,
	FindSemaphorePPC, powerpc/semaphoresPPC.i


powerpc.library/AddTailPPC                          powerpc.library/AddTailPPC

    NAME
	AddTailPPC - insert a node at the tail of a list (V8)

    CPU
	PowerPC

    SYNOPSIS
	AddTailPPC(_PowerPCBase, list, node)
		   r3            r4    r5

	void AddTailPPC(struct Library *, struct List*, struct Node*);

    FUNCTION
	Insert a node to the tail of a standard exec list. This is the
	mirror function of exec/AddTail.

    INPUTS
	_PowerPCBase - base of powerpc.library (can be omitted)
	list - a pointer to the target list
	node - the node to insert

    NOTES
	This function is guaranteed to work correctly, if the PowerPCBase
	is not passed in r3.

	Assembler programmers may use the macro _ADDTAIL located in
	'powerpc/listsPPC.i'

	This function is safe to call from exception handlers.

    SEE ALSO
	InsertPPC, AddHeadPPC, RemovePPC, RemHeadPPC, RemTailPPC,
	EnqueuePPC, FindNamePPC, powerpc/listsPPC.i


powerpc.library/AddTimePPC                          powerpc.library/AddTimePPC

    NAME
	AddTimePPC - adds one time request to another (V7)

    CPU
	PowerPC

    SYNOPSIS
	AddTimePPC(_PowerPCBase, Dest, Source)
		   r3            r4    r5

	void AddTimePPC(struct Library *, struct timeval *, struct timeval *);

    FUNCTION
	This routine adds one timeval structure to another. The results are
	stored in the destination (Dest + Source -> Dest)

	This is the mirror function of timer/AddTime.

    INPUTS
	_PowerPCBase - base of powerpc.library
	Dest - pointer to a timeval structure
	Source - pointer to a timeval structure

    NOTES
	This function is safe to call from exception handlers

    SEE ALSO
	GetSysTimePPC, SubTimePPC, CmpTimePPC


powerpc.library/AllocSignalPPC                  powerpc.library/AllocSignalPPC

    NAME
	AllocSignalPPC - allocate a signal (V8)

    CPU
	PowerPC

    SYNOPSIS
	signalnum = AllocSignalPPC(_PowerPCBase, signalNum)
	r3                         r3            r4

	LONG AllocSignalPPC(struct Library *, LONG);

    FUNCTION
	Allocate a signal bit from the current task's pool. Either a
	particular bit or the next free bit may be allocated. This
	is the mirror function of exec/AllocSignal.

    INPUTS
	_PowerPCBase - base of powerpc.library
	signalNum - the desired signal bit number (0..31) or -1
		    if the next free bit should be allocated

    RESULT
	signalnum - the signal bit allocated or -1 for failure.

    NOTES
	IMPORTANT: The signal bit numbers are returned in the
	68K notation! For example, if the number 27 is returned,
	the waiting mask must be $08000000.

	All signal allocations are kept coherent on both CPU's.
	A signal allocated on the 68K side is not free anymore
	for the mirror PPC task and vice versa. The PPC also
	can wait for signals or send signals allocated on the
	68K side and vice versa (V11).

    SEE ALSO
	FreeSignalPPC, SetSignalPPC, SignalPPC, WaitPPC


powerpc.library/AllocVecPPC                        powerpc.library/AllocVecPPC

    NAME
	AllocVecPPC - allocates memory for PPC with MMU support (V7)

    CPU
	PowerPC

    SYNOPSIS
	memblock = AllocVecPPC(_PowerPCBase, memsize, attributes, alignment)
	r3                     r3            r4       r5          r6

	void *AllocVecPPC(struct Library *, ULONG, ULONG, ULONG);

    FUNCTION
	This function allocates memory which is correctly aligned for the use
	by PowerPC applications. It's the mirror function of exec/AllocVec
	but offers some additional features.
	AllocVecPPC supports user defined alignment and allocation of memory-
	blocks with a desired cache mode (MMU support only for V9+)
	Since V12, it's possible to allocate memory, which is protected
	against other tasks (either full- or write-protected).

    INPUTS
	_PowerPCBase - base of powerpc.library
	memsize - the amount of memory to be allocated.
	attributes - the requirements as explained in exec/AllocMem
		     This function offers some additional attributes:

	    MEMF_WRITETHROUGH: maps the allocated memory as writethrough
	    MEMF_COPYBACK:     maps the allocated memory as copyback
	    MEMF_CACHEON:      maps the allocated memory as cachable
	    MEMF_CACHEOFF:     maps the allocated memory as noncachable
	    MEMF_GUARDED:      maps the allocated memory as guarded
	    MEMF_NOTGUARDED:   maps the allocated memory as not guarded
	    MEMF_BAT:          puts the allocated memory block into a
			       BAT register
	    MEMF_PROTECT:      the memory block should be full-protected
			       against other tasks (no user-accesses of
			       other tasks allowed).
	    MEMF_WRITEPROTECT: the memory block should be write-protected
			       against other tasks (no user-write-acesses
			       of other tasks allowed).

	alignment - the desired alignment of the memory block. The system
		    may round this value up to a minimal alignment. It's
		    safe to pass 0 as alignment.

    RESULT
	memblock - The address of the allocated memory. If the
		   memory couldn't be allocated 0 is returned.

    NOTES
	The amount of memory effectively allocated is usually bigger
	than the given memsize. It's not a good idea to call this
	function many times to allocate very small pieces of memory.

	If some of the additional memflags are specified, the alignment
	and the size is internally rounded up to meet the requirements
	of the MMU.

	The additional MMU memflags are intended for highly optimizing
	code and shoud not be used by standard applications.

	The memflag MEMF_BAT can improve the performance of the memory
	accesses heavily (especially on CPU's with software tablesearch).
	But DON'T use this flag unless you really need the speed. Note:
	The required free memory has to be much bigger than the size of
	the memory to be allocated, because there are severe alignment
	restrictions when using BAT registers.

	The memflag MEMF_BAT has no effect if the task runs with BAT MMU
	Setup.

	Note that no other tasks should access memory which was allocated
	using special MMU memflags, because the other task can probably
	run under a different MMU setup which can cause cache problems,
	if the other one writes to the same memory in copyback mode
	while this task accesses the data in noncachable mode, for
	example.

	The MMU support ist not implemented in powerpc.library <= V9.
	The memory protection support ist not implemented in
	powerpc.library <= V11.

    SEE ALSO
	FreeVecPPC, FreeAllMem, powerpc/memoryPPC.i


powerpc.library/AllocXMsgPPC                      powerpc.library/AllocXMsgPPC

    NAME
	AllocXMsgPPC - allocates a message for Inter-CPU communication (V12)

    CPU
	PowerPC

    SYNOPSIS
	message = AllocXMsgPPC(_PowerPCBase, bodysize, replyport)
	r3                     r3            r4        r5

	struct Message *AllocXMsgPPC(struct Library *, ULONG, struct MsgPort *);

    FUNCTION
	This function allocates memory for a message which can be used
	for Inter-CPU communication. Some fields of the message are
	initialized.
	After this function was called, the message body must be
	created before sending this message.

    INPUTS
	_PowerPCBase - base of powerpc.library
	bodysize - the size of the message body (max. 65535-MN_SIZE)
	replyport - the reply port

    RESULT
	message - The address of an initialized message (except for
		  the message body, which must be initialized by the
		  programmer).

    NOTES
	Calling this function is the only way allowed to create a
	message which can be sent to a 68K task.

	A message allocated with 'AllocXMsgPPC' should be freed using
	'FreeXMsgPPC' if it is not used anymore.

	An Inter-CPU message must be sent with 'PutXMsgPPC' to a 68K
	task.

	A replyport should always be specified. Inter-CPU messages
	should always be replied and the reply should be read.

    SEE ALSO
	FreeXMsgPPC, PutXMsgPPC


powerpc.library/AttemptSemaphorePPC        powerpc.library/AttemptSemaphorePPC

    NAME
	AttemptSemaphorePPC - try to obtain without blocking (V8)

    CPU
	PowerPC

    SYNOPSIS
	status = AttemptSemaphorePPC(_PowerPCBase, SignalSemaphorePPC)
				     r3            r4

	LONG AttemptSemaphorePPC(struct Library *,
				  struct SignalSemaphorePPC *);

    FUNCTION
	Tries to get exclusive access to a signal semaphore. If the semaphore
	is locked by another task, this function returns with an appropriate
	status value. This is the mirror function of exec/AttemptSemaphore

    INPUTS
	_PowerPCBase - base of powerpc.library
	SignalSemaphorePPC - pointer to a signalsemaphorePPC structure

    RESULT
	status - status value:
	    ATTEMPT_SUCCESS: operation successful
	    ATTEMPT_FAILURE: semaphore couldn't be locked

    NOTES
	This call is guaranteed to preserve all GPR (except r0 and r3)
	and the CTR.

    SEE ALSO
	InitSemaphorePPC, FreeSemaphorePPC, ObtainSemaphorePPC,
	ReleaseSemaphorePPC, AddSemaphorePPC, RemSemaphorePPC
	FindSemaphorePPC, powerpc/semaphoresPPC.i


powerpc.library/ChangeMMU                            powerpc.library/ChangeMMU

    NAME
	ChangeMMU - changes the MMU setup of the current task (V10)

    CPU
	PowerPC

    SYNOPSIS
	ChangeMMU(_PowerPCBase, MMUMode)
		  r3            r4

	void ChangeMMU(struct Library *, ULONG);

    FUNCTION
	Changes the MMU setup of the currently running task. A task is able
	to run with two different MMU setups:

	- paged MMU setup: The standard method, where almost every memory
	  access is controlled by the page table
	- BAT MMU setup: Almost all the memory is controlled by the 4 BAT
	  registers.

    INPUTS
	_PowerPCBase - base of powerpc.library
	MMUMode - CHMMU_STANDARD: change MMU setup to standard
		  CHMMU_BAT     : change MMU setup to BAT setup

    NOTES
	This function should usually NOT be called. It is intended for
	highly optimizing code and should only be used, if enough MMU
	knowledge is present.

	The state of the current task can be changed from the shell by
	using the tool 'changemmu' (and this is the better way how to
	change the setup rather than calling the library function)

    SEE ALSO
	powerpc/tasksppc.i


powerpc.library/CmpTimePPC                          powerpc.library/CmpTimePPC

    NAME
	CmpTimePPC - compares two timeval structures (V7)

    CPU
	PowerPC

    SYNOPSIS
	result = CmpTimePPC(_PowerPCBase, Dest, Source)
	r3                  r3            r4    r5

	LONG CmpTimePPC(struct Library *, struct timeval *, struct timeval *);

    FUNCTION
	This routine compares two timeval structures.

	This is the mirror function of timer/CmpTime.

    INPUTS
	_PowerPCBase - base of powerpc.library
	Dest - pointer to a timeval structure
	Source - pointer to a timeval structure

    RESULT
	0  - if both timeval structures are equal
	-1 - if Dest is greater than Source
	1  - if Dest is less than Source


    NOTES
	This function is safe to call from exception handlers

    SEE ALSO
	GetSysTimePPC, AddTimePPC, SubTimePPC


powerpc.library/CopyMemPPC                          powerpc.library/CopyMemPPC

    NAME
	CopyMemPPC - copies memory the fastest way possible (V12)

    CPU
	PowerPC

    SYNOPSIS
	CopyMemPPC(_PowerPCBase, source, dest, size)
		   r3            r4      r5    r6

	void CopyMemPPC(struct Library *, void *, void *, ULONG);

    FUNCTION
	This function copies a source memory area to a destination memory
	area. No overlapping is supported. CopyMemPPC tries to copy with
	the highest bandwidth possible.

    INPUTS
	_PowerPCBase - base of powerpc.library
	source - address of the source memory area
	dest - address of the destination memory area
	size - size of the memory area to be copied

    NOTES
	The highest performance can be achieved if both memory areas have
	a minimal alignment of 8.


powerpc.library/CreateMsgPortPPC              powerpc.library/CreateMsgPortPPC

    NAME
	CreateMsgPortPPC - creates a new PPC message port (V11)

    CPU
	PowerPC

    SYNOPSIS
	MsgPortPPC = CreateMsgPortPPC(_PowerPCBase)
	r3                            r3

	struct MsgPortPPC *CreateMsgPortPPC(struct Library *);

    FUNCTION
	This function creates a new PowerPC message port. This is the only
	way allowed to create a PPC message port. It is the mirror function
	of exec/CreateMsgPort.

    INPUTS
	_PowerPCBase - base of powerpc.library

    RESULT
	MsgPortPPC - pointer to a MsgPortPPC structure or NULL for failure

    NOTES
	A PowerPC message port should be deleted using 'DeleteMsgPortPPC'
	if it is not used anymore.

	It's forbidden to access PPC message ports by the standard
	exec message handling routines.

    SEE ALSO
	DeleteMsgPortPPC,FindPortPPC,AddPortPPC,RemPortPPC
	powerpc/portsPPC.i


powerpc.library/CreateTaskPPC                    powerpc.library/CreateTaskPPC

    NAME
	CreateTaskPPC - creates a new PPC task (V8)

    CPU
	PowerPC

    SYNOPSIS
	TaskPPC = CreateTaskPPC(_PowerPCBase, TagItems)
	r3                      r3            r4

	struct TaskPPC *CreateTaskPPC(struct Library *, struct TagItem *);

    FUNCTION
	This function creates a new PPC task under control of the tags passed.
	All memory (inclusive stack) is allocated automatically.

	PPC tasks are similar to exec tasks (the first element of the TaskPPC
	structure is an exec task structure). The scheduling of these tasks
	works similar to exec, so a running task blocks all tasks with lower
	priority.

    INPUTS
	_PowerPCBase - base of powerpc.library
	TagItems - pointer to a tagitem array. The following tags are
		   supported:

	    TASKATTR_CODE:      pointer to the entry point of the new task
				(MUST be specified)
	    TASKATTR_EXITCODE:  pointer to the exit routine of the new task
	    TASKATTR_NAME:      task name (MUST be specified)
	    TASKATTR_PRI:       task priority (-128 ... 127). Default = 0.
	    TASKATTR_STACKSIZE: the desired stack size. If this tag is omitted
				the default stack size will be 16K.
	    TASKATTR_R2:        smalldata base of the PPC program
	    TASKATTR_R3:
	    ...
	    TASKATTR_R10:       parameters to be passed to the new task
				in the specified registers
	    TASKATTR_MOTHERPRI: the priority is taken from the currently
				running task (TASKATTR_PRI is ignored) (V9)
	    TASKATTR_BAT:       lets the task run under BAT MMU setup by
				default (V10)

    RESULT
	TaskPPC - pointer to a TaskPPC structure or NULL for failure

    NOTES
	If a 68K application only wants to call a PPC function, it's
	better to use Run68K instead of creating a new PPC task.

	While a PPC task created by Run68K is always connected to
	the calling 68K process, a task created by CreateTaskPPC is
	completely independent. If such a task peforms 68K calls, a
	new mirror process on the 68K side is created.

	If an alternative exit code is specified (TASKATTR_EXITCODE)
	the value passed in TASKATTR_R2 remains intact in this exit
	code.

    SEE ALSO
	DeleteTaskPPC,FindTaskPPC,powerpc/tasksPPC.i


powerpc.library/DeleteMsgPortPPC              powerpc.library/DeleteMsgPortPPC

    NAME
	DeleteMsgPortPPC - deletes a PPC message port (V11)

    CPU
	PowerPC

    SYNOPSIS
	DeleteMsgPortPPC(_PowerPCBase, MsgPortPPC)
			 r3            r4

	void DeleteMsgPortPPC(struct Library *, struct MsgPortPPC *);

    FUNCTION
	This function deletes a PowerPC message port created using
	'CreateMsgPortPPC'. It is the mirror function of exec/DeleteMsgPort.

    INPUTS
	_PowerPCBase - base of powerpc.library
	MsgPortPPC - Pointer to the message port to delete. It's safe to
		     pass NULL as parameter

    NOTES
	Calling 'DeleteMsgPortPPC' is the ONLY way allowed to delete a PPC
	message port.

    SEE ALSO
	CreateMsgPortPPC,FindPortPPC,AddPortPPC,RemPortPPC
	powerpc/portsPPC.i


powerpc.library/DeleteTaskPPC                    powerpc.library/DeleteTaskPPC

    NAME
	DeleteTaskPPC - deletes a PPC task (V8)

    CPU
	PowerPC

    SYNOPSIS
	DeleteTaskPPC(_PowerPCBase, PPCTask)
		      r3            r4

	void DeleteTaskPPC(struct Library *, struct TaskPPC *);

    FUNCTION
	Deletes a PPC task created by CreateTaskPPC.

    INPUTS
	_PowerPCBase - base of powerpc.library
	TaskPPC - PPC task to remove or NULL for self removal

    NOTES
	It's not encouraged to delete other tasks. This function
	should only be called with a NULL parameter to remove the
	calling task itself.

	The system may also remove an existing 68K mirror process
	connected to the calling PPC task.

    SEE ALSO
	CreateTaskPPC,FindTaskPPC,powerpc/tasksPPC.i


powerpc.library/EnqueuePPC                          powerpc.library/EnqueuePPC

    NAME
	EnqueuePPC - inserts a node into a list sorted by priority (V8)

    CPU
	PowerPC

    SYNOPSIS
	EnqueuePPC(_PowerPCBase, list, node)
		   r3            r4    r5

	void EnqueuePPC(struct Library *, struct List*, struct Node*);

    FUNCTION
	Inserts a node to a standard exec list based on the node priority.
	In this way a list can be kept sorted by priority all the time.
	New nodes will be inserted in front of the first node with a
	lower priority. This is the mirror function of exec/Enqueue.

    INPUTS
	_PowerPCBase - base of powerpc.library (can be omitted)
	list - a pointer to the target list
	node - the node to enqueue

    NOTES
	This function is guaranteed to work correctly, if the PowerPCBase
	is not passed in r3.

	This function is safe to call from exception handlers.

    SEE ALSO
	InsertPPC, AddTailPPC, AddHeadPPC, RemovePPC, RemHeadPPC,
	RemTailPPC, FindNamePPC, powerpc/listsPPC.i


powerpc.library/FindNamePPC                        powerpc.library/FindNamePPC

    NAME
	FindNamePPC - finds a node with given name (V8)

    CPU
	PowerPC

    SYNOPSIS
	node = FindNamePPC(_PowerPCBase, start, name)
	r3                 r3            r4     r5

	struct Node *FindNamePPC(struct Library *, struct List*, STRPTR);

    FUNCTION
	Searches a list for a node with the given name. If multiple nodes
	with same names should be found, this function can be called with
	a node starting point.

    INPUTS
	_PowerPCBase - base of powerpc.library
	list - a list header or a node to start the searche (if node,
	       this one is skipped)
	name - the name of the node

    NOTES
	This function is guaranteed to work correctly, if the PowerPCBase
	is not passed in r3.

	This function is safe to call from exception handlers.

    SEE ALSO
	InsertPPC, AddTailPPC, AddHeadPPC, RemovePPC, RemHeadPPC,
	RemTailPPC, EnqueuePPC, powerpc/listsPPC.i


powerpc.library/FindPortPPC                        powerpc.library/FindPortPPC

    NAME
	FindPortPPC - finds a public PPC message port by name (V11)

    CPU
	PowerPC

    SYNOPSIS
	MsgPortPPC = FindPortPPC(_PowerPCBase, name)
	r3                       r3            r4

	struct MsgPortPPC* FindPortPPC(struct Library *, STRPTR);

    FUNCTION
	This function will search the global list of PPC message ports
	for a port with the given name. No arbritation is needed. This
	is the mirror function of exec/FindPort.

    INPUTS
	_PowerPCBase - base of powerpc.library
	name - name of the PPC message port to search

    RESULT
	MsgPortPPC - pointer to a PPC message port or NULL if it was not
		     found.

    SEE ALSO
	CreateMsgPortPPC,DeleteMsgPortPPC,AddPortPPC,RemPortPPC
	powerpc/portsPPC.i


powerpc.library/FindSemaphorePPC              powerpc.library/FindSemaphorePPC

    NAME
	FindSemaphorePPC - finds a public semaphore (V8)

    CPU
	PowerPC

    SYNOPSIS
	SignalsemaphorePPC = FindSemaphorePPC(_PowerPCBase, SemaphoreName)
	r3                                    r3            r4

	struct signalsemaphorePPC *FindSemaphorePPC(struct Library *, STRPTR);

    FUNCTION
	Finds a public semaphore added to the system semaphore list by
	AddSemaphore. This is the mirror function to exec/FindSemaphore.

    INPUTS
	_PowerPCBase - base of powerpc.library
	SemaphoreName - name of the semaphore to find

    RESULT
	SignalsemaphorePPC - signal semaphore requested or 0 if it was not
			     found

    SEE ALSO
	InitSemaphorePPC, FreeSemaphorePPC, ObtainSemaphorePPC,
	AttemptSemaphorePPC, ReleaseSemaphorePPC, AddSemaphorePPC,
	RemSemaphorePPC, powerpc/semaphoresPPC.i


powerpc.library/FindTagItemPPC                  powerpc.library/FindTagItemPPC

    NAME
	FindTagItemPPC - scan a tag list for a specific tag (V8)

    CPU
	PowerPC

    SYNOPSIS
	tag = FindTagItemPPC(_PowerPCBase, tagValue, tagList)
	r3                   r3            r4        r5

	struct TagItem *FindTagItemPPC(struct Library *, ULONG,
				       struct TagItem *);

    FUNCTION
	Scans a tag list and returns a pointer to the first item with
	ti_Tag matching the 'tagValue' parameter. This is the mirror
	function of utility/FindTagItem.

    INPUTS
	_PowerPCBase - base of powerpc.library
	tagValue - tag value to search for
	tagList - tag item list to search (may be NULL)

    RESULT
	tag - a pointer to the item with ti_Tag matching 'tagValue'
	      or NULL if no match was found.

    NOTES
	This function is safe to call from exception handlers.

    SEE ALSO
	GetTagDataPPC, NextTagItemPPC, utility/tagitem.i


powerpc.library/FindTaskPPC                    powerpc.library/FindTaskPPC

    NAME
	FindTaskPPC - finds a task by name (or find oneself) (V8)

    CPU
	PowerPC

    SYNOPSIS
	TaskPPC = FindTaskPPC(_PowerPCBase, Name)
	r3                    r3            r4

	struct TaskPPC *FindTaskPPC(struct Library *, STRPTR);

    FUNCTION
	Tries to find a task with the given name (or the current task if
	NULL is specified). This is the mirror function of exec/FindTask.

    INPUTS
	_PowerPCBase - base of powerpc.library
	Name - name of the task to find or NULL for the current task

    RESULT
	TaskPPC - pointer to the TaskPPC structure or NULL if the task
		  was not found

    NOTES
	Be cautious that a task may be removed at any time, so the
	pointer returned may not be valid anymore when used.

	It's allowed to call FindTaskPPC with a NULL parameter from
	an exception handler. In this case the interrupted task is
	returned.

    SEE ALSO
	CreateTaskPPC,DeleteTaskPPC,powerpc/tasksPPC.i


powerpc.library/FreeAllMem                          powerpc.library/FreeAllMem

    NAME
	FreeAllMem - frees all memory allocated by the calling task (V11)

    CPU
	PowerPC

    SYNOPSIS
	FreeAllMem(_PowerPCBase)
		   r3

	void FreeVecPPC(struct Library *);

    FUNCTION
	Frees all memory which was allocated by the calling task. This is an
	easy way to free the memory rather than calling FreeVecPPC for every
	allocation made.

    INPUTS
	_PowerPCBase - base of powerpc.library

    SEE ALSO
	AllocVecPPC,FreeVecPPC,powerpc/memoryPPC.i


powerpc.library/FreeSemaphorePPC              powerpc.library/FreeSemaphorePPC

    NAME
	FreeSemaphorePPC - frees a signal semaphore (V8)

    CPU
	PowerPC

    SYNOPSIS
	FreeSemaphorePPC(_PowerPCBase, SignalSemaphorePPC)
			 r3            r4

	void FreeSemaphorePPC(struct Library *, struct SignalSemaphorePPC *);

    FUNCTION
	Frees a signal semaphore initialized by InitSemaphorePPC. There
	is no similar function in exec.library!

    INPUTS
	_PowerPCBase - base of powerpc.library
	SignalSemaphorePPC - pointer to a signalsemaphorePPC structure

    SEE ALSO
	InitSemaphorePPC, ObtainSemaphorePPC, AttemptSemaphorePPC,
	ReleaseSemaphorePPC, AddSemaphorePPC, RemSemaphorePPC,
	FindSemaphorePPC, powerpc/semaphoresPPC.i


powerpc.library/FreeSignalPPC                    powerpc.library/FreeSignalPPC

    NAME
	FreeSignalPPC - frees a signal (V8)

    CPU
	PowerPC

    SYNOPSIS
	FreeSignalPPC(_PowerPCBase, signalNum)
		      r3            r4

	void FreeSignalPPC(struct Library *, LONG);

    FUNCTION
	Frees a signal bit allocated by AllocSignalPPC. This is the
	mirror function of exec/FreeSignal.

    INPUTS
	_PowerPCBase - base of powerpc.library
	signalNum - the signal bit number to free (0..31). It's
		    safe to pass -1 as input parameter.

    SEE ALSO
	AllocSignalPPC, SetSignalPPC, SignalPPC, WaitPPC


powerpc.library/FreeVecPPC                          powerpc.library/FreeVecPPC

    NAME
	FreeVecPPC - frees memory allocated by AllocVecPPC (V7)

    CPU
	PowerPC

    SYNOPSIS
	status = FreeVecPPC(_PowerPCBase, memblock)
	r3                  r3            r4

	LONG FreeVecPPC(struct Library *, void *);

    FUNCTION
	Frees memory allocated by AllocVecPPC. This is the mirror function
	of exec/FreeVec.

    INPUTS
	_PowerPCBase - base of powerpc.library
	memblock - address of memory to be freed. It's safe to pass NULL
		   as input parameter.

    RESULT
	status - a status value:
	    MEMERR_SUCCESS - operation was successful

    SEE ALSO
	AllocVecPPC, FreeAllMem, powerpc/memoryPPC.i


powerpc.library/FreeXMsgPPC                        powerpc.library/FreeXMsgPPC

    NAME
	FreeXMsgPPC - frees a message allocated with 'AllocXMsgPPC' (V12)

    CPU
	PowerPC

    SYNOPSIS
	FreeXMsgPPC(_PowerPCBase, message)
		     r3           r4

	void FreeXMsgPPC(struct Library *, struct Message *);

    FUNCTION
	This function frees a memory allocated using 'AllocXMsgPPC'.

    INPUTS
	_PowerPCBase - base of powerpc.library
	message - a message allocated by 'AllocXMsgPPC'.

    NOTES
	An Inter-CPU message must not be freed, if it was sent to
	a 68K task and the reply has not yet arrived back.

    SEE ALSO
	AllocXMsgPPC, PutXMsgPPC


powerpc.library/GetInfo                                powerpc.library/GetInfo

    NAME
	GetInfo - evaluates many CPU related information (V10)

    CPU
	PowerPC

    SYNOPSIS
	GetInfo(_PowerPCBase, PPCInfoTagList)
		r3            r4

	void GetInfo(struct Library *, struct TagItem *);

    FUNCTION
	This function is able to evaluate many CPU related information
	such as CPU type, cache states and more. The values which should
	be evaluated are specified using the appropriate tags (defined
	in powerpc/powerpc.i) and the value is returned in the appropriate
	ti_Data field.

    INPUTS
	_PowerPCBase - base of powerpc.library
	PPCInfoTagList - pointer to a tagitem array. The following tags are
			 supported:
	    PPCINFO_CPU:        evaluates the PowerPC CPU type (see powerpc/
				powerpc.i for a description of the possible
				return values)
	    PPCINFO_PVR:        returns the PVR register which also contains
				the revision number of the CPU besides the
				CPU type.
	    PPCINFO_ICACHE:     returns the state of the instruction cache
				See powerpc/powerpc.i for a description of
				the possible values.
	    PPCINFO_DCACHE:     returns the state of the data cache. The
				values possible are the same as for PPCINFO_
				ICACHE.
	    PPCINFO_PAGETABLE:  returns the location of the standard page table
	    PPCINFO_TABLESIZE:  returns the size of the page table (in KBytes)
	    PPCINFO_BUSCLOCK:   returns the bus clock value (in Hz)
	    PPCINFO_CPUCLOCK:   returns the CPU clock value (in Hz)

    NOTES
	The CPU clock cannot be evaluated on PowerPC systems without the
	extension E (for example PPC603,PPC604) because the supervisor
	register HID1 is missing. In this case, 0 is returned.

	Usually the PPC-CPU's available for AMIGA will have this register
	(for example: PPC603E, PPC604E)

    SEE ALSO
	powerpc/powerpc.i


powerpc.library/GetMsgPPC                            powerpc.library/GetMsgPPC

    NAME
	GetMsgPPC - get next message from a message port (V11)

    CPU
	PowerPC

    SYNOPSIS
	message = GetMsgPPC(_PowerPCBase, MsgPortPPC)
	r3                  r3            r4

	struct Message *GetMsgPPC(struct Library *, struct MsgPortPPC *);

    FUNCTION
	This function receives a message from a given message port. This
	is the mirror function of exec/GetMsg.

    INPUTS
	_PowerPCBase - base of powerpc.library
	port - a pointer to a message port

    RESULTS
	message - a pointer to the first available message or NULL if none
		  is available.

    SEE ALSO
	WaitPortPPC, PutMsgPPC, ReplyMsgPPC, powerpc/portsPPC.i


powerpc.library/GetSysTimePPC                    powerpc.library/GetSysTimePPC

    NAME
	GetSysTimePPC - get the current (relative) time (V7)

    CPU
	PowerPC

    SYNOPSIS
	GetSysTimePPC(_PowerPCBase, Dest )
			    r3      r4

	void GetSysTimePPC(struct Library *, struct timeval * );

    FUNCTION
	Returns the current system time. This time is NOT absolute, there
	is no relation between the real time and the time returned by
	GetSysTimePPC. This function can be used for measurement of
	time spans.

	This is the mirror function of timer/GetSysTime.

    INPUTS
	_PowerPCBase - base of powerpc.library
	Dest - pointer to a timeval structure (where the time is stored)

    NOTES
	This function has different behaviour on powerpc.library V7 and
	powerpc.library V8+.

	V7: The time is evaluated using the timer.device (via a cross
	call) because it isn't possible to evaluate the busclock frequency
	of the PPC with V7 (and ppc.library below) until now.

	V8+: The time is evaluated completely native (and fast) using the
	internal timers and the busclock frequency evaluated by WarpOS.

	This function is safe to call from exception handlers ONLY in
	powerpc.library V8 and higher !!

    SEE ALSO
	AddTimePPC, SubTimePPC, CmpTimePPC


powerpc.library/GetTagDataPPC                    powerpc.library/GetTagDataPPC

    NAME
	GetTagDataPPC - obtain the data corresponding to a tag (V8)

    CPU
	PowerPC

    SYNOPSIS
	value = GetTagDataPPC(_PowerPCBase, tagValue, defaultVal, tagList)
	r3                    r3            r4        r5          r6

	ULONG *GetTagDataPPC(struct Library *, ULONG, ULONG, struct TagItem* );

    FUNCTION
	Searches a tag list for a matching tag and returns the corresponding
	ti_Data value for the TagItem found. If no match is found,
	this function returns the value passed in as 'defaultVal'. This
	is the mirror function of utility/GetTagData.

    INPUTS
	_PowerPCBase - base of powerpc.library
	tagValue - tag value to search for
	defaultVal - value to be returned if tagValue is not found
	tagList - tag item list to search (may be NULL)

    RESULT
	value - the ti_Data value for the first matching TagItem, or
		'defaultVal' if a ti_Tag matching Tag is not found.

    NOTES
	This function is safe to call from exception handlers.

    SEE ALSO
	FindTagItemPPC, NextTagItemPPC, utility/tagitem.i


powerpc.library/InitSemaphorePPC              powerpc.library/InitSemaphorePPC

    NAME
	InitSemaphorePPC - initializes a signal semaphore (V8)

    CPU
	PowerPC

    SYNOPSIS
	status = InitSemaphorePPC(_PowerPCBase, SignalSemaphorePPC)
	r3                        r3            r4

	LONG InitSemaphorePPC(struct Library *, struct SignalSemaphorePPC *);

    FUNCTION
	Initializes a signal semaphore. This is the mirror function of
	exec/InitSemaphore with some changes.

    INPUTS
	_PowerPCBase - base of powerpc.library
	SignalSemaphorePPC - pointer to a signalsemaphorePPC structure
			     (all fields to zero)

    RESULT
	status - status value:
	    SSPPC_SUCCESS: function was successful
	    SSPPC_NOMEM: function failed due to lack of memory

    NOTES
	In opposite to exec/InitSemaphore a signal semaphore for PPC
	has to be freed with FreeSemaphorePPC, because InitSemaphorePPC
	allocates memory which should be freed after use.

    SEE ALSO
	FreeSemaphorePPC, ObtainSemaphorePPC, AttemptSemaphorePPC,
	ReleaseSemaphorePPC, AddSemaphorePPC, RemSemaphorePPC,
	FindSemaphorePPC, powerpc/semaphoresPPC.i


powerpc.library/InsertPPC                            powerpc.library/InsertPPC

    NAME
	InsertPPC - insert a node into a list (V8)

    CPU
	PowerPC

    SYNOPSIS
	Insert(_PowerPCBase, list, node, nodepredecessor)
	       r3            r4    r5    r6

	void InsertPPC(struct Library *, struct List*, struct Node*,
		       struct Node*);

    FUNCTION
	Insert a node into an standard exec list. This is the mirror
	function of exec/Insert.

    INPUTS
	_PowerPCBase - base of powerpc.library (can be omitted)
	list - a pointer to the target list
	node - the node to insert
	nodepredecessor - the node after which to insert. If 0 is passed,
			  the node is inserted at the head of the list.

    NOTES
	This function is guaranteed to work correctly, if the PowerPCBase
	is not passed in r3.

	This function is safe to call from exception handlers.

    SEE ALSO
	AddHeadPPC, AddTailPPC, RemovePPC, RemHeadPPC, RemTailPPC,
	EnqueuePPC, FindNamePPC, powerpc/listsPPC.i


powerpc.library/LockTaskList                      powerpc.library/LockTaskList

    NAME
	LockTaskList - locks a list of all tasks (V10)

    CPU
	PowerPC

    SYNOPSIS
	TaskPtr = LockTaskList(_PowerPCBase)
	r3                     r3

	struct TaskPtr* LockTaskList(struct Library *);

    FUNCTION
	This function locks a list of all PPC tasks currently available.
	The main purpose of this function is to allow examining the
	PPCtask structures without to worry about protecting the access
	by semaphores (this is done internally).

	The usual method of accessing the task information is the
	following:

	- Lock the task list using 'LockTaskList'
	- Get the pointer to the first task (by reading out the entry
	  TASKPTR_TASK of the returned TaskPtr structure)
	- Scan trough the list and read out all infomation you need until
	  you find the end of the list
	- Unlock the list using 'UnLockTaskList'

    INPUTS
	_PowerPCBase - base of powerpc.library

    RESULTS
	TaskPtr - Ptr to the first node of a list of TaskPtr structures
		  (see powerpc/tasksppc.i)

    NOTES
	The WarpOS multitasking is NOT halted between LockTaskList and
	UnLockTaskList.

	No new tasks are created and no resources of removed tasks are
	freed between LockTaskList and UnLockTaskList. So don't lock the
	list for a too long time.

    SEE ALSO
	UnLockTaskList, powerpc/tasksppc.i


powerpc.library/ModifyFPExc                        powerpc.library/ModifyFPExc

    NAME
	ModifyFPExc - enables/disables specific floating point exceptions (V9)

    CPU
	PowerPC

    SYNOPSIS
	ModifyFPExc(_PowerPCBase, FPflags)
		    r3            r4

	void ModifyFPExc(struct Library *, ULONG);

    FUNCTION
	This function allows to enable/disable particular floating
	point exceptions. Multiple exceptions can be affected
	simultaneously.

    INPUTS
	_PowerPCBase - base of powerpc.library
	FPflags - action to be performed:
	    FPF_EN_OVERFLOW:    Enables FP overflow exception
	    FPF_EN_UNDERFLOW:   Enables FP underflow exception
	    FPF_EN_ZERODIVIDE:  Enables FP zero divide exception
	    FPF_EN_INEXACT:     Enables FP inexact operation exception
	    FPF_EN_INVALID:     Enables FP invalid operation exception
	    FPF_DIS_OVERFLOW:   Disables FP overflow exception
	    FPF_DIS_UNDERFLOW:  Disables FP underflow exception
	    FPF_DIS_ZERODIVIDE: Disables FP zero divide exception
	    FPF_DIS_INEXACT:    Disables FP inexact operation exception
	    FPF_DIS_INVALID:    Disables FP invalid operation exception

    NOTES
	Floating point exceptions must be enabled globally using 'SetHardware'
	otherwise this function doesn't have any effect.

    SEE ALSO
	SetHardware, powerpc/powerpc.i


powerpc.library/NextTagItemPPC                  powerpc.library/NextTagItemPPC

    NAME
	NextTagItemPPC - iterate through a tag list (V8)

    CPU
	PowerPC

    SYNOPSIS
	tag = NextTagItemPPC(_PowerPCBase, tagItemPtr)
	r3                   r3            r4

	struct TagItem *NextTagItemPPC(struct Library *, struct TagItem **);

    FUNCTION
	Iterates through a tag list, skipping and chaining as dictated by
	system tags. Each call returns either the next item to be examined
	or NULL when the end of the list has benn reached. This is the
	mirror function of utility/NextTagItem.

    INPUTS
	_PowerPCBase - base of powerpc.library
	tagItemPtr - double-indirect reference to a TagItem structure.
		     The pointer will be changed to keep track of the
		     iteration.

    RESULT
	tag - each TagItem in the array that should be processed is
	      returned in turn with succesive calls.

    NOTES
	This function is safe to call from exception handlers.

    SEE ALSO
	FindTagItemPPC, GetTagDataPPC, utility/tagitem.i


powerpc.library/ObtainSemaphorePPC          powerpc.library/ObtainSemaphorePPC

    NAME
	ObtainSemaphorePPC - gain exclusive access to a semaphore (V8)

    CPU
	PowerPC

    SYNOPSIS
	ObtainSemaphorePPC(_PowerPCBase, SignalSemaphorePPC)
			   r3            r4

	void ObtainSemaphorePPC(struct Library *, struct SignalSemaphorePPC *);

    FUNCTION
	Tries to get exclusive access to a signal semaphore. If the semaphore
	is occupied, the task adds itself into a waiting queue. This is the
	mirror function of exec/ObtainSemaphore.

    INPUTS
	_PowerPCBase - base of powerpc.library
	SignalSemaphorePPC - pointer to a signalsemaphorePPC structure

    NOTES
	This call is guaranteed to preserve all GPR (except r0) and the CTR.

    SEE ALSO
	InitSemaphorePPC, FreeSemaphorePPC, AttemptSemaphorePPC,
	ReleaseSemaphorePPC, AddSemaphorePPC, RemSemaphorePPC
	FindSemaphorePPC, powerpc/semaphoresPPC.i


powerpc.library/PutMsgPPC                            powerpc.library/PutMsgPPC

    NAME
	PutMsgPPC - put a message to a message port (V11)

    CPU
	PowerPC

    SYNOPSIS
	PutMsgPPC(_PowerPCBase, MsgPortPPC, message)
		  r3            r4          r5

	void PutMsgPPC(struct Library *, struct MsgPortPPC *, struct Messge *);

    FUNCTION
	This function attaces a message to the end of the given port. In
	opposition to exec/PutMsg, only ports with PA_SIGNAL are supported.
	This is the mirror function of exec/PutMsg.

    INPUTS
	_PowerPCBase - base of powerpc.library
	port - a pointer to a message port
	message - a pointer to the message to be sent

    NOTES
	This function is safe to call from exception handlers.

    SEE ALSO
	WaitPortPPC, GetMsgPPC, ReplyMsgPPC, powerpc/portsPPC.i


powerpc.library/PutXMsgPPC                          powerpc.library/PutXMsgPPC

    NAME
	PutXMsgPPC - sends an Inter-CPU message to a 68K task (V12)

    CPU
	PowerPC

    SYNOPSIS
	PutXMsgPPC(_PowerPCBase, MsgPort, message)
		   r3            r4       r5

	void PutXMsgPPC(struct Library *, struct MsgPort *, struct Message *);

    FUNCTION
	This function sends an Inter-CPU message allocated by 'AllocXMsgPPC'
	to a 68K task.

    INPUTS
	_PowerPCBase - base of powerpc.library
	MsgPort - an exec message port
	message - a message allocated by 'AllocXMsgPPC'.

    NOTES
	Inter-CPU messages get a different node type, if they are
	sent. If you want to filter out Reply-Messages from standard
	or Inter-CPU messages, compare the LN_TYPE field to NT_REPLYMSG.
	Replied Inter-CPU messages still get the same node type
	(NT_REPLYMSG). Any assumptions about the value of the new
	node type are ILLEGAL!!

	As soon as an Inter-CPU message is sent, the PPC looses ownership
	over the message. No access to the message is allowed until the
	reply has been arrived.

	Inter-CPU messages can be reused if they have been replied.

	Inter-CPU messages are read and replied using the standard
	message handling mechanisms (exec/WaitPort,exec/GetMsg,exec/ReplyMsg
	for 68K, powerpc/WaitPortPPC, powerpc/GetMsgPPC, powerpc/ReplyMsgPPC
	for PPC).

	The receiving task must NOT access message data, which are not
	explicitely located in the message body (for example data which is
	referenced by a pointer) unless both tasks care for the cache
	consistency. Only the message itself is flushed/invalidated
	automatically by the system.

	The receiving task may write to the message body of an Inter-CPU
	message.

	Inter-CPU messages should always be replied and the reply should
	be read and filtered out.

    SEE ALSO
	AllocXMsgPPC, FreeXMsgPPC


powerpc.library/ReleaseSemaphorePPC        powerpc.library/ReleaseSemaphorePPC

    NAME
	ReleaseSemaphorePPC - make signal semaphore available to others (V8)

    CPU
	PowerPC

    SYNOPSIS
	ReleaseSemaphorePPC(_PowerPCBase, SignalSemaphorePPC)
			    r3            r4

	void ReleaseSemaphorePPC(struct Library *,
				 struct SignalSemaphorePPC *);

    FUNCTION
	Releases a semaphore locked by either ObtainSemaphorePPC or
	AttemptSemaphorePPC. If other tasks are waiting, the foremost
	in the waiting queue is waked up.

    INPUTS
	_PowerPCBase - base of powerpc.library
	SignalSemaphorePPC - pointer to a signalsemaphorePPC structure

    NOTES
	This call is guaranteed to preserve all GPR (except r0) and the CTR.

	If the semaphore is in an illegal state after calling
	ReleaseSemaphorePPC, a system message will appear and the task is
	put into waiting state.

    SEE ALSO
	InitSemaphorePPC, FreeSemaphorePPC, ObtainSemaphorePPC,
	AttemptSemaphorePPC, AddSemaphorePPC, RemSemaphorePPC
	FindSemaphorePPC, powerpc/semaphoresPPC.i


powerpc.library/RemExcHandler                    powerpc.library/RemExcHandler

    NAME
	RemExcHandler - removes a custom exception handler (V9)

    CPU
	PowerPC

    SYNOPSIS
	RemExcHandler(_PowerPCBase, XLock)
		      r3            r4

	void RemExcHandler(struct Library *, void *);

    FUNCTION
	Removes an exception handler inserted by the function SetExcHandler.

    INPUTS
	_PowerPCBase - base of powerpc.library
	XLock - The lock value returned by SetExcHandler. It's safe to pass
		NULL as parameter

    SEE ALSO
	RemExcHandler, powerpc/powerpc.i


powerpc.library/RemHeadPPC                          powerpc.library/RemHeadPPC

    NAME
	RemHeadPPC - removes the head node from a list (V8)

    CPU
	PowerPC

    SYNOPSIS
	node = RemHeadPPC(_PowerPCBase, list)
	r3                r3            r4

	struct Node *RemHeadPPC(struct Library *, struct List*);

    FUNCTION
	Removes the head node of a list. This is the mirror function of
	exec/RemHead.

    INPUTS
	_PowerPCBase - base of powerpc.library (can be omitted)
	list - the target list from which the head node should be removed

    RESULT
	node - the node removed or 0 if the list was empty

    NOTES
	This function is guaranteed to work correctly, if the PowerPCBase
	is not passed in r3.

	Assembler programmers may use the macro _REMHEAD located in
	'powerpc/listsPPC.i'

	This function is safe to call from exception handlers.

    SEE ALSO
	InsertPPC, AddTailPPC, AddHeadPPC, RemovePPC, RemTailPPC,
	EnqueuePPC, FindNamePPC, powerpc/listsPPC.i


powerpc.library/RemovePPC                            powerpc.library/RemovePPC

    NAME
	RemovePPC - removes a node from a list (V8)

    CPU
	PowerPC

    SYNOPSIS
	RemovePPC(_PowerPCBase, node)
		   r3           r4

	void RemovePPC(struct Library *, struct Node*);

    FUNCTION
	Removes a node from whatever list it is in. This is the mirror
	function of exec/Remove.

    INPUTS
	_PowerPCBase - base of powerpc.library (can be omitted)
	node - the node to remove

    NOTES
	This function is guaranteed to work correctly, if the PowerPCBase
	is not passed in r3.

	Assembler programmers may use the macro _REMOVE located in
	'powerpc/listsPPC.i'

	This function is safe to call from exception handlers.

    SEE ALSO
	InsertPPC, AddTailPPC, AddHeadPPC, RemHeadPPC, RemTailPPC,
	EnqueuePPC, FindNamePPC, powerpc/listsPPC.i


powerpc.library/RemPortPPC                          powerpc.library/RemPortPPC

    NAME
	RemPortPPC - removes a public PPC message port from the system (V11)

    CPU
	PowerPC

    SYNOPSIS
	RemPortPPC(_PowerPCBase, MsgPortPPC)
		   r3            r4

	void RemPortPPC(struct Library *, struct MsgPortPPC *);

    FUNCTION
	This function removes a public message port from the global list
	of message ports. It is the mirror function of exec/RemPort.

    INPUTS
	_PowerPCBase - base of powerpc.library
	MsgPortPPC - pointer to a PPC message port. It's safe to pass a NULL
		     parameter.

    SEE ALSO
	CreateMsgPortPPC,DeleteMsgPortPPC,FindPortPPC,AddPortPPC
	powerpc/portsPPC.i


powerpc.library/RemTailPPC                          powerpc.library/RemTailPPC

    NAME
	RemTailPPC - removes the tail node from a list (V8)

    CPU
	PowerPC

    SYNOPSIS
	node = RemTailPPC(_PowerPCBase, list)
	r3                r3            r4

	struct Node *RemTailPPC(struct Library *, struct List*);

    FUNCTION
	Removes the tail node of a list. This is the mirror function of
	exec/RemTail.

    INPUTS
	_PowerPCBase - base of powerpc.library (can be omitted)
	list - the target list from which the tail node should be removed

    RESULT
	node - the node removed or 0 if the list was empty

    NOTES
	This function is guaranteed to work correctly, if the PowerPCBase
	is not passed in r3.

	Assembler programmers may use the macro _REMTAIL located in
	'powerpc/listsPPC.i'

	This function is safe to call from exception handlers.

    SEE ALSO
	InsertPPC, AddTailPPC, AddHeadPPC, RemovePPC, RemHeadPPC,
	EnqueuePPC, FindNamePPC, powerpc/listsPPC.i


powerpc.library/RemSemaphorePPC                powerpc.library/RemSemaphorePPC

    NAME
	RemSemaphorePPC - removes a global signal semaphore (V8)

    CPU
	PowerPC

    SYNOPSIS
	RemSemaphorePPC(_PowerPCBase, SignalSemaphorePPC)
			r3            r4

	void RemSemaphorePPC(struct Library *, struct SignalSemaphorePPC *);

    FUNCTION
	Removes a global signal semaphore created by AddSemaphorePPC. This
	is the mirror function of exec/RemSemaphore.

    INPUTS
	_PowerPCBase - base of powerpc.library
	SignalSemaphorePPC - pointer to a signalsemaphorePPC structure

    SEE ALSO
	InitSemaphorePPC, FreeSemaphorePPC, ObtainSemaphorePPC,
	AttemptSemaphorePPC, ReleaseSemaphorePPC, AddSemaphorePPC,
	FindSemaphorePPC, powerpc/semaphoresPPC.i


powerpc.library/ReplyMsgPPC                        powerpc.library/ReplyMsgPPC

    NAME
	ReplyMsgPPC - put a message to its reply port (V11)

    CPU
	PowerPC

    SYNOPSIS
	ReplyMsgPPC(_PowerPCBase, message)
		    r3            r4

	void ReplyMsgPPC(struct Library *, struct Messge *);

    FUNCTION
	This function sends a message to its reply port, if one is present.
	This is the mirror function of exec/ReplyMsg.

    INPUTS
	_PowerPCBase - base of powerpc.library
	message - a pointer to the message to be replied

    NOTES
	This function is safe to call from exception handlers.

    SEE ALSO
	WaitPortPPC, PutMsgPPC, GetMsgPPC, powerpc/portsPPC.i


powerpc.library/Run68K                                  powerpc.library/Run68K

    NAME
	Run68K - runs a 680x0 function resp. AMIGA-OS library function (V7)

    CPU
	PowerPC

    SYNOPSIS
	status = Run68K(_PowerPCBase, PPStruct )
	r3              r3           r4

	LONG RunPPC (struct Library *, struct PowerPC *);

    FUNCTION
	Runs a 680x0 function or an AMIGA-OS library function. All registers
	can be transferred to 68K as well as parameters on stack. All cache
	management actions are handled automatically.

	All registers are transferred back from 68K after the 68K call
	is completed. They are stored in the PowerPC structure.

	See RunPPC for the register assignment.

    INPUTS
	_PowerPCBase - base of powerpc.library
	PPStruct - Pointer to an initialized PowerPC Structure

	  PP_CODE       : Pointer to the 680x0 code resp. pointer to the
			  library base (if PP_OFFSET is not zero).
	  PP_OFFSET     : Library offset or 0 if no library function is
			  called.
	  PP_FLAGS      : Flags which can be ore'd together
	  - PP[F/P]_ASYNC   : call 68K function asynchronely (PPC process
			      returns immediately)
	  PP_STACKPTR   : Pointer to the arguments on the stack to be
			  transferred. The pointer must point to the top
			  of the calling process' stackframe. The stack area
			  to be transferred is located at offset 24 from this
			  position. If no arguments on stack should be
			  transferred, set this to zero.
	  PP_STACKSIZE  : Size of the stack area to be transferred. If no
			  stack parameters should be transferred, set this
			  to zero.
	  PP_REGS       : Array of longwords where the registers to be
			  transferred can be stored (d0-a6)
	  PP_FREGS      : Array of quadwords (8 bytes) where the FP-registers
			  to be transferred can be stored (fp0-fp7)

    RESULT
	status - PPERR_SUCCESS if the call was successfully
		 PPERR_ASYNCERR if a synchrone 68K call was made after an
				asynchrone 68K call

    NOTES
	Calling a 68K function asynchronely is dangerous. Take care of
	possible cache conflicts. Avoid calling system functions as much
	as possible.

	If an asynchrone 68K call is done, the function WaitFor68K MUST be
	called ONCE after the call was done. No other 68K call is allowed
	for this PPC process after an asynchrone 68K call and before a call
	to WaitFor68K.

	If an asynchronely called 68K function performs a PPC call, the call
	is only performed when WaitFor68K is called by the PPC process. Note
	that the 68K mirror process is still connected to the calling PPC
	process.

	DON'T pass arguments on stack when calling a 68K function asynchronely.
	The stack is most likely to be trashed before it is copied to the 68K
	stack.

	Assembler programmers should use the macros RUN68K and
	RUN68K_XL located in the include file 'powerpc/powerpc.i'

    SEE ALSO
	WaitFor68K,powerpc/powerpc.i


powerpc.library/SetCache                              powerpc.library/SetCache

    NAME
	SetCache - cache manipulation function (V8)

    CPU
	PowerPC

    SYNOPSIS
	SetCache(_PowerPCBase, cacheflags, start, length)
		 r3            r4          r5     r6

	void SetCache(struct Library *, ULONG, void *, ULONG);

    FUNCTION
	This function offers many possibilities to affect the caches of
	the PPC. It performs the action defined by the cache flags. Only
	one action can be performed at the same time.

    INPUTS
	_PowerPCBase - base of powerpc.library
	cacheflags - action to be performed:
	    CACHE_DCACHEOFF:    Data cache is disabled. The Cache is flushed
				automatically.
	    CACHE_DCACHEON:     Data cache is enabled.
	    CACHE_DCACHELOCK:   Data cache is locked (is ignored if either
				'start' or 'length' is zero).
	    CACHE_DCACHEUNLOCK: Data cache is unlocked.
	    CACHE_DCACHEFLUSH:  Data cache is flushed.
	    CACHE_ICACHEOFF:    Instruction cache is disabled.
	    CACHE_ICACHEON:     Instruction cache is enabled.
	    CACHE_ICACHELOCK:   Instruction cache is locked.
	    CACHE_ICACHEUNLOCK: Instruction cache is unlocked.
	    CACHE_ICACHEINV:    Instruction cache is invalidated.

	start - pointer to the start address of the area to be affected.
		The following cacheflags support an area specification:
		CACHE_DCACHELOCK, CACHE_DCACHEFLUSH, CACHE_ICACHEINV

		if 'start' is 0 the whole address space is affected

	length - length of the area to be affected (see above for the
		 cache flags which support area specification).
		 if 'length' is 0 the whole address space is affected

    NOTES
	Invalidating the whole instruction cache is much more efficient
	than flushing only a part of it.

	Flushing the whole data cache is less efficient than flushing
	a specific area, if this area is not too large.

	The cacheflag DCACHELOCK requires 'start' and 'length' to be not
	zero. The area specified is then copied into the data cache and
	the data cache is locked afterwards.

	The caches should not be switched on/off resp. locked/unlocked
	without GOOD justification. Global manipulations of the cache
	should be avoided. Better affect the cache locally by using
	AllocVecPPC.

	This function is safe to call from exception handlers

    SEE ALSO
	powerpc/powerpc.i


powerpc.library/SetExcHandler                    powerpc.library/SetExcHandler

    NAME
	SetExcHandler - insert a custom exception handler (V9)

    CPU
	PowerPC

    SYNOPSIS
	XLock = SetExcHandler(_PowerPCBase, ExcTags)
	r3                    r3            r4

	void *SetExcHandler(struct Library *, struct TagItem *);

    FUNCTION
	This function allows applications to insert custom exception
	handlers. Those handlers can be global or task dependant,
	priorities are also supported. Multiple exceptions can be
	selected for one exception handler.

	The exception handlers are executed in supervisor mode and
	have access to all supervisor registers.

	The handlers are called in one of two possible ways (dependant
	of the tag EXC_FLAGS):

	1) EXC_FLAGS has the flag EXCF_SMALLCONTEXT set:


	   Status = CustomHandler(SmallContext)
	   r3                     r3

	   ULONG CustomHandler(struct XCONTEXT*)

	   Inputs:
		SmallContext - a pointer to a XCONTEXT structure (see
			       powerpc/powerpc.i)

	   Result:
		Status - a return value which decides, whether the
			 exception should be leaved immediately or
			 if following exception handlers should be
			 executed, too (see powerpc/powerpc.i)


	  In this first method, the handler gets all registers directly,
	  except for r3, which is passed in the XCONTEXT structure. The
	  exception ID, which gives information about the kind of
	  exception occurred, is passed also in XCONTEXT structure.

	  All registers which are modified by the exception handler are
	  also modified for the interrupted task. If r3 should be modified
	  for the interrupted task, the appropriate field of the XCONTEXT
	  structure has to be modified.

	  Some of the interrupted task's registers are passed in special
	  supervisor registers. If they should be changed, the appropriate
	  supervisor registers have to be changed:

	  SPRG1 -       The interrupted task's Link Register
	  SPRG2 -       The interrupted task's Stackpointer (r1)
	  SPRG3 -       The interrupted task's Smalldata Base (r2)

	  The exception stack, which is passed in r1, is allocated from the
	  user stack of the interrupted task.


	2) EXC_FLAGS has the flag EXCF_LARGECONTEXT set:


	   Status = CustomHandler(LargeContext)
	   r3                     r3

	   ULONG CustomHandler(struct EXCCONTEXT*)

	   Inputs:
		LargeContext - a pointer to a EXCCONTEXT structure (see
			       powerpc/powerpc.i)

	   Result:
		Status - a return value which decides, whether the
			 exception should be leaved immediately or
			 if following exception handlers should be
			 executed, too (see powerpc/powerpc.i)

	  In this second method, the handler gets all registers in the
	  EXCCONTEXT structure. If the handler wishes to change some
	  of the register contents it must change the appropriate fields
	  in the EXCCONTEXT structure which are copied back to the
	  registers after the custom handler has completed. If no
	  field is provided for a certain register, it has to be modified
	  directly.

	  The exception stack, which is passed in r1, is allocated from the
	  user stack of the interrupted task.

    INPUTS
	_PowerPCBase - base of powerpc.library
	ExcTags - pointer to a tagitem array. The following tags are
		  supported:

	    EXCATTR_CODE:       pointer to the exception handler code
				(required)
	    EXCATTR_DATA:       a user data which is passed in r2 to the
				custom exception handler. This is usually
				a base register which provides access to
				all global data required.
	    EXCATTR_TASK:       specifies the task which is allowed to take
				the exception handler. If this tag is 0 or
				omitted, the current task is taken instead.
				This tag has no effect if the exception
				handler is specified as global (see below
				at EXCATTR_FLAGS)
	    EXCATTR_EXCID:      Defines which exceptions should call this
				exception handler. See powerpc/powerpc.i
				for a description of all supported exceptions.
				Multiple exceptions can be selected.
	    EXCATTR_FLAGS:
		EXCF_GLOBAL:       Marks the exception handler as global. It
				   is then called for every exception occurred.
		EXCF_LOCAL:        Marks the exception handler as local. It is
				   then only called, if the interrupted task
				   matches the task specified in EXCATTR_TASK.
		EXCF_SMALLCONTEXT: The exception handler is called with a
				   XCONTEXT structure as parameter (see above
				   for a description of this mode).
		EXCF_LARGECONTEXT: The exception handler is called with a
				   EXCCONTEXT structure as parameter (see above
				   for a description of this mode).

				One flag of EXCF_GLOBAL and EXCF_LOCAL and one
				flag of EXCF_SMALLCONTEXT and EXCF_LARGECONTEXT
				must be specified, otherwise this function
				fails.

	    EXCATTR_NAME:       An identification name for this handler
	    EXCATTR_PRI:        The priority of this exception handler

    RESULT
	XLock - A lock to be passed to RemExcHandler or 0 if something
		failed.

    NOTES
	Exception handlers should generally take care that they don't
	destroy any registers of the interrupted task except if it is
	desired. Special care must be taken if the exception handler is
	called with the small context structure (take care of r0!). All
	registers, inclusive CR, CTR, LR and others must be restored if
	they should not be changed.

	IMPORTANT: The exception handler is called with MMU switched off!
	The whole address space is accessed in cachable copyback mode, so
	no access to critical locations such as custom chip space must
	be performed. If such locations should be accessed, a temporary
	MMU setup must be done using the library functions 'SetExcMMU'
	and 'ClearExcMMU' (V10)

	Note that changes to the MSR of the interrupted task must be done
	by writing to SRR1 (i.e. setting the trace bit).

	Note that exception handlers should generally not call system
	functions with some exceptions (for example 'SignalPPC' is often
	useful to call from exception handlers). System functions must not
	be called unless it's allowed explicitely by the documentation of
	each function.

	Note that the content of the program counter (SRR0) differs depending
	on the exception type. Sometimes it contains the address of the
	excepting instruction and sometimes the address of the next
	instruction to complete. Exception handlers must take care about
	this and should set the program counter appropriately.
	Here follows a table of all supported exceptions and their behaviour:

	Machine check (EXCF_MCHECK):        PC -> maybe next instruction
	Data access (EXCF_DACCESS):         PC -> excepting instruction
	Instruction access (EXCF_IACCESS):  PC -> next instruction
	Alignment (EXCF_ALIGN):             PC -> excepting instruction
	Program (EXCF_PROGRAM):             PC -> excepting instruction
	FP unavailable (EXCF_FPUN):         PC -> excepting instruction
	Trace (EXCF_TRACE):                 PC -> next instruction
	Performance Monitor (EXCF_PERFMON): unknown
	Instruction breakpoint (EXCF_IABR): PC -> excepting instruction

	Exception handlers should not waste stack space. The system
	allocates an extra space for this purpose but it may not be
	sufficient if very stack-intensive routines are called as
	exception handlers.

	If every exception handler returns the state EXCRETURN_NORMAL
	then the standard WarpOS exception handler is executed (except
	for Trace- and PerformanceMonitor-Exceptions).

	If exception handlers are written to emulate commands causing
	an exception they should return EXCRETURN_ABORT as return value
	to suppress following exception handlers which might output
	some alert messages. The priority should be probably high enough
	to ensure that no unwanted reactions occur.

	The WarpOS debugging system is disabled during exception
	processing.

	It's completely ILLEGAL to exit an exception handler by an RFI
	instruction!! It's also illegal to trash SPRG0!

    SEE ALSO
	RemExcHandler, powerpc/powerpc.i


powerpc.library/SetHardware                        powerpc.library/SetHardware

    NAME
	SetHardware - hardware manipulation function (V9)

    CPU
	PowerPC

    SYNOPSIS
	Status = SetHardware(_PowerPCBase, hardwareflags, parameter)
			     r3            r4             r5

	ULONG SetHardware(struct Library *, ULONG, void *);

    FUNCTION
	This function offers some functions to access the PPC hardware.

    INPUTS
	_PowerPCBase - base of powerpc.library
	hardwareflags - action to be performed:
	    HW_TRACEON:         Enables trace mode for the current task
	    HW_TRACEOFF:        Disables trace mode for the current task
	    HW_BRANCHTRACEON:   Enables branch trace mode for the current task
	    HW_BRANCHTRACEOFF:  Disables branch trace mode for the current task
	    HW_FPEXCON:         Enables the floating point exceptions for the
				current task
	    HW_FPEXCOFF:        Disables the floating point exceptions for the
				current task
	    HW_SETIBREAK:       Sets the global instruction breakpoint
	    HW_CLEARIBREAK:     Clears the global instruction breakpoint
	    HW_SETDBREAK:       Sets the global data breakpoint
	    HW_CLEARDBREAK:     Clears the global data breakpoint

	parameter - additional parameter only used if a breakpoint should be
		    set. Then it contains the breakpoint address.

    RESULT
	Status - HW_AVAILABLE: The requested feature is available on this CPU
		 HW_NOTAVAILABLE: The requested feature is not available on
				  this CPU

    NOTES
	Floating point exceptions are only enabled globally with HW_FPEXCON.
	It's necessary to call 'ModifyFPExc' to enable the desired floating
	point exceptions.

	Floating point exceptions should not be enabled by standard
	applications. They are intended to use for debugging purposes.

	The data breakpoint feature is not available on PPC603[E].

    SEE ALSO
	ModifyFPExc, powerpc/powerpc.i


powerpc.library/SetSignalPPC                      powerpc.library/SetSignalPPC

    NAME
	SetSignalPPC - define the state of this task's signals (V8)

    CPU
	PowerPC

    SYNOPSIS
	oldSignals = SetSignalPPC(_PowerPCBase, newSignals, signalMask)
	r3                        r3            r4          r5

	ULONG SetSignalPPC(struct Library *, ULONG, ULONG);

    FUNCTION
	This function can query or modify the state of the current
	signals. This function is the mirror function of exec/SetSignal.

    INPUTS
	_PowerPCBase - base of powerpc.library
	newSignals - the new values for the signals
	signalMask - the set of signals to be affected.

    RESULT
	oldSignals - the prior values for all signals

    NOTES
	It's possible to check for the system signals (i.e. CTRL_C)
	if the PPC task was started using RunPPC.

    SEE ALSO
	AllocSignalPPC, FreeSignalPPC, SignalPPC, WaitPPC


powerpc.library/SetTaskPriPPC                    powerpc.library/SetTaskPriPPC

    NAME
	SetTaskPriPPC - get and set the priority of a task (V8)

    CPU
	PowerPC

    SYNOPSIS
	oldpriority = SetTaskPriPPC(_PowerPCBase, taskPPC, priority)
	r3                          r3            r4       r5

	LONG SetTaskPriPPC(struct Library *, struct TaskPPC *, LONG);

    FUNCTION
	This function changes the priority of a task regardless of its
	state. The old priority of the task is returned. A reschedule
	may be performed. This is the mirror function of exec/SetTaskPri.

    INPUTS
	_PowerPCBase - base of powerpc.library
	taskPPC - task to be affected
	priority - the new priority for the task

    RESULT
	old priority - the tasks previous priority


powerpc.library/Signal68K                            powerpc.library/Signal68K

    NAME
	SignalPPC - signal a 68K task (V8)

    CPU
	PowerPC

    SYNOPSIS
	Signal68K(_PowerPCBase, task, signals)
		  r3            r4       r5

	void Signal68K(struct Library *, struct Task*, ULONG);

    FUNCTION
	This function signals a 68K task with the given signals. If
	the signalled task is sleeping, it's woken up and a reschedule
	may occur.

    INPUTS
	_PowerPCBase - base of powerpc.library
	task - the 68K task to be signalled
	signals - the signals to be sent


powerpc.library/SignalPPC                            powerpc.library/SignalPPC

    NAME
	SignalPPC - signal a task (V8)

    CPU
	PowerPC

    SYNOPSIS
	SignalPPC(_PowerPCBase, taskPPC, signals)
		  r3            r4       r5

	void SignalPPC(struct Library *, struct TaskPPC*, ULONG);

    FUNCTION
	This function signals a task with the given signals. If the
	signalled task is sleeping, it's woken up and a reschedule
	may occur. This is the mirror function of exec/Signal.

    INPUTS
	_PowerPCBase - base of powerpc.library
	taskPPC - the task to be signalled
	signals - the signals to be sent

    NOTES
	This function is safe to call from exception handlers.

	Since V11 it's possible to signal a 68K task directly
	with 'SignalPPC' and the 68K task structure in r4 (this
	works only if the 68K task has a mirror PPC task; use
	'Signal68K' if this is not the case).
	Furthermore, all signals, which are sent to a task currently
	waiting for its mirror task to complete, are transferred
	automatically to the mirror task. In fact, the whole signal
	system is shared and can be viewed as one single 'virtual
	signaling system'. It really doesn't matter, on which CPU
	a program is running, the signals are always transferred to
	the currently active part.

    SEE ALSO
	AllocSignalPPC, FreeSignalPPC, SetSignalPPC, WaitPPC


powerpc.library/SPrintF                                powerpc.library/SPrintF

    NAME
	SPrintF - prints a formatted string to the serial port (V7)

    CPU
	PowerPC

    SYNOPSIS
	SPrintF (_PowerPCBase, Formatstring, values )
		 r3             r4             r5

	void SPrintF (struct Library *, STRPTR, APTR);

    FUNCTION
	Prints a formatted string to the serial port using the AMIGA-OS
	functions 'exec/RawPutChar' and 'exec/RawDoFmt'. Can be used to add
	debugging features and to improve the maintenance of software.

    INPUTS
	_PowerPCBase - base of powerpc.library
	Formatstring - A C style string with % commands to indicate where
		       parameters have to be inserted (see 'exec/RawDoFmt'
		       for a detailed description of these commands).
	values - A pointer to an array of parameters to be inserted into
		 specified places in the string.

    SEE ALSO
	exec/RawDoFmt


powerpc.library/SubTimePPC                          powerpc.library/SubTimePPC

    NAME
	SubTimePPC - subtracts one time request from another (V7)

    CPU
	PowerPC

    SYNOPSIS
	SubTimePPC(_PowerPCBase, Dest, Source)
		   r3            r4    r5

	void SubTimePPC(struct Library *, struct timeval *, struct timeval *);

    FUNCTION
	This routine subtracts one timeval structure from another. The results
	are stored in the destination (Dest - Source -> Dest)

	This is the mirror function of timer/SubTime.

    INPUTS
	_PowerPCBase - base of powerpc.library
	Dest - pointer to a timeval structure
	Source - pointer to a timeval structure

    NOTES
	This function is safe to call from exception handlers

    SEE ALSO
	GetSysTimePPC, AddTimePPC, CmpTimePPC


powerpc.library/Super                                    powerpc.library/Super

    NAME
	Super - switch to supervisor mode (V9)

    CPU
	PowerPC

    SYNOPSIS
	SuperKey = Super(_PowerPCBase)
	r3               r3

	ULONG Super(struct Library *);

    FUNCTION
	This function changes the current task to supervisor mode.

    INPUTS
	_PowerPCBase - base of powerpc.library

    RESULT
	SuperKey - A key value which must be passed to 'User' to switch back
		   to user mode

    NOTES
	Applications should generally not enter supervisor mode. Check first
	if there exists a library function which gives you access to the
	supervisor resources required.

    SEE ALSO
	User


powerpc.library/UnLockTaskList                  powerpc.library/UnLockTaskList

    NAME
	UnLockTaskList - unlocks a list locked by LockTaskList (V10)

    CPU
	PowerPC

    SYNOPSIS
	UnLockTaskList(_PowerPCBase)
		       r3

	void UnLockTaskList(struct Library *);

    FUNCTION
	Unlocks the task list which was locked by LockTaskList

    INPUTS
	_PowerPCBase - base of powerpc.library

    SEE ALSO
	LockTaskList, powerpc/tasksppc.i


powerpc.library/User                                      powerpc.library/User

    NAME
	User - switch to user mode (V9)

    CPU
	PowerPC

    SYNOPSIS
	User(_PowerPCBase, SuperKey)
	     r3            r4

	void User(struct Library *, ULONG);

    FUNCTION
	This function changes the current task to user mode.

    INPUTS
	_PowerPCBase - base of powerpc.library
	SuperKey - The return value of the matching call of 'Super'

    SEE ALSO
	Super


powerpc.library/WaitFor68K                          powerpc.library/WaitFor68K

    NAME
	WaitFor68K - waits for the completion of an asynchrone 68K call (V7)

    CPU
	PowerPC

    SYNOPSIS
	status = WaitFor68K(_PowerPCBase, PPStruct )
	r3                  r3             r4

	LONG WaitFor68K (struct Library *, struct PowerPC *);

    FUNCTION
	After an asynchrone 68K call was done (see Run68K) this function must
	be called to wait for the completion of the 68K function. All
	registers transferred to the PowerPC with Run68K are returned into the
	PowerPC Structure.

    INPUTS
	_PowerPCBase - base of powerpc.library
	PPStruct - Pointer to a PowerPC Structure (see Run68K for a description
		   of the elements). The structure has not to be initialized.
		   The structure must be transferred to hold the returned
		   registers by the 68K function.

    RESULT
	status - PPERR_SUCCESS if the call was successfully
		 PPERR_WAITERR if WaitFor68K is called after a synchrone 68K
			       call.

    NOTES
	Assembler programmers should use the macros WAITFOR68K and
	WAITFOR68K_XL located in the include file 'powerpc/powerpc.i'

    SEE ALSO
	Run68K,powerpc/powerpc.i


powerpc.library/WaitPortPPC                        powerpc.library/WaitPortPPC

    NAME
	WaitPortPPC - wait for a given port to be non-empty (V11)

    CPU
	PowerPC

    SYNOPSIS
	message = WaitPortPPC(_PowerPCBase, MsgPortPPC)
	r3                    r3            r4

	struct Message *WaitPortPPC(struct Library *, struct MsgPortPPC *);

    FUNCTION
	This function waits until the given port becomes non-empty. The
	first message in the port is returned without removing it from
	the port. This is the mirror function of exec/WaitPort.

    INPUTS
	_PowerPCBase - base of powerpc.library
	port - a pointer to a message port

    RESULTS
	message - a pointer to the first available message

    SEE ALSO
	PutMsgPPC, GetMsgPPC, ReplyMsgPPC, powerpc/portsPPC.i


powerpc.library/WaitPPC                                powerpc.library/WaitPPC

    NAME
	WaitPPC - wait for one or more signals (V8)

    CPU
	PowerPC

    SYNOPSIS
	signals = WaitPPC(_PowerPCBase, signalSet)
	r3                r3            r4

	ULONG WaitPPC(struct Library *, ULONG);

    FUNCTION
	This function attempts to wait for the given signals. If at
	least one of these signal is already set, the task returns
	immediately, otherwise it changes to waiting state. This is
	the mirror function of exec/Wait.

    INPUTS
	_PowerPCBase - base of powerpc.library
	signalSet - the set of signals for which to wait

    RESULTS
	signals - the signals which were received

    NOTES
	Since V11 it's possible to wait for signals which might
	be sent by 68K tasks (and maybe only to the mirror 68K
	task of this PPC task here). Calling exec/Signal with a
	PPC task structure as first argument will work, too.
	See the desription of 'SignalPPC' for more information
	about the shared signaling system.

    SEE ALSO
	AllocSignalPPC, FreeSignalPPC, SetSignalPPC, SignalPPC


powerpc.library/WaitTime                              powerpc.library/WaitTime

    NAME
	WaitTime - wait for a given time or for given signals (V10)

    CPU
	PowerPC

    SYNOPSIS
	signals = WaitTime(_PowerPCBase, signalSet, time)
	r3                 r3            r4         r5

	ULONG WaitTime(struct Library *, ULONG, ULONG);

    FUNCTION
	This function attempts to wait for a specific time of for
	given signals. This function acts just like 'WaitPPC' with
	the difference that the task returns when the time specified
	is over.

    INPUTS
	_PowerPCBase - base of powerpc.library
	signalSet - the set of signals for which to wait (can be 0
		    if the task should only wait for a given time)
	time - the time in microseconds to wait

    RESULTS
	signals - the signals which were received (if this value is 0,
		  then the time is up).

    NOTES
	The time which explicitly passes between calling 'WaitTime' and
	returning from it can vary dependant of current system state. If
	many tasks are active, the time can be delayed. Furthermore the
	overhead of this function must be taken in account.

    SEE ALSO
	WaitPPC