[1mThe Cloanto Personal Input/Output Library System[22m

 [3mDecember 12, 1996 - Personal I/O Libraries Version 5 [23m
 [3mFor more information please send E-mail to <support@cloanto.com>, [23m
 [3mor visit our web site <http://www.cloanto.com>. [23m


 [1mIntroduction[22m

 The Personal I/O Library System was designed by Cloanto to simplify the
 development of modular I/O code that could be shared by different
 applications. Cloanto programs like Personal Paint, Personal Fonts Maker 2
 and ColorType use these libraries.

 A functional implementation of the Personal I/O Library System is divided
 in a library and a client part. The library part resides in the external
 I/O library, whereas the client part resides in the application (which is
 the "client" of the library). This documentation and the included skeleton
 and example source code files are library-centric, and explain how to write
 libraries compatible with different versions of clients. The library
 version described here remains always version 5. Libraries developed
 following these guidelines should have a version root number of "5", and a
 freely selectable revision number (5.0 to 5.999...)

 Each Personal I/O library can support one or more picture types. The number
 of picture types can be fixed or variable (i.e. defined at run time). The
 "SView" I/O library, for example, can handle zero or more picture types,
 based on the presence of "superview.library" (tested with version 11.7) and
 on the available "svobjects").

 Further control is achieved by properly setting the library options. Within
 the library, each picture type can have its own options. They allow the
 client program to control some details of the loaded/saved data.

 The I/O libraries can handle file-based (e.g. ILBM, PNG, etc.),
 device-based (scanned, digitized, etc.) or rendered (e.g. fractal, random
 dot, etc.) images. The client program doesn't even know where a picture
 comes from or where it goes to: the I/O libraries hide the loading and
 saving details, while offering power and flexibility.

 The I/O libraries can selectively load or save certain pieces of
 information (e.g. a palette or an image mask, instead of the whole image).

 The Personal I/O interface and functions are a superset of other picture
 I/O systems (e.g. "DataType", "iffparse", "SView", "MultiPic", etc.): some
 "translator" I/O libraries are available and some others can easily be
 created. These libraries provide the foreign picture system's functionality
 via the Personal I/O interface.

 This documentation and the included source code files are aimed at
 developers of Personal I/O libraries version 5. No information is provided
 here about the client program side of the interface (as is integrated in
 Personal Paint, ColorType, etc.), nor about certain specific features and
 behaviors of I/O library versions prior to version 5. All versions of the
 I/O library specification are designed to remain usable by all versions of
 I/O library clients (except by client versions 1 and 2, which were used
 only to process files in limited formats, and never reached wide
 diffusion). I/O library clients, however, make use of additional
 information about the different library versions which is not included
 here.

 There are two known bugs ("SeekFile" section) affecting older versions of
 I/O library clients, in parts which are used mainly by more complex
 libraries. Since it has always been a policy of the I/O library
 specification to remain as compatible as possible both backwards and
 forwards, simple workarounds are described here for the two bugs. I/O
 libraries are requested to check the version of the client, and to act
 accordingly.


 [1mInitialization and Picture Type Query[22m

 The client program first searches for I/O libraries in its own "Libs"
 directory (e.g. "PPaint/Libs"), and then performs a new search in the
 system "LIBS:" path. If different versions of the same library are found in
 the two locations, the client automatically selects the newer library.

 Library names must match the "personal_#?_io.library" pattern and should
 use only lowercase characters.

 The client program opens each library conforming to the above
 specifications and queries it about the picture types supported. The
 functions involved are GetFirstDataInfo() and GetNextDataInfo(); the
 following is a typical client program's loop:

    for (ok = GetFirstDataInfo(dinfo); ok; ok = GetNextDataInfo(dinfo))
    {
       /*
          The program here stores or somehow processes the DataInfo
          structure which describes a specific picture type.
       */
    }

 Some I/O libraries may count on the fact that this loop calls
 GetNextDataInfo() until FALSE is returned to perform resource deallocation.
 A support library can be opened or some memory can be allocated by the
 GetFirstDataInfo() function, then GetNextDataInfo() keeps on using the
 resources until it has no more picture types to describe (the resources are
 deallocated and a FALSE code is returned).

 While I/O libraries and clients prior to version 4 use different types of
 authentication and handshaking on a case by case basis, from version 5 a
 simplified authentication mechanism is part of each picture type
 description (both in GetFirstDataInfo() and in GetNextDataInfo()):

 1) A "Cloanto®" character string (case sensitive) must be part of the file
 containing the I/O library.

 2) If the client is a version prior to 5, points 3) and 4) must be skipped
 by the I/O library.

 3) The I/O library must check if the HandshakeText field of the DataInfo
 structure points to a "Cloanto®" string (case sensitive). If this is not
 the case, the library must abort the query phase.

 4) The HandshakeText field must be changed to point to a "Cloanto®" string
 inside the library memory. If conditions 1) and 4) are not met, the client
 (or a future client) may abort the query phase.

 Use of the "Cloanto" registered trademark is subject to a license
 agreement, as explained in the dedicated section of this documentation.


 [1mThe DataInfo Structure[22m

 The DataInfo structure identifies and describes a specific picture type
 within an I/O library. Picture types are local to the I/O library: there is
 no danger of accidentally duplicating picture type information (the
 Priority field being an exception) of other I/O libraries.

 DataInfo structures are used in several contexts: in the query phase (to
 describe the library's picture types), during a load operation (to force
 the loading of a specific type), during a save operation (to select the
 save format) and, in general, in every situation where a picture type must
 be specified.


 [1mDataInfo fields[22m

 [3mVersion [23m

 This is the client program interface version. Third parts I/O libraries
 should abort every operation based on a DataInfo with a Version less than
 3.


 [3mCode [23m

 The Code field identifies a library picture type. Any value can be used as
 a type code, as long as there are no duplicated codes within the library.
 The code 0xFFFFFFFF (DIC_ANYDATA) is reserved and is used in a load
 operation to allow every picture type to be loaded.


 [3mFlags [23m

 This field describes the picture type characteristics:

 DIF_LOAD

 Planar (up to 256 colors) images can be loaded.

 DIF_LOAD_24

 True color (16.7 million colors) images can be loaded.

 DIF_SAVE

 Planar (up to 256 colors) images can be saved.

 DIF_SAVE_24

 True color (16.7 million colors) images can be saved.

 DIF_LOADFILE

 Pictures are loaded from file. The file data can be accessed through the
 client program's I/O functions (asynchronous, double buffered, speed
 optimized) or using the plain filing system (see DIF_CUSTOMIO). If this bit
 is not set, the picture data is rendered (e.g. fractal images) or otherwise
 acquired (e.g. scanner loader).

 DIF_SAVEFILE

 Pictures are saved to a file. The data can be written using the client
 program's I/O functions (asynchronous, double buffered, speed optimized) or
 the plain filing system (see DIF_CUSTOMIO).

 Writers of non-DIF_SAVEFILE libraries should read the "SeekFile"
 (PictureInfo structure field) section.

 DIF_RECOGNIZE

 The library can identify picture files based on this format. A
 DIF_RECOGNIZE type must be DIF_LOADFILE too, but not vice versa: the
 structure of some file types (e.g. raw data files) cannot be recognized.

 DIF_ENCRYPTED

 The file format is encrypted. The client program's encryption functions can
 be used to encrypt/decrypt the file. These functions hide the encryption
 mechanism used, which can be based on user specified keys or not.

 DIF_CUSTOMIO

 The client program is not allowed to perform any I/O operation on the file
 to be loaded or saved. When the flag is not set, the program opens the
 file, provides high-level, speed-optimized I/O functions to read and write
 data and, finally, closes the file.

 Writers of DIF_CUSTOMIO libraries should read the "SeekFile" (PictureInfo
 structure field) section.

 DIF_LOADOPTS

 A group of options is available to fine-tune the loading process.

 DIF_SAVEOPTS

 A group of options is available to fine-tune the saving process.

 DIF_SELFLOPT

 The library's user interface is used to set the load-options. The interface
 must be activated whenever the client program issues the command:
 "SetOption(dinfo, SOPT_SELFLOPT);". When the flag is not set, the client
 program's Option requester is used instead.

 DIF_SELFSOPT

 The library's user interface is used to set the save-options. The interface
 must be activated whenever the client program issues the command:
 "SetOption(dinfo, SOPT_SELFSOPT);". When the flag is not set, the client
 program's Option requester is used instead.

 DIF_CONVERTED

 The picture type is based on a "foreign" picture I/O system (e.g.
 "DataType", "SView", "MultiPic", etc.). This flag is checked by the client
 program to avoid possible deadlocks or endless loops if the Personal I/O
 library is being called, directly or indirectly, by one of the same foreign
 I/O systems which the I/O library itself, directly or indirectly, may try
 to access. In case of doubts about the use of this flag when a Personal I/O
 library uses another library, it is usually safe to set the flag. If it is
 absolutely certain that the foreign I/O system terminates the chain by, for
 example, getting all of its I/O data from a hardware device such as a
 scanner, then it is not necessary to set this flag.


 [3mProcessData [23m

 This field of bits states which information can be loaded/saved:

 PCDT_FORMAT

 Format information (image width, height and depth).

 PCDT_IMAGE

 Image bitmap.

 PCDT_MASK

 Stencil mask.

 PCDT_PALETTE

 Color palette.

 PCDT_PRJINFO

 Project information: author, copyright and annotation strings.

 PCDT_DPI

 Picture ratio: horizontal and vertical DPI (dots per inch).

 PCDT_DISPID

 Amiga display mode ID.

 PCDT_HANDLE

 Handle (or hot spot). Brush related information.

 PCDT_EDGES

 Left edge and top edge. Brush related information (coordinates where the
 brush was cut from).

 PCDT_SRCDIM

 Width and height of the source image. Brush related information (format of
 the image where the brush was cut from).

 PCDT_TRANSPT

 Transparency type.

 PCDT_TRANSPC

 Transparent color.


 [3mPriority [23m

 This is the sort priority of the picture type. The priority affects the
 order in which the I/O libraries are queried to detect file type (low
 priority types are checked first) and the order in the client program's
 listboxes (low priority types are listed first). The picture types which
 share the same priority are sorted by name.

 The currently used priorities are:

 Format             Priority    Load   Save   Library
 --------------------------------------------------------------------------
 IFF ILBM           100         Yes    Yes    personal_ilbm_io.library
 PNG                150         Yes    Yes    personal_png_io.library
 GIF                200         Yes    Yes    personal_gif_io.library
 Windows Bitmap     250         Yes    Yes    personal_bmp_io.library
 OS/2 Bitmap        251         Yes    Yes    personal_bmp_io.library
 PCX                300         Yes    Yes    personal_pcx_io.library
 IFF ACBM           350         Yes    Yes    personal_ilbm_io.library
 Encrypted          400         Yes    Yes    personal_gif_io.library
 PBM                450         Yes    Yes    personal_pbm_io.library
 JPEG               475         Yes    No     personal_jpeg_io.library
 Photo CD           487         Yes    No     personal_pcd_io.library
 Photo CD Overview  488         Yes    No     personal_pcd_io.library
 C Source           500         No     Yes    personal_csrc_io.library
 Raw Data           550         No     Yes    personal_raw_io.library
 ASCII              600         No     Yes    personal_ascii_io.library
 SV AUTOMATIC       9000        Yes    No     personal_sview_io.library
 SV ...             9001        ...    ...    personal_sview_io.library
 DataType           10000       Yes    No     personal_datatypes_io.library
 Plasma             10100       Yes    No     personal_plasma_io.library
 Scanner I/O        20000       Yes    No     personal_scanquix_io.library

 In general, DIF_CONVERTED types should be positioned after
 non-DIF_CONVERTED types and non-DIF_LOAD/SAVEFILE should follow file-based
 types.

 It is suggested to always keep some free entries between the priorities
 used by different libraries, and to register both the library name and its
 priorities with Cloanto. Additional information on the above libraries is
 available from Cloanto.


 [3mName [23m

 Full name of the picture type (up to 39 characters, 12 recommended). It is
 typically used in the progress requester (e.g. "Reading ... File") and in
 contexts where space is not an issue.


 [3mShortName [23m

 Short name of the picture type (up to 15 characters, 6 recommended). It is
 typically used in file requesters (file type selection listboxes) and in
 other situations where it is important to save space.


 [3mFileSuffix [23m

 Up to three suffixes (15 characters maximum, including leading ".", case
 insensitive) generally used for file names based on this format (e.g.
 ".jpeg" and ".jpg" for the JPEG format). These fields are used to
 automatically detect the file type from a file name (e.g. in the system
 file requester, which lacks a format selection listbox).


 [3mHandshakeText [23m

 Used by the authentication mechanism of the library query functions
 (GetFirstDataInfo() and GetNextDataInfo(), see above). This field is
 present in DataInfo structures having version 5 or greater.


 [1mOptions Query[22m

 Just like each library can be queried about its picture types, each picture
 type can be queried about its options. The typical client program options
 loop resembles the picture type loop described above:

    for (ok = GetFirstOption(dinfo, dopt);
         ok;
         ok = GetNextOption(dinfo, dopt))
    {
       /*
          The program here stores or somehow
          processes the DataOption structure.
       */
    }

 There are several types of options: integer, fraction, boolean, depth
 values and strings. The options can be set (SetOption() function) before
 starting a load or a save operation; the assigned values remain valid until
 new values are assigned (they are stored in a copy of the library memory
 owned by the client program). The ResetOptions() function sets all the
 options of a given type back to their default values.


 [1mThe DataOption Structure[22m

 An option is made up of a name, a value and other attributes describing its
 characteristics (needed to control the user interface input).


 [1mDataOption Fields[22m

 [3mVersion [23m

 This is the client program interface version. New I/O libraries should
 abort every operation based on a DataOption with a Version lower than 3.


 [3mType [23m

 It is the type of value stored in the option:

 DOT_INTSTR

 Integer value. The client program should use a string gadget to set this
 option.

 DOT_INTSLIDE

 Integer value. The client program should use a proportional gadget to set
 this option.

 DOT_10000STR

 Fractional value in integer form (10000=1.0, 15000=1.5, ...). The client
 program should use a string gadget to set this option and the values should
 be displayed in a fractional form (1.0, 1.5, ...).

 DOT_BOOL

 Boolean value (0/1). The client program should use a check box to set this
 option.

 DOT_STRING

 String (79 characters maximum). The client program should use a string
 gadget to set this option.

 DOT_COLSLIDE

 Number of bitplanes. The client program should use a proportional gadget to
 set this option and the value displayed should be expressed in number of
 colors (2 to the power of <value>).


 [3mName [23m

 The option's name (up to 39 characters, upper case recommended). It is used
 to identify the option (e.g. in SetOption() operations) and as a gadget
 label (client program's Option requester) when no UITextStr is given (see
 below). It should be as descriptive as possible.


 [3mUITextStr [23m

 This field contains a user interface text code (see defines in
 "libraries/personal_io.h"): it defines the gadget label to be used in the
 client program's Option requester (the string displayed matches the
 language selected). When no predefined string is applicable, the code
 DOUI_NONE should be used (the option's name is used as a gadget label).


 [3mFlags [23m

 When the DOF_LOADOPTION bit is set, the option can be used to control load
 operations. When the bit is not set, the option just affects picture
 saving.


 [3mValue [23m

 The option's value (not for DOT_STRING options).


 [3mMin, Max, Default [23m

 The option's minimum, maximum and default values (not for DOT_STRING
 options).


 [3mString [23m

 The string of a DOT_STRING option (79 characters maximum).


 [1mLoading a Picture[22m

 When the GetPictureInfo() is called, the library must identify the picture
 file (DIF_LOADFILE libraries only) and provide image format information.
 When the DIF_CUSTOMIO bit is not set, the file has already been opened and
 its first 128 bytes have been stored in the FileHead field of the
 PictureInfo structure (GetPictureInfo()'s argument). When the first 128
 bytes are not sufficient to identify the file type, further file analysis
 can be performed. When the file has been identified, it can be accessed to
 retrieve the picture format (size, depth, etc.) information.

 The GetPictureInfo() function overhead should be minimum. When the file has
 been identified, but retrieving the image format would require much more
 time, the function return code should be PIOERR_OK (file identified), but
 the PCDT_FORMAT bit of the ProcessedData field (PictureInfo structure)
 should not be set. The client program can now use the picture type
 information (e.g. a "Reading xxx File" requester is opened) and ask for the
 file analysis to be completed (GetPictureInfo() is called again).

 As mentioned above, when GetPictureInfo() is called for a non-DIF_LOADFILE
 picture type (e.g. a fractal image), no file recognition must be performed
 and just the image format must be provided. The format could be based on
 load-options (e.g. "WIDTH", "HEIGH" and "DEPTH") or on the format of the
 client program's image being replaced (the Width, Height and Depth fields
 of the PictureInfo structure are preloaded with this information). The user
 could, for example, define a "dummy" brush in the client program, then
 replace it by loading a fractal brush of the same size and same number of
 colors.

 The client's "AUTO" pseudo-loader submits the file being loaded to every
 DIF_RECOGNIZE library (in order of priority). When GetPictureInfo() does
 not recognize the file, a PIOERR_BADTYPE error code must be returned: the
 file will be submitted to the next library. Other codes are associated to
 other situations: the file has been identified (PIOERR_OK), the file is
 encrypted and the current encryption key is wrong (PIOERR_NODECRYP: in such
 a case, the client asks the user for a new key, then GetPictureInfo() is
 called again) or the file has been identified but some error occurred (e.g.
 PIOERR_FILE_ERR, when the file cannot be read).

 Once the format information is known, the client program allocates the
 needed resources (image bitmap, color palette, etc.) and passes them to the
 ReadPicture() function. The required file data (PCDT_XXX bits in the
 ProcessData field) is now read in the storage areas provided.

 The bitmap data can be organized in bitplanes (palette based images, chip
 memory storage) or in hybrid chunky format (true color, fast memory
 storage). The hybrid chunky format uses the first three planes of a bitmap
 to store, respectively, red, green and blue information. Each byte of a
 chunky plane describes a pixel color component.

 Many file formats store the image data in chunky format (even for palette
 based images). The PictureInfo structure gives access to powerful and fast
 "chunky to planar" functions, which can be used to store this kind of data
 in a standard (planar) bitmap. True color data, instead, must be
 manipulated directly (note: HAM image data must be converted to true color
 data).

 While reading a HAM or true color picture, the client program can display
 it in a "preview" screen: the original (unconverted HAM or true color)
 image data is fed to it, row by row.

 Some kind of save-options must be updated while the picture is being read.
 This is the case for some file attributes (e.g. progressive display, image
 compression, file subtype, etc.). After the picture has been read, the
 client program queries the I/O library about the save-options and stores a
 copy of these options. When the picture is saved again, the original format
 and the original options can be used.

 When ReadPicture() returns, the IOLibCleanup() function is called to
 release allocated resources (if any). This is done because the file
 recognition and the file reading phases can share such resources (opened
 libraries, temporary bitmaps, etc.). The IOLibCleanup() function is [4mnot[24m
 called if just a simple file recognition has been performed
 (GetPictureInfo() has set the PCDT_FORMAT bit and returned PIOERR_OK) and
 no ReadPicture() command has been issued.


 [1mSaving a Picture[22m

 The saving process is much simpler than the loading process. Picture data
 and information is stored or referenced to in the PictureInfo structure,
 which is passed to the WritePicture() function.

 The client program may just want a few pieces of information to be written
 (e.g. palette saving). The ProcessData field describes which data should be
 saved.


 [1mProgress Requester Information[22m

 The GetProgressBumps() function gives information about the "time" required
 for the load and save operations to be completed. The value returned should
 be the number of BumpProgress() calls (see below) made by the ReadPicture()
 and WritePicture() functions (if zero, the operations won't be
 interruptible). The PictureInfo structure (function argument) can be used
 to adapt the bump value to the picture being load/saved (the value returned
 is usually equal to the picture height).


 [1mThe PictureInfo Structure[22m

 A PictureInfo structure pointer is the only argument passed to the
 GetPictureInfo(), ReadPicture(), WritePicture() and GetProgressBumps()
 functions. The structure is used to store information, to reference storage
 areas, to pass library bases and to give access to the client's file or
 picture handling functions.


 [1mPictureInfo Fields[22m

 [3mVersion [23m

 This is the client program interface version. Third party I/O libraries
 should abort every operation based on a PictureInfo with a Version number
 smaller than 3.


 [3mFileName [23m

 The field points to the name (including path) of the file being loaded or
 saved (DIF_LOADFILE and DIF_SAVEFILE picture types only). It can be used by
 DIF_CUSTOMIO libraries to open the picture file.


 [3mFileHead [23m

 This array contains the first 128 bytes of the file to be identified
 (GetPictureInfo() function, non-DIF_CUSTOMIO types only).


 [3mData [23m

 This DataInfo structure identifies the library format to be used.

 Load operations (multiple-type libraries only): if the DataInfo Code is
 DIC_ANYDATA, any of the library file formats can be recognized/loaded,
 otherwise just Code-typed files can be loaded.

 Save operations (multiple-type libraries only): the DataInfo Code selects
 which file format should be used to save the picture.


 [3mProcessData [23m

 The PCDT_XXX bits (see above) select which pieces of information should be
 loaded/saved (the remaining data should be skipped/ignored).


 [3mProcessedData [23m

 The ReadPicture() and WritePicture() functions should set a PCDT_XXX bit in
 this field for every piece of information loaded/saved. In load operations,
 the PCDT_FORMAT bit must be set by GetPictureInfo() (see above).


 [3mFlags, Parameters [23m

 Currently unused.


 [3mUser1, User2, User3 [23m

 General-purpose pointers to library data extensions. These fields are
 ignored by client programs.


 [3mWidth, Height, Depth [23m

 Size of the picture being loaded/saved. Load operations: before calling
 GetPictureInfo(), the client program sets the fields to the format of the
 picture/brush being replaced. Some libraries (e.g. fractal loader) can use
 this information to load pictures based on the same format. These fields
 are associated to the PCDT_FORMAT bit.


 [3mHandleX, HandleY [23m

 Picture handle (or hot spot), relative to the upper left image pixel. It is
 typically used in brush load/save operations. These fields are associated
 to the PCDT_HANDLE bit.


 [3mHorizDPI, VertDPI [23m

 Picture ratio (in dots per inch units). These fields are associated to the
 PCDT_DPI bit.


 [3mLeftEdge, TopEdge [23m

 Source picture coordinates where a brush was cut from. These fields are
 associated to the PCDT_EDGES bit.


 [3mSourceWidth, SourceHeight [23m

 Source picture format (brush-related information). These fields are
 associated to the PCDT_SRCDIM bit.


 [3mTranspType [23m

 One of the following transparency types (which match the IFF-ILBM masking
 types):

 BTR_NONE

 No transparency. All the image pixels should be considered opaque.

 BTR_CUSTOM

 The image data includes a transparency plane.

 BTR_TRANSPCOL

 A background color is defined. All the background-colored pixels are
 transparent.

 BTR_BACKFILL

 Only the background-colored areas which surround the image are set to be
 transparent.

 The TranspType field is associated to the PCDT_TRANSPT bit.


 [3mTransparentColor [23m

 This is the background color index (used by BTR_TRANSPCOL and BTR_BACKFILL
 images). The field is associated to the PCDT_TRANSPC bit.


 [3mDisplayID [23m

 An Amiga display mode ID (system include file "graphics/modeid.h"). The
 specified video mode (where available) should be used to display the image.
 The field is associated to the PCDT_DISPID bit.


 [3mBMap [23m

 This field points to the image bitmap. Resource allocation, bitmap formats
 an data manipulation are discussed in the section "Loading a picture". The
 field is associated to the PCDT_IMAGE bit.


 [3mMaskPlane [23m

 Transparency/stencil plane (BTR_CUSTOM images only). The plane shares the
 same BMap format (BytesPerRow, Rows, etc.). The field is associated to the
 PCDT_MASK bit.


 [3mPalette [23m

 Points to an array of Color structures (array size = 1 << Depth), where
 image palette information is stored.

 struct Color
 {
    UBYTE Red, Green, Blue;  /* color components */
    UBYTE EFlag;             /* unused: set to 0 */
 };

 The Red, Green and Blue range is 0..255 (white is 255,255,255, black is
 0,0,0). EFlag is currently unused and should be set to 0.

 The field Palette is associated to the PCDT_PALETTE bit.


 [3mProjInfo [23m

 This field points to a ProjectInfo resource. The project information
 (author, copyright and annotation strings) can be accessed using the
 GetProjectInfo() and SetProjectInfo() functions (see below). Starting from
 version 4 of the library interface, there is no length limit for such
 strings. The field is associated to the PCDT_PRJINFO bit (note: even though
 this bit is set, one or more information strings can be empty: only
 non-empty string must be saved).


 [3mPreviewDepth [23m

 GetPictureInfo() should set this field to 0 (no preview possible or
 desired), 6 or 8 (HAM-6 or HAM-8 preview screen) or 24 (true color preview
 screen), if a HAM or a 24-bit image is being loaded/inquired. The client
 program can disable the preview feature by setting this field back to 0
 (e.g. video hardware unavailable, user deselection, etc.): the
 ReadPicture() function should only supply image preview rows (see below)
 when the PreviewDepth field is not 0.


 [3mPreviewPalette [23m

 This field points to the color palette to be used for the HAM preview
 screen (typically 16 or 64 colors, for HAM-6 and HAM-8 respectively).
 Unlike other PictureInfo resources, the owner of the color array memory is
 the I/O library, which is responsible for allocating/deallocating the
 needed memory.


 [3mPreviewDisplayID [23m

 This field describes the display mode to be used for the HAM preview
 screen. True color screen modes are selected at run-time (choice based on
 the hardware availability).


 [3mUILanguage [23m

 This is the language code currently active in the client program:

 00 = English
 01 = German
 02 = Italian
 03 = French
 04 = Spanish
 05 = Dutch
 06 = Swedish
 07 = Danish
 08 = Norwegian
 09 = Finnish
 10 = Portuguese
 11 = Polish
 12 = Hungarian
 13 = Czech
 14 = Slowak
 15 = Slovenian
 16 = Croatian
 17 = Serbo-Croatian
 18 = Lithuanian
 19 = Latvian
 20 = Welsh


 [3mLibUIText [23m

 This field points to an array of string pointers. The texts referenced
 (localized to the client program's currently active language) are those
 associated to the DataOption UITextStr field (see defines in
 "libraries/personal_io.h").


 [3mSysBase, DOSBase, GfxBase, IntuitionBase, IconBase [23m

 System libraries. They can be directly used in conjunction with the
 compiler pragmas (see the included I/O library sample code).


 [3mReadFile [23m

 This field points to the function

    BOOL ReadFile (UBYTE *buffer, LONG bytes);

 It can be used to read a variable amount of data from the picture file,
 starting from the current file position (see SeekFile()). This and the
 following file I/O functions are only available to non-DIF_CUSTOMIO picture
 types.

 Arguments:
 buffer - area to read bytes into
 bytes  - number of bytes to read

 Result:
 TRUE, if the transfer was fully successful,
 FALSE otherwise.


 [3mWriteFile [23m

 This field points to the function

    BOOL WriteFile (UBYTE *buffer, LONG bytes);

 It can be used to write a variable amount of data to the picture file, at
 the current file position (see SeekFile()).

 Arguments:
 buffer - area to write bytes from
 bytes  - number of bytes to write

 Result:
 TRUE, if the transfer was fully successful,
 FALSE otherwise.


 [3mSeekFile [23m (multiple seeks from V5)

 This field points to the function

    LONG SeekFile (WORD mode, LONG bytes);

 SeekFile() sets/queries the read/write position of the picture file.

 Arguments:
 mode - SKF_ABSOLUTE: the position specified is an absolute file position
        SKF_FROMCURR: the position is relative to the current position
 bytes - position (can be negative, in conjunction with SKF_FROMCURR, to
         move backward in the file)

 Result:
 the previous absolute position in the file or -1, if an error occurred.

 Bugs:
 I/O library clients up to version 4 have a problem in the file caching
 system which produces erratic behavior when the I/O library requests a
 sequence of more than one seek from the client. A single seek is performed
 properly. Successive seeks are not. To ensure total compatibility with all
 versions of I/O clients, any library requiring complex seek functionality
 should access files directly, using AmigaDOS commands (this is what version
 5.1 of the "personal_jpeg_io.library" does, for example). This bug was
 fixed at some time in version 4 of the client code, but it is not possible
 to determine the presence of the bug from the library side. The original
 Personal Paint 6.4 (Amiga Magic pack), for example, has this bug, whereas
 the version later published by Cloanto (with the anim-brush extensions)
 doesn't. This is not considered a serious bug, because a single seek is
 sufficient for most types of file format detection and access, and multiple
 seeks can be implemented using AmigaDOS rather than the library client.

 Due to a different bug in some client programs up to version 4, the
 function pointed to by SeekFile is called after WritePicture() operations
 (in order to flush the write buffer) even when it shouldn't (DIF_SAVEFILE
 or DIF_CUSTOMIO picture type saving). Before terminating such operations,
 the SeekFile field should be changed to point to a dummy, do-nothing
 function (within the library body), like the following:

    static LONG DummySeekFile(WORD mode, LONG bytes) { return(0); }

 This is a DIF_SAVEFILE/DIF_CUSTOMIO WritePicture() sample:

    __asm WORD __saveds WritePicture(register __a0
                                     struct PictureInfo *picinfo)
    {
         ...

         if (picinfo->Version < 5)
            picinfo->SeekFile = DummySeekFile;

         return(...);
    }


 [3mBumpProgress [23m

 This field may point to the function

    BOOL BumpProgress (void);

 Each time this function is called, the client program's progress bar
 advances (more in the section "Progress Requester Information"). The user
 break status is also checked.

 Result:
 TRUE, if the user pressed the progress requester Stop gadget,
 FALSE, otherwise

 Note: this field may be NULL (progress requester feature disabled).


 [3mFastReadPix [23m

 This field points to the function

    UBYTE FastReadPix (struct BitMap *bmap, WORD x, WORD y);

 Planar bitmap access can often be quite slow. This function reads the color
 index at a given pixel position, using fast (buffered) techniques. The
 fastest performance is achieved by reading contiguous pixels. An
 initialization call must precede the reading, as in the following example:

    picinfo->FastReadPix(img_bmap, FBMP_INIT, 0);

    for (y = 0; y < height; y++)
    {
       for (x = 0; x < width; x++)
       {
          color = picinfo->FastReadPix(img_bmap, x, y);
       }
    }

 Arguments:
 bmap - bitmap to read from
 x    - x coordinate or FBMP_INIT (read initialization)
 y    - y coordinate

 Result:
 pixel color index (pen)


 [3mFastWritePix [23m

 This field points to the function

    void FastWritePix (struct BitMap *bmap, WORD x, WORD y, UBYTE col);

 This is the counterpart of FastReadPix. The specified color index is stored
 in the given planar bitmap. The fastest performance is achieved by writing
 contiguous pixels. An initialization call must precede the writing and,
 before accessing a new row, a flush action must be performed, just like in
 the following example:

    picinfo->FastWritePix(img_bmap, FBMP_INIT, 0, 0);

    for (y = 0; y < height; y++)
    {
       for (x = 0; x < width; x++)
       {
          picinfo->FastWritePix(img_bmap, x, y, color_index);
       }
       picinfo->FastWritePix(img_bmap, FBMP_FLUSH, 0, 0);
    }

 Arguments:
 bmap - bitmap to write to
 x    - x coordinate or
        FBMP_INIT (write initialization) or
        FBMP_FLUSH (row buffer flush)
 y    - y coordinate
 col  - pixel color index (pen)


 [3mChunkyToBMap [23m

 This field points to the function

    void ChunkyToBMap (UBYTE *pixbuf, struct BitMap *bmap, LONG offs);

 This low-level function is more efficient in writing to planar bitmaps than
 FastWritePix(). There are some restrictions in the number of pixels which
 can be written and their position. ChunkyToBMap() can only write exactly 32
 pixel at a time, and their horizontal position must be word-aligned, like
 in the following example:

    if ((width & 31) == 0)
    {
       for (y = 0; y < height; y++)
       {
          offs = img_bmap->BytesPerRow * y;
          for (lw = width / 32; lw > 0; --lw, pixbuf += 32, offs += 4)
          {
             picinfo->ChunkyToBMap(pixbuf, img_bmap, offs);
          }
       }
    }

 Arguments:
 pixbuf - pointer to 32 color indexes
 bmap   - bitmap to write to
 offs   - offset in the plane memory (must be an even number)


 [3mCommentToProjInfo [23m

 This field points to the function

    void CommentToProjInfo (UBYTE *buffer, struct ProjectInfo *pinfo);

 Some file formats do not provide for the separate storage of project
 information fields (author, copyright, annotation): two or more strings
 must be packed into a longer non-specific comment string. The string format
 is:

    "<author>string <(c)>string <note>string"

 where each piece of information is optional and may appear in any order. An
 unformatted string (not introduced by a <xxx> code) is considered an
 annotation string.

 This function parses such strings and stores the information in a
 ProjectInfo resource.

 Arguments:
 buffer - pointer to a formatted/unformatted string
 pinfo  - pointer to a ProjectInfo resource


 [3mProjInfoToComment [23m

 This field points to the function

    BOOL ProjInfoToComment (struct ProjectInfo *pinfo,
                            UBYTE *buffer, WORD maxsize,
                            BOOL do_auth, BOOL do_cpyr, BOOL do_note);

 The project information is translated into a formatted string (see
 CommentToProjInfo()). If the client program interface version is greater
 than 3, the ProjectInfoToComment() function should be used instead (by the
 client).

 Arguments:
 pinfo   - pointer to a ProjectInfo structure
 buffer  - destination string buffer
 maxsize - buffer size
 do_auth - if TRUE, the author string is included
 do_cpyr - if TRUE, the copyright string is included
 do_note - if TRUE, the annotation string is included

 Result:
 TRUE, if the information was successfully translated,
 FALSE otherwise (e.g. the supplied buffer was not big enough)


 [3mCryptKeyChar [23m

 This field points to the function

    UBYTE CryptKeyChar (BOOL reset);

 Each time this function is called a new encryption character is returned.
 Such codes are based on a user specified encryption key and can be combined
 (e.g. XORed) with the image data being encrypted/decrypted. When the
 supplied argument is TRUE, the encryption character sequence is restarted.

 Arguments:
 reset - if FALSE, an encryption character is returned,
         if TRUE, the encryption character sequence is restarted

 Result:
 an encryption character


 [3mCryptKeySign [23m

 This field points to the function

    WORD CryptKeySign (void);

 This function returns a 16 bit encryption signature, based on the
 user-specified encryption key. The signature can be stored in the first
 bytes of an encrypted file. When the file is read, the signature can be
 compared to the current signature: if they match, the key entered by the
 user is likely to be correct and the data can be successfully decrypted.

 Result:
 an encryption signature


 [3mPreviewRow [23m

 This field points to the function

    void PreviewRow (struct BitMap *bmap, WORD y);

 When the client program's preview screen is opened (the PictureInfo
 PreviewDepth is not 0), HAM or 24-bit data can be transferred to it with
 this function. The image must be transferred row by row, from top to
 bottom.

 Arguments:
 bmap - HAM or true color bitmap (source)
 y    - source bitmap row


 [3mCreateBitMap [23m

 This field points to the function

    struct BitMap *CreateBitMap (WORD width, WORD height, UBYTE depth,
                                 UWORD flags);

 This function allocates and initializes a bitmap structure and the
 associated resources. Unles a specific memory type flag is specified
 (CB_ANYMEM, CB_FASTMEM or CB_CHIPMEM), the software allocates whatever type
 of memory is supported by the virtual blitter library currently in use
 (e.g. Agnus Blitter, 68K or PowerPC).

 Arguments:
 width  - the bitmap width
 height - the bitmap height
 depth  - the bitmap depth (1..8 / 24)
 flags  - CB_CLEAR  : clear all the bitplane memory to 0
          CB_CLEAN  : clear the unused (rightmost) bitplane memory to 0
          CB_KEEPWB : do not use virtual memory or close the Workbench
                      screen to collect enough memory for the bitmap
          CB_ANYMEM : use fast (preferred) or chip memory bitplanes
                      (it is implicit for 24-bit bitmaps)
          CB_FASTMEM: use only fast memory for bitplanes
          CB_LONGW  : force the bitmap's BytesPerRow to a multiple of 4.
          CB_CHIPMEM: use only chip memory for bitplanes

 Result:
 a bitmap pointer, if successful,
 NULL otherwise


 [3mDeleteBitMap [23m

 This field points to the function

    void DeleteBitMap (struct BitMap *bmap);

 Free a bitmap structure and the allocated resources.

 Arguments:
 bmap - a bitmap created by CreateBitMap()


 [3mGetProjectInfo [23m (V4)

 This field points to the function

    UBYTE *GetProjectInfo (struct ProjectInfo *pinfo, WORD type);

 Starting with version 4 of the library interface, the ProjectInfo structure
 cannot be accessed directly. This function selectively reads a string
 (returning a pointer to it) from the project information.

 Arguments:
 pinfo - pointer to a ProjectInfo resource
 type  - piece of information to read:
         AUTHOR_INFO, COPYRIGHT_INFO or ANNOTATION_INFO

 Result:
 pointer to the desired string


 [3mSetProjectInfo [23m (V4)

 This field points to the function

    BOOL SetProjectInfo (struct ProjectInfo *pinfo, WORD type,
                         UBYTE *string);

 Starting with version 4 of the library interface, the ProjectInfo structure
 cannot be accessed directly. This function stores a string in the project
 information.

 Arguments:
 pinfo  - pointer to a ProjectInfo resource
 type   - piece of information to memorize:
          AUTHOR_INFO, COPYRIGHT_INFO or ANNOTATION_INFO
 string - the string to memorize

 Result:
 TRUE, if the string was successfully stored,
 FALSE otherwise (e.g. not enough memory)


 [3mProjectInfoToComment [23m (V4)

 This field points to the function

    BOOL ProjectInfoToComment (struct ProjectInfo *pinfo, UBYTE *buffer,
                               WORD maxsize, ULONG do_flags);

 This is the V4 equivalent of ProjInfoToComment() (see above).

 Arguments:
 pinfo    - pointer to a ProjectInfo structure
 buffer   - destination string buffer
 maxsize  - buffer size
 do_flags - a mix of the following flags:
            AUTHOR_INFOF (the author string is included)
            COPYRIGHT_INFOF (the copyright string is included)
            ANNOTATION_INFOF (the annotation string is included)

 Result:
 TRUE, if the information was successfully translated,
 FALSE otherwise (e.g. the supplied buffer was not big enough)


 [1mSample Library Code: The PBM Library[22m

 The PBM library is a typical file loading/saving library. Both true color
 and planar bitmaps can be loaded (the true color preview mechanism is also
 used): standard code to write data in such bitmaps is included. The library
 can only save planar bitmaps: due to the PBM file structure, the bitmap
 data is automatically converted to true color, grayscale or monochrome
 data, before being written to the file. The PBM library source code is
 simple enough to be used as a base for a new file loading/saving library.

 [1m
 Sample Library Code: The SView Library[22m

 [3m[The author of the "SuperView" system kindly requested that this sample be
 removed from this distribution. As a replacement sample of a "universal"
 library code, we are including the Datatypes loader.][23m

 The SView library code is more complex than the PBM code. Many functions
 just deal with the SView library system, while others deal with specific
 Personal I/O features: splitted file recognition, picture types defined at
 run time, loading and saving of DIF_CONVERTED images, etc. As mentioned
 above, splitted recognition is a technique required in those contexts
 (SView, DataType, etc.) where the only way to get the picture format is
 actually loading it. In such cases, the format information is given in two
 steps: the first one (low overhead) provides the file type information, the
 picture size is retrieved in the second step (high overhead - image
 loading).

 [3mImportant: [23mThe SView I/O code was developed when the "SuperView" system and
 its complete documentation were freely distributable, and implementations
 (including commercial ones) of compatibility interfaces were actively and
 expressly encouraged by the Author. It now appears that this policy is
 being changed. We therefore recommend to carefully study the instructions
 included with newer versions of the "SuperView" system in order to ensure
 both technical and legal compliance.


 [1mI/O Libraries Implementation: The Global Data Storage[22m

 The Personal I/O libraries usually contain global data: picture type
 tables, type option settings, etc. Some information (e.g. the option
 settings) should be client based: when two client programs (e.g. PPaint and
 ColorType) open an I/O library and set their options, no access conflict
 nor data overwriting should affect the operations (each program might use
 different option settings).

 The typical Personal I/O library implementation is based on a special SAS/C
 feature which allows automatic creation of global data copies: each library
 client just acts on its own copy of the library data. The "LIB:libinitr.o"
 library initialization module provides this special mechanism: it must be
 included in the linking process (see "smakefile" in the source directory).


 [1mLicensing[22m

 Ever since the development of the first I/O libraries, at Cloanto we have
 taken a very "liberal" approach over the release and distribution of new
 and enhanced libraries. Now that the libraries are fully documented, and
 that any third party has the technical information to develop new
 libraries, we would like to retain certain rights over certain steps. In
 particular, we would like to be in agreement with developers about library
 names, version numbers, picture type priorities, and about the fact that
 the release of a new library is constructive for all parties involved. We
 care a lot about the quality of each new library, and about the consistency
 of the complete set of libraries. The only way in which we can release the
 complete documentation on the I/O libraries and at the same time retain
 some control over its use, is by maintaining the client/library handshaking
 mechanism documented here, which uses our registered trademark. In order to
 use and distribute a library compliant with this specification, the use of
 the handshaking procedure must be licensed. Non-commercial licenses are
 usually concluded at no charge to the developer.


 [1mCopyright[22m

 This documentation and the accompanying files are Copyright © 1994-1996
 Cloanto Italia srl (Cloanto), unless otherwise indicated in the files or in
 the following notice. No part of this material may be reproduced,
 transmitted, transcribed, stored in a retrieval system, or translated into
 any language or computer language, in any form or by any means, optical,
 electronic, magnetic, biological, chemical, mechanical, acoustic, manual or
 otherwise without the prior written permission of Cloanto.


 [1mDisclaimer and Limitation of Liability[22m

 This documentation and the accompanying files are provided "as is", without
 warranty of any kind, either expressed or implied, statutory or otherwise.
 By using this material, you accept the entire risk as to its quality and
 performance.

 Neither Cloanto nor any other party involved in the creation, production or
 delivery of the documentation, software and data files shall be liable for
 any direct, indirect, special, consequential or incidental damages,
 including without limitation damages for loss of profits, loss of use or
 loss of anticipated costs, expenses or damages, and any data or information
 which may be lost or rendered inaccurate, even if Cloanto is advised of the
 possibility of such damages.


 [1mTrademarks[22m

 Cloanto and the Cloanto logo are registered trademarks, and ColorType,
 Personal Fonts Maker, PFM, Personal Paint, PPaint, Personal Write, PWrite,
 Personal Suite, PSuite and The Kara Collection are trademarks of Cloanto
 Italia srl. All other trademarks, property of their respective owners, are
 acknowledged.