$VER: SHELTER DOC Mailer Manager Installation & Operation  Williamson 2.75

    This  is  the  documentation  for  the  Shelter  Mailers Manager.  This
program  controls  the  operation  of  the  Umbrella,  Gazebo, and Porticus
Shelter  Mailers.   It  can  also  be  used  with  the  ROOF mailer, but is
redundant  as  all  operations  are  available in the various ROOF Function
Hosts.   All  Shelter  Mailers  have the same set of commands, although the
options may be different.

    Shelter.TXT or shelternnn.readme discusses the features of each mailer.
Use this as a guide to choose which mailer meets your needs.

    GenMailer.DOC  discusses  the  configuration of each mailer.  Read this
carefully,  as  errors  in your configuration could cause the mailer not to
work, or may even cause a system exception.

    Extras.DOC  describes  some  the  various  utilities  included  in  the
distribution.

    XPACK.DOC descibes the various xferq utilities included for advanced
users.

    NOTE:   the  word <SHELTER> is used in place of the particular mailer's
name thoughout the remainder of this document.

    Installation and Configuration:
        
        Click  on  Install-GenMailer,  making sure beforehand that you have
Installer  in  SYS:utilities.   This  will  create  S:GenMailer-Startup and
modify  your  S:User-Startup  to  execute  it.   GenMailer-Startup  creates
assigns,  directories, paths, Mounts NEWAUX:  and NULL:  devices and starts
up Arexx, Loading and Rxlib'ing required libraries.

    If  your  Startup-Sequence executes RexxMast or executes a script which
does,  comment  it  out.  GenMailer-Startup will execute RexxMast AFTER all
ASSIGNS  and PATHS are defined, so that Arexx will be able to find programs
it calls.  This requirement is the same situation that exists with LoadWB.

    These   are   the   files  you  must  edit.   See  GenMailer.DOC  for
explanations.
        cfg:wpl/gen/<SHELTER>/GEN.cfg           - mailer config
        cfg:wpl/gen/<SHELTER>/CACHE.cfg         - site cache config
        cfg:wpl/gen/<SHELTER>/modems/MODEM?.cfg - modem and line configs 
        cfg:wpl/gen/<SHELTER>SCREEN.cfg         - public screen config

    See GenMailer.doc for keyword desciptions.
            
    Procedure:
        Edit GEN.cfg with your site info.
        Edit cache.cfg for sites you call regularly.
        Edit MODEM?.CFG for your serial device, port and modem.
            Note that Roof and Porticus use modem configs 2 and up,
            because 1 is reserved for internal uses.

    Execute:
    (Use RX xxxx if you do not have the compiled versions)
  
    >GENMAILER <SHELTER> options

                    - path defaults to CFG:WPL/GEN/<MAILER>
                      carefully observe any ERROR or WARNINGS
                      GenMailer will EXIT on an ERROR. WARNINGS indicate
                      that  a  parameter is incorrect or missing, it will
                      be ignored or a default will be used.

     NOTE:   There is no checking for MISSING keywords
             in either Cache.cfg or Modem?.CFG

    >SHELTER START


    Polling and Dialing with SCALL:

    >RUN >NIL: (RX) SCALL <site> [phonenumber|line] [line]
    
    An alias simplifies the command line.
        ALIAS DIAL "Run >NIL: Rx SCALL " 

       Usage: Scall Site_Address/A,LINE/K,NUMBER/K,
                    HAND/K,PRO/K,
                    PRI/K,REDIALDELAY/K,DURATION/K,CRASH/S,NOPICKUP/S

       Site_Address    FTN-  [domain#][z:][net/]node[.p] CLOCK- clock<n>
                       UUCP- uu<site> FAX- fax_<site> BBS- bbs_<site>

       Number          phone number when manual dialing

       Line            modem line to use for dialing
           DEFAULT DEF_LINE

       Hand            desired handshake to use, comma separated
           DEFAULT DEF_LINE, available FTS,WAZOO,EMSI,FAST"

       Pro             desired emsi protocols, comma separated
           DEFAULT DEF_LINE, available DEF_LINE
                       This effective for current dial session ONLY 

       Pri             task priority for poll
           DEFAULT -1

       RedialDelay     number of seconds to wait between dials
           DEFAULT 180

       Duration        number of minutes to attempt connection
           DEFAULT 60

   Switches
       crash           send crash mail only
       nopickup        do not accept inbound files

    If  site  is  not  in  the  Cache,  you  must provide the phone number.
SHELTER  MAILERS will expand addresses based upon your own default address.
This  mean  that  if you are, for example, fidonet#1:167/104.99, you simply
type:

    SCALL 104  -  to call your boss.
    or 
    SCALL 151   - to call fidonet#1:167/151.0

    Shelter  will  allow  the  slave to dial with the 'REDIALDELAY' seconds
delay  between  attempts.   This is defined in the Mailer configuration but
can be changed on the Scall command line (redialdelay=n" The total duration
of the redial attempts to get through will be limited to the period defined
by  'CALLWINDOWMIN'  or  by  a 'duration=n' on the command line.  This is a
POLL window.
    The  number of seconds of REDIALDELAY and BUSYDELAY may also be changed
DURING a poll, using "RXSET variablename seconds", but this will not affect
polls  where  a  new value was specified on the commad line.  The number of
minutes  of the CALLWINDOWMIN can also be changed but only PRIOR to a poll,
changing it during a poll will have no effect.
    If  the  variable 'IGNORENOANSWER' is set, dial will not abort when the
called node does not answer (very common in the case of an IBM-based HUB.)

    Calling UUCP sites:
        
    SCALL uu<sitename>

        sitename may be a Cached uucp site alias or a FQDA (Fully Qualified
Domain Address)

    Calling Atomic Clock sites:

    SCALL CLOCK[?]

        CLOCK[?]  is  the  sitename  specified  in the Cache.  Atomic Clock
sites MUST be Cached.
        

    AUTO MODE:

        An  AUTO  mode  is included which will start up the Mailer, convert
any  .FLO  files  found  and  call  the  defined BOSS site.  In the case of
Umbrella, it will then exit.  For security purposes, the directory in which
the  ?LO files are placed by the external program should NOT be the same as
your outbound directory.


    SHELTER Mailer Manager usage:

       Usage: SHELTER <command> <options>
           START       - load mailer
           EXIT        - unload mailer
           RESTART     - unload, recompile and reload mailer
           AUTO        - startup, flo convert and call BOSS/HUB

           POLL        - Call all sites with pending mail 
                         If  priority  specified,  only sites with priority
                         equal or greater will be called. NORM, DIRECT, CRASH

           CALL        - start a site poll
                         [domain#][z:][net/]node[.p] [ (phonenumber|line ) | line ]

                         expansion is done based upon our address

           KILL        - abort a site poll 
                         [domain#][z:][net/]node[.p]
                         expansion is done based upon our address

           FLOCVT      - Converts 4D .?LO files entries to Xfreq.  FLOCVT
                         function will also scan and add any remaining
                         ?UT  files  to  queue.   .OUT  files  will be
                         ignored, as these should be echomail which is
                         waiting  to  be  archived.  CUT, DUT, NUT and
                         HUT will be added according to priority.
                         NOTE:   there  is an internal switch to allow
                         FLOCVT  to queue .OUT files.  You may need to
                         set  this  to  1  if your tosser creates .OUT
                         files  instead  of .NUT files for NORMAL mail
                         or  does  not create .NUT, .CUT, DUT, .HUT at
                         all..

           ADDWORK site fullfilename (disposition priority)
                       - Add a file to the queue of a site 
                         if file is *.?UT then it will be send as a *.PKT
                         with disposition=D and priority 50
                         if file is ARCmail, sendas name will be created
                         Priority may also be specified as text:
                         HOLD, NORM, DIRECT, CRASH
           CLEAN       - removes non-existing files from queue.
  
           These two commands are used internally by the mailer.
           OPENSTATUS  - open mailer GUI
           CLOSESTATUS - close mailer GUI


    The Mailer Display:

        Each  Mailer line has an addressable display which is controlled by
LOGPROC.  LOGPROC is an Arexx Function Host by Alan Kelms.

    Title Bar contains 6 or 7 fields:
    Mailer Name, Version, Port Name, Serial Device, Serial Unit, Modem Name
                                                                [Locked Rate]

    The field descriptions:

        Status:     Current status of the line
        Response:   Last event or modem response
        Baud:       Baud rate of the last connect
        Number:     Phone number of last connect
        Password:   DEFFERED|CACHE|LOOKUP and  SENT|OK|BAD|NONE
        Session:    Type WAZOO|EMSI|LOGIN|UUCP|HUMAN|BBS|FAX|etc
                    After the Session, duration is displayed in hh:m:ss
        Protocol:   File transfer protocol

        Login:      Username (and command) or remote site mailer/version
        H_Adr:      Current host address, 
                    this may be different during a session
        R_Adr:      Remote address (primary if EMSI)
        Sysop:      Remote sysop's name and sitename
        H_Ofr:      Wazoo/Emsi offer to remote
        R_Ofr:      Wazoo/Emsi offer from remote

        H_Freqs:    TRUE|FALSE, 
                    indicates if we will accept a file request
        R_Freqs:    TRUE|FALSE
                    indicates if remote will accept a file request
                    request is not sent if host will not accept it
        Inbound:    SECURE|NONSECURE|USER|UUCP|FAX
                    Indicates inbound security type.
        Domain:     Indicates remote domain when remote provides it

                    (Note:   when  the  remote does not provide a Domain,
                    the  Shelter  Mailer  AUTOAKA  feature  will  try  to
                    determine the correct one, or use the default domain.


    External Control via AmigaDOS scripts:

    S:?boot     - a script that will set a wpl variable to boot a human 
                  caller when he is at a menu prompt.

    External Control via Environmental Variables:

    You may set the following ENV:  variables TRUE or FALSE directly or via
a  cron  event to enable or disable the feature.  The variable will only be
effective if the feature is present in the mailer.

    NOANSWER    - if TRUE, a RING will be IGNORED and phone will not
                  be answered 
                  DEFAULT:  FALSE
                  LOCATION: ENV:<SHELTER>/
  
    ACCESS      - if TRUE, will allow user access, BBS spawning, Menus
                  and WPLRX Utilities for human callers
                  DEFAULT:   TRUE
                  LOCATION: ENV:<SHELTER>/

    BBS         - if TRUE, and ACCESS TRUE, selected bbs is spawned
                  This will allow you to selectively disable BBS spawning,
                  while still allow user access to other features. 
                      eg: ACCESS TRUE and BBS FALSE  
                  DEFAULT:  TRUE
                  LOCATION: ENV:<SHELTER>/

    ALLOWFREQS  - if TRUE inbound file requests will be processed
                  DEFAULT: TRUE
                  LOCATION: ENV:<SHELTER>/

    FTSFREQS    - if TRUE, , and ALLOWFREQS is TRUE, inbound file requests 
                  received during FTS1 sessions will be processed 
                  DEFAULT:  FALSE
                  LOCATION: ENV:<SHELTER>/

    UUCP        - if TRUE, accept inbound uucp calls
                  DEFAULT:  set by UUCP keyword
                  LOCATION: ENV:<SHELTER>/

    FAX         - if TRUE, accept inbound fax calls
                  DEFAULT: set by FAX keyword
                  LOCATION: ENV:<SHELTER>/

    

    During  ZMH, you should set ACCESS and BBS FALSE, and if you wish, UUCP
and  FAX  FALSE  also.   A FULLY compliant FidoNet system would set ALL the
above FALSE (except NOANSWER, of course :)


    External Control via CLipList Variables:

    You  may  set  the following clip variables directly (using RXSET) or
via  a  cron  event  to  change  the  value.   The  variable will only be
effective if the feature is present in the mailer.

    CALLWINDOWMIN   duration of a call window in minutes
    REDIALDELAY     delay  in  seconds to wait between dials on BUSY
                    response
    BUSYDELAY       delay  in  seconds  to wait between dials on SLAVE
                    DIALING  response
    IGNORENOANSWER  TRUE|FALSE Treat a no answer same as busy 


    Direct control via ARexx:

    It is possible to change the value of many variables while the mailer
is active.  One method is as follows: (example for GAZEBO)
        Rx 'Address GAZEBO1 Set umh "05:00 06:00"'

    A  ROOF utility, Irexx.rexx (freqable name) is an interactive arexx/wpl
interpreter which allows easy access.

    Cron:

    CyberCron  v1.5  or better is HIGHLY recommended as your event handler.
It  features  an  arexx port and named event queues which make it ideal for
the  Shelter  Mailer  environment.  I use CyberCron heavly in ROOF and have
nothing but praise for this program.  Unlike others, it is source-released,
so even if the original author abandons it, others may continue suport.


    Adding Files to the queue:

    WPL  mailers  do not use the .FLO flat file format due to the collision
and  security  problems associated with that method.  Xferq.library manages
the outbound queue.
    The  SHELTER  MAILERS  MANAGER  includes  two  functions:   FLOCVT  and
ADDWORK, which should remove the necessity of external utilities.

    There  are,  however,  a  number  of  powerful  utilities to manage the
outbound queue included.

    Xpack       -   5D echomail archiver/router/queuer/scheduler    *
    XList       -   lists queue for a site, a pattern or all sites  *
    Xkill       -   remove a filepattern from a sitepattern         *
    Xrmv        -   remove a file from a site queue
    AddWork     -   add a file to a site queue, aware of filetypes
    SendFile    -   a simple version of AddWork
    Xq          -   FLO convert, scan outs, Xpack front-end
    Xflo        -   online flo conversion

        The above are also included in the freqable archive: XPACK.LHA


    Using terminal programs:
    
    WPL Mailers support OwnDevUnit.library, making the use of term programs
that also support this standard quite trivial.


                           DISTRIBUTION

    The  compiler  of  the  CAM  disks refused to even consider this freely
available archive.
    Therefor,  inclusion  of  any part of this archive on a CAM DISK, or on
the CAM/RCS BBS is STRICTLY FORBIDDEN.
    If you have obtained this archive from one of these sources, there will
be NO support.

    Registration:
        Please  send  netmail  or  email  to one of the following addresses
indicating  the  Shelter  mailer  and versions of the Manager and Genmailer
that you are using..
                        Yup..that's it!

    Support:
        via netmail:
            FidoNet#1:167/104.0
            AmigaNet#40:600/104.0

        via echos:
            WELMAT @ FIDONET
            COMMS_AMY @ AMIGANET
            comp.sys.amiga.datacomm @ USENET
            tpg.ml.wpl.application @ MTLNET
            WPL_APP @ FIDONET

        via InterNet:
            robert@ecs.mtlnet.org
            bobw@amigaecs.1choice.login.qc.ca

            User support mailing list:  
                wpl-application@alfred.ccs.carleton.ca
            Requests to join the list:
                wpl-application-request@alfred.ccs.carleton.ca
 
        Support Echo:
            ROOF_PROJECT @ FIDONET#1:167/151.0 (Zyxel)
            ROOF_PROJECT @ FIDONET#1:167/104.0 (v42bis)

    Thanks  to  Matthew  Mondor and Yanik Grignon for their invaluable Beta
Testing  of  the  SHELTER  MAILERS  and GenMailer.  Also thanks to Frederic
Morin,  Denis Turcotte, Yanik and the many others who have contributed over
the years to the ROOF PROJECT, making the Shelter Mailers possible.

    Beta Testers:
        Porticus
            Len Lekx            FidoNet#1:250/701.2
            Kenneth Bartlett    FidoNet#1:291/37.0
            Matthew Mondor      FidoNet#1:167/104.2 
            Mike Manning        Fidonet#1:229/326.0

        Gazebo
            Yanik Grignon       FidoNet#1:167/207.0
            Matthew Mondor      FidoNet#1:167/104.2 
            Mike Manning        Fidonet#1:229/326.0

       Umbrella
            Matthew Mondor      FidoNet#1:167/104.2 

        Xpack/Xq
            Denis Turcotte      FidoNet#1:167/151.0

        RoofLOG
            Denis Turcotte      FidoNet#1:167/151.0

    The  above  are  those  who have made the effort to contact me with bug
reports and enhancement requests...thanks to all of you.