HOW TO WRITE SERVER PROGRAMS

SERVERS are run on demand by the DNET device driver.	This is
accomplished by DNET doing a LoadSeg() and CreatProc().  The server
CANNOT GO THROUGH A NORMAL STARTUP for several reasons:

	(1) There is no CLI and the message passed over the process
	    port is DNET specific (NOT a workbench message)

	(2) Registers contain garbage (no argument line)

	(3) No standard file handles exist


For AZTEC C, this is accomplished by overiding the standard _main with
your own.  You must then setup the listen port and wait/reply the startup
message from DNET.  See the source (for example, SERVER/STERM.C) for
an example.

The server can exit at any time after it DUnListen()'s the port.  Multiple
DNET's will all use the same server for a specific port #.

_main()
{
    struct Message *msg;
    long mask, pmask, hdmask;
    PROC *proc = FindTask(NULL);

    Enable_Abort = 0;
    LisPort= DListen(PORT_IALPHATERM);
    WaitPort(&proc->pr_MsgPort);
    ReplyMsg(GetMsg(&proc->pr_MsgPort));
    if (!LisPort)
	exit(1);

	    ...