ALARMCLOCK ACCESSORY


The Micro-Time AlarmClock accessory consists of the following 
files:

ALARMCLK.ACC
COLORCLK.RSC
MONO_CLK.RSC
ALARMCLK.DAT

In order for the AlarmClock accessory to work properly with your 
monitor, you must have either the COLORCLK.RSC (for color monitors) 
or the MONO_CLK.RSC (for monochrome monitors) on the same disk as 
the ALARMCLK.ACC file.

When these files are put on your boot disk, the AlarmClock 
accessory will be properly installed and can be selected from the 
Desk dropdown menu.

When selected, the AlarmClock accessory will open up a window on 
your screen. It is divided into three parts:

Corner Clock
Alarms
Today's Time & Date

Corner Clock
This will allow you to turn ON/OFF the digital clock, which will 
be displayed in the upper right hand corner of the screen. You 
also have the choice between 12 and 24 hour display format of the 
clock.

Alarms
This section will allow you to set up to 5 alarms, which can be 
used as reminders when you are using the computer.  To set an 
alarm, click on an alarm number, click alarm status to ON, and set 
the Alarm Time & Date.  Then enter in an alarm message that you 
want to be displayed when the alarm goes off.  When an alarm goes 
off, a bell will sound and the alert box will open and show you 
your message. Pressing return will make the alert box disappear.

If you are not in a GEM program, you will only hear the alarm 
bell. Returning to the desktop will bring up the alert box with 
its message.

NOTE: Time, Date and _M will allow you to use the "?" character as 
      a wild card. Here is an example:

      Alarm Time:   ??:00:00 ?M
      Alarm Date:   ??-??-??

      In this example, an alarm would go off every hour, both
      AM & PM, of every day, month, and year.

Today's Time & Date
This section allows you to set the current Time and Date.  After 
you are finished, click on DONE with the mouse or just press 
RETURN.  The computer's Time & Date will now be set and your 
Corner Clock will be displayed, if selected ON, as well as any of 
your alarms. If you click on SAVE, a file will be saved to drive A 
or C, which will contain the current settings of the Corner Clock 
and the Alarms.  This file, ALARMCLK.DAT will be loaded into your 
computer on boot up.



&Ü&ÔIù(z&Ü&”"9†0<ÈNB09 ÜGùº6üJ6ü6ü6ü6¼Gù