Storm VT100/VT102 terminal emulation

Features:
    Graphics character set (line drawing)
    Double-width, double-height characters
    Text effects include bold, underline, inverse. (Blinking effect displayed
    as 'light' characters).

Detailed specifications.

Note: Columns and rows are numbered starting at row 1, column 1 in the upper
left corner.

Note: In the following table, 'Pn' indicates a numeric parameter. Numeric
parameters are simply Ascii numbers that are used to modify the effect of
an escape sequence. e.g. specify how many columns the cursor is to move.

If multiple numeric parameters are sent, they are separated by a semicolon.
The absence of a parameter means a default value is assumed.

Scrolling regions: Under software control, a host computer can set up a
region of lines as a 'scrolling region'. Control characters and escape
sequences that normally cause the entire screen to scroll up or down will
cause only the area of the scrolling regions to scroll up or down instead.

Character(s)    Effect

5       ENQ. Terminal replies with Answerback string. To add an
        answerback string, you need to edit the STORM.INI file to
        add an entry in [VT100] of the form:
        Answerback="string"
        You could also use the Basic command SET
        e.g. SET "STORM","VT100","Answerback","string"
        The answerback string is limited to 80 characters.

        Note that answerback is disabled if the CompuServe BPLUS.TRF
        file transfer module is loaded because ENQ is required for
        B-PLUS file transfers.

7       Bell. Causes a bell sound, if it's enabled by your system
        setup. This is controlled by the control panel usually.

8       Backspace. Moves the cursor to the previous column. No action
        taken if the cursor is already in column 1. Backspaces are
        non-destructive in VT100, though that can be overridden by
        selecting "BS Erases" in the generic Terminal setup dialog.

9        Tabs to the next tab stop. Default tab stops are every 8 columns,
        starting at column 9. Tab stops can be set and cleared by the
        host computer by sending the appropriate escape sequences.

10       Line Feed. Causes the cursor to move to the next line. If the
        cursor is already at the bottom of the screen or scrolling
        region, scrolls the screen upwards. 'New Line' mode, if set,
        causes the cursor to move to column 1 when a line feed occurs,
        simulating the effect of a carriage return.

11
12        Generate line feeds.

13      Carriage return. Causes the cursor to move to column 1 on the
        current line. A separate setting in the generic Terminal
        setup dialog can add a line feed to all carriage returns
        received, though that is not really a part of the VT100
        emulation.

14      Shift Out. Selects 'G1' character set. Specific
        escape sequences (described later) allow you to specify what
        character set is used as the G1 character set.

15      Shift In. Selects 'G0' character set. G0 character set can
        be altered by escape sequences (described later)

27 (ESC)The escape character introduces an escape sequence, which is
        used to control many terminal features.


ESC [   CSI or Control String Introducer. Consists of the ESC
        (Ascii 27) followed by a left square bracket. Indicates the
        start of a category of escape sequences.

ESC D   Index. Moves the cursor to the next line, scrolling the screen
        up if necessary.

ESC E   Next Line. Equivalent in effect to a Carriage Return + Line
        Feed combination. Moves the cursor to the start of the next
        line, scrolling the screen up if necessary.

ESC M   Reverse Index. Moves the cursor to the previous line, scrolling
        the screen down if necessary.

ESC H   Sets a tab stop at the current cursor location.

ESC 7   Saves the currrent cursor location, character set, and text
        effects for later restoring via the cursor restore sequence.

ESC 8   Restores a cursor state saved by a previous ESC 7 sequence.

ESC =   Sets Application Keypad mode. Causes the numeric keypad on the
        ST to send special escape sequences that can be interpreted
        by a host program.

ESC >   Resets keypad to normal numeric mode.

ESC c   Resets the terminal to default settings. i.e. whatever settings
        you selected in the setup dialog box.


ESC [ Pn @  Inserts the number of characters specified by the numeric
            parameter at the current cursor location. Characters at the
            end of the line are lost.

ESC [ Pn A  Moves the cursor up by the number of rows specified by the
            numeric parameter. The cursor will not move above the top of
            the screen or the top line of a scrolling region.

ESC [ Pn B  Moves the cursor down by the number of rows specified by the
            numeric parameter. The cursor will not move above the bottom of
            the screen or the top line of a scrolling region.

ESC [ Pn C  Moves the cursor right by the number of columns specified by
            the numeric parameter. Will not move past the end of the line.

ESC [ Pn D  Moves the cursor right by the number of columns specified by
            the numeric parameter. Will not move past the end of the line.

ESC [ Pn E  Moves the cursor down, as with ESC [ Pn B, but the cursor is
            always repositioned to column 1.

ESC [ Pn F  Moves the cursor up, as with ESC [ Pn A, but the cursor is
            always repositioned to column 1.

ESC [ Pn G  Cursor Horizontal Absolute. Moves the cursor to the column
            specified by the numeric parameter.


ESC [ Pn;Pn H  Position Cursor. Moves the cursor to the specified row and
ESC [ Pn;Pn f  column. The first number is the row, the second number is the
               column. Default if a parameter is absent is row/column 1.
               When relative origin mode is in effect (discussed later) then
               the cursor row is calculated relative to the top of the
               scrolling region.

ESC [ 0 J    Clears from the current cursor location to the end of the
ESC [ J      screen. Does not move the cursor.

ESC [ 1 J    Clears from the start of the screen to the current cursor
             location. Does not move the cursor.

ESC [ 2 J    Clears the entire screen. Does not move the cursor.

ESC [ K      Clears from the current cursor location to the end of the line.
ESC [ 0 K    Does not move the cursor.

ESC [ 1 K    Clears from the start of the line to the cursor location. Does
             not move the cursor.

ESC [ 2 K    Clears the entire line that the cursor is on. Does not move the
             cursor.

ESC [ Pn L   Insert Line. Inserts Pn blank lines at the current cursor
             location and scrolls the rest of the screen (or scrolling
             region) down.

ESC [ Pn M   Delete Line. Deletes Pn lines at the current cursor location
             and scrolls the rest of the screen (or scrolling region) up.

ESC [ Pn P   Delete Character. Deletes Pn characters at the current cursor
             location and shifts the line to fill in the space. Blank
             characters are placed at the end of the line when characters
             are deleted.

ESC [ Pn X   Erase Character. Erases Pn characters at the current cursor
             location.

ESC [ c      Report Device Attributes. Responds by transmitting an escape
ESC [ 0 c    sequence identifying the terminal. The default response is
             "ESC[?6;2c", which is a VT102 response. This reponse can be
             changed by inserting a line in the [VT100] section of the
             STORM.INI file with the heading ID="(Replacement ID)".
             e.g. ID="\33[1;2c" would change the reponse to a VT100 type
             response.


ESC [ g      Clear Column Tab. Clears the tab stop (if any) at the cursor
ESC [ 0g     location.

ESC [ 3 g    Clear All Column Tabs. Clears all tab stops.

ESC [ Pn h   Sets various terminal modes detailed below. Note that more
             than one mode can be set if multiple parameters are sent.

ESC [ 4 h    Set Insert mode. Subsequent characters are inserted at the
             current cursor location and the rest of the line is scrolled
             over to. Characters at the end of the line are lost.

ESC [ 12 h   Set Local Echo. Turns half duplex on.

ESC [ 20 h   Set Newline mode. Causes received Line Feed characters
             (Ascii 10) to also move the cursor to the start of the line.

ESC [ Pn l   Resets the various terminal modes detailed above. Reverses the
             effect of the corresponding ESC [ Pn h escape sequence. Note:
             'l' is a lowercase L, not the number one '1'.

ESC [ 4 l    Set Replace mode. Subsequent characters overwrite.

ESC [ 12 l   Resets local echo. Turns full duplex on.

ESC [ 20 l   Resets Newline mode.

ESC [ Pn m   Sets/resets various character attributes used in subsequent
             terminal output. Multiple parameters allow the setting of
             more than one attribute in the same escape sequence.

ESC [ m
ESC [ 0 m    No attributes. Turns all attributes off.

ESC [ 1 m    Set Bold attribute.

ESC [ 4 m    Set Underlined attribute.

ESC [ 5 m    Set Blinking attribute. Instead of the characters actually
             blinking, this attribute is indicated by printing 'light'
             characters.

ESC [ 7 m    Set Reversed attribute. Subsequent characters are displayed in
             reverse video.

ESC [ 22 m   Turn Bold attribute off.

ESC [ 24 m   Turn Underlined attribute off.

ESC [ 25 m   Turn Blinking attribute off.
ESC [ 27 m   Turn Reversed attribute off.

ESC [ 5 n    Report Terminal Status. Emulator responds by sending ESC [ 0 n

ESC [ 6 n    Report Cursor Location. Emulator responds by sending an
             escape sequence reporting the current cursor location.

ESC [ Pn;Pn r  Set Scrolling region. The first parameter is the top of the
               scrolling region, the second is the bottom. Also causes the
               cursor to move to location 1,1 (either top of the scrolling
               region or top of the screen, depending on origin mode).

ESC [r       Resets the scrolling region to full screen.
ESC [0;0r

ESC ( 0      Sets the G0 character set as the Graphics character set.

ESC ( 1      Sets the G0 character set as the Alternate ROM character set.
             This is not currently supported by the emulator, mostly to
             save memory. However, it could easily be added.

ESC ( 2      Sets the G0 character set as the Alternate ROM graphics set.
             This is also not currently supported by the emulator.

ESC ( A      Sets the G0 character set as the UK character set. The only
             change is that '#' is replaced by the UK Pound Sterling
             symbol.

ESC ( B      Sets the G0 character set as the ASCII character set. This is
             the default character set.

ESC ) 0      Perform the same functions as the corresponding ESC ) escape
ESC ) 1      sequences, but affect the G1 character set instead.
ESC ) 2
ESC ) A
ESC ) B

ESC # 5      Set character width single on current line.

ESC # 6      Set double character width on current line.

ESC # 3      Set double-width/double-height character display on current
             line. Displays the top half of each character as double-height
             and double width. Used in conjunction with ESC # 4 to display
             a line of double-height, double-width characters.

ESC # 4      Set double-width/double-height character display on current
             line. Displays the bottom half of each character as
             double-height and double-width.

ESC # :      Sets double-height character display on current line. Displays
             the top half of each character double-height;

ESC # ;      Sets double-height character display on current line. Displays
             the bottom half of each character double-height;

ESC [ ? Pn h Sets various extended terminal modes described below. Multiple
             modes can be set if more than one parameter is sent.

ESC [ ? 1 h  Set cursor key Application mode. Causes the cursor keys to
             send escape sequences which can be interpreted by a host
             computer.

ESC [ ? 3 h  Sets 132 column mode. Currently not supported.

ESC [ ? 4 h  Sets Smooth Scroll. Not implemented.

ESC [ ? 5 h  Sets Reverse Screen. Toggles output to white characters on a
        black background. Note that Storm uses white and black by
        default. However you can set different colors for fore and
        back colors by inserting entries in the [Terminal] section
        of the STORM.INI file. The default entries are
             Fore=1
             Back=0
        which set foreground to black, background to white. The digits
        are GEM color indexes as detailed in the following table:
        The number of colors supported depends on video mode. The
        actual color that appears depends on how you have setup the
        color palette. Setting reverse screen simply swaps foreground
        and background colors.
        This feature has not been testing on the Falcon or TT.

        Index    Color
        ===============
        0    White
        1    Black
        2    Red
        3    Green
        4    Blue
        5    Cyan
        6    Yellow
        7    Magenta
        8    White
        9    Black
        10    Light Red
        11    Light Green
        12    Light Blue
        13    Light Cyan
        14    Light Yellow
        15    Light Magenta
        16 or greater is device dependant.

ESC [ ? 6 h  Set Relative Origin Mode. Cursor positioning commands in
             Relative Origin mode are relative to the top of the scrolling
             region (if any) rather than the top of the screen.

ESC [ ? 7 h  Set Line Wrap. When line wrap is set, typing a character at
             the end of a row will cause the cursor to move to the start
             of the next line.

ESC [ ? Pn l Resets verious extended terminal modes. Has opposite effect
             of corresponding Esc [ ? Pn h setting.

ESC [ ? 1 l  Resets cursor keys to normal mode.
ESC [ ? 2 l  Set VT52 Mode. This will cause the emulator to switch to
             emulating a VT52 terminal. To return from VT52, use the
             sequence ESC < from within VT52 emulation.

ESC [ ? 3 l  Set 80 column mode. Since the emulator doesn't yet support
             132 column mode, this has no effect.

ESC [ ? 4 l  Set Jump Scroll. Since smooth scroll is not supported, this
             has no effect.

ESC [ ? 5 l  Set Normal Screen. Restores normal foreground and background
             colors.

ESC [ ? 6 l  Reset Origin Mode. Restores absolute cursor origin mode.

ESC [ ? 7 l  Reset Line Wrap. When entering characters, the cursor will
             not automatically wrap to the next line.

ESC [ ? 15 n Report Local Printer Status. No printer support at present.
             The emulator responds with "ESC ? 13 n" to indicate that
             no printer is present.

Other VT100 Info

    The VT100 default settings are saved in the STORM.INI file in a section
labelled [VT100]. The entry Reset=00000000000 contains the settings. Each
digit is a VT100 setting. Most settings are either 0 or 1. A few have
larger ranges The settings are (in order)
    Digit = 1            Digit = 0
=================================================
    Keypad Application Mode    Keypad Numeric Mode
    Cursor Application Mode    Normal Cursor Mode
    Relative Origin Mode    Absolute Origin Mode
    Insert Mode            Overwrite Mode
    New Line Mode Set        New Line Mode Reset
    -----------------
    G0 (can range from 0 to 3)
    G1 (can range from 0 to 3)
    Current Selected Set. 0 or 1 at present, indicating G0 (0) or G1 (1). In
future this could change to 0 to 3 if support for four character sets is
added.
    -----------------
    Line Wrap On        Line Wrap Off
    Destructive Backspace    Non-Destructive Backspace
    ReverseVideo        Normal Video

Note that this includes extra settings not available from the setup dialog.
When the ESC c sequence is received and the terminal is reset, these values
are used in resetting the terminal. This is useful if you want a particular
setup to be retained when the terminal is reset. e.g. keypad application mode
to remain set.


I should note that Line Wrap, Destructive Backspace, and Reverse Video are
actually part of the general terminal setup. They are included here in order
to be able to override the general terminal settings when resetting the
VT100 terminal. When you use the VT100 setup dialog, the current state of
these three settings are automatically saved in the VT100 Reset setting.

Note: Setting the VT100 New Line mode alters the general terminal settings to
set Add Linefeeds Inbound in addition to the VT100 New Line setting. If you
have New Line selected in VT100, but Add Linefeeds Inbound is not selected
in the general terminal setup, then loading VT100 will automatically set
Add Linefeeds Inbound.