NETWORK V1.0

                  AC ELECTRONIC CIRCUIT ANALYSIS PROGRAM























                  Configured for the IBM by:         Bruce A. Trolli
                                                         
                                                         

                  Converted to ST by Mammoth
















                                        1






        1.0) GENERAL

                NETWORK  outputs  the ac frequency reponse for a user 
            described  electronic  circuit.  The circuit  description  is 
            prepared  as  an  input  text  file  containing  a  two  line 
            specification   for  each  element  in   the   circuit.   The 
            specification  of  each element requires the user  to  assign 
            node  numbers  to each node in the circuit.  This  method  is 
            similar  to  many  commercially  available  circuit  analysis 
            programs.

                  When  NETWORK is run,  it builds a matrix from  the 
            user's circuit description file and evaluates the output node 
            voltage at each frequency under the assumption that the input 
            node has a 1 volt signal with zero phase angle applied to it.

                  At run time the user may specify the  frequencies to be 
            calculated  as  either a linearly or  logarithmically  spaced 
            interval.  Output  is  sent to the screen by default  but  an 
            optional output datafile may be specified at runtime.

                  Models   are   provided  for   Resistors,   Capacitors, 
            Inductors,  Bipolar  transistors (current controlled  current 
            sources),  Fets  (voltage  controlled  current  sources,  and 
            Opamps (voltage controlled voltage sources).





























                                        2





            2.0) ACKNOWLEDGEMENTS

                  Network  is  an adaptation of an  existing  circuit 
            analysis  program  to  run on  the  IBM  PC.   The  origional 
            article:  "Verify Network Frequency Response With This Simple 
            Basic Program",  Werner A. Schnider, EDN magazine, October 5, 
            1977,   was  written  for  a Hewlett  Packard  9830A  desktop 
            calculator. 

                  The  program  was  modified to run on an Apple  II  and 
            reappeared  in  the  magazine  as:  "Basic  Program  Performs 
            Circuit   Analysis",   Richard  Steincross,   EDN   magazine, 
            September 1,  1982. This version expanded the capabilities of 
            the  program  by  adding inductors to  the  network  elements 
            supported.  It  also  allowed the user to specify  input  and 
            output nodes at run time.  After testing this program, I have 
            removed  this  feature because it did  not  produce  reliable 
            output for a number of simple circuits.





































                                        3





            3.0) REQUIREMENTS

            NETWORK  requires a single disk drive. 
                  Because the program output has been limited to text, it 
            can  run  with either the monochrome or  color  adapter.  The 
            input  and output formats have purposely been kept simple  to 
            allow  most  systems to run the  program.  (Besides,  I  have 
            enough  problems making programs print the correct answer let 
            alone print it on a jazzed up screen.) 








































                                        4






            4.0) RUNNING THE PROGRAM


            4.1) Number the nodes     

                  To analyze your circuit, it will be necessary to number 
            the nodes on your schematic diagram.  These node numbers will 
            be  used to prepare a precise description of the  circuit  so 
            that NETWORK can construct the circuits network equations.

                  The  input  node must be node number 1 and  the  output 
            node must be the highest node in the circuit.

                  AC  ground is node 0.  The 1 volt input that is applied 
            to node number 1 is referenced to node 0.


            4.2) Prepare Input File

                  Prepare   a  text  file  that  contains  a   two   line 
            description   for  each  circuit  element  according  to  the 
            definitions below. Note that comments may be added after the
            element  type so that the origional reference designations of 
            your circuit's schematic may be retained as part of the input 
            file.  This should make it easy to go back and forth  between 
            your schematic and the input file.

                  Also  comments may be added anywhere in the input  file 
            by placing a ";" at the beginning of the line.


             Resistors:

                  R              
                  from node, to node, value (in ohms)

                       Example:  A 1000 ohm resistor between nodes 1 and 2.


                       R
                       1,2,1000

                                 
             Capacitors:
                  C
                  from  node,  to node,value(in micro farads)

                       Example: A 10 uf capacitor between nodes 3 and 6.

                       C
                       3,6,10



                                        5





             Inductors:

                  L
                  from node, to node, value (in henries)


             Fets: 

                  F
                  gate node,  source node,  drain node,  transconductance
                                                           (amps/volt)
                                 
                  Example: A common source fet with 10 mmhos transconductance.
                            
                       F           
                       2,0,4,.01

             Bipolar Transistors:

                  B
                  base node, emitter node, collector node, beta, b-e resistance 
                                                                 (ohms)

                  Example: Emitter follower with beta=100
                  
                       B
                       3,4,0,100,.001


                                                Bruce  Trolli

                                                Cleveland RBBS
                                                (216-3310510)

               



























                                        9
-3310510)