==============
                    FONTS and GDOS
                    ==============

            (c) zzSoft 1989, all rights reserved 




For use with the ATARI ST program EASY TEXT+.

Companion file to the EASY TEXT+ tutorial.


This file details some of the tecniques and methods of using GDOS 
fonts, and the ASSIGN.SYS file.

Please note that your EASY TEXT+ disk is directly usuable. You do 
not need to know any of the following information in order to use 
EASY TEXT+ properly. This file is for the benfit of people who 
wish to alter their ASSIGN.SYS file; use different fonts; use a 
different printer driver etc.


     It is essential that GDOS.PRG (in the folder called AUTO)
     is in Drive A at program boot up.  If it is not a warning  
     message will be issued by EASY TEXT+ informing you that 
     you must boot with GDOS in an AUTO folder. You should not 
     directly run GDOS.PRG by double- clicking on it.

     Hard disk users may have configured their disk to auto boot 
     from there. This is ok.

     Also it is essential that the ASSIGN.SYS file is on the same 
     disk as the GDOS.PRG.  The ASSIGN.SYS file lets you specify
     what GDOS fonts can be loaded and used by EASY TEXT+.  This 
     is not peculiar to EASY TEXT+, it is the usual method used by 
     DTP and art programs, eg Degas Elite.

     You also need the FONTS folder on the same disk, or on the 
     disk pointed to by the path statement at the head of the 
     ASSIGN.SYS file. The fonts folder contains the actual fonts 
     used by EASY TEXT+. The FONTS folder contains GDOS screen 
     fonts, printer fonts, and the printer driver, eg FX80.SYS.

                    ----------------
     If  GDOS  is successfully installed at boot-up then a message  
should come onto your screen (top left-hand corner) for a short 
period of time before you are returned to the ST's desktop. The 
message should read:

       ATARI GDOS Ver. 1.1 resident. 

If, however, GDOS was not installed other messages will appear
briefly on the screen,  for example telling you that the 
ASSIGN.SYS  file contains an illegal workstation, ETC. You must 
correct this problem before you can use EASY TEXT+.
                    ---------------

     
     To  modify the ASSIGN.SYS file so that diferent fonts may be 
     loaded other than the ones already specified in the file, you 
     have to modify the file. This is acheived by loading the 
     ASSIGN.SYS file  into First Word and then turning off Word 
     Processing (WP Mode - top of the EDIT menu). The file can 
     then be modified to your purposes.

     To change the printer driver you neeed only place the 
     appropriate driver in the FONTS folder and change the name 
     of the driver at 21, in the ASSIGN.SYS file.

     As an example an ASSIGN.SYS file could contain the following 
     text:
     

path=A:\FONTS
;
01p  screen.sys          ;Default screen 
;
02p  screen.sys          ;Low-resolution screen
;
03p  screen.sys          ;Medium-resolution screen    
;
04p  screen.sys          ;High-resolution screen
;
COURIE10.FNT
COURIE14.FNT
COURIE18.FNT
COURIE28.FNT
COURIE36.FNT
;
21 FX80.SYS         ; EPSON FX80 and compatibles
EPSON_10.FNT        
EPSON_14.FNT
EPSON_18.FNT
EPSON_28.FNT
EPSON_36.FNT

     Note that this file does not specify any med res screen 
     fonts, therefore no GDOS fonts will be available for use in 
     medium reolution. 

     Do not leave a blank space in the ASSIGN.SYS file between the 
     font names as this will cause the remainder of font names  in 
     the file to be ignored. Eg do not do this:

     COMPUT16.FNT
     COMPUT18.FNT
     
     COMPUT28.FNT        
     
     You  should  not give any GDOS fonts a name starting  with  a 
     number, eg 42NDST.FNT. This will cause GDOS not to be installed.
     In all events check your ASSIGN.SYS file carefully.

     To  use the fonts you want substitute the new font names  for 
     the  present ones,  or alternatively include your new  choice 
     of fonts with the present ones.  Then save the new ASSIGN.SYS 
     file and place on your working disk with the other files  and 
     EASY TEXT program. Only have one ASSIGN.SYS file on your copy 
     working  disk.

     Replace the fonts in the FONTS folder by the fonts specified 
     in the ASSIGN.SYS file.

     If you want to keep your FONTS folder on another disk you 
     should  alter the path statement in the ASSIGN.SYS file eg
     Path = C:\FONTS

     You may call the folder what you will, so long as the name 
     in the ASSIGN.SYS file corresponds with it.

     Note that the ';' used in an ASSIGN.SYS file is there so that 
     comments  can be  placed in the file.  Any text on the same line
     as  a  ';' and  placed  after  it will be  ignored  by  GDOS, 
     which  is occasionally useful.  

 
     To Summarise

     (a) You need  ASSIGN.SYS, the AUTO folder containing GDOS.PRG,
     on your boot disk, and the FONTS folder on the disk pointed 
     to by the Path statement in the ASSIGN.SYS file.
  
        
FONTS                
     
     Note that all fonts are loaded at start-up if there is enough 
     RAM,  If there is not enough RAM to accommodate all the fonts 
     NO   fonts will be  loaded at all OR only some.  This is  why 
     the PARAMETERS selection in the OPTIONS menu is so useful. It 
     allows you to determine exactly how many fonts to place in an 
     ASSIGN.SYS file.

     It  is possible to have many different ASSIGN.SYS  files,  by 
     naming  them  slightly differently from  ASSIGN.SYS.  So  you 
     could  have 4 different ASSIGN.SYS files  called  ASSIGN.SY1, 
     ASSIGN.SY2,  ASSIGN.SY3 and the one you are using at start-up 
     ASSIGN.SYS. By having different combinations of fonts in each 
     ASSIGN.SYS file it is possible at start-up time by  correctly 
     renaming  any one of the other three files to ASSIGN.SYS  and 
     renaming the other now unwanted ASSIGN.SYS to some other name  
     to load different font styles. 

     -------------------------------------------------------------
     Always  reboot the computer if you change the ASSIGN.SYS FILE, 
     or use a different printer driver.
     ------------------------------------------------------------- 

     Selecting  a font size that is not available results in the 
     next smaller size being used.

     Note that you must have the correct printer fonts for the 
     EASY TEXT+ print program to operate correctly. Having only 
     screen fonts is not sufficient, although it is perfectly 
     possible to use different printer fonts when printing to 
     get different print styles.

     The software allows you to have a screen font half the 
     printer font size. So, if you have a screen font 18 points 
     high it is only necessary to have a printer font 9 points 
     high to reproduce the screen font on your printer as the 
     print program will double-up the printer font for you. This 
     useful feature saves time and space.

* end of file