06601030305800
F0110030
9[...................................................]001
€************************************************************************
*                                                                      *
*         DigiTape Effect Module Construction Kit                      *
*         ---------------------------------------                      *
*                                                                      *
*           How to build loadable Modules for                          *
*                 DigiTape Release 2.0                                 *
*                   7. Juli 1993                                       *
*                                                                      *
************************************************************************

DigiTape unterst�tzt ab der Version 1.03  freie Effektmodule.

Das heižt, daž jeder, der sich zu einem bižchen C- und 
etwas mehr DSP-Assembler-Programmierung in der Lage sieht, 
nachladbare Module mit Klageffekten erstellen kann, die in 
DigiTape eingebunden werden.

Wir stellen anbei-Entwicklerinformationen �ber das Softwareinterface
und die Verbindung zu DigiTape zur Verf�gung.

Weitere Informationen, die ben”tigt werden, finden sich im 
Motorola Entwicklerhandbuch zum DSP 56k sowie im Falcon 
Entwicklerkit von Atari, das Sie bei Atari Computer GmbH in
Schwalbach bestellen k”nnen.

Beachten Sie bitte die Artikelserie "DSP-Programierung" in der
ST Comuter, Heim Verlag.

Weiterhin m”chten wir auf eine Artikelserie mit dem Titel
"Klangwunder" in der Zeitschrift c't verweisen, die auf 
Soundprogrammierung f�r den DSP 56k / Falcon 030 
gezielt eingeht:

"Klangwunder" in c't Heise Verlag, Heft  9/93 S. 226ff
                                   Heft 10/93 S. 212ff
                                   Heft 11/93 S. 260ff


External Digitape modules contain DSP56000 code, GEM Recources and the
user-interface code in one file. The modules are loadable from within the
Digitape desktop and can be handled like interanal ones. If an external
module is used together with a recording, it is automatically loaded
next time the recording tape is opened.

As an Example we supply a complete module wich implements a reverb effect:

Sourcefiles:
-------------
resource:      HALL.RSC
               HALL.H
               HALL.DFN

DSP assembler: HALL.ASM
€
User interface:HALL.C
               DT_DEFIN.H
               DT_LOCAL.H

projectfiles:  HALL.PRJ
               MAKEFILE

Tools:
------
You need:      C Programming Environment
               Resource Construction Set
               DSP56000 Assembler
               (a Make Programm, not nessesary but simplifies the calls
               the other tools)

We supply:     CLN_TO_D.TTP   builds a C source file out of a DSP
                              assembler object file.
                              HALL.CLN becomes HALL.D and HALL.DH.

               RSC_TO_C.TTP   GEM resource to C converter.
                              HALL.RSC becomes HALL.R

Building procedure:
-------

      *---------------*       *----------*  *----------*  *-----------*
      |   HALL.ASM    |       | HALL.RSC |  |  HALL.H  |  | HALL.C    |
      |               |       |          |  |          |  |           |
      | DSP assembler |       |   GEM    |  | resource |  |  C file   |
      |   source      |       | resource |  |  defines |  | interface |
      *---------------*       *----------*  *----------*  *-----------*
              |                     |             |             |
              V                     V             |             |
      =================    ==================     |             |
      = ASM56000.TTP  =    = RSC_TO_C.TTP   =     |             |
      = DSP assembler =    =   resource     =     --------> #include
      =               =    =   converter    =                   |
      =================    ==================                   |
              |                     |                           |
              V                     V                           |
      *---------------*      *-------------*                    |
      |   HALL.CLN    |      |   HALL.R    |                    |
      |               |      |             |                    |
      |  DSP object   |      |  resource   |                    |
      |               |      | as C source |                    |
      *---------------*      *-------------*                    |
              |                     |                           |
              V                     |                           |
     ===================            |                           |
     =  CLN_TO_D.TTP   =            |                           |
     =  convert tool   =            ----------------------> #include
     =                 =                                        |
     ===================                                        |
€         |          |                                           |
         V          V                                           |
*-------------*  *-------------*                                |
|   HALL.D    |  |   HALL.DH   |                                |
|             |  |             |                                |
| DSP object  |  | DSP defines |                                |
| as C source |  | as C source |                                |
*-------------*  *-------------*                                |
       |                |                                       |
       |                ----------------------------------> #include
       |                                                        |
       ---------------------------------------------------> #include
                                                                |
                           DT_DEFIN.H --------------------> #include
                                                                |
                           DT_LOCAL.H --------------------> #include
                                                                |
                                                                V
                                             =========================
                                             =  C-Compiler & Linker  =
                                             =     Make HALL.PRJ     =
                                             =                       =
                                             =========================
                                                         |
                                                         V
                                               *------------------*
                                               |*----------------*|
                                               ||   HALL.DTM     ||
                                               ||                ||
                                               || DigiTape-Module||
                                               |*----------------*|
                                               *------------------*



A few restrictions to your DSP code:
------------------------------------

Identifiers have to be at most 7 characters long.

ORG-Directives are not permitted.

Calculations in Directtives are not permitted.
Example:  move  X1,X:DATUM   ; OK
          move  X1,X:DATUM+1 ; not OK

Modules should return with RTS.

Access to L-Memory (X- and Y-Memory together) is not permitted.

Following registers are used internally and you should absolutely
NOT use them within your code: R3,M3,N3

Registers M0-M2 and M4-M7 have to contain 0xFFFF after each module call,
€that means, if you change them, set them back to $FFFF

All other registers are at your disposal.