A d l i b   D o o r
                            -------------------
                          by Shvat Shaked, VS inc.
                                 Ver. 1.00
                                 25.2.1992

            ___________________________________________________
            samples playing driver for the Adlib and Adlib Gold


Revision 1.1 : 4.6.1992 by Shvat Shaked

This package contains:

     ADL.EXE     - The executable
     ADL.DOC     - This file
     MP.CHG      - Command file for DEBUG. See below.
     MP219.BAT   - Batch file for using MP v2.19 with AdLib. See below.
     MP219.ADD   - Command file for MP219.BAT. See below.


What it does?

     After running, Adlib Door will turn the lower 6 bits of port 0389H
     into a door to the Adlib card. This will allow you to play samples
     by outputing them to this port. It will also allow you to use some
     programs like MODPLAY or SCREAM TRACKER, after making some easy
     changes in them.


How to use it?

     The sytax of the executable program ADL.EXE is as follows:

     > ADL /ON : installs Adlib Door
     > ADL /OFF : Unistalls Adlib Door

     The second function is not available for UNREGISTERED users.


And technically ...

     Adlib Door is not a TSR (Terminate and Stay Resident) program. It
     will not take any memory, and it takes only 5Kb on disk. Its only
     purpose is to put ten to twelve words into the control ports of
     the Adlib card. You certainly think that I could write a 100 bytes
     assembly program that does that ... so be sure I couldn't. The
     complexity of the timing needed to write something to the Adlib
     forced me to use Turbo Pascal to right the program. To play a
     sample just take its HIGHER 6 bits and output them into the LOWER
     6 bits of port 0389H (905 Decimal). You can output the sample in
     any speed.


Using Scream Tracker v2.2

     To use ST you have step the following:

     1. Make sure you have DEBUG or SYMDEB in your path.
     2. Run ST.
     3. Choose Other/Setup and set:
        Output Device - Covox LPT1
        Playing Speed - To fit your computer speed
        Enable Timer  - No
     4. Choose Save Setup
     5. Press Ctrl+D for Dos Shell
     6. Check in what segment the ST is (in DOS 5 you can do it by
        typing > MEM /P).
     7. Type the following:

        > ADL /ON
        > DEBUG or SYMDEB

     Next, type the following by changing seg to the correct segment:

        - RCSseg
        - A65F1
          MOV DX,0389H
          SHR AL,1
          SHR AL,1
          OUT DX,AL
          JMP 65A8
          <ENTER>
        - A65A3
          JMP 65F1
          <ENTER>
        - Q

     Back in the DOS prompt, type:

        > EXIT

     7. Now load a song, a module or an Amiga module and play it.
     8. Have Fun!


Using MODPLAY v1.12

     The steps needed to use MP contain two parts. The first part has
     to be done one time, and will make a program called MP1. The
     second part has to be done anytime you want to run the MP.

     First part (for one time running!):

     1. Make sure you have DEBUG or SYMDEB in your path.
     2. From DOS prompt, type:

        > DEBUG MP.COM < MP.CHG

     This will produce a program called MP1.COM. Any action concerning
     the Adlib card must be done on this program, and this program
     only!

     Second part (everytime you run):

     1. From DOS prompt, type:

        > ADL /ON
        > MP1 /6 /i  (the 'i' must be lowercase!)

     2. Choose a module, and play.


Using MODPLAY Pro. v2.19 (and v2.19b)

     It is very easy to change the MP v2.19 to run any kind of hardware
     product. I'm doing it by adding some assembler statements to the
     MODPLAY.CFG (the MP configuration file). The things YOU have to do
     follows:

     1. Copy the files MP219.BAT and MP219.ADD to your MODPLAY
        directory. For example:

        > COPY MP219.* C:\MODPLAY

     2. In your MODPLAY directory, run the MP219.BAT by typing:

        > MP219

     3. Don't forget to run ADL.EXE anytime you want to use the adlib.
        Because it isn't a TSR program, you can run it through your
        AUTOEXEC.BAT.

     4. That's it. Now run the MP the way you always did. It will play
        the modules through your Adlib. Note that because the new MP
        playes in stereo, and I mix the two channels myself, some of the
        quality of the sound is lost. Next time buy Adlib-Gold 2000 or
        a Sound Blaster...

        For example:

        > ADL /ON
        > MP


And what now ?!

     If you find this program fine, fun, or thin, please, register it
     by sending a minimal fee of 12 NIS (5 U.S dollars) to the address
     below. Registration will make you able to turn off the noisy card
     and on the other hand, will make ME more glad, happy, merry,
     joyful but not rich. Questions, answers, bug reports, suggestions
     and other vegetables should be left for me on FIDONET (NET 401) or
     in one of the following BBSs:

     The Small BBS   +972-2-634-203
     The C.I.A BBS   +972-2-785-038

     InterNet address:

     lando@brachot.jct.ac.il
     (It is not mine, but of a friend. Put my name on the mail).
     
                                  My address:

                                        Shvat Shaked
                                        Shimoni 54, Jerusalem
                                        92630, Israel
                                        Tel. +972-2-781510


                      ### End of Original Documention ###