і Gravis Ultrasound Tech Specs і
                    АДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДЩ
                           The Unofficial Dox

                         Written December, 1992
                By Tran of Renaissance and Joshua Jensen

OK, folks, here it is.  This is the programming information that Gravis
didn't and won't give you any time soon.  These dox have been obtained
through long hours of debug sessions and experimentation.

Let's clear up some things that have been debated in comp.sys.ibm.pc.soundcard
for quit sometime now:

  ю The GUS can play 32 mono samples at once, fully pannable through 16
    different positions.

  ю This is still a bit unclear.  The SDK says that samples have to be
    32-byte aligned in memory.  I've been following this.  Maybe that is
    not the case, though, and I haven't tested it.

Credits:  Tran came up with the initial information about programming the
card.  Josh documented it and included actual assembly language information
in this archive on how it works.  It's relatively simple, but some things are
unclear and are explained here in the dox and in the code.

ДДДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Methods і
ДДДДДДДДЩ
@DELAY = (in byte 300h)*7

Description:  All this function does is give a short idle wait for the card
              to do whatever processing it needs to.
ДДДДДДДДДДДДДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Probe Ultra Sound і
ДДДДДДДДДДДДДДДДДДЩ
  out BASE+103h, 4Ch
  out BASE+105h, 0
  @DELAY
  @DELAY
  out BASE+103h, 4Ch
  out BASE+105h, 1
  Poke Data Byte   Loc:   0h, Byte: AA    ; Don't think this HAS to be an AA.
  Poke Data Byte   Loc: 100h, Byte: 55    ; Don't think this is needed.
  Peek Data Byte   Loc:   0h
  Store Byte
  out BASE+103h, 4Ch
  out BASE+105h, 0
  Restore Byte
  Is it AA?  If so, then we have found a GUS.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДД
Test for amount of memory installed on UltraSound і
ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДЩ
  Poke Data Byte   Loc: 40000h, Byte: AA
  Peek Data Byte   Loc: 40000h
  Is it an AA?  If not, then there is 256k of DRAM.  Exit.
  Poke Data Byte   Loc: 80000h, Byte: AA
  Peek Data Byte   Loc: 80000h
  Is it an AA?  If not, then there is 512k of DRAM.  Exit.
  Poke Data Byte   Loc: C0000h, Byte: AA
  Peek Data Byte   Loc: C0000h
  Is it an AA?  If not, then there is 768k of DRAM.  Exit.
  Poke Data Byte   Loc: 0FFFFFh, Byte: AA
  Peek Data Byte   Loc: 0FFFFFh
  Is it an AA?  If not, then there is 1024k of DRAM.  Exit.

Description:  Poke these bytes on the boundaries of 256k, 512k, 768k, and
              1024k.  If the memory isn't there, then it won't return what
              is poked.
ДДДДДДДДДДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Peek Data Byte і
ДДДДДДДДДДДДДДДЩ
  out BASE+103h, 43h
  out BASE+104h, low word address
  out BASE+103h, 44h
  out BASE+105h, high byte address
  in  BASE+107h, INBYTE

Description:  The card's memory can be from 00000h to fffffh.  INBYTE is the
              byte value returned from the card that was at that memory
              location.
ДДДДДДДДДДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Poke Data Byte і
ДДДДДДДДДДДДДДДЩ
  out BASE+103h, 43h
  out BASE+104h, low word address
  out BASE+103h, 44h
  out BASE+105h, high byte address
  out BASE+107h, OUTBYTE
ДДДДДДДДДДДДДДДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Set Voice Frequency і
ДДДДДДДДДДДДДДДДДДДДЩ
  out BASE+102h, voice number
  out BASE+103h, 1
  out BASE+104h, word frequency number (actual frequency / 19.0579083837)

Description:  Tran thought he'd give you the exact value :)  Dividing by 19
              will give enough accuracy for the task, though.
ДДДДДДДДДДДДДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Set Voice Balance і
ДДДДДДДДДДДДДДДДДДЩ
  out BASE+102h, voice number
  out BASE+103h, 0ch
  out BASE+105h, byte balance (0-0fh)

Description: The Balance byte can range from 0 to 15.  0 is far left,
             15 is far right, and 7 is right in the middle.
ДДДДДДДДДДДДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Set Voice Volume і
ДДДДДДДДДДДДДДДДДЩ
  out BASE+102h, voice number
  out BASE+103h, 9
  out BASE+104h, word volume value (0-0ffffh, log ... not linear)
ДДДДДДДДДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Set Loop Mode і
ДДДДДДДДДДДДДДЩ
  out BASE+102h, voice number
  out BASE+103h, 80h
  in  BASE+105h, TEMP
  out BASE+103h, 0
  out BASE+105h, (TEMP & 0e7h) or MODE

Description:  This is not really necessary.  Actually, the Set Loop Mode and
              Stop Voice Immediately could be one function.
ДДДДДДДДДДДДДДДДДДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Stop Voice Immediately і
ДДДДДДДДДДДДДДДДДДДДДДДЩ
  out BASE+102h, voice number
  out BASE+103h, 80h
  in  BASE+105h, TEMP
  out BASE+103h, 0
  out BASE+105h, (TEMP & 0dfh) | 3
  @DELAY
  out BASE+103h, 0
  out BASE+105h, (TEMP & 0dfh) | 3

Description:  Dunno why the extra delay and duplicated code is there.
ДДДДДДДДДДДДДДДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Start Voice Playing і
ДДДДДДДДДДДДДДДДДДДДЩ
  out BASE+102h, voice number
  out BASE+103h, 0ah
  out BASE+104h, word BEGIN >> 7
  out BASE+103h, 0bh
  out BASE+104h, word BEGIN << 9
  out BASE+103h, 2
  out BASE+104h, word START >> 7
  out BASE+103h, 3
  out BASE+104h, word START << 9
  out BASE+103h, 4
  out BASE+104h, word END >> 7
  out BASE+103h, 5
  out BASE+104h, word END << 9
  out BASE+103h, 0
  out BASE+105h, MODE & 0fch

ДДДДДДДДДДДДДДДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Read Voice Location і
ДДДДДДДДДДДДДДДДДДДДЩ
  out BASE+102h, voice number
  out BASE+103h, 8ah
; in  BASE+104h, low byte TEMP0
; in  BASE+105h, high byte TEMP0
  in  BASE+104h, word TEMP0
  out BASE+103h, 8bh
; in  BASE+104h, low byte TEMP1
; in  BASE+105h, high byte TEMP1
  in  BASE+104h, word TEMP1

    LOC = ((TEMP0 << 7) | (TEMP1 >> 9)) & 0xfffff

Note: Word read at BASE+104h seems to work same as sequential byte reads
      from BASE+104h then BASE+105h.
ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД

ДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Ports і As you can see, there are a lot of blanks to be filled.  Hope Gravis
ДДДДДДЩ will take a hint soon.

BASE - write only, mix control
ЪДДДВДДДВДДДВДДДВДДДВДДДВДДДВДДДї
і 7 і 6 і 5 і 4 і 3 і 2 і 1 і 0 і
АДВДБДВДБДВДБДВДБДВДБДВДБДВДБДВДЩ
  ?   ?   ?   ?   ?   і   і   і
                      і   і   А 0 = Line in on.  1 = Line in off.
                      і   АДДДД 0 = Output on.   1 = Output off.
                      АДДДДДДДД 0 = Mic in off.  1 = Mic in on.   ???

BASE+102h - Active voice select (byte port)

BASE+103h - command port (byte port)
  Bitmap so far:
  ЪДДДВДДДВДДДВДДДВДДДВДДДВДДДВДДДї
  і 7 і 6 і 5 і 4 і 3 і 2 і 1 і 0 і
  АДВДБДВДБДВДБДВДБДВДБДВДБДВДБДВДЩ
    і   і   ?   ?   і   і   і   і
    і   і           і   і   і   і
    і   і           і   і   АДДДґ
    і   і           і   АДДДДДДДЕ Command for voice
    і   і           АДДДДДДДДДДДЩ
    і   АДДДДДДДДДДДДДДДДДДДДДДДД Command for card.
    АДДДДДДДДДДДДДДДДДДДДДДДДДДДД Read from voice.

   0h - write voice mode (loop and data type)           - byte on 105h
  ЪДДДВДДДВДДДВДДДВДДДВДДДВДДДВДДДї
  і 7 і 6 і 5 і 4 і 3 і 2 і 1 і 0 і     Designated as MODE through dox
  АДВДБДВДБДВДБДВДБДВДБДВДБДВДБДВДЩ
    ?   ?   ?   і   і   і   і   і
                і   і   і   і   А Voice On/Off (If both set to 0, voice on.)
                і   і   і   АДДДД Voice On/Off (If both set to 1, voice off.)
                і   і   АДДДДДДДД 0 = 8 bit data.  1 = 16 bit data.
                і   АДДДДДДДДДДДД 0 = No loop.     1 = Loop Sample.
                АДДДДДДДДДДДДДДДД 0 = Go forward.  1 = Go backward.
   1h - voice frequency                                 - word on 104h
   2h - loop start location / 80h                       - word on 104h
   3h - loop start location << 9                        - word on 104h
   4h - loop end location / 80h                         - word on 104h
   5h - loop end location << 9                          - word on 104h
   9h - voice volume                                    - word on 104h
  0ah - voice location / 80h                            - word on 104h
  0bh - voice location << 9                             - word on 104h
  0ch - voice balance                                   - byte on 105h
  0eh - Unsure.  Has something to do with turning       - byte on 105h
          stereo on and off.  See U_Reset for an
          example of usage.
  43h - low word of DRAM address                        - word on 104h
  44h - high byte of DRAM address                       - byte on 105h
  4Ch - Unsure exactly of what this does                - byte on 105h
          However, a 1 must be output to BASE+105h for
          the card to do memory writes.  At least, that's
          the only way I could get it to work.
  80h - read voice mode                                 - byte on 105h
  8ah - read voice location                             - bytes on 104h, 105h
  8bh - read voice location                             - bytes on 104h, 105h

Notes:  Any >= 80h plus a number might be the read mode of the value - 80h.
        In other words, to read the voice volume (this is untested), you'd
        output an 89h through BASE+103h and then read BASE+105h.

BASE+104h - word writes/reads
BASE+105h - byte writes/reads

ДДДДДДВДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
Notes і
ДДДДДДЩ
To stop an instrument when the sample ends (not immediately), change its
loop type to 'no loop'.

If you are making a lot of changes to just ONE voice, the
OUT BASE+102h, Channel needs only to be done once.