FMPCM - Intercept FM to PCM TSR


Syntax

        fmpcm -i                 

		to install as a TSR set of FMPCM routines

        fmpcm -h                 

		to display more information

        fmpcm -l [command]       

		to load the ISR, run command, then unload

        fmpcm -s                 

		to display status on the TSR

        fmpcm -u                 

		to unload the TSR

	fmpcm -iv#           

		to install and intercept voice number "#"


Operation

Use this program in conjunction with "pcmfun.com" and "fm.com" 
(or "sound.com").

This program intercepts the "Direct Note On" function (13h) for
interrupt 65h (the FM TSR), and routes it to the Special Function
8016h (simulate double-shift-key) of interrupt 94h (the PCM TSR).

Care must be taken in the order of installation of interrupt 
vectors, as the FM TSR reprograms the timer, which can cause early
termination of timing-dependent programs.  The correct ordering
is as follows:

	pcmfun
	fm
	fmpcm

A typical sequence would be to load the pcmfun.com TSR, load sounds
into channels 1 through 96, load the fm.com TSR, then load the 
fmpcm.com TSR.  Then, use "playrol.exe" to play fm sounds, and the
notes for instrument 0 will be routed through the PCM TSR.

	--- bat file ---
	pcmfun -i
	setdma -x
	loadpcm %dmabuf% 16
	loadpcm x *.wav
	fm -i
	fmpcm -i
	----------------