FM - TSR for FM Synthesis


Syntax

	fm -i

		This installs the TSR

	fm -u

		This uninstalls the TSR

	bo
	bf

		This turns on/off the "background" sound

	qo
	qf

		This turns on/off the "queue"

	mm
	mp

		This sets melodic/percussive mode

	i65

		This initializes the TSR and the chip


Operation

	
This program is used to provide "Adlib" (copyright/trademark Adlib
something-or-other) functionality for programs using that format
to play FM sounds.

	Basically, this format is a method for "queueing" notes
	and setting "instrument sounds".  See "fm.doc" for information
	on programming the TSR to accomplish this.

This program will also generate "random" notes, in the background,
which can be interesting, pleasing, or weird.  


Program Explanations

fm.com	- This program installs into interrupt 64h to provide the
	queue services, and interrupt 08h (timer) for background
	events.

	Use "-i" to install the TSR.
	Use "-u" to uninstall the TSR.
	Use "-s" to report installation status.

bo.com	- This program will turn on the "background" sounds.
bf.com	- This program will turn off the "background" sounds.

	I use this (sometimes) when:

	playing a game without sound
	programming late at night by myself

		these alleviate boredom, and sometimes provide
		an interesting diversion

	executing a long process that may crash

		if the sounds continue, the system has not 
		"halted", and may just have "echo off" or
		needs the "mode" set...

	need a source of sound input for testing recording abilities

		I get sick of my own voice, or the CDROM is too slow

qo.com	- This program will turn "on" the queue processing
qf.com	- This program will turn "off" the queue processing

	This process will "speed up" or "slow down" the hardware
	timer (interrupt 08h).  When the queue is on, the timer
	runs fast.

	Some "jukebox" programs do not reset the timer when they
	stop playing, and if they are then "removed" from memory
	the timer is running fast, so your DOS time is sped up.

	Use "qf" to reset the timer to normal speed before removing
	the TSR, especially after using programs that require the TSR.

mm.com	- This program will set "melodic" mode.
mp.com	- This program will set "percussive" mode.

	Use these programs to change the TSR and the chip to either
	of the two modes.

	If "background" sounds are enabled, the "drum set" will be
	heard after using "mp".

i65.com	- This program initializes the TSR and the chip.

	This will clear the queue and reset the chip, essentially
	setting the state to that of load-time.