WINDOWS DRIVER UPDATE
                            Aug 17, 1992
                          Version 1.4 BETA        


This is the latest release of improved Windows drivers for the Pro
AudioSpectrum family of audio cards from Media Vision.  Media Vision
will continue to do testing, bug-fixing, and enhancements.

We recommend that you make a backup of your existing drivers before
using the ones provided with this release.  If you discover any
further bugs, please notify us via CompuServe ID 75300,2772.

WARNING:  The powerful nature of Media Vision's Windows drivers exceed
          the ability of Windows' Control Panel Driver Installation 
          applet.  We have provided SETUP.EXE to automate the
          installation process.  We strongly recommend that you
          use SETUP to install the drivers.  

          If you are comfortable with editing system.ini yourself,
          you may wish to install the drivers manually.

          If you insist on using the control panel to install, use
          the following procedure:        


TO INSTALL USING THE CONTROL PANEL APPLET:

  1) From Windows, run the Control Panel's drivers applet.

  2) Click on the Add button.

  2 1/2) Now would be a good time to add the [MCI] CD Audio driver if
     you have a CD
                                       
  3) Select 'Unlisted or Updated Driver'

  4) Select browse and find the directory where the new drivers are

  5) Select the appropriate WAVE/MIDI/AUX driver for your hardware.
     (This will cause all other drivers for your hardware to load as
     well)  Allow the system to overwrite per-existing drivers.

  6) Restart Windows




TO INSTALL USING THE MEDIA VISION SETUP UTILITY:


  1) Insert the Windows Drivers Disk.

  2) CD to the drive that contains that disk

  3) Type WIN SETUP



TO INSTALL WINDOWS DRIVERS MANUALLY:

  1) Copy *.drv, *.dll, *.cfg and *.386 from the Windows drivers disk
     to the \WINDOWS\SYSTEM directory.

  2) Copy *.exe from the Windows drivers disk to the \WINDOWS directory.

  3) Make the following changes to your system.ini file:

     [386Enh]
     device=*vdmad            <-- make sure this line is first (Win 3.1 only)
     device=vpasd.386         <--- add this line for PAS PLUS, 16 or CDPC
     dmabuffersize=64         <--- add this line 
     device=vadlibd.386       <-- remove this entry if you have it        
     device=vsbd.386          <-- remove this entry if you have it        
     device=vtbd.386          <--  add this line for ThunderBoard

     [mci]
     WaveAudio=mciwave.drv 9  <--- should already be there
     Sequencer=mciseq.drv     <--- should already be there
     CDAudio=mcicda.drv       <--- should already be there
     mixer=mcimixer.drv       <--------- add this line
     
     [drivers]
     timer=timer.drv
     midimapper=midimap.drv
     midi=opl3.drv            <--- for PAS Plus, PAS 16 and CDPC only
     midi=mvfm.drv            <--- add this if you have the original PAS
     midi=adlib.drv           <--- add this for ThunderBoard or Thunder 
                                   & Lightning
     midi1=mvproaud.drv       <--- add this line 
     Wave=mvproaud.drv        <--- add this line for PAS Plus, 16 or CDPC
     Wave=tbwave.drv          <--- add this line for ThunderBoard only
     Wave=tlwave.drv          <--- add this line for Thunder & Ligtning only
     Mixer=mvmixer.drv        <--- add this line 
     aux=mvproaud.drv         <--- add this line 
     Wave1=sbwave.drv         <--- for PAS 16 only (adds 2nd wave driver)
        

     Also you must add the following line to system.ini's
     [mvproaud.drv] section:
 
     buffer=32

  4) Add the following executeables to your Windows desktop:
     PMIX.EXE, PREC.EXE, PROMIX.EXE, MIX.EXE        


GENERAL NOTES

  1) Central Point's BACKUP and PCTOOLS 7.1 are reported to be
     installing their own VDMAD.386 over the Windows 3.1.
     Central Point's VDMAD.386 has the wrong version number and will
     prevent mvproaud.drv from loading. 

  2) After changing one or more MIDI drivers, check the control
     panel's MIDImapper applet.  Channels 1 thru 10 should be patched
     to the MIDI interface and channels 13 thru 16 should be patched
     to the on-board synthesizer (MVFM.DRV or OPL3.DRV

     When playing 'Old Style' MIDI files (not General MIDI) use
     the Vintage MIDI file patch map.        

  3) Pro Mixer has two extra sliders on the Pro-16 that are not
     documented in the manual.  The BLSTR channel is the volume 
     selector for the Snd Blaster compatible DAC output.  The REC IN
     slider controls the recording level of the sum of the signals 
     mixed for recording.

  4) Pocket Recorder has greyed-out compression controls.  They will
     be enabled when compression becomes part of the Multimedia
     Windows architecture.

  5) TrakBlaster Pro does not support the higher IRQ's or DMA's.  

  6) We have provided a small program called DMAFIX.EXE that restores 
     the DMA channels to a safe state when run after running
     TrakBlaster Pro.  We suggest you make a file called TBPRO.BAT
     that has 3 lines in it:
           @ECHO OFF
           FILE_REQ
           DMAFIX
     Make sure you copy DMAFIX.EXE to your TrakBlaster Pro
     subdirectory.  TrakBlaster Pro leaves the DMA channel in a state
     that causes Windows to slow to a crawl.  This program is a
     temporary fix.  We will contact Volker Zinke, the author of 
     TrakBlaster Pro, to make the correct fix.         
        

**********************************************************************
                    CONTACTING MEDIA VISION
**********************************************************************

 Media Vision, Inc        Main:         (800) 348-7116 or (510) 770-8600                                   
 3815 LaurelView Ct.      Sales:        (800) 845-5870
 Fremont, CA 94539        Tech Support: (800) 638-2807 or (510) 770-9905
                          FAX:          (510) 770-8648 or (510) 770-9592


 Developer Assistance Program:  (800) 472-6147

 BBS: (510) 770-0968 2400 (8 bits, no parity, 1 stop bit)
      (510) 770-1661 2400 (8 bits, no parity, 1 stop bit)
      (510) 770-0527 9600 (8 bits, no parity, 1 stop bit)

 CIS: GO MEDIAVISION or send CIS mail to 75300,2772
**********************************************************************

INSTALLATION FILES        WINDOWS DRIVERS        WINDOWS APPLICATIONS
------------------       -----------------       --------------------        
file1.lis                 mcimixer.drv              pmix.exe
file2.lis                 mvmixer.drv               prec.exe
file3.lis                 mvproaud.drv              promix.exe
file4.lis                 vadmad.386                mix.exe
file5.lis                 vpasd.386
install.ins               vtbd.386
setup.exe                 opl3.drv   
oemsetup.inf              mmmixer.dll
                          tbwave.drv
                          tlwave.drv
                          mvfm.drv
                          sbwave.drv
 
DOCUMENTATION             MISCELANEOUS
--------------           ----------------  
mixapi.wri                midimap.cfg
prec.wri                  mmmixer.h
readme.doc                musicbox.ini
                          mmmixer.lib
                          


WINDOWS DRIVERS
---------------
MCIMIXER.DRV    This driver provides a set of extended MCI commands
                for accessing mixer capabiities.  
                See MCIMIXER.WRI for details of the command set.

MVMIXER.DRV     This is Media Vision's Mixer driver.


                The mixer driver adds mixer state information to
                your WIN.INI file:

                [mvmixer.drv]
                LineIn1=SYNTH     MUS]  PLAY     L=100% R=100%  @=0000
                LineIn2=MIXER     MIX]  PLAY     L= 72% R= 72%  @=0000
                LineIn3=AUX       AUX|  PLAY     L=100% R=100%  @=0000
                LineIn4=CD        CDA|  PLAY     L=  0% R=  0%  @=0000
                LineIn5=MIC       MIC|  PLAY     L=  0% R=  0%  @=0000
                LineIn6=DIGITAL   WAV]  RECORD   L=  0% R=  0%  @=0000
                LineIn7=SPKR      SPK]  PLAY     L=100% R=100%  @=0000
                LineIn7=BLSTR     WAV]  PLAY     L=100% R=100%  @=0000
                LineOut1=MASTER   AMP|  PLAY     L= 79% R= 79%  @=0000
                LineOut2=RECORD   WAV|  PLAY     L=100% R=200%  @=0000 
                StereoEnhance=ON
                Loudness=ON
                Bass=50
                Treble=78
                SaveSettingsOnWindowsExit=YES

                LINE FIELD:
                There are 7 input Lines and 1 output line.  
                Note: the Pro AudioSpectrum 16 has a second output
                line.  

                PATCH NAME:
                The field immediately after the '=' is the patch name.
                These names (ie. SYNTH) appear in promix.exe at the
                bottom of each slider pair.

                DEVICE TYPE
                The next field is the device type field.  The device
                type determines the type of icon displayed in MIX.EXE
                Each device type has a standard 3-letter mnemonic name
                that can be obtained by calling mixGetDeviceName.  The
                current list of types is:

                N/C   No Connection             SPK        PC speaker
                CDA   Compact Disk Player       AAT        Analog Audio Tape
                AUX   Auxillary                 DAT        Digital Audio Tape
                MIC   Microphone                TEL        Telephone
                VTR   Video Tape Recorder       MIX        Mixer
                VDP   Video Disc Player         EQU        Equalizer
                MUS   Musical Instrument        AMP        Amplifier
                WAV   Digital Waveform Player   LPA        Phonograph Audio                 
                RAD   Radio                     TVA        Television Audio
                UNK   Unknown Device Type
                
                The fourth character indicates whether the user is
                responsible for making the physical device connection.
                Think of the character as the mounting bracket of an audio
                card.  A hole, the '|' character, represents a mini 
                phone jack.  If the fourth character is ']', the connection
                is made by the driver.  The '|' character indicates a jack
                or connector must be hooked up before audio can be 
                heard.  User-friendly applications may use this information
                to remind the user to connect a particular device.
                
                OUTPUT CONNECTION
                The next field corresponds to the internal mixer
                connection info.  The word PLAY indicates that input
                is routed to the PLAY output (LineOut1).  RECORD
                means the input is routed to the ADC circuitry.

                VOLUMES
                If it isn't obvious, the L= and R= fields specify the
                volumes of the left and right channels at start-up.

                ASSOCIATION
                This field is used to save information that specifies
                a relationship between a mixer input and some other
                device in the system.  For example, if there are two
                CD's in the system and one is connected to LineIn4
                and the other is connected to LineIn3, the
                dwAssociation can be used to determine which MCI CD
                device is on which input. 

                MISC
                The other lines are self explanatory.  In the future
                we will let users change the settings through control
                panel's driver setup.

                CHANGING WIN.INI
                As an example, if you connect your Walkman to LineIn3
                (AUX), you can replace the word AUX with RADIO. 
                Then, change the device type field to RAD|
                
                 /////////////////////////////////////////////////////


MVPROAUD.DRV    This driver supports WAVE (digital sound) audio, MIDI I/O
                and auxillary volume control.

                
                This driver keeps configuration information in your
                system.ini file under the header [mvproaud.drv]
                If it fails to find that entry, it will
                check to see if MVSOUND.SYS is loaded and use it's
                settings.  Failing that, it will look for the
                outmoded [mvwave.drv] and [mvmidi.drv] entries.
                As a last resort, the driver will default to IRQ=7
                and DMA=1.  

                When our aux driver is the only one referred to 
                in the drivers section, a call to auxGetNumDevs
                returns a value indicating 4 aux devices are in the system:

                     Device 0 is internal CD-ROM volume
                     Device 1 is auxillary (line in) volume
                     Device 2 is microphone volume
                     Device 3 is master volume 

                While we provide a Multimedia Mixer library, we also
                support the existing volume control calls, auxGetVolume
                and auxSetVolume, when this driver is installed.


VADMAD.386        system patch file required for digital audio under
                Windows 3.0

VPASD.386       This driver provides extra buffer space needed to handle 
                16-bit digital audio.  If you experience problems
                with using audio during a Windows DOS session, remove
                this driver from system.ini.


VTBD.386        This driver provides device contention services for
                the ThunderBoard.

OPL3.DRV        OPL-3 is the name of the Yamaha FM-synthesizer chip
                on the PAS Plus, PAS 16 and CDPC.  This driver treats
                the OPL-3 as a stereo MIDI device.


MMMIXER.DLL     MMMIXER.DLL is like MMSYSTEM.DLL in a couple of ways.
                First, it provides a driver-independent layer for all
                mixer API's.  Second, it loads any mixer device drivers
                in the system.

                This DLL was developed to provide MultiMedia developers
                better control over audio mixing functionality than
                is afforded by the current volume API's.  We have
                offered this DLL to Microsoft and the MPC council as a
                standard for Multimedia Windows volume control.  There

                See the MIXSPEC directory for detailed information on the
                Multimedia Mixer API.


OEMSETUP.INF    This file allows you to add drivers to Windows using
                the drivers applet in the control panel.


TBWAVE.DRV      This is the .WAV driver for the ThunderBoard.
                
TLWAVE.DRV      This is the .WAV driver for the Thunder & Lightning.

MVFM.DRV        This driver is for the original Pro AudioSpectrum.
                It supports the two OPL-2 chips on that card as a
                single stereo MIDI device.

SBWAVE.DRV      This is a Snd Blaster compatible WAVE driver for the
                Sound Blaster compatible section of the Pro
                AudioSpectrum 16. It can be used in addition to the 
                mvproaud.drv wave driver giving Windows the
                capability to play two digital audio sounds at once.




WINDOWS APPLICATIONS
---------------------


MIX.EXE         This program allows you to modify those mixing controls
                that you'll want to change most often.
                Its main difference from promix is that it doesn't
                cover nearly as much screen area.

PROMIX.EXE      ProMix can be launced from the WIN.INI 'load' line. 
                If you have Windows 3.1, use the Program Manager's
                File/Preferences menu item to select the open
                minimized option.

                Here's a nifty feature:  When running Windows, you can
                use the keyboard to affect the volume and the 
                equalization

                CTRL-ALT-U                raises master volume
                CTRL-ALT-D                lowers master volume
                CTRL-ALT-M                 Mutes the amplifier

                CTRL-ALT-S                Toggles Stereo Enhance
                CTRL-ALT-L                Toggles Loudness
                CTRL-ALT-B                Sets BASS mode
                CTRL-ALT-T                Sets TREBLE mode
                
                When in Treble or Bass mode, you can affect the level:
        
                CTRL-ALT +                Increases BASS or TREBLE level
                CTRL-ALT -                Reduces   BASS or TREBLE level

                ProMix now features a real-time VU meter that will
                display the current recording level.  The VU meter
                will be active all the time on the PAS Plus
                and PAS 16 but on the CDPC and origintal PAS, the VU
                meter will only be active during recording and
                playback of digital audio.

PMIX.EXE         Pocket Mixer - another mixer application

PREC.EXE        Pocket Recorder - a Windows WAV file recorder.
                See PREC.WRI for more info



MISCELLANEOUS
----------------

MMMIXER.H        Header file for access to the Multimedia Mixer 
                API documented in MIXAPI.DOC
                
MMMIXER.LIB        Library file for access to the Multimedia Mixer 
                API documented in MIXAPI.DOC
                

MIDIMAP.CFG        Configuration file for the Control panel's MIDI
                Mapper applet

MUSICBOX.INI        CD definition file for Microsoft's MUSICBOX.EXE
                application (only distributed with Win 3.0 MME's)


DOCUMENTATION
----------------

PREC.WRI        This file contains information on Pocket Recorder


MCIMIXER.WRI    This file describes the MCI Mixer command set.
                Examples command strings are included.


MIXAPI.WRI      This file describes the Multimedia Mixer API.

_____________________________________________________________________

CHANGES THIS RELEASE:


  1) Using MCI player to play short .WAV files no longer skips

  2) MediaPlayer 'thumb' not correct on playback of some WAV formats

  3) "Audio dropouts when running Microsoft Works, Kings Quest V,
     Grandma and Me and BattleChess" have been fixed.

  4) Pocket Recorder's level indicators now work.

  5) Pocket Recorder now supports CUT, COPY and PASTE        
 


---------------------------------------------------------------------
--------------- FREQUENTLY ASKED QUESTIONS --------------------------
---------------------------------------------------------------------

Q:  What is the format of .WAV file?


A:  Here's a sample header from a common WAV file.
    
    00 : 52 49 46 46 94 6C 00 00-57 41 56 45 66 6D 74 20   RIFF.l..WAVEfmt 
    10 : 10 00 00 00 01 00 01 00-22 56 00 00 22 56 00 00   ........"V.."V..
    20 : 01 00 08 00 64 61 74 61-70 6C 00 00 80 80 80 80   ....datapl......
    30 : 80 80 80 80 80 80 80 80-80 80 80 80 80 80 80 80   ................
    
    
    OFFSET   SIZE        NAME                  DESCRIPTION
    ----------------------------------------------------------------------
     00     DWORD        dwRIFF         Must be ascii values for 'RIFF'
    
     04     DWORD        dwRIFFSize     size in bytes of all data following this
                                        dword
    
     08     DWORD        dwRIFFType     Must be ascii values for 'WAVE'
    
    
       << start of first chunk which is 'fmt ', the wave format chunk >>
    
     0C     DWORD        dwChunkType    Must be ascii values for 'fmt '
    
     10     DWORD        dwChunkSize    size of format chunk (currently 10h)
    
     14     FORMATCHUNK                 see format chunk broken down below
    
    
       << start of second chunk which is 'data ', the wave format chunk >>
    
    
     24     DWORD        dwChunkType    Must be ascii values for 'data '
                                        (may be different for other format types)
    
     28     DWORD        dwChunkSize    size of data chunk
    
     2C     DATACHUNK                   actual sound data.  80h is centerline
                                        value for 8-bit. 0000h is centerline
                                        for 16-bit.
    
    
    ======================================================================
    
    This describes the format chunk of a standard RIFF .WAV file:
    
       
    OFFSET  SIZE     NAME                    DESCRIPTION
    ----------------------------------------------------------------------
     0      WORD     wFormatTag        Defines format of data.  Currently
                                       only one type is defined: PCM (a value of 1)
    
    
     2      WORD     nChannels         1 for mono, 2 for stereo
    
     4      DWORD    nSamplesPerSec    usually 11025, 22050 or 44100 but can
                                       be any value.
    
     8      DWORD    nAvgBytesPerSec   this value is calculated by
                                       (samplerate * nChannels) * (wBitsPerSample/8)
    
     12     WORD     nBlockAlign       this value is calculated by
                                       (nChannels) * (wBitsPerSample/8)
    
     14     WORD     wBitsPerSample    common values are 8 and 16.  You code
                                       should handle the 12 case.
    
    All numbers above are in base 10 (decimal).
    ----------------------------------------------------------------------
    
    
    Be aware that all of the above information is based on standard PCM
    uncompressed wave files.  Evolving digital audio file formats will 
    invalidate some of the information described above.
    
    
    **********************WAV FILE FORMAT***********************
    4 bytes         'RIFF'
    4 bytes         <length>
    4 bytes         'WAVE'
    4 bytes         'fmt '
    4 bytes         <length>        ; 10h - length of 'data' block
    2 bytes         01              ; format tag
    2 bytes         01              ; channels (1=mono, 2=stereo)
    4 bytes         xxxx            ; samples per second
    4 bytes         xxxx            ; average samples per second
    2 bytes         01              ; block alignment
    2 bytes         08              ; bits per sample
    4 bytes         'data'                  
    4 bytes         <length>
      bytes         <sample data>

----------------------------------------------------------------------
----------------------------------------------------------------------


Q:  What CD-ROM drives are supported?
    
A:  *****************SUPPORTED SCSI CD-ROM DRIVES***************
    INTERNAL DRIVES:
    Chinon CDS-431.  Contact Chinon at 310-533-0274 to get the 
            40-pin  to 50-pin converter.
    Hitachi CDR-3650
    NEC CDR-80,  CDR-82, CDR-83, CDR-83J, CDR-83M, CDR-84
    Sony    CDU-541
    Texel DM-3020, DM-3021
    Toshiba XM-3201B
    
    EXTERNAL DRIVES:
    Chinon CD-SC(Sony CDU-8001), CD-SC Plus (Sony CDU-8002)
    CD Technologies Porta-Drive
    Chinon CDX-431
    Denon DRD-253
    Hitachi CDR-1553S, CDR-1650, CDR-1750S
    IBM 3510
    Laser Magnetics CM212,  CM214,  CM231
    NEC CDR-35, CDR-36, CDR-36M, CDR-72, CDR-73, CDR-73M, CDR-
            74, CDR-77
    Panasonic CR-501-S
    Pioneer DRM-600 6-disc changer
    Sony CDU-6211, CDU-7211
    Texel DM3010, DM-3120, DM-5020, DM-5021, DM-5120, DM-7120A, 
            DM-7120B
    Toshiba XM-3201A, XM-3301, XM-5100A
    
    If your CD-ROM drive is not on this list, it will NOT work 
    with the PAS16 (the SONY CDU-535 and the Laser Library are 
    not SCSI).  If it is on this list and you would like to use 
    the PAS16's SCSI interface to control the CD-ROM drive, 
    please contact Media Vision Sales at 1-800-845-5870 to order 
    an Internal SCSI Cable/Driver Kit for $39.00 or an External 
    SCSI Cable/Driver Kit for $79.00.
    

**************WINDOWS DRIVERS AND POCKET TOOLS**************
The Windows Drivers disk uses InstallSHIELD v1.3 by The 
Stirling Group. 

1.      Q:      What do I need to do before I install the PAS16 Windows 
                Drivers disk?
        A:      If you have the PAS8 Windows drivers installed or have 
                an older version of PAS16 drivers,  go into the Control 
                Panel, Drivers, and remove every driver which 
                references Pro AudioSpectrum or Media Vision.  Restart 
                WIN31 and then install the new drivers.

                Or, if you have Norton Desktop For Windows which will 
                interfere with our Windows Driver's INSTALL program.  
                To work around the problem, go into SYSTEM.INI, [boot] 
                section.  Replace "SHELL=NDW.EXE" with 
                "SHELL=PROGMAN.EXE".  Install the Windows drivers, 
                restart WIN31, and make sure that all sounds work.  
                Replace the "PROGMAN" by "NDW" in SYSTEM.INI.  Restart 
                WIN31.  Go into Program Manager, File, Run to execute 
                "SETUP /P" so that Norton will register the Multimedia 
                Tools Group which has just been created by the INSTALL 
                program.

                Or, if you are using DR DOS 6.0's SHARE which causes 
                our INSTALL program to crash the system.  To work 
                around the problem, remove SHARE.  Re-boot the 
                computer.  Then install our Windows drivers.

2.      Q:      While installing the PAS16 WIN31 drivers, I get the 
                error "You must first load Multimedia Extensions."      
        A:      First, go into the Control Panel, Drivers applet to 
                check the installed drivers list.  There must be MIDI 
                Mapper, Timer, [MCI] Sound, [MCI] MIDI Sequencer.  
                Second, check the SYSTEM.INI file.  Under the [boot] 
                section, there should be "DRIVERS=MMSYSTEM.DLL".  If 
                any of these items are missing, WIN31 has not been 
                properly installed.  Installing WIN31 over an older 
                version of windows may have caused this problem.  The 
                only solution is to install WIN31 from scratch and then 
                install the PAS16 WIN31 drivers again.

3.      Q:      After the PAS16 WIN31 drivers installation, runing 
                WIN31 causes the error "Can't find ver. 2.00 of 
                VDMAD.386."
        A:      Some Windows applications replace this driver by their 
                own DMA driver, such as Norton tape backup software 
                which puts under the [386Enh] section of the 
                SYSTEM.INI, the statement "DEVICE=VDMADX.386".  First, 
                put a semi-colon ";" infront of  the whole statement.  
                Second, add the statement "DEVICE=*VDMAD" to the 
                beginning of the [386Enh] section.  Restart WIN31 and 
                try again.

4.      Q:      After the PAS16 WIN31 drivers installation, running 
                WIN31 causes the computer to lock up.           
        A:      This is caused by a DMA and/or IRQ conflict.  Check for 
                all possible conflicts; a bus mouse is usally set for 
                IRQ 5 which will conflict with the SB IRQ 5 default 
                setting.   Use a text editor to go into SYSTEM.INI.  Go 
                the the end of the file to locate [MVPROAUD.DRV] and 
                change the DMA and IRQ settings.  Bring up WIN31 and 
                try again.

5.      Q:      Do I need MVSOUND.SYS for Windows?
        A:      Currently, yes.  In the future, the PAS16's Windows 
                drivers will not have to depend on MVSOUND.SYS.

6.      Q:      Can I use different IRQ and DMA settings under Windows, 
                than under DOS?
        A:      The DMA set in SYSTEM.INI for Windows can be different 
                from the DMA set in CONFIG.SYS for DOS as long as WIN31 
                is started in 386-Enhanced mode.  However , if you 
                start WIN31 is started in standard mode, you make make 
                the settings the same.

7.      Q:      What is the advantage of using a high-order DMA and 
                IRQ?
        A:      High-order DMA allows 16-bit DMA transfer which enables 
                the MVPROAUD.DRV sound driver to handle digital audio 
                more efficiently and also to provide more available DMA 
                selections.  High-order IRQ only provides more 
                available IRQ selections.

8.      Q:      I have just received the latest version of the PAS16 
                Windows Drivers Disk.  Do I have to remove the older 
                version first?
        A:      Yes.  After removing the old drivers, restart Windows and 
                then install the new drivers.

9.      Q:      Sound plays normally under DOS using the selected DMA 
                and IRQ setttings, but loops under Windows using the 
                same DMA and IRQ settings.
        A:      This is caused by an IRQ conflict.  Edit the SYSTEM.INI 
                file to change the IRQ setting under [mvproaud.drv] 
                section.

10.     Q:      Pro Mixer's wave meter points at the beginning of the 
                red area instead of at zero.
        A:      Our future release of WIN31 drivers v1.4 will correct 
                this problem.  Please check with Customer Service after 
                9/1.

11.     Q:      What do I have to do before I can record using Pocket 
                Recorder or Sound Recorder?
        A:      Go into Pro Mixer or Pocket Mixer to set the audio 
                input source to recording mode.

12.     Q:      When I record at 16-bit mode, there is very bad 
                clipping or it does not work at all.  8-bit recording 
                works fine.
        A:      If you are using an low-order DMA then change to a 16-
                bit DMA under the [mvproaud.drv] section of SYSTEM.INI 
                and try again.

13.     Q:      Recording at 8-bit is very scratchy.  16-bit recording 
                does not have this problem.
        A:      The PAS16 has a 16-bit PCM DAC.  Recording at 8-bit 
                using a 16-bit DAC is definitely more noisy than 
                recording at 8-bit on the PAS8 which only has an 8-bit 
                DAC.  In the next release, Pocket recorder will have a 
                feature to convert a 16-bit recorded file to 8-bit to 
                resolve the problem.  Please check with Customer 
                Service after 9/1 to find out if WIN31 Drivers and 
                Pocket Tools v1.4 is available which will have this 
                feature.

14.     Q:      Does the Pocket Recorder support the Cut, Copy and 
                Paste features?
        A:      These features will be supported in the next release.  
                Please check with Customer Service after 9/1 to find 
                out if WIN31 Drivers and Pocket Tools v1.4 is 
                available.

15.     Q:      I get the errors "Can't find input device with pid." 
                and "Can't find output device with pid." when trying to 
                run Pocket Recorder.
        A:      Make sure the MVSOUND.SYS statement appears in 
                CONFIG.SYS and that the driver loads properly when the 
                computer boots up.  

16.     Q:      I get the error "PREC has caused a General Protection 
                Fault error in USER.EXE..."
        A:      This error occurs most frequently in 286 computers and 
                also in faster computers which have less than 2MB of 
                virtual memory under Windows.  To help us troubleshoot 
                this problem, first, please download PRECGPF.ZIP 
                (PREC.EXE with GPF error checking) from the BBS.  
                Second, run DRWATSON.EXE (a WIN31 utility).  Third, run 
                the new Pocket Recorder.  When WIN31 issues the GPE, 
                all the necessary information are stored in 
                DRWATSON.LOG.  Fourth, print out this log and fax it to 
                Technical Support.  Upon receiving the information, we 
                will forward to Engineering and await their response.

17.     Q:      If Pocket Recorder is used to record a 16-bit wav file, 
                and is saved then played from Media Player, the file 
                will play properly to the end but the thumb button on 
                the position slider will not have eached the end.  The 
                thumb button usually stops around the halfway mark.  If 
                the position button is dragged to the right of this 
                mark, the message "The specified parameter is out of 
                range for the specified command" will pop up.  Dragging 
                past the halfway mark and playing the file sometimes 
                results in white noise.
        A:      This problem has been reported to Engineering and will 
                be fixed in the future release of WIN31 Drivers v1.4.  
                Please contact Customer Service after 9/1 to find out 
                if this is available.

18.      Q:     While recording under Pocket Recorder, if I 
                open/close/use other applications, there are 
                licking/popping sounds that also get recorded.
        A:      This problem has been reported to Engineering and is 
                currently being researched.

19.     Q:      Pocket Recorder's OLE (Object Linking & Embedding) does 
                not work properly.
        A:      The OLE feature is not fully implemented.  Please 
                document the problems in detail and fax or mail to 
                Technical Support to be forwarded to Engineering.
        
20.     Q:      Pocket Recorder issues "Cannot write WAV files".
        A:      This problem is caused by slow system throughput.  
                First, make sure VPASD.386 is installed in SYSTEM.INI.  
                This driver allocates a 32KB buffer for faster DMA 
                transfer.  Second, take out SMARTDRV and STACKER, if 
                installed.  Third, increase the CPU speed, if possible.

21.     Q:      A file recorded using RECFILE.EXE (PAS16's DOS utility) 
                plays back fine under Pocket Recorder but this same 
                file will not play back under Media Player.  And under 
                Sound Recorder, loading this file will cause the 
                "General Protection Fault Error In Sound Recorder".
        A:      A new version of RECFILE.EXE, dated 6-22-92 or later, 
                does not have this problem.  On BBS, download 
                P16REC.ZIP; on Compuserve, download TOOLS.ZIP.

22.     Q:      How do I play CD-Audio under WIN31?
        A:      First, put a CD-Audio disk into the CD-ROM drive.  
                Failure to do this will cause the [MCI] CD-Audio driver 
                to not install properly  Second, go into the Control 
                Panel, Drivers.  Click on the Add button.  Select 
                "[MCI] CD-Audio" driver.  Click on the OK button.  
                WIN31 will prompt you for the Microsoft Windows Disk 4.  
                Third, after this driver has been properly installed, 
                go into Media Player.  Select Device.  CD-Audio should 
                be one of the choices for you to select from.  If  not, 
                edit MPLAYER.INI to change "CDAUDIO=0," to "CDAUDIO=17, 
                CDAUDIO".

23.     Q:      I do not get any FM sound when I run DOS games under 
                the DOS shell of Windows.
        A:      The OPL3 FM synthesizer chip on the PAS16 can operate 
                in either OPL3 (4-operator) mode or 3812 (2-operator) 
                mode.  Under Windows, Voyetra's OPL3.DRV driver puts 
                this FM chip into the OPL3 mode to produce rich FM 
                sounds.  However, existing games only support the 3812 
                mode.  This driver will put the OPL3 chip back in 3812 
                mode upon exiting WIN31 to go back to DOS.  However, 
                wihle still under Windows, if the user attempts to run 
                a DOS game or application which supports AdLib, FM 
                sound will not play.  To work around this problem, go 
                into SYSTEM.INI, [drivers] section, change 
                MIDI=OPL3.DRV to become MIDI=MVFM.DRV.  Then restart 
                Windows.  Go into the Control Panel, MIDI Mapper.  
                Click on New.  Give it a name like "3812 mode".  Under 
                the Port Name column, select "Media Vision FM Synth" 
                for channels 1-10 and 13-16 and then save the setup.  
                Now DOS games and applications can produce FM sounds.

24.     Q:      Under Media Player, CANYON.MID plays properly but when 
                I play other MIDI files, I don't hear any music.
        A:      WIN31 only supports General MIDI.  The MIDI files that 
                you have may be Non-General MIDI.  Try the following.  
                Go into Control Panel, MIDI Mapper.  Select the Pro 
                AudioSpectrum setup.  Click on Edit.  Under the Port 
                Name column, select "Media Vision FM Synth" for 
                channels 1-10 and 13-16 and then save the setup.  Now 
                all MIDI songs should play; however, they may not sound 
                correct.

25.     Q:      Do you have PAS16 drivers for Windows 3.0 with 
                Multimedia Extentions?
        A:      Download from the BBS a file called MVPROAUD.ZIP.  This 
                file contains a special version of MVPROAUD.DRV for 
                Windows 3.0 with MME.  Replacing the MVPROAUD.DRV that 
                came with the PAS16 WIN31 Drivers disk with this 
                version is all you need to do.

*************************PAS.EXE****************************
1.      Q:      How do I adjust the volume for the SB section of the 
                sound card.
        A:      Run "PAS SET SB TO XX" where xx is 0-100.

2.      Q:      DOS software produces no volume or very low volume, 
                especially after exiting WIN31.
        A:      Run "PAS RESET" and try again.

3.      Q:      When I run "PAS *", how do I enable the recording mode 
                for an input source?
        A:      Use the up and down arrow keys to move to the input 
                source desired.  Then press the Enter key to toggle 
                between PLAY and PLAY & RECORD.

*********************RECFILE, PLAYFILE**********************
NOTE:  Before running RECFILE.EXE, make sure that you have 
run PAS * to enable the recording mode for the input 
source(s).  See the PAS.EXE section above.

1.      Q:      How do I use the command parameters Vxxx, V+xxx and Fx 
                for RECFILE.EXE?
        A:      Vxxx, where xxx is a number from 000-127 for voice-
                        activated level.  Only sounds at and above this level 
                        get recorded.  
                V+xxx, where xxx is 000-127.  Record all when voice is 
                        activated at threshold.
                Fx, where x is between 0-6 and selected using the 
                following guidelines:
                Filter Value    Limiting Frequency   Sampling Rate
                Frequency Range       18 KHz              44 KHz     near CD
                       5              16 KHz              32 KHz     cassette
                       4              12 KHz              24 KHz     FM radio
                       3               9 KHz              18 KHz     AM radio
                       2               6 KHz              12 KHz     telephone
                       1               3 KHz               6 KHz     male voice
                       0               0 KHz                         mute

2.      Q:      When PLAYFILE.EXE starts and stops, it produces a 
                "popping" sound.  
        A:      Get a newer version of  PLAYFILE.EXE.  Please download 
                P16REC.ZIP from the BBS.

3.      Q:      I am having trouble recording 16-bit wave files using 
                the V+xxx parameter.
        A:      Get a newer version of RECFILE.EXE.  Please download 
                P16REC.ZIP from the BBS.

4.      Q:      I do not hear any sound when I play back under WIN31's 
                Media Player a file which has been recorded using 
                RECFILE.EXE.
        A:      Get a newer version of RECFILE.EXE.  Please download 
                P16REC.ZIP from the BBS.

5.      Q:      I get the error "File is full or blocked" when I run 
                RECFILE.EXE.
        A:      This problem is caused by slow system throughput.  
                First, try running RECFILE with the /M parameter to 
                allocate as much memory to RECFILE as possible.  
                Second, reduce to a generic CONFIG.SYS and 
                AUTOEXEC.BAT.  Third, make sure the hard disk has been 
                optimized (unfragmented).  Fourth, try at a lower 
                sampling rate or try recording to a ramdrive (use DOS's 
                RAMDRIVE.SYS).

*********************CD-ROM APPLICATIONS********************
1.      Q:      After running Compton's Multimedia Encyclopedia, I only 
                hear sounds out of one channel.
        A:      When Compton's plays digital audio (represented by .WAV 
                file extension), it puts the CD-ROM drive into mono 
                mode and also shuts down one channel.  For a temporary 
                solution, you need to do a cold boot to reset the CD-
                ROM drive.  To resolve this problem, download 
                COMPTONS.ZIP from the BBS or contact Customer Service 
                to have this file sent via mail.

2.      Q:      While installing MS Bookshelf, at 99% completion, 
                installation aborts with an error message in SETUP.INF 
                file.
        A:      First, back up SETUP.INF.  Second, go into SETUP.INF 
                and remove all lines that start with a semi-colon ";" 
                and then save it and re-install Bookshelf

3.      Q:      National Geographic Society's Presidents Starting With 
                George runs fine but does not produce audio.
        A:      This application uses IBM Linkway and supports SB.  
                During installation, the driver statement 
                "DEVICE=SNDBK12.SYS 1" gets added to CONFIG.SYS.  This 
                driver defaults to IRQ 7 and I/O port 220h and DMA 1.  
                The SB section of the sound card defaults to IRQ 5 and 
                I/O port 220h.  Edit the CONFIG.SYS to show 
                "DEVICE=SNDBK12.SYS 1 5 220", where 5 is for IRQ 5 and 
                220 is for I/O port 220h, or which ever settings you 
                have at J10 and J12 on the sound card.

********************BUS MASTERING DEVICE********************
1.      Q:      I hear periodic clicking sound or static noise whenever 
                the hard disk's light goes on (while drive is being 
                accessed).
        A:      Lower the bus on-time and increase the bus off-time by 
                the same amount so that the on-time is smaller than the 
                off-time, or experiment to find the best ratio.  We 
                discovered this from using the Adaptec 1542B SCSI Hard 
                Disk Controller.  The install program for this card 
                adds the following statements to CONFIG.SYS:
                        DEVICE=C:\ASPI4DOS.SYS /N11 /F5
                        DEVICE=C:\ASPIDISK.SYS
                Where N11 is 11/16ms and F5 is 5/16ms (default 
                settings).  The problem was resolved when we changed to 
                N5 and F11. 

********************OS/2 DRIVER SUPPORT*********************
1.      Q:      Are there any plans to support OS/2 v2.0?
        A:      Yes, we are currently working on it.  Please contact 
                Customer Service after 10-1-92.

********************WINDOWS NT SUPPORT**********************
1.      Q:      Are there any plans to support Windows NT?
        A:      Please check with Customer Service after 10-1-92.