Motorolla PINOUT DIAGRAMS
______________________________________________________________________________
 
 CABLE FOR "Bag & Installed phones" (gray, silver, or black Box)
 
DB25 MALE to PRN PORT - - - - - - - - - connector "A"
DB25 FEMALE to TRANCEIVER - - - - - - - connector "B"
 
 
 A.1 to B.18
 A.2 to B.21
 A.3 to A.14 to B.17
 A.4 to B.1
 A.12 to B.12
 A.13 to B.11
 A.17 to B.20
 A.18 to B.14 to B.23
 A.20 to B.23
 
         B.3 to Ground (12 volt supply to Tranceiver)
         B.4 & B.5 to +12 volts (use a cig lighter plug)
 
_______________________________________________________________________________
 
 CABLE FOR "Classic, Ultra-Classic, also known as "brick" or 8000 series"
 
 Numbers = PRN PORT DB25 MALE CONNECTOR
 Letters = connections on back of phone
 
                             Back of phone - O o's are contacts
                                   _______________________
 1 to K                           | A  B  C |   | D  E  F |
 2 to F                           |         |   |         |
 3 to C                           | O  O  O |   | O  O  O |
 4 to D                           |         |   |         |
 12 to J                          | G  H  I |   | J  K  L |
 13 to H                          | o  o  o |___| o  o  o |
 18 to G                          |                       |
                                  |                       |
                                  |_______________________|
 
 
 * NOTE ! *                      |                          |
   this phone type uses
   7.5 to 8.0 Volts !            |                          |
 
                                 |  -    Battery conn.   +  |
                                 |  O                    O  |
                                 |__________________________|
 
_______________________________________________________________________________
 
 CABLE FOR "Flip phone" 550 series (micro-tac portable)
 
 A = PRN PORT DB25 CONNECTOR
 B = "FLIP PHONE JACK"
 
 A.1 to B.4
 A.2 to diode (band towards A conn.) other side of diode to TEST LEAD
  The TEST LEAD connects to the center pin of the Battery Connection Area
 A.4 to diode (band towards A conn.) other side of diode to B.1
 A.12 to B.5
 A.13 to B.6
 A.18 to B.8
 
 also tie pins 18 thru 25 on conn. "A" together (for grounding)
 
 Pin 8 on "B" connector to - (ground) of 8 Volt power supply
 Pin 7 on "B" connector to + (positive) of the 8 Volt supply
 
 * NOTE *
 THIS PHONE TYPE REQUIRES 8.0 VOLTS TO PROGRAM
 
_______________________________________________________________________________