COPYROM.LIB 
Author: [burhan h. afandi] 
  Date: Sun Jul 07 1991  
 
COPYROM is a library which enables you to copy ROM to RAM.  You can send the 
contents of a ROM card directly to a PC for storage, or copy the contents to a 
port on your calculator.  COPYROM allows you to copy an entire port (ROM or 
RAM) or just a selected number of files. 
 
 
==========STORAGE ON A COMPUTER DISK============= 
 
(COPY TO PC) COMMAND:->->PC 
 
If the argument is a number (0,1 or 2) the entire given port is copied. 
 
If the argument is a library identifier (:port#:library#) only the identified 
library is copied. 
 
If the argument is a list of library identifiers, only the files in the list 
are copied. 
 
 
===========COPY TO STACK===================== 
 
(COPY TO STACK) COMMAND: STK  
               
This command takes the same arguments as ->->PC, however, the result is 
returned to stack. 
 
 
==============COPY TO PORT=================== 
 
(COPY TO PORT) COMMAND:  PORT 
 
This command takes an additional argument in level one which is the port# to 
which you want to copy the files. 
 
So this command takes two arguments: 
The level two argument may be a library identifier (:port#:library#), or a list 
of library identifiers, or a port#(0,1 or 2).  The level one argument must be a 
number (0, 1 or 2) (this is the port number to which you want to copy the 
files). 
 
EXAMPLE: Let us assume that we have a ROM card in port #2 and we want to copy 
this ROM card to a RAM card located in port #1. 
 
solution: 
 
simply Enter the source port (2) 
             then the destination port(1) 
             implement  port to copy port 2 to port one 
 
summary: 
 
2 [ENTER] 
1 [ENTER] 
Now press the key labeled {  PORT } 
 
The contents of port 2 are copied to port 1. 
 
This command also accepts a list containing two port #s as an argument. 
 
In the above example we could also have entered {2 1} as an argument where the 
first element of the list is the source port# and the second is the destination 
port#. 
 
 
==============ATTACHING COPY-ROM================= 
 
Transfer the library to your calculator.  Press [VAR] [COPYROM]. 
COPYROM.LIB will appear on the stack.  Store it in a port as follows: 
 
0 [STO]   or   1 [STO]   or   2 [STO] 
 
Turn your calculator OFF and then ON.  The library will attach itself.