CW: A Morse Code Practice Program for the HP-48SX 
by ? 
 
CW is a directory containing several programs and variables which 
comprise a capable Morse code practice system for the user.  The 
program can send code using the beeper at speeds slightly over 20 
words per minute continuously, without encountering delays due to 
calculator "garbage collection".  The user can set the overall 
speed and element speed independently, or can manually set the 
timing and delay for each element type.  The program will create, 
send, and display five character random code groups, or the user 
can store any size string in a variable to be sent and displayed 
manually.  The following descriptions explain the programs and 
variables and their use. 
 
CGR (Code GRoups) is a program which creates a string of 25 five 
character random groups, sends them using the present speed 
parameters, and then displays them so the user can check his 
copy.  The characters are selected from a string in CGR 
which contains all the characters and prosigns used in amateur 
radio license tests.  If the user wishes to practice only certain 
characters, this string can be changed with 'CGR' RCL EDIT or 'CGR' 
VISIT and the groups will then include only the characters from 
the modified string. 
 
SPD (SPeeD) is a program which calculates and sets the various 
parameters affecting the timing of each type of element.  The 
program prompts the user for the overall speed in words per 
minute and the element speed, also in words per minute.  After 
entering these two numbers on the stack, the user presses [LSHFT] 
CONT and the program stores values in ST, LT, ET, CT, and WT. 
SPD will not signal an error if speeds are set too high or if 
element speed is less than overall speed, but one of the values 
in ST, LT, etc. will be set to zero or negative and CWO will halt 
or hang.  Calculator speed and overhead as well as time to do 
the garbage collect operation limit the speed to slightly more 
than 20 wpm if overall and element speeds are the same.  If 
the element speed is set faster than the overall speed, somewhat 
higher speeds can be reached, 26 wpm overall with 29 wpm element 
speed being about the maximum in any case.  The speed will be 
quite accurate, within 1% or so in most cases.  The user can 
measure the speed if desired by storing the string 
"paris paris paris ..." in TXT and using a stopwatch to time from 
the first element of a word to the same first element a few words 
later.  Divide the number of words timed by the number of seconds 
on the stopwatch and then multiply that by 60 to obtain the speed 
in words per minute. 
 
CWO (CW Output) is the program which actually sends the Morse 
code using the beeper.  CWO sends the characters contained in the 
string TXT.  TXT is set and CWO is called automatically by the 
CGR program, but the user can set TXT and then execute CWO 
manually to practice something other than random code groups. 
 
DSP (DiSPlay) is a program which display a screenful of 
characters from the TXT string.  CGR calls this program to 
display the code groups it creates and sends.  If TXT is more 
than one screen long, DSP halts after each successive screen. 
The user can view the next screen by pressing [LSHFT] CONT. 
 
TXT (TeXT) is a variable which contains a string which will 
be sent as Morse code by the CWO program.  Any ACSII character 
with decimal code 32 through 128 can be contained in TXT. 
Characters that have no representation in Morse code will be 
sent as a space.  Note that some of the radio prosigns which 
have no representation in ASCII have been placed on some of 
those characters.  For a listing of these, see the CODE 
variable.  Note that lower case characters are folded into 
upper case. 
 
CODE (CODE) is a variable which contains a list of short 
programs, one for each character.  CWO disassembles this list 
on the stack before sending so that it can access the 
character codes much more quickly than by other methods. 
Prosigns which have no associated ASCII character are rather 
arbitrarily placed on the following characters: 
     understood (SN)           ! 
     error (HH)                # 
     paragraph (AL)            * 
     starting signal (KA)      [ 
     wait (AS)                 \ 
     end of work (SK)          ] 
 
ST (Short Time) is a numeric variable containing the basic 
element (dit) time in seconds, normally set at 1.2/WPM. 
 
LT (Long Time) is a numeric variable containing the longer 
element (dah) time, set at 3*ST. 
 
ET (interElement Time) is a numeric variable containing the 
delay time between elements.  This is generally set at the 
same value as ST, less the calculator overhead time between 
elements, .04 sec. 
 
CT (Character Time) is a numeric variable containing the 
delay time between characters.  This is usually set to the 
same value as LT, adjusted for various calculator overhead 
times in the program. 
 
WT (Word Time) is a numeric variable containing the delay 
time between words.  This is normally set to 7*ST, adjusted 
for various calculator overhead delays. 
 
FR (FRequency) is the frequency in hertz of the beeper. 
Set at 500 hertz, but the user may store any value which 
suits individual taste. 
 
S (Short beep) is a program which actually sends a single 
dit element.  The user will not use this program. 
 
L (Long beep) is a program which actually sends a single 
dah element.  The user will not use this program. 
 
W (Word wait) is a program which generates the delay for 
a space character.  The user will not use this program.