(Comp.sys.handhelds) 
Item: 3567 by ftg0673 at tamsun.TAMU.EDU 
Author: [Rick Grevelle] 
  Subj: HP48 HACKIT, version 4 (BYTES: #F675h, 2712) 
  Date: Tue Jun 25 1991 
 
[Note: This "HACKIT" Library is truly a 48 hacker's dream come true.  It was 
developed by Rick Grevelle over a long period of time.  The following 
documentation was pieced together as best I could from snippits that were 
attached to each posted revision.  Its COPY function is not documented, which 
is just as well, because only true hackers should have access to its power, and 
only they will be patient enough to use the tools herein to figure out what it 
does and how to use it.  It's worth it!  Many thanx to Rick for this excellent 
library.  Every "real programmer" will keep this permanently in a port.  -jkh-] 
 
 
This is an enhanced version of the HACKIT thing.  It includes several new 
features which further facilitate hacking in the 48, and are as follows: 
 
        o   Multifunctional PEEK will now allow the normally hidden 
            32k of ROM to be peeked.  When flag 14 is clear the 32k 
            of memory between #70000h and #7FFFFh is RAM.  When the 
            flag is set this is shifted to #F0000h through #FFFFFh, 
            and #70000h through #7FFFFh becomes what was previously 
            covered by RAM; this configuration is identical to that 
            of the built in memory scanner. 
 
        o   Bank switching capabilities have also been incorporated 
            in the SEEK scheme, functioning exactly as described in 
            the PEEK routine. 
 
        o   DIR-> is a new addition to the OUT-> command; it allows 
            a directory in level 1 to be decomposed on the stack in 
            to its constituent parts.  Due to this change, it's not 
            necessary to include the RCLDR scheme in the library as 
            it was added to the original HACKIT post only after all 
            first attempts to produce a successful DIR-> had failed. 
 
        o   Flag 15 affects the way in which the ->ASCI, and  
            ASCI-> routines handle code objects.  Currently a ->STR, 
            and STR-> scheme is being conceived that will provide a 
            superior editing scheme for queer objects. 
 
 
At the risk of being reiterative, I'm including an improved version of the 
documentation which appeared in the original posting of this library.  It 
should be a bit more articulate, and contain examples for those whose time 
is allowing.  Much work still remains to be done regarding the completely 
bullet proof hacking library, but since all the fun seems to be in getting 
there, hopefully it will take a long time. 
 
A final word of caution; do *not* attempt to implement a bank shift using 
either PEEK, or SEEK, if this library is stored in port 0, or anywhere in 
the address space being displaced.  This means both of the 32k banks that 
are affected by setting flag 14 are off limits, as far as this feature is 
concerned, for the storing of this library.  Should there be any question 
about this, or anything else, feel free to call, or write, and I shall be 
glad to provide any answers of which I might be capable :-). 
 
 
Rick Grevelle 
(409) 774-1169 
ftg0673@tamsun.tamu.edu 
 
                                   HACKIT 
 
============================================================================== 
 
 
HACKIT is a library of utilities designed to facilitate hacking in the HP48SX. 
The fourteen programs it contains were conceived for two fundamental purposes: 
 
 o   Exploration, documentation, and accessing of the machine code, and RPL 
     operating system contained in the 48's vast ROM. 
 
 o   Construction, and manipulation of the various object types not supported 
     by the 48's editor, user language commands, functions, or operations. 
 
 
 
                                   ->ASCI 
 
This is a generalized binary-to-ascii conversion scheme that returns a string 
of hexadecimal characters which are the equivalent internal representation of 
the argument.  When USER FLAG 15 is set both the prolog and the length of code 
objects are truncated meaning that the result string contains in-line machine 
code only.  When this flag is clear, which is the default, truncation does not 
occur.  All other object types are unaffected by the flag setting. 
 
                                   ASCI-> 
 
Reversing the result of the previous routine is made possible with this scheme, 
which converts ascii-to-binary, taking as its argument a string of hexadecimal 
characters.  When USER FLAG 15 is set all strings are treated as in-line machine 
code, whereby a code object would be the result.  When flag 15 is clear one of 
two things happens depending on the string argument itself, and is explained in 
the following summary. 
 
 
 
                               IMPORTANT POINTS 
 
 o   The above routines were intended to provide a means for *toggling* stack 
     objects back between their internal string representation and immediately 
     executable form, which means ROM objects must be dealt with differently. 
     An important attribute associated with these two schemes is their ability 
     to differentiate between ROM and RAM objects. 
 
 o   When an argument taken by the ->ASCI routine is a ROM object, a character 
     string representing the five nibble address where that object is located 
     in ROM is returned.  Strings containing only five characters that are used 
     as arguments for ASCI-> are treated as pointers; solitary prologs are not 
     permitted though (i.e. "D9D20", "C2A20", "11920").  Future versions should 
     be more than capable of dealing with such complexities as this. 
 
 o   Spaces and newline carriage returns are allowed in strings that are to be 
     converted by ASCI->.  This helps to alleviate some of the confusion when 
     looking at long strings of hexadecimal characters in that spaces can now 
     be used to separate groups of characters, and newline carriage returns to 
     segment the string into several lines when editing.  [Comments are also 
     deleted; see note below.  -jkh-] 
 
 o   Any object encoded using ->ASC can be unencoded using ASCI->.  There's no 
     longer a need for these silly schemes to delete newline carriage returns, 
     or calculate a new checksum to tack onto an ->ASC encoded object that has 
     been altered in order to get ASC-> to work.  ->ASC, and ASC-> were written 
     to provide a safe means of transferring data, and not for hacking.  It is 
     therefore not recommended to use these two schemes in place of ->ASC, and 
     ASC->. 
 
 o   ASCI-> performs equally well on strings of odd number lengths because the 
     RPL segments of the program correctly utilize the block allocate routine 
     at #61C1Ch.  But because of its very nature, it's still quite possible to 
     suffer a memory loss from abusing this routine; so be careful. 
 
 
 
      Example:  Construct the DUP command from its ASCII string representation. 
 
 
        £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨               £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨ 
        3{HOME}                 3               3{HOME}                 3 
        ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ'               ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ' 
        34:                     3               34:                     3 
        33:                     3               33:                     3 
        32:                     3               32:                     3 
        31:              "78BF1"3               31:                  DUP3 
        3### ### ### ### ### ###3               3### ### ### ### ### ###3 
        …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ—               …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ— 
      1) Enter the string "78DF1".            2) Implement ASCI-> to obtain 
                                                 the command DUP. 
 
 
Note:   New Version of HP48 HACKIT: ASCI-> Accepts Strings With Comments 
 
This new version of the HACKIT library takes a significant step forward. 
Now, when preparing strings of hex nibbles for use with ASCI-> (to build the 
various types of HP48 ob- jects), one may include comments in a manner similar 
to those in regular HP48 program objects.  Strings of nibbles containing not 
only spaces and carriage returns but also embedded comments which fall between 
a leading "@" symbol and a line-terminating carriage return are now handled 
like strings containing only nibble characters 0 through F.  For example, a 
simple RPL object to contain the ROM number 1 can be represented by the the 
string "D9D209C2A2B2130".  (The string "9C2A2" by itself would also suffice, 
but we are including the "begin RPL" and "end marker" addresses here to simply 
embellish the example.) Passing "D9D209C2A2B2130" as an argument to ASCI-> will 
yield a 1.  In addition, this version of ASCI-> will also accept a string like 
the following: 
 
"D9D20 @ Begin RPL 
 9C2A2 @ 1 
 B2130 @ End Marker" 
 
This means that system RPL code developed on PC screens may be commented, 
with the source code available directly for HACKIT. It also means that  
HACKIT can accept input virtually identical to the output of Voyager (if the 
"@" signs are added to each commented line).  Now, HP's PDL becomes a valid 
development platform for system RPL code. 
 
 
                                   SCRC 
 
Calculates the checksum of a string of hexadecimal characters as if they were 
in immediately executable form.  So objects which have been converted to their 
internal hexadecimal character string form (ASCII) using ->ASCI will have the 
same checksum when SCRC is used on the ASCII string, as they would have had in 
their binary form using the BYTES command.  This allows queer objects such as 
libraries and backups that contain checksums which do not include the complete 
data structure to be altered, or even constructed from scratch, in the 48.  So 
for an example a trivial backup object will be built utilizing SCRC, ->ASCI, 
and the ASCI-> routines. 
 
 
 
      Example:  Build a backup object named "Hex" containing the 
hexadecimal 
                integer, # 123456789ABCDEF0h. 
 
 
                o  Construct the backup object's appropriate name. 
 
        £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨               £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨ 
        3{HOME}                 3               3{HOME}                 3 
        ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ'               ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ' 
        34:                     3               34:                     3 
        33:                     3               33:                     3 
        32:                     3               32:                     3 
        31:                'Hex'3               31:      "84E2030845687"3 
        3### ### ### ### ### ###3               3### ### ### ### ### ###3 
        …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ—               …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ— 
      1) Enter the name 'Hex'.                2) Implement ->ASCI on the 
                                                 name. 
 
        £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨               £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨ 
        3{HOME}                 3               3{HOME}                 3 
        ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ'               ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ' 
        34:                     3               34:                     3 
        33:                     3               33:                     3 
        32:                     3               32:                     3 
        31:           "30845687"3               31:         "3084568730"3 
        3### ### ### ### ### ###3               3### ### ### ### ### ###3 
        …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ—               …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ— 
      3) Edit the string to delete            4) Concatenate "30" by using 
         the first five characters.              the plus (+) key. 
 
 
 
                o  Prepare the backup object's contents for concatenation. 
 
        £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨               £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨ 
        3{HOME}                 3               3{HOME}                 3 
        ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ'               ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ' 
        34:                     3               34:                     3 
        33:                     3               33:                     3 
        32:         "3084568730"3               32:         "3084568730"3 
        31:  # 123456789ABCDEF0h3               31: "E4A20510000FEDCBA..3 
        3### ### ### ### ### ###3               3### ### ### ### ### ###3 
        …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ—               …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ— 
      1) Enter the integer data.              2) Implement ->ASCI once again. 
 
 
 
                o  Make final preparations for checksumming. 
 
        £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨               £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨ 
        3{HOME}                 3               3{HOME}                 3 
        ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ'               ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ' 
        34:                     3               34:                     3 
        33:                     3               33:                     3 
        32:                     3               32: "3084568730E3A2051..3 
        31: "3084568730E4A2051..3               31:              "33000"3 
        3### ### ### ### ### ###3               3### ### ### ### ### ###3 
        …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ—               …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ— 
      1) Concatenate the previous             2) DUP the result string, and 
         two result strings using                use SIZE to obtain its size. 
         the plus (+) key again.                 Add 10 to the size, convert 
                                                 the result to a hexadecimal 
                                                 number, and enter backwards 
                                                 as a five character string. 
 
        £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨               £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨ 
        3{HOME}                 3               3{HOME}                 3 
        ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ'               ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ' 
        34:                     3               34:                     3 
        33:                     3               33:                     3 
        32:                     3               32: "330003084568730E4..3 
        31: "330003084568730E4..3               31:             "119200"3 
        3### ### ### ### ### ###3               3### ### ### ### ### ###3 
        …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ—               …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ— 
      3) Perform a SWAP, and using            4) Append the string "119200" 
         the plus (+) key, prepend               to the end of the string, 
         the length onto the front               DUP the result, and using 
         of the string.                          SCRC calculate the object's 
                                                 proper checksum. 
 
 
 
                o  Make final preparations for coverting the string. 
 
        £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨               £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨ 
        3{HOME}                 3               3{HOME}                 3 
        ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ'               ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ' 
        34:                     3               34:                     3 
        33:                     3               33:                     3 
        32: "330003084568730E4..3               32:              "26B20"3 
        31:               "0B41"3               31: "330003084568730E4..3 
        3### ### ### ### ### ###3               3### ### ### ### ### ###3 
        …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ—               …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ— 
      1) Enter the four hexadecimal           2) Enter the prolog for the 
         characters of the checksum              backup object backwards, 
         backwards in a string, and              and perform another SWAP. 
         append this to the string 
         for which the checksum was 
         calculated. 
 
 
        £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨               £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨ 
        3{HOME}                 3               3{HOME}                 3 
        ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ'               ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ' 
        34:                     3               34:                     3 
        33:                     3               33:                     3 
        32:                     3               32:                     3 
        31: "26B20330003084568..3               31:           Backup Hex3 
        3### ### ### ### ### ###3               3### ### ### ### ### ###3 
        …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ—               …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ— 
      3) Prepend the prolog using             4) Convert the string using 
         the plus (+) key one last               ASCI-> to its binary form. 
         time. 
 
 
 
                                   SEEK 
 
Appearing first in his Processor Notes, SEEK is in fact a modified version of 
Alonzo Gariepy's FIND routine.  SEEK was specifically modified to run in the  
48; it's one third the size of the original version for the 28, and should run 
a bit quicker too. 
 
Alonzo's predominately register, rather than memory oriented algorithm remains 
unchanged.  Recall the overall increase in speed was only about 10% over that  
of the brute force approach, which he attributed to an increased time spent in 
the looping structures.  Because it demonstrates several programming features 
specific to the 48, I've taken the liberty of renaming the routine. 
 
The way to use this program is to specify a memory pattern and a place to start 
looking.  A memory pattern can be sequence of up to fifteen nibbles, and a one 
nibble length (the number of nibbles in the pattern minus one).  An application 
for SEEK could be to locate the occurrences of the instruction 808C in memory. 
To do this enter # C8083h in level two, and a starting place such as # 0h.  All 
that remains to be done is to implement SEEK, and to continue doing so to find 
any subsequent instances.  This is because the result returned will be a binary 
integer which is the address one higher than where the pattern exist in memory. 
 
 
 
                               IMPORTANT POINTS 
 
 o   Bank shifting capabilities have been incorporated into SEEK, allowing the 
     normally hidden 32k bank of ROM to be searched.  With USER FLAG 14 clear, 
     the 32 kilobytes of memory between #70000h, and #7FFFFh, is RAM.  Setting 
     flag 14 shifts the RAM to #F0000h through #FFFFFh, and reconfigures what 
     was previously hidden ROM in its place. 
 
 o   This version does not stop until it finds an instance, or scans the entire 
     address space.  So even though the routine is fast, due to the size of the 
     48's address space, matching certain patterns could take several seconds. 
 
 
 
      Example:  Determine the first occurrence of the ARRAY prolog, # 029E8h, 
                in the normally hidden 32k bank of ROM. (flag 14 set) 
 
 
        £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨               £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨ 
        3{HOME}                 3               3{HOME}                 3 
        ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ'               ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ' 
        34:                     3               34:                     3 
        33:                     3               33:                     3 
        32:             # 29E84h3               32:             # 29E84h3 
        31:             # 70000h3               31:             # 72001h3 
        3### ### ### ### ### ###3               3### ### ### ### ### ###3 
        …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ—               …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ— 
      1) Enter the bit pattern with           2) The result returned is the 
         the number of nibbles minus             one higher than where the 
         one, and the address where              actual pattern was found. 
         to begin searching. 
 
                                   PEEK 
 
Speed is still an essential attribute of this dual functioning PEEK.  Only the 
variable length version will slow slightly when large result strings hundreds 
of characters long are returned.  The routine is smart enough to know which of 
the PEEKs to implement based on the arguments it's given.  When string results 
are preferred, level two should contain a binary integer that's the address to 
be peeked, while level one should be a real number representing the length of 
the result string.  The bank shifting features as described in SEEK scheme are 
also available in this version of PEEK; an example follows. 
 
 
 
      Example:  Using PEEK and ASCI->, recover the message array from the 
                hidden ROM found in the previous example. (flag 14 set) 
 
 
        £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨               £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨ 
        3{HOME}                 3               3{HOME}                 3 
        ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ'               ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ' 
        34:                     3               34:                     3 
        33:             # 29E84h3               33:                     3 
        32:             # 72000h3               32:             # 29E84h3 
        31:                  6413               31:      Array of String3 
        3### ### ### ### ### ###3               3### ### ### ### ### ###3 
        …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ—               …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ— 
      1) Subtract one from the above          2) Now implement ASCI-> on the 
         result, enter the number of             result to obtain the ARRAY. 
         nibbles to be returned, and 
         implement PEEK.                  
 
 
                                   POKE 
 
Complimenting PEEK is this dual functioning variable length POKE scheme which 
will accept either a string of hexadecimal characters, or a binary integer for 
the level two argument that represents the data to be poked.  Level one should 
be a binary integer that is the address to poke.  It is important to note that 
when the level two argument is a binary integer, the wordsize of that specific 
integer will be used to determine the number of nibbles to poke, and isn't in 
any way dependent upon the current wordsize returned by RCWS. 
 
 
 
                                   OUT-> 
 
Multifunctioning OUT-> encompasses several of the object types on which OBJ-> 
will not work.  In addition, and analogous to the LIST-> command, ALG-> and 
PRG-> are intended to function on algebraics, and programs.  ARR-> functions 
identically to ARRY->, but works on all the various array types such as the 
array of string, algebraic, list, etc.  DIR-> decomposes a directory that is 
in level one into its constituent parts.  XLIB-> has also been included; it 
decomposes visible, and hidden XLIBs into their library and command numbers.   
 
 
 
      Example:  Decompose the Array of String obtained in previous example 
                into its constituent parts. 
 
        £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨               £ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨ 
        3{HOME}                 3               3{HOME}                 3 
        ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ'               ~AŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ' 
        34:                     3               34: "Try To Recover Me..3 
        33:                     3               33: "Replace RAM, Pres..3 
        32:             # 29E84h3               32: "No Mem To Config ..3 
        31:      Array of String3               31:               { 16 }3 
        3### ### ### ### ### ###3               3### ### ### ### ### ###3 
        …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ—               …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ— 
      1) Using the array obtained             2) Recompose the array again 
         in the previous example,                by using the ->ARR routine. 
         implementing OUT-> will                 The result will look like 
         reveal the strings.                     that of frame 1). 
 
 
                                   ->ALG 
 
Be careful with this one; the stack arguments must be in strict RPN order.  As 
before, ->ALG is analogous to ->LIST, only the result is an algebraic, rather 
than a list. 
 
 
                                   ->ARR 
 
This is my version of ->ARRY; it will build an array of any kind providing all 
stack arguments are of the same type. (i.e. strings, reals, algebraics, etc.) 
It functions identically to ->ARRY, except that real and complex numbers can't 
be mixed.  Level one can be either a real number, a list containing a real, or 
a list containing two reals that is the size the resulting array is to be. 
 
 
                                   ->DIR 
 
Builds a directory from the stack on the stack.  Level one must contain a real 
which is the total number of variables that the directory is to contain, level 
two a global name, and level three the contents of that global name.  Because 
the entire process utilizes dynamic RAM, it is relatively fast for moderately 
sized directories, but slows substantially on very large ones.  Using both the 
DIR-> feature found in the OUT-> command along with this routine, a directory 
on the stack can be effectively toggled between its constituent parts, and its 
composite form. 
 
 
                                   ->PRG 
 
Functions identically to ->LIST, only the result is a program, and not a list. 
 
 
                                   ->XLIB 
 
Builds an XLIB from two stack arguments.  Level two can be either a real number 
or a binary integer that's the number of the library to which the XLIB belongs. 
Level one must be the same argument type as level two and should be the command 
number of the desired XLIB.   
 
                                   ADDR 
 
Returns the address where the following stack arguments are located in memory: 
any ROM object, any XLIB belonging to a library stored in a port, any TAGGED 
that's either a BACKUP object or a LIBRARY stored a port.  One final attribute 
associated with ADDR that merits mentioning, regards those XLIBs that belong 
to the three intrinsic ROM libraries with a link table.  This routine can just 
as easily locate these address, as it can those in port memory.  Even if the 
memory location happens to be that of the hidden ROM, ADDR will determine its 
address. 
 
  
 
                                   RCLIB 
 
This multifunctional routine is to a library what RCL is to a directory.  RCLIB 
will recall a library as a fully operational directory.  All that is necessary 
to do is to put either the library's name or (real) number in level one.  Again 
this is slowed greatly on very large libraries.  RCLIB will work on any library 
including ROM (i.e. 2, 240, 1792).  Finally, the contents of any library's XLIB 
can be recalled to the stack; simply put the appropriate XLIB in level one, and 
the result will be comparable to using RCL on variable stored in a directory. 
 
---------- 
 
A final word of caution; do *not* attempt to implement a bank shift using 
either PEEK, or SEEK, if this library is stored in port 0, or anywhere in 
the address space being displaced.  This means both of the 32k banks that 
are affected by setting flag 14 are off limits, as far as this feature is 
concerned, for the storing of this library.  Should there be any question 
about this, or anything else, feel free to call, or write, and I shall be 
glad to provide any answers of which I might be capable :-). 
 
 
Rick Grevelle 
(409) 774-1169 
ftg0673@tamsun.tamu.edu