H P   4 8 S X   I n t e r n a l s 
 
                               Derek S. Nickel 
 
                               30 January 1991 
 	================================================================ 
		Forward 
	================================================================ 
 
	This documnent describes some of the internals of the HP 48SX 
	calculator.  Its intended audience is people with a good under- 
	standing of the basic HP 48SX who want to explore the internals 
	of the HP 48SX. 
 
	The information contained here is from a variety of 
	sources:  HP-71B Internal Design Specifications, ROM analysis 
	and other posted information. 
 
	Nothing is perfect.  Double check these notes if you plan to use 
	the information that they contain. 
 
	Send comments and questions to: 
 
		Derek S. Nickel 
		15 Maple Lane 
		Walnut Creek, CA 94595-1718 
 	================================================================ 
		Usage Notes 
	================================================================ 
 
	In the examples, when ASC\-> is used, the last four characters 
	are the checksum and are not part of the object.  Note that 
	when atomic objects are viewed as a string (via \->ASC or the 
	Memory Scanner) they appear backwards.  This is because the 
	string representation is viewed least-significant-nibble to 
	most-significant nibble in left to right order, whereas binary 
	data is viewed in right to left order. 
 
	Most of the examples list the internal representation as: 
	12345 6789 ABC DEF0 
 
	This corresponds to a memory dump ('48 style) of: 
	xxxxx: 543219876CBA0FED 
 
	or a HEX dump (VAX/VMS style) of: 
	                  DE F0 AB C6 78 91 23 45 E#.x....         xxxxx 
 	================================================================ 
		Prologs 
	================================================================ 
 
	In the HP 48SX, there are many different data types.  Some are 
	common and easy to use: Real Number, Complex Number, Array, 
	String, Binary Integer, List, Directory, Algebraic, Unit, 
	Tagged, Graphic, Backup, Program, Global Name and Local Name. 
	Some are common but hard to create:  Library, Library Data and  
	XLIB Name.  And some, at the user level are nonexistant: 
	System Binary, Long Real, Long Complex, Character, Linked Array 
	and Code. 
 
	One thing that all of these data types have in common is a five 
	nibbles header. This header identifies the data type of the data 
	that follows the header.  This header is called a prolog. 
 	================================================================ 
		Prologs (by prolog address) 
	================================================================ 
 
	Prolog	Object Name	Type # 
	------	--------------	------ 
	02911	System Binary	  20 
	02933	Real Number	   0 
	02955	Long Real	  21 
	02977	Complex Number	   1 
	0299D	Long Complex	  22 
	029BF	Character	  24 
	029E8	Array		 3,4 
	02A0A	Linked Array	  23 
	02A2C	String		   2 
	02A4E	Binary Integer	  10 
	02A74	List		   5 
	02A96	Directory	  15 
	02AB8	Algebraic	   9 
	02ADA	Unit		  13 
	02AFC	Tagged		  12 
	02B1E	Graphic		  11 
	02B40	Library		  16 
	02B62	Backup		  17 
	02B88	Library Data	  26 
	02D9D	Program		   8 
	02DCC	Code		  25 
	02E48	Global Name	   6 
	02E6D	Local Name	   7 
	02E92	XLIB Name	  14 
 
 	================================================================ 
		Prologs (by type number) 
	================================================================ 
 
	Type #	Prolog	Object Name 
	------	------	-------------- 
	   0	02933	Real Number 
	   1	02977	Complex Number 
	   2	02A2C	String 
	   3	029E8	Real Array 
	   4	029E8	Complex Array 
	   5	02A74	List 
	   6	02E48	Global Name 
	   7	02E6D	Local Name 
	   8	02D9D	Program 
	   9	02AB8	Algebraic 
	  10	02A4E	Binary Integer 
	  11	02B1E	Graphic 
	  12	02AFC	Tagged 
	  13	02ADA	Unit 
	  14	02E92	XLIB Name 
	  15	02A96	Directory 
	  16	02B40	Library 
	  17	02B62	Backup 
	  18	none	Command 
	  19	none	Function 
	  20	02911	System Binary 
	  21	02955	Long Real 
	  22	0299D	Long Complex 
	  23	02A0A	Linked Array 
	  24	029BF	Character 
	  25	02DCC	Code 
	  26	02B88	Library Data 
	  27	other	Unknown prolog 
 
	Commands and Functions can be expressed as either their address 
	or as XLIB Names.  For example, DUP is normallay represented by 
	the address 1FB87, but it can also be represented by XLIB 2 269 
	(02E9E 002 10D). 
 	================================================================ 
		Internal Object Type Numbers 
	================================================================ 
 
	The following table lists the internal object types (iTypes) and 
	the objects that they match.  These iTypes are used in the 
	internal RPL operations to do argument type checking.  Note that 
	if the first nibble is an F, then a second nibble follows. 
 
	Also, if a operation requires more that one argument, then each 
	argument will be represented as a digit in the Systen Binary 
	that is used for argument type checking.  For example, the 
	System Binary number <C15h> would mean that stack level one 
	must contain a List, stack level two must contain a Real Number 
	and stack level three must contain a Graphic. 
 
	One nibble iTypes: 
	iType	Objects 
	------	-------------------------------------------------------- 
	<0h>	Any 
	<1h>	Real Number 
	<2h>	Complex Number 
	<3h>	String 
	<4h>	Array 
	<5h>	List 
	<6h>	Global Name 
	<7h>	Local Name 
	<8h>	Program 
	<9h>	Algebraic 
	<Ah>	Symbolic (Algebraic or Global Name) 
	<Bh>	Binary Integer 
	<Ch>	Graphic 
	<Dh>	Tagged 
	<Eh>	Unit 
 
	Two nibble iTypes (starts with F): 
	iType	Objects 
	------	-------------------------------------------------------- 
	<Fh>	XLIB Name 
	<1Fh>	System Binary 
	<2Fh>	Directory 
	<3Fh>	Long Real 
	<4Fh>	Long Complex 
	<5Fh>	Linked Array 
	<6Fh>	Character 
	<7Fh>	Code 
	<8Fh>	Library 
	<9Fh>	Backup 
	<AFh>	Library Data 
	<BFh>	?? prolog <02BAAh> 
	<CFh>	?? prolog <02BCCh> 
	<DFh>	?? prolog <02BEEh> 
	<EFh>	?? prolog <02C10h> 
	<FFh>	?? <191BEh> 
 	================================================================ 
		Atomic Data Types 
	================================================================ 
 
	Atomic data types are listed after each field description, in 
	parenthesis.  Note that some atomic data types are more atomic 
	than others. 
 
	**** ASCIC **** 
 
	ASCII counted character strings are represented by length and 
	data fields.  ASCII counted character strings are the basis for 
	Global Name, Local Name and Tagged data types, as well as 
	components in other objects. 
 
	  N          2  1     0 
	+-------------+--------+ 
	| String Data | Length | 
	+-------------+--------+ 
            Length        2 
 
	where N = Length/2 + 1. 
 
	**** ASCII **** 
 
	ASCII character strings are represented as a sequence of bytes 
	(ASCII characters).  The length of the ASCII character string is 
	specified elsewhere.  ASCII character strings are called ASCII 
	in the field descriptions.  ASCII character strings are the 
	basis for String data types. 
 
	  N          0 
	+-------------+ 
	| String Data | 
	+-------------+ 
            Length 
 
	**** ASCIX **** 
 
	Extended ASCII counted character strings are represented by 
	length and data fields.  If the length is zero, only a single 
	length field is present.  If the length is non-zero, then there 
	are two identical length fields, one before and one after the 
	string data.  Extended ASCII counted character strings are the 
	used in Directory, Library and Backup data types. 
 
	  N   N-1 N-2         2  1     0 
	+--------+-------------+--------+ 
	| Length | String Data | Length | 
	+--------+-------------+--------+ 
            2        Length        2 
 
	where N = Length/2 + 2. 
 	Atomic Data Types (cont) 
 
	Or, if length is zero: 
 
	  1 0 
	+----+ 
	| 00 | 
	+----+ 
	  2 
 
	**** BCDx **** 
 
	BCD numbers (binary coded decimal) are represented by a mantissa, 
	sign and exponent fields.  These are two kinds of BCD numbers in 
	the HP48SX, 12-form and 15-form BCD numbers, called BCD12 and 
	BCD15 in the field descriptions. 
 
	Both kinds have several things in common: 
 
	    *	A mantissa.  Each digit of the number is represented by 
		one nibble in the mantissa.  12-form BCD numbers have a 
		12 digit mantissa and 15-form BCD numbers have a 15 
		digit mantissa.  There is an implied decimal point after 
		the Most Significant Digit (msd) with respect to the 
		exponent. 
 
	    *	A sign nibble.  Positive numbers are represented by a 
		0 and negative numbers are represented by a 9. 
 
	    *	An exponent.  The exponent is in 10's compement. 
		12-form BCD numbers have a 3 nibble exponent and 15-form 
		BCD numbers have a 5 digit exponent. 
 
	12-form BCD numbers are the basis for Real Number, Complex 
	Number, Real Array and Complex Array data types. 
 
	15-form BCD numbers are the basis for Long Real and Long 
	Complex data types. 
 
	BCD12: 
 
         15 14                     3  2   0 
	+--+------------------------+------+ 
	|S | msd..  Mantissa  ..lsd | Exp  | 
	+--+------------------------+------+ 
	 1             12              3 
 
	BCD15: 
 
	 21 20                           5  4       0 
	+--+------------------------------+----------+ 
	|S | msd...    Mantissa    ...lsd |   Exp    | 
	+--+------------------------------+----------+ 
 	Atomic Data Types (cont) 
 
	**** BINx **** 
 
	Binary integers are represented by a data field.  Binary integers 
	are called BINx in the field descriptions (where x = the number 
	of nibbles that the number occupies).  Binary integers are the 
	basis for Binary Integers and System Binary data types. 
 
	  N          0 
	+-------------+ 
	| Binary Data | 
	+-------------+ 
	       x 
 
	where N = x - 1. 
 
	**** CHAR **** 
 
	ASCII characters are represented by a one byte (two nibble) data 
	field.  ASCII characters are called CHAR in the field 
	descriptions.  ASCII characters are the basis for the Character 
	data type. 
 
	  1        0 
	+-----------+ 
	| Character | 
	+-----------+ 
	      2 
 
	**** CODE **** 
 
	Machine code is represented as a sequence of nibbles that is the 
	machine code.  Machine code is called CODE in the field 
	descriptions.  Machine code is the basis for the Code data type. 
 
	Examples in this document use the HP mneumonics. 
 	================================================================ 
		System Binary (02911) 
	================================================================ 
 
	<prolog><data> 
 
	<prolog> = 02911 (BIN5) 
 
	<data> = five nibble binary integer (BIN5) 
 
	There are several tables of System Binary numbers: 
 
	 addr	  HEX    description 
	------	-------  ------------------------------------------------ 
	03F8B	<2933h>  Real Number prolog 
	03F95	<2977h>  Complex Number prolog 
	03F9F	<2A74h>  List prolog 
	03FA9	<2911h>  Global Name prolog 
	03FB3	<2D9Dh>  Program prolog 
	03FBD	<2AB8h>  Algebraic prolog 
	03FC7	<2A96h>  Directory prolog 
	03FD1	<2E6Dh>  Local Name prolog 
	03FDB	<2955h>  Long Real prolog 
	03FE5	<2ADAh>  Unit prolog 
 
	 addr	 HEX	 DEC 
	------	------	------ 
	03FEF	<0h>	<0d> 
	03FF9	<1h>	<1d> 
	04003	<2h>	<2d> 
	0400D	<3h>	<3d> 
	04017	<4h>	<4d> 
	04021	<5h>	<5d> 
	0402B	<6h>	<6d> 
	04035	<7h>	<7d> 
	0403F	<8h>	<8d> 
	04049	<9h>	<9d> 
	04053	<Ah>	<10d> 
	0405D	<Bh>	<11d> 
	04067	<Ch>	<12d> 
	04071	<Dh>	<13d> 
	04073	<Eh>	<14d> 
	04085	<Fh>	<15d> 
	0408F	<10h>	<16d> 
	04099	<11h>	<17d> 
	040A3	<12h>	<18d> 
	040AD	<13h>	<19d> 
	040B7	<14h>	<20d> 
	040C1	<15h>	<21d> 
	040CB	<16h>	<22d> 
	040D5	<17h>	<23d> 
	040DF	<18h>	<24d> 
	040E9	<19h>	<25d> 
	040F3	<1Ah>	<26d> 
	040FD	<1Bh>	<27d> 
	04107	<1Ch>	<28d> 
	04111	<1Dh>	<29d> 
	0411B	<1Eh>	<30d> 
	04125	<1Fh>	<31d> 
 	System Binary (cont) 
 
	0412F	<20h>	<32d> 
	04139	<21h>	<33d> 
	04143	<22h>	<34d> 
	0414D	<23h>	<35d> 
	04157	<24h>	<36d> 
	04161	<25h>	<37d> 
	0416B	<26h>	<38d> 
	04175	<27h>	<39d> 
	0417F	<28h>	<40d> 
	04189	<29h>	<41d> 
	04193	<2Ah>	<42d> 
	0419D	<2Bh>	<43d> 
 
	There are several routines to convert between System Binary and 
	other data types.  No error checking is performed by these 
	routines. 
 
	 addr	 name	description 
	------	------	------------------------------------------------ 
	18CEA	R\->SB	Real Number to System Binary 
	18DBF	SB\->R	System Binary to Real Number 
 
	Example: 
 
	Create a System Binary with a decimal value of 48. 
 
	02911 00030 
 
	"1192003000C53E" ASC\-> returns <30h> 
 
	 - or - 
 
	48 #18CEAh SYSEVAL returns <30h> 
 	================================================================ 
		Real Number (02933) 
	================================================================ 
 
	<prolog><data> 
 
	<prolog> = 02933 (BIN5) 
 
	<data> = 12-form BCD number (BCD12) 
 
	There are several tables of Real Number and Long Real numbers: 
 
	 addr	 value 
	------	---------------- 
	2A2B4	0 
	2A2C9	1 
	2A2DF	2 
	2A2F3	3 
	2A308	4 
	2A3D1	5 
	2A332	6 
	2A347	7 
	2A35C	8 
	2A371	9 
	2A386	-1 
	2A39B	-2 
	2A3B0	-3 
	2A3C5	-4 
	2A3DA	-5 
	2A3EF	-6 
	2A404	-7 
	2A419	-8 
	2A42E	-9 
	2A443	3.14159265359 
	2A458	3.14159265358979 (Long Real) 
	2A472	9.99999999999E499 
	2A487	-9.99999999999E499 
	2A49C	1.E-499 
	2A4B1	-1.E-499 
	2A4C6	0 (Long Real) 
	2A4E0	1 (Long Real) 
	2A4FA	2 (Long Real) 
	2A514	3 (Long Real) 
	2A52E	4 (Long Real) 
	2A548	5 (Long Real) 
	2A562	.1 (Long Real) 
	2A57C	.5 (Long Real) 
	2A596	10 (Long Real) 
 
	There are several routines to convert between Real Number and 
	other data types.  No error checking is performed by these 
	routines. 
 
	 addr	 name	description 
	------	------	------------------------------------------------ 
	2A5B0	LR->R	Long Real to Real Number 
	2A5C1	R->LR	Real Number to Long Real 
 	Real Number (cont) 
 
	Example: 
 
	Create a Real Number with the value of the golden mean: 
 
	02933 0161863398875000 
 
	"3392000057889330816106AB0" ASC\-> returns 
		1.61863398875 
 
 	================================================================ 
		Long Real (02955) 
	================================================================ 
 
	<prolog><data> 
 
	<prolog> = 02955 (BIN5) 
 
	<data> = 15-form BCD number (BCD15) 
 	================================================================ 
		Complex Number (02977) 
	================================================================ 
 
	<prolog><real-part><imaginary-part> 
 
	<prolog> = 02977 (BIN5) 
 
	<real-part> = 12-form BCD number (BCD12) 
 
	<imaginary-part> = 12-form BCD number (BCD12) 
 	================================================================ 
		Long Complex (0299D) 
	================================================================ 
 
	<prolog><real-part><imaginary-part> 
 
	<prolog> = 0299D (BIN5) 
 
	<real-part> = 15-form BCD number (BCD15) 
 
	<imaginary-part> = 15-form BCD number (BCD15) 
 	================================================================ 
		Character (029BF) 
	================================================================ 
 
	<prolog><data> 
 
	<prolog> = 029BF (BIN5) 
 
	<data> = ASCII coded character (CHAR) 
 	================================================================ 
		Array (029E8) 
	================================================================ 
 
	<prolog><size><item-prolog><#dims><dim-1>...<dim-n><item-1>... 
	    <item-m> 
 
	<prolog> = 029EB (BIN5) 
 
	<size> = number of nibbles remaining (BIN5) 
 
	<item-prolog> = prolog for array elements (BIB5) 
 
	<#dims> = number of array dimensions (BIN5) 
 
	<dim-i> = i-th dimension (BIN5) 
 
	<item-j> = j-th item (ANY) 
 
	n = <#dims> 
	m = <dim-1> * <dim-2> * ... * <dim-n> 
 
	The items in the array are stored in Row Major order (all of the 
	first rows elements are group together, followed by the second 
	row, and so forth.) 
 
	In normal calculator operations: 
 
	    *	Only one and two dimensional arrays are supported. 
 
	    *	Only Real Numbers and Complex Numbers are supported as 
		array elements (items). 
 
	Some assumtions are made about various fields with normal 
	operations: 
 
	    *	If <item-prolog> is not Real Number, then its assumed to 
		be Complex Number. 
 
	    *	If #Dims is not 1, its assumed to be 2. 
 
	This applies to the Matrix Editor, GET and so forth. 
 
	But the '48 uses other types of arrays internally.  For example, 
	message tables are "Array of String". 
 	================================================================ 
		Linked Array (02A0A) 
	================================================================ 
 
	<prolog><size><???> 
 
	<prolog> = 02A0A (BIN5) 
 
	<size> = number of nibbles remaining (BIN5) 
 
	<???> = undetermined... 
 	================================================================ 
		String (02A2C) 
	================================================================ 
 
	<prolog><size><data> 
 
	<prolog> = 02A2C (BIN5) 
 
	<size> = number of nibbles remaining (BIN5) 
 
	<data> = (<size>-5)/2 byte character string (ASCII) 
 	================================================================ 
		Binary Integer (02A4E) 
	================================================================ 
 
	<prolog><size><data> 
 
	<prolog> = 02A4E (BIN5) 
 
	<size> = number of nibbles remaining (BIN5) 
 
	<data> = binary integer (BINx, where x = <size> - 5) 
 
	Most Binary Integers have a data size of 16 nibbles or 64 bits 
	(<size> = 21).  But some have a smaller data size.  For example, 
	the BYTES command returns a Binary Integer (the checksum) with a 
	data size of 4 nibbles or 16 bits (<size> = 9), whereas the Hash 
	Table in a Library looks like a very large Binary Integer. 
 	================================================================ 
		List (02A74) 
	================================================================ 
 
	<prolog><object-1>...<object-n><end-marker> 
 
	<prolog> = 02A74 (BIN5) 
 
	<object-i> = i-th object (ANY) 
 
	<end-marker> = 0312B (BIN5) 
 	================================================================ 
		Directory (02A96) 
	================================================================ 
 
	<prolog><attachments><offset-1><end-dir> 
	    <name-n><object-n><offset-n>... 
	    <name-2><object-2><offset-2> 
	    <name-1><object-1> 
 
	<prolog> = 02A96 (BIN5) 
 
	<attachments> = see comments (BIN3) 
 
	<end-dir> = 00000; end of directory marker (backwards scanned). 
	    This is in the position that the <offset-n+1> field would 
	    have occuppied (BIN5) 
 
	<offset-i> = offset (backward pointing) from the beginning of 
	    the i'th offset field to the beginning of the i'th object's 
	    name.  (BIN5) 
 
	<name-i> = the name of the i-th object (ASCIX) 
 
	<object-i> = the i'th object in the directory (ANY) 
 
	Comments: 
 
	The meaning of the <attachments> field is based on whether or 
	not the directory is the HOME directory. 
 
	HOME directory:  the <attachments> field contains the number of 
	libraries attached to the HOME directory, including the default, 
	'hidden' libraries: Library 2, standard functions; Library 1792, 
	flow control statments. 
 
	Subdirectory:  the <attachments> field contains the library 
	number of the library attached to this subdirectory or 7FF if 
	no library is attached. 
 	================================================================ 
		Algebraic (02AB8) 
	================================================================ 
 
	<prolog> ... <end-marker> 
 
	<prolog> = 02AB8 (BIN5) 
 
	The "..." part is a sequence of objects and operations. 
 
	<end-marker> = 0312B (BIN5) 
 
	Example: 
 
	Create the expression 'A-2'. 
 
	02AB8		Algebraic 
	02E48 01 41	'A' (Global Name) 
	2A2DE		2 (address in ROM) 
	1AD09		- 
	0312B		End Marker 
 
	"8BA2084E201014ED2A209DA1B21303637" \-> returns 
		'A-2' 
 	================================================================ 
		Unit (02ADA) 
	================================================================ 
 
	<prolog><numeric-data><unit-1>...<unit-n><operation-1>... 
	    <operation-n><end-marker> 
 
	<prolog> = 02ADA (BIN5) 
 
	<numeric-data> = the base data, if not Real Number, then will 
	    be displayed as UNKNOWN (ANY) 
 
	<unit-i> = unit component (normally String or Real Number) (ANY) 
 
	<operation-j> = unit arithmetic indicator.  These indicators 
	    point to null lists { }, but are interpreted by the OS as 
	    simple unit operations (* / and so forth) (BIN5) 
 
	    10B5E * (unit operator) 
	    10B68 / (unit operator) 
	    10B72 ^ (unit operator) 
	    10B7C Character prefix (unit operator) 
	    10B86 _ (unit operator) 
 
	<end-marker> = 0312B (BIN5) 
 	================================================================ 
		Tagged (02AFC) 
	================================================================ 
 
	<prolog><name><object> 
 
	<prolog> = 02AFC (BIN5) 
 
	<name> = the tag (ASCIC) 
 
	<object> = the tagged object (ANY) 
 
	Example: 
	Create a the Real Number 1.23456789012 with a tag of "ABC" 
 
	02AFC 03 41 42 43 02933 0123456789012000 
 
	"CFA20301424343392000021098765432107141" ASC\-> returns 
		ABC: 1.23456789012 
 	================================================================ 
		Graphic (02B1E) 
	================================================================ 
 
	<prolog><size><#rows><#columns><data> 
 
	<prolog> = 02B1E (BIN5) 
 
	<size> = number of nibbles remaining (BIN5) 
 
	<#rows> = number of pixel rows (BIN5) 
 
	<#columns> = number of pixel columns (BIN5) 
 
	<data> = graphic data, <size>-15 nibbles (BINx) 
 
	Each pixel in the Graphic is represented by a bit in <data>. 
	The pixels are grouped first by row and then by column. 
 
	The pixels for each row run for left to right and the bits for 
	those pixels run from least significant bit to most significant 
	bit.  Note that each row of pixels is padded to an even number 
	of nibbles.  For example:  a normal 131 X 64 Graphic requires 
	34 nibbles (136 bits) per row for a total of 2176 nibbles (not 
	counting the overhead of 20 nibbles). 
 
	X = <#columns> - 1 
	Y = <#rows> - 1 
 
	   0                       X 
	  +-------------------------+ 
	0 |                         | 
	  |                         | 
	  |         Display         | 
	  |                         | 
	Y |                         | 
	  +-------------------------+ 
 
	M = <#rows> - 1 
	N = 2*CEIL(<#columns>/8) - 1 
	N' = unpadded row size 
	??? = padding 
 
	  N  N'                     0 
	+---+-->>--------------------+ 
	|???|                        |  Row 0 
	+---+--<<--------------------+ 
	|???|                        |  Row 1 
	+---+-->>--------------------+ 
		:			: 
	+---+-->>--------------------+ 
	|???|                        |  Row M 
	+---+--<<--------------------+ 
 	================================================================ 
		Library (02B40) 
	================================================================ 
 
	<prolog><size><library-name><library-number><hash-table-offset> 
	    <message-table-offset><link-table-offset><config-offset> 
	    <bulk-of-library><checksum> 
 
	<prolog> = 02B40 (BIN5) 
 
	<size> = number of nibbles remaining (BIN5) 
 
	<library-name> = Extended ASCII counted character string (ASCIX) 
 
	<library-number> = library number (BIN3) 
 
	<hash-table-offset> = offset to hash table (BIN5) 
 
	<message-table-offset> = offset to message table (BIN5) 
 
	<link-table-offset> = offset to link table (BIN5) 
 
	<config-offset> = offset to configuration code (BIN5) 
 
	<bulk-of-library> : <hash-table>, <message-table>, <link-table>, 
	    <config-code> and the rest (in any order) 
 
	<checksum> = internal library checksum (BIN4) 
 
	<hash-table> : <ht-prolog><ht-size><offset-1>...<offset-16> 
	    <nt-size><nt-entry-1>...<nt-entry-n><nt-offset-1>... 
	    <nt-offset-n> 
 
	<ht-prolog> = 02A4E (Binary Integer) (BIN5) 
 
	<ht-size> = size of hash table without the prolog (BIN5) 
 
	<offset-i> = offset into the name table for the first command 
	    with an i-character name (BIN5) 
 
	<nt-size> = size in nibbles of the name table (BIN5) 
 
	<nt-entry-j> : <command-name><xlib-number> 
 
	<command-name> = ASCII counted character string (ASCIC) 
 
	<xlib-number> = XLIB command number (BIN3) 
 
	<nt-offset-k> = offset to <nt-entry-j> for XLIB command k (BIN5) 
	    This offset is backward pointing. 
 
	<message-table> = Array of String.  Each array element is a 
	    message. 
 
	<link-table> : <lt-prolog><lt-size><lt-entry-1>...<lt-entry-n> 
 
	<lt-prolog> = 02A4E (BIN5) 
 
	<lt-size> = size of link table without the prolog (BIN5) 
 	Library (cont) 
 
	<lt-entry-i> = offset to i-th command in this library (BIN5) 
 
	<config-code> = RPL subprogram that performs configuration 
	    commands 
 
	Comments: 
 
	The hash table and link table are very large Binary Integers. 
	The message table is an Array of String. 
 
	Example: 
 
	Unthread part of the stop watch library.  See the Voayager 
	Reference Manual for details on Voyager commands. 
 
	Voyager> load 1 sw-a 
	Voyager> ut 80000 
	80000: ; *** Library 768: SW-A *** 
	80000: 02B40 ! Library 
	80005: 01608 ! 5640 nibbles (next RPL at 8160D) 
	8000A: [...] ! Library name: "SW-A" 
	80016: 300   ! Library number 768 
	80019: 00014 ! Hash table at 8002D 
	8001E: 001F2 ! Message table at 80210 
	80023: 00107 ! Link table at 8012A 
	80028: 01543 ! Configuration code at 8156B 
	Voyager> exam hash 8002D 300 
	8002D: ; *** Hash table for library 300 (XLIB 768) *** 
	8002D: 02A4E ! (Binary Integer) 
	80032: 000F8 ! 248 nibbles (next at 8012A) 
	80037: 00000 !    1 none 
	8003C: 00000 !    2 none 
	80041: 00000 !    3 none 
	80046: 00046 !    4 at 8008C 
	8004B: 00000 !    5 none 
	80050: 00000 !    6 none 
	80055: 00085 !    7 at 800DA 
	8005A: 00093 !    8 at 800ED 
	8005F: 00000 !    9 none 
	80064: 00000 !   10 none 
	80069: 00000 !   11 none 
	8006E: 00000 !   12 none 
	80073: 00000 !   13 none 
	80078: 00000 !   14 none 
	8007D: 00000 !   15 none 
	80082: 00000 !   16 none 
	80087: 0007B ! 123 nibbles (next at 80102) 
	8008C: [...] !   DOSW (XLIB 768 0) 
	80099: [...] !   PALL (XLIB 768 5) 
	800A6: [...] !   PSP+ (XLIB 768 4) 
	800B3: [...] !   VALL (XLIB 768 3) 
	800C0: [...] !   VSP+ (XLIB 768 1) 
	800CD: [...] !   VSP- (XLIB 768 2) 
	800DA: [...] !   RESETSW (XLIB 768 7) 
	800ED: [...] !   RCLSPLIT (XLIB 768 6) 
	80102: 00076 !   name for XLIB 768 0 at 8008C 
 	Library (cont) 
 
	80107: 00047 !   name for XLIB 768 1 at 800C0 
	8010C: 0003F !   name for XLIB 768 2 at 800CD 
	80111: 0005E !   name for XLIB 768 3 at 800B3 
	80116: 00070 !   name for XLIB 768 4 at 800A6 
	8011B: 00082 !   name for XLIB 768 5 at 80099 
	80120: 00033 !   name for XLIB 768 6 at 800ED 
	80125: 0004B !   name for XLIB 768 7 at 800DA 
	Voyager> exam link 8012A 300 
	8012A: ; *** Link table for library 300 (XLIB 768) *** 
	8012A: 02A4E ! (Binary Integer) 
	8012F: 000E1 ! 225 nibbles (next at 80210) 
	80134: 00167 !   XLIB 768 0 at 8029B 
	80139: 00183 !   XLIB 768 1 at 802BC 
	8013E: 001A4 !   XLIB 768 2 at 802E2 
	80143: 001C5 !   XLIB 768 3 at 80308 
	80148: 001E1 !   XLIB 768 4 at 80329 
	8014D: 00202 !   XLIB 768 5 at 8034F 
	80152: 0021E !   XLIB 768 6 at 80370 
	80157: 0023F !   XLIB 768 7 at 80396 
	8015C: 00254 !   XLIB 768 8 at 803B0 
	80161: 002DE !   XLIB 768 9 at 8043F 
	80166: 00303 !   XLIB 768 10 at 80469 
	8016B: 00328 !   XLIB 768 11 at 80493 
	80170: 0037D !   XLIB 768 12 at 804ED 
	80175: 0044F !   XLIB 768 13 at 805C4 
	8017A: 004E7 !   XLIB 768 14 at 80661 
	8017F: 00500 !   XLIB 768 15 at 8067F 
	80184: 00514 !   XLIB 768 16 at 80698 
	80189: 005BC !   XLIB 768 17 at 80745 
	8018E: 005E1 !   XLIB 768 18 at 8076F 
	80193: 00605 !   XLIB 768 19 at 80798 
	80198: 0069D !   XLIB 768 20 at 80835 
	8019D: 006CD !   XLIB 768 21 at 8086A 
	801A2: 0072A !   XLIB 768 22 at 808CC 
	801A7: 00753 !   XLIB 768 23 at 808FA 
	801AC: 00792 !   XLIB 768 24 at 8093E 
	801B1: 00819 !   XLIB 768 25 at 809CA 
	801B6: 00832 !   XLIB 768 26 at 809E8 
	801BB: 008B1 !   XLIB 768 27 at 80A6C 
	801C0: 008DA !   XLIB 768 28 at 80A9A 
	801C5: 00E8C !   XLIB 768 29 at 81051 
	801CA: 00F55 !   XLIB 768 30 at 8111F 
	801CF: 00F95 !   XLIB 768 31 at 81164 
	801D4: 00FBC !   XLIB 768 32 at 81190 
	801D9: 00FE7 !   XLIB 768 33 at 811C0 
	801DE: 010AC !   XLIB 768 34 at 8128A 
	801E3: 0111D !   XLIB 768 35 at 81300 
	801E8: 0113A !   XLIB 768 36 at 81322 
	801ED: 01155 !   XLIB 768 37 at 81342 
	801F2: 0116A !   XLIB 768 38 at 8135C 
	801F7: 011EE !   XLIB 768 39 at 813E5 
	801FC: 0136F !   XLIB 768 40 at 8156B 
	80201: 01383 !   XLIB 768 41 at 81584 
	80206: 01396 !   XLIB 768 42 at 8159C 
	8020B: 013A9 !   XLIB 768 43 at 815B4 
 	Library (cont) 
 
	Voyager> exam message 80210 300 
	80210: ; *** Message table for library 300 (XLIB 768) *** 
	80210: 029E8 ! Array 
	80215: 0007F ! 127 nibbles 
	8021A: 02A2C ! ...of String 
	8021F: 00001 ! 1 dimensional 
	80224: 00003 ! Dim-1 = 3 
	 . . . . . . ! 3 total elements 
	80229: [...] ! "Invalid SWDAT" 
	80248: [...] ! "Invalid Split#" 
	80269: [...] ! "Invalid Environment" 
	Voyager> ut 8156B 
	8156B: ; *** Configuaration code for library 300 (XLIB 768 40) *** 
	8156B: 02D9D ! Program 
	81570: [...] ! <300h> 
	8157A: 07709 ; Internal ATTACH to HOME directory (1:System Binary) 
	8157F: 0312B ! End Marker 
	Voyager> ut 8029B 
	8029B: ; *** DOSW (XLIB 768 0) *** 
	8029B: 02D9D ! Program 
	802A0: 18A1E ; save last RPL token, stack size, clear @706FD.S 
	802A5: [...] ! XLIB 768 8 
	802B0: 0312B ! End Marker 
	Voyager> exit 
 	================================================================ 
		Backup (02B62) 
	================================================================ 
 
	<prolog><size><name><data><???> 
 
	<prolog> = 02B62 (BIN5) 
 
	<size> = number of nibbles remaining (BIN5) 
 
	<name> = the name of the backup (ASCIX) 
 
	<data> = the backed-up data (ANY) 
 
	<???> = a System Binary, possably a checksum. 
 	================================================================ 
		Library Data (02B88) 
	================================================================ 
 
	<prolog><size><ident><data-1>...<data-n><end-marker> 
 
	<prolog> = 02B88 (BIN5) 
 
	<size> = number of nibbles remaining (BIN5) 
 
	<ident> = <library-number><object-number> (BIN5) 
 
	<library-number> = library number (BIN3) 
 
	<object-number> = object number (library specific) (BIN2) 
 
	<data-i> = the 'hidden' library data (ANY) 
 
	<end-marker> = 0312B (BIN5) 
 
	Example: 
 
	What's in 'MHpar' (MINEHUNT parameter) (EQ Library required)? 
 
	MINEHUNT STO MHpar \->ASC returns: 
 
	"88B205C900C010047A20E1B20... 
	...B21300040" 
 
	which translates to Library Data 268/0, contents: 
 
	{ Graphic 131 x 64 
	<1h> <1h> <1h> 
	"20000001000100000... 
	} 
 	================================================================ 
		Program (02D9D) 
	================================================================ 
 
	<prolog> ... <end-marker> 
 
	<prolog> = 02D9D (BIN5) 
 
	The "..." part is a sequence of objects. 
 
	<end-marker> = 0312B (BIN5) 
 
	Examples: 
 
	1) Write a strictly user-mode program to drop the stack level 
	two object.  This operation is called NIP by some people. 
 
	02D9D	Program 
	2361E	\<< 
	1FBBD	  SWAP 
	1FBD8	  DROP 
	23639	\>> 
	0312B	End Marker 
 
	"D9D29E1632DBBE18DDF193632B21306A65" ASC\-> returns 
	    \<< SWAP DROP \>> 
 
	2) Write the same program using internal routines, with error 
	checking (standalone version, non-library). 
 
	02D9D	Program 
	18A8D	Verify DEPTH >= 2 
	60F9B	drop level two object 
	0312B	End Marker 
 
	"D9D20D8A81B9F06B2130D01D" ASC\-> returns 
		External External 
 	================================================================ 
		Code (02DCC) 
	================================================================ 
 
	<prolog><size><machine-code> 
 
	<prolog> = 02DCC (BIN5) 
 
	<size> = number of nibbles remaining (BIN5) 
 
	<machine-code> = machine code (<size>-5 nibbles) (CODE) 
 	================================================================ 
		Global Name (02E48) 
	================================================================ 
 
	<prolog><name> 
 
	<prolog> = 02E48 (BIN5) 
 
	<name> = ASCII counted character string (ASCIC) 
 
	Example: 
	Create a Global Name called 'GBL'. 
 
	02E48 03 47 42 4C 
 
	"84E20307424C4A205" ASC\-> returns 'GBL' 
 	================================================================ 
		Local Name (02E6D) 
	================================================================ 
 
	<prolog><name> 
 
	<prolog> = 02E6D (BIN5) 
 
	<name> = ASCII counted character string (ASCIC) 
 
	Example: 
	Create a Local Name called 'LCL'. 
 
	02E6D 03 4C 43 4C 
 
	"D6E2030C434C4DCA1" ASC\-> returns 'LCL' 
	Executing EVAL at this point will generate an 'EVAL Error: 
	Undefined Local Name'. 
 	================================================================ 
		XLIB Name (02E92) 
	================================================================ 
 
	<prolog><library-number><object-number> 
 
	<prolog> = 02E92 (BIN5) 
 
	<library-number> = library number (BIN3) 
 
	<object-number> = object number with library (BIN3) 
 
	Example: 
	The XLIB name for the EQ Library's MINEHUNT is XLIB 268 0 
 
	02E92 10C 000 
 
	If you have the EQ Library: 
	"29E20C01000FEA7" ASC\-> returns MINEHUNT 
 
	If you don't: 
	"29E20C01000FEA7" ASC\-> returns XLIB 268 0