by Jeff Broido 
                               TRAC.DOC file 
 
               Copyright 1990 by Broido Computer Consulting. 
                All rights reserved.  The right is granted 
                    to anyone to copy these materials, 
                        but they must not be sold. 
 
 
OVERVIEW 
-------- 
 
The HP48SX Print Trace system provides a facility for the HP48SX externally 
similar to the built-in print trace feature of the HP28C and HP28S.  This  
facility of the 28s allows you to trace almost all calculator operations to 
an 82240A or 82240B thermal printer.  The HP48SX provides no native print  
trace feature, but does provide a generalized facility called "Vectored  
ENTER" which I have used to implement this system.  Note that my output  
format is almost identical to that of the HP28 series calculators.  I chose 
this format for consistency, not because I find it aesthetically pleasing.  
This system can be modified by the user to print in almost any format  
desired. 
 
PROCEDURE 
--------- 
 
 1. Using Kermit, load TRAC into the HOME directory.  For your reference,  
    the BYTES command yields a checksum of # D720h and a size of 780.5  
    bytes. 
 
 2. Optional: Put 'TRAC' on stack level 2 and 81.2 on stack level 1.  Go to 
    the right-shift-MODES menu and hit ASN.  This will assign TRAC to user  
    keyboard position 81.2, or left-shift-right-shift.  In other words, if  
    the HP48SX is in user mode, hitting the orange key followed by the blue 
    key will evaluate the TRAC function.  To put your calculator into user  
    keyboard mode, hit left-shift-USR twice.  If you are successful, the  
    USER annunciator will appear just below the top line of the display. 
 
 3. To toggle between tracing mode and normal mode, either type TRAC, hit  
    the TRAC key from the HOME menu or, if you've performed optional step  
    2. above, do a left-shift-right-shift (orange followed by blue).   
    Either "Print trace on." or "Print trace off." will appear at the top  
    of the stack display as appropriate. 
 
 
SYSTEM DESCRIPTION 
------------------ 
 
IMPORTANT NOTE: in this document, [alpha] refers to the greek lowercase  
alpha which is accessed in alhpa mode, right-shift A and [beta] refers to  
the greek lowercase beta which is accessed in alpha mode right shift B.   
For example, if I mention a variable named '[beta]ENTER', to type the name  
you would hit the apostrophe key followed by the alpha key twice (to put  
the calculator in alpha mode) followed by right-shift B followed by E, N,  
T, E and R. 
 
This Print Trace system uses an as-yet undocumented facility called  
"Vectored ENTER."  The only reference so far to this facility is in  
Appendix E of the HP48SX Owner's Manual.  This states that when flag -63 is 
set, User-defined ENTER is activated.  I am indebted to Ron at the Hewlett- 
Packard Calculator Support department, Corvalis, OR for explaining it  
further.  To summarize his explanation and my findings: 
 
    If "Vectored ENTER" mode (flag -63) is set and the calculator is in  
    USER (NOT 1USR) mode (via the keyboard or setting flag -62) 
 
    AND     There is a variable named '[alpha]ENTER' in the current path,  
            BEFORE any operation, whenever the command line would normally  
            be pushed to the stack, it is pushed to stack level 1 delimited 
            by " characters on either end instead.  Following this action,  
            the variable named '[alpha]ENTER' is evaluated.  Typically  
            [alpha]ENTER would be a program.  If the contents of the  
            command line are not a single string, this action causes the  
            entire command line to be placed on the stack as a single  
            string.  If it was already a string, it winds-up on the stack  
            with an extra set of delimiting " characters.  This means that  
            if either the OBJ-> or STR-> command is executed in the  
            [alpha]ENTER program, the stack will contain precisely what it  
            would have if the calculator were not in Vectored ENTER mode. 
 
    AND/OR  There is a variable named '[beta]ENTER' in the current path,  
            AFTER any operation is performed, the name of the operation is  
            placed on stack level 1 as a string.  PURGE and ENTER itself  
            are represented by the null string ("").  If, however, ENTER is 
            acting as DUP, "DUP" is returned.  If the operation is  
            unsuccessful, its name is not placed on the stack.  Menu  
            navigation is not reported, but path navigation is. 
 
The TRAC function checks a list in the home directory with the name  
'[alpha][beta]FG'.  If the first element of the list indicates that tracing 
is off (or the list doesn't exist), tracing is turned on and that fact is  
indicated in the first element of the list.  If the first element of the  
list indicates that tracing is on, it is turned off and similarly noted.  
When tracing is turned on, the state of flag -62 is indicated in element 2  
of the '[alpha][beta]FG' list.  When tracing is turned off, the former  
state of flag -62 is restored.  In other words, if the calculator was in  
USER mode when tracing was turned on, it is left in USER mode when it is  
turned off.  If the calculator was not in USER mode when tracing was turned 
on, it is taken out of USER mode when tracing is turned off.  This is  
necessary since the Vectored ENTER mode is only effective if the calculator 
is also in USER mode.  To turn tracing on, TRAC sets flags -62 and -63 and  
places programs in variables named '[alpha]ENTER' and '[beta]ENTER' in the  
HOME directory.  To turn tracing off, TRAC clears flag -63 and when  
appropriate clears flag -62 and purges the variables named '[alpha]ENTER'  
and '[beta]ENTER' from the home directory.   
 
The [alpha]ENTER program simply makes a copy of the command line as a  
string padded on the right with a blank in variable [alpha][beta]ENTER and  
executes the OBJ-> command to leave the stack in the same state it would  
have been in had Vectored ENTER not been in effect. 
 
The [beta]ENTER program concatenates the current function to the end of the 
command line saved in [alpha][beta]ENTER and prints it.  If there is no  
variable [alpha][beta]ENTER, this means that there was no command line and  
[beta]ENTER simply prints the operation.  After it has done this,  
[beta]ENTER prints level 1 of the stack prefixed by the characters "1: "  
unless the stack is empty, in which case it prints the character string  
"[Empty Stack]".  [beta]ENTER then prints 0000300000081000000810000000700000060000000081FFFFF1000000000EFFFF300000000000EFF7000000 
GROB 64 64 0000006FF700000000000EDBFF30000000008BFFFFF100000000FEFFFFF700000008FFFFFFFF100000067FFFFFFF3000000BFFFFFFFFF0000089FFFFFFFFF100006CFFFFFFFFF300003FFFFFFFFFF700089FFFFFFFFFFF0008C7DFFFFFFFFF100CCF7FFFFFFFFF3006CF3EFFFFFFFF300BEFB3EFFFFFFF7001FFFFFFFFFFFF708DFFFFFFFFFFFFF08CFFFFFFFFFFFFF14EFFFFFFFFFFFFF14EFFFFFFF3EFFFF16FFFFFFFF3CFFF722FFFFF7FF10F7F736FFFFFFFF10F3E77EFFFFFFF300F1E779FFFFFFF400E1A769FFFFFFFF00 nothing when you turn tracing on and 
    prints TRAC when you turn it off. 
 
If you find any other differences or problems, please post them as  
responses to this entry.  If you have any questions, don't hesitate to call 
me at (201) 455-0362.  Good luck!            
 
                                                   Jeff Broido