(Comp.sources.hp48) 
Item: 52 by perre@picea 
Author: [Per Stenius] 
  Subj: Circut Simulator v2.61 
  Date: Sun Feb 16 1992 
 
Csim 2.61 SHORT DESCRIPTION AND MANUAL 12/17/91 (c) Per Stenius 
 
RELEASE NOTE 
 
This version differs from the previous (2.3, 2.5, 2.51, 2.6) in the 
following: 
Version 2.3: 
- Lossless transmission line for AC analysis at a single freq. point. (T) 
- The functions CV(node) and CI(branch) that fetch the voltage/current of 
  given node/branch in the previous solution point. CV = ControlVoltage, 
  can be used in other sources to define any functional dependency of a 
  voltage/current in the circuit. Note that there is a delay of 'tstep' 
  when using these functions. 
- The program 'iterdc' for iterative dc solving to be used with nonlinear 
  components. 
- Additional examples of circuits in manual. 
- New sample circuit. 
Version 2.5, 2.51, (and previous versions): 
- ABCD-matrix for two-port added. 
- Minor changes in code for improved speed (during setup) 
- BOTH NODES GND error removed, BOTH NODES SAME used instead. 
Version 2.6 (and previous): 
- ABCD, y and z matrix two-ports can be used in DC analysis if all matrix 
  elements are real (i.e. the imaginary part must be zero) 
- A->L converts array into list (for easier handling of matrices) 
 
INTRODUCTION 
 
This text describes a simple circuit simulator called Csim for the HP48. 
It makes DC, AC and transient simulations and supplies the user with all 
matrices used. The method used is modified nodal analysis, and thus 
elements such as an inductor or ideal voltage source require that a current 
branch is also specified together with the nodes. As soon as a setup is 
done, single analyses can be made with the 'dc', 'ac' or 'tran' sub- 
programs. All subprograms return the result as a vector, whereas Csim 
provides the user with a plot in transient and AC analysis. Note that for 
Csim to work correctly, the 'node' variable should be defined (either a 
node or branch number) when plotting a result. Note also that the RES 
variable (in PLOTR) should be 0. Finally, if SYM (in MODES) is not set 
Csim does not work correctly. 
 
For a demo on how Csim works do the following: 
- download the code (creates the directory CSIM in the current directory) 
- enter the directory CSIM and enter the custom menu (the button marked CST 
  between the PRG and VAR buttons on your HP48) 
- press [Csim]: 
  for: Setup? Y  press: <enter> 
  for: Analysis? (D,A,T) press: T <enter> 
  for: Sweep range? 
       :tstart:0 
       :tstep:0 
       :tstop:1          press: <backspc> 5 <enter> i.e. :tstop:5 
  after which a time-domain plot is drawn (if you have something that 
  you previously have plotted, press [CLRSC] before doing this). 
  Press <ON> to exit the graph environment. 
  Now, press 3 <left-shft> [node] <enter> and redo the above ([node] is 
  a variable in the custom menu). 
  Finally, press the CST button, <next> [CIR] [CIR->] to see the circuit 
  description. 
 
Here is an explanation on the custom menu of Csim (the custom menu is 
obtained by pressing the button marked CST on your HP48, and contains 
those variables and programs you need for using Csim): 
 
Csim - the simulator program. Runs setup (if requested) and a single 
        analysis. For ac, a single run directly from the custom menu 
        provides a fast solution in one freq-point. When choosing T 
        for transient analysis either tstep (time resolution) or tstop 
        should be given. If both are given tstep is used and tstop 
        ignored. 
 
View  - the StackView application, for easy check on components. Use 
        ATTN (ON) to exit. You can also use the Interactive Stack the 
        HP48 provides (see manual p.70). 
 
node  - the node or branch the value of which is wanted as a solution. 
        Used to GET the right value from the solution vector. 
 
ymin, ymax 
      - define the picture y-axis (ac or tran analysis) 
 
CLRSC - Clears the screen (simply the ERASE command) 
 
outp  - a program that takes a vector from the stack and returns one value. 
        it can be used to plot a result that is a function of the values 
        in the solution vector. To be edited by the user. 
        (default << node GET >> ) 
 
CIR-> - takes a list of lists, such as the one used to store circuit 
        descriptions (see also CIR, ->CIR) and puts the lists in it to 
        the stack (inverse to ->CIR). Usage: Press a variable containing 
        a circuit description (e.g. CIR) and press CIR->. 
 
->CIR - takes the circuit description used by Csim and puts it to a list, 
        that can be stored in a variable. 
 
CIR   - when 'Setup' is run, the stack containing the circuit is stored in 
        this variable as a list. To use again, recall CIR and run 'CIR->'  
        (see above). Contains a sample circuit as default. Any circuit 
        description can be stored in a variable as a list of components 
        (which also are lists). 
 
dc    - single DC analysis.  Requires that setup is done (the matrices are 
        ready). Takes no argument from stack and returns a solution vector. 
 
ac    - single AC analysis. Requires that setup is done (the matrices are 
        ready) and that 'w' is specified (rads/s angular freq). Takes no 
        argument from stack and returns a solution vector. Note: Complex 
        values! When A is chosen in Csim, the actual program stored by STEQ 
        is 'acplot', which executes 'ac' and then 'outp'. The program 
        'outp' should take a vector from stack and return a single number. 
        E.g. << node GET ABS >> would return the absolute value of a node 
        voltage (or branch current) that is to be plotted. 
 
A->L  - converts an array into a list. 
 
tran  - single transient analysis. Takes one time step and returns a 
        solution vector. The method used is trapezoidal rule. When T is 
        chosen in Csim, the actual program stored by STEQ is 'tranBE' (or 
        'tranTR'). These return the result vector and call 'outp'. The 
        program 'outp' should take a vector from stack and return a single 
        number. E.g. << node GET >> would return the value of a node voltage 
        (or branch current) that is to be be plotted. 
 
Setup - setup routine for the simulator. Creates and loads the matrices 
        needed and stores the stack as a list into CIR. Takes the circuit 
        description from the stack as an argument (only component declara- 
        tions are allowed on stack). Setup must be done once before analy- 
        zing, however, after that the matrices are ready to be used multi- 
        ple times. This should be remembered e.g. when calculating a DC 
        solution and thereafter starting a transient analysis from the 
        obtained results. In this case running Setup a second time would 
        zero the result vector. Setup also clears flag -3 (i.e. enables 
        SYM), sets flag -17 and clears flag -18 (i.e. sets radians mode). 
 
w     - angular frequency (2*pi*f) rad/s. 
 
G     - conductance matrix. Contains all real valued entries, i.e. those 
        caused by elements the values of which do not have an s or jw 
        factor. 
 
C     - s-matrix. Contains all elements that have an s or jw factor. 
 
Cc    - constant valued complex matrix. Can be used in AC analysis only, 
        at a single value of 'w' (angular frequency). Contains entries 
        from Z, Y, z, y (See Section on syntax). 
 
W     - numerical values of the sources as a vector. This vector is 
        updated in every analysis point. 
 
Wlist - the functions representing each source as a list, from which 
        the numerical values for 'W' are obtained. 
 
Euler - specifies the method used in the tran analysis. If Euler = 1 then 
        backward Euler ('tranBE') is used (faster but more inaccurate), if 
        Euler = 0 then the trapezoidal rule is used, which is rather 
        accurate but slower ('tranTR' and 'tran'). 
 
iterdc 
      - if CV() or CI() are used in DC analysis, iterative solution is 
        required in order to obtain the correct solution. 'iterdc' can 
        be used for this after setup has been done. Note that very few 
        nonlinear circuits can actually be solved by iteration only. 
        Usually some linearization method must also be used, e.g. the 
        Newton-Raphson algorithm. Giving good initial guesses for node 
        voltages and branch currents in the X vector also helps. 
 
THE SYNTAX USED TO DESCRIBE A CIRCUIT 
 
The syntax by which the components are entered is (NOTE! Each circuit 
needs a ground node and its number is always 0 (zero)): 
  
{R node1 node2 numval branch} - resistance [ohm] 
 
{G node1 node2 numval}        - conductance [mho] 
 
{C node1 node2 numval}        - capacitance [F] 
 
{L node1 node2 numval branch} - inductance [H] 
 
{Y node1 node2 complexnumval} - admittance with a constant complex value 
                                (re,im). In DC analysis each entry must 
                                be real (im = 0). 
 
{Z node1 node2 complexnumval} - impedance with a constant complex value 
                                (re,im) In DC analysis each entry must 
                                be real (im = 0). 
 
{J node1 node2 funcval}       - indep. current source 
 
{E node1 node2 funcval branch} 
                              - indep. voltage source   
 
{S node1 node2 branch}        - short circuit (the current is fetched by 
                                branch GET). Can be used to define a current 
                                branch for dependent sources. 
 
{O in+ in- out+ out- outbranch} 
                              - ideal opamp (out- should be ground, 
                                outbranch returns the output current) 
 
{M l1node1 l1node2 l2node1 l2node2 l1val l2val mval l1branch l2branch} 
                              - transformer i.e. two inductors (l1, l2) with 
                                mutual inductance (mval). The values required 
                                are the four nodes, the value of l1, l2, mval 
                                [H] and the branches of l1 and l2. The dots  
                                for m are at l1node1 and l2node1. 
 
{m l1branch l2branch mval}    - mutual inductance of mval [H]. As M, but can 
                                be used to define e.g. three inductances 
                                that all have mutual inductances. To do 
                                this, define the 3 L:s and then 3 m:s be- 
                                tween them. Note that m takes the branches 
                                of the L:s. Make sure you specify the in- 
                                ductors the right way (the branch of L runs 
                                from n1 to n2). Note also that m is not a 
                                component, it merely states a dependency 
                                between two L:s that should be defined se- 
                                parately. No checking is done that l1branch 
                                and l2branch actually belong to L:s. 
 
{T node1 node2 node3 node4 llval Zoval} 
                              - lossless transmission line (to be used in AC 
                                analysis only) of length ll (in wavelengths) 
                                and with the characteristic impedance Zo. 
                                Note that nodes 2 and 4 must have the same 
                                value (equivalent pi-circuit used). 
 
{g node1 node2 node3 node4 numval} 
                              - voltage-controlled current source i.e. 
                                transconductance. The source current is 
                                from node3 to node4 and the controlling 
                                voltage from node1 to node2. 
 
{r node1 node2 node3 node4 numval branch1 branch2} 
                              - current-controlled voltage source. Defines 
                                a short circuit between node1 and node2 
                                and a controlled voltage source between 
                                node3 and node4 (node3 being the positive 
                                node). The controlling current runs through 
                                branch1 and the current of the source is 
                                fetched from branch2. Branch1 must not be 
                                a previously defined branch. 
 
{p node3 node4 numval branch1 branch2} 
                              - same as r but does not define a short 
                                circuit between node1 and node2. Instead 
                               branch1 must be a predefined branch (e.g. 
                                that of a resistor or inductor).  
  
{a node1 node2 node3 node4 numval branch} 
                              - current-controlled current source. Defines 
                                a short circuit between node1 and node2 
                                and a controlled current source the current 
                                of which runs from node3 to node4. The 
                                controlling current runs through branch 
                                which must not be previously defined. 
                                 
{b node3 node4 numval branch} - same as a but does not define a short 
                                circuit between node1 and node2. Instead 
                                branch must be a predefined branch (e.g. 
                                that of a resistor or inductor). Compare 
                                with p. 
 
{u node1 node2 node3 node4 numval branch} 
                              - voltage-controlled voltage source. The 
                                current through the source is fetched 
                                from branch. 
 
{y node1p1 node2p1 node1p2 node2p2 y11 y12 y21 y22} 
                              - a two-port with y-parameters that are 
                                constant complex values (re,im). In DC 
                                analysis each entry must be real (im = 
                                0). 
 
{z node1p1 node2p1 node1p2 node2p2 z11 z12 z21 z22} 
                              - a two-port with z-parameters that are 
                                constant complex values (re,im). In DC 
                                analysis each entry must be real (im = 
                                0). 
{A node1p1 node2p1 node1p2 node2p2 A B C D} 
                              - a two-port with ABCD-parameters that 
                                are constant complex values (re,im). 
                                In DC analysis each entry must be real 
                                (im = 0). 
FUNCTIONS 
 
CV(node)                      - returns previously calculated value of 
                                the voltage of node. In code << X node 
                                GET >> 
 
CI(branch)                    - returns previously calculated value of 
                                the current of branch. In code << X 
                                branch GET >>, the same as CV(). 
 
In the above, nodes and branches are integer numbers. The ground node is 
represented by 0. All nodes and branches should have a unique number and 
they should be given in order e.g. nodes 0,1,2,3 and branches 4,5,6. These 
numbers refer DIRECTLY to the position in the matrices/vectors. Thus the 
4'th element in the result vector would be the current through branch 4 and 
the first element is the voltage of node 1. To help remembering the syntax, 
you could e.g. have a variable y with the following contents: 
 
y 
{y n1p1 n2p1 n1p2 n2p2 y11 y12 y21 y22} 
 
NOTE: The two-port y, z and ABCD parameters are valid in DC analysis ONLY 
IF ALL THE ENTRIES in the corresponding matrix are real. 
 
The following components form equivalent circuits: 
 
{S 1 2 5} 
{p 3 4 100 5 6} is the same as 
 
{r 1 2 3 4 100 5 6}, 
 
{S 1 2 5} 
{b 3 4 100 5} is the same as 
 
{a 1 2 3 4 100 5}, 
 
{L 1 2 0.1 5} 
{L 3 4 0.2 6} 
{m 5 6 0.05} is the same as 
 
{M 1 2 3 4 0.1 0.2 0.05 5 6}. 
 
Finally, an example of usage for transient analysis: 
(This is how your stack should look) 
 
{E 1 0 '10*SIN(10*t)' 4} 
{C 1 2 0.01} 
{L 2 3 1 5} 
{R 3 0 10 6} 
 
This defines a RLC-circuit with nodes 1,2,3 (and ground) and current 
branches 4,5,6. The current through branch 4 is equal to the current 
through the ideal voltage source E, the current through branch 5 equals 
the current through the inductor L, and the current through branch 6 
equals the current through the resistor R. The values of the components 
(which ALWAYS must be numerical) are 10 ohms, 1 henry and 0.01 farads. 
The voltage source has a time-dependent value (used in transient analysis). 
If 'node' is set to 3 the voltage over the resistor R is plotted in 
transient analysis. On the other hand, 'outp' could be written as << DUP 
1 GET SWAP 2 GET - >> to return the voltage between nodes 1 and 2 as a 
result. Note that sources (E,J) may have functional values (should be 
suitable for the analysis requested! Time dependency for transient 
analysis and 'w' dependency (angular freq) for AC). When running Csim, 
the stack may ONLY contain component declarations! 
 
Press the CST button and then [View]. Now press ATTN (low-left corner, i.e. 
ON). Press [Csim], press <enter> on "Setup? Y", press D (or T), <enter> on 
analysis.   
 
An example for AC analysis (using A in Csim): 
 
{E 2 0 1 3} 
{G 2 1 1} 
{C 1 0 1} 
 
Set 'node' equal to 1 and write 'outp' equal to << node GET ABS >>. Se- 
lect A on analysis and choose wstart 0 and wstop 10 (ymin = 0, ymax = 1). 
 
Another example for AC analysis (using 'w' = 1 and 'ac'): 
 
{J 0 1 10} 
{G 3 0 1} 
{G 2 0 1} 
{Z 1 0 (0,-1)} 
{M 3 1 2 1 2 1 0.5 4 5} 
 
Setup 
1 left-shft w ac 
 
The currents through the transformer are the 4'th and 5'th elements in the 
result vector. Here's an example involving a transistor for which we have 
the y-parameters y11 = 0.001, y12 = -j0.0001, y21 = 0.1 and y22 = 0.0001. 
Its base is at node 1, emitter at gnd (node 0) and collector at node 2. 
 
{J 0 1 1} 
{Z 1 0 1E3}       @ resistance of 1 kohms 
{Z 2 0 1E3} 
{Z 1 2 (0,-1000)} @ capacitance of -j1000 ohms 
{y 1 0 2 0 1E-3 (0,-1E-4) 0.1 1E-4} 
 
Setup 
ac 2 GET ABS (returns |Uo/Jin| = 884.035 V/A) 
 
For the use of the lossless transmission line we have the following ex- 
ample (analysis can be made at a single frequency point only, at which ll 
is valid): 
 
{J 0 1 1} 
{Z 2 0 (75,-69)} 
{T 1 0 2 0 0.583 50} 
 
Setup ac 1 GET 
 
returns (25.2092, -34.5800) which is the input impedance (J = 1) of a loss- 
less transmission line of the length 0.583 wavelengths (at some frequency) 
and with the characteristic impedance of 50 ohms, terminated with a load of 
(75,-69) ohms. 
 
DC analysis: 
 
{J 0 1 1} 
{R 1 0 1E3 3} 
{p 2 0 10 3 4} 
 
The voltage of node 2 (the 2'nd element in the result vector) should be 
10V. The current through the controlled voltage source should be 0A (the 
4'th element in the result vector). 
 
For iterative DC solving of  circuits, consider these two examples: 
 
{E 1 0 1 3} 
{G 1 0 1} 
{G 1 2 1} 
{J 0 2 'SQ(CV(1))'} 
 
and 
 
{J 0 1 1} 
{G 1 0 1} 
{G 1 2 1} 
{E 2 0 'SQ(CV(1))' 3} 
 
Setup iterdc 
 
The first circuit converges after only two iterations, but the second one 
requires several hundred to reach the exact solution ([[1] [1] [0]] in the 
second case). Good initial guesses may help, and also the use of e.g. the 
Newton-Raphson algorithm (see Vlach-Singhal; Computer Methods for Circuit 
Analysis and Design). Note that 'iterdc' should actually also be used at 
every time step in transient analysis to avoid the delay when using CV() 
and CI(). 
 
A simple small signal model for a transistor (B-1 C-2 E-3): 
 
{R 1 3 1E3 4} 
{G 2 3 0.0001} 
{b 2 3 100 4} 
 
A voltage source used as an digital inverter; if the voltage of node 2 is 
higher than 2.5 volts, then the voltage of node 3 is 0 volts, otherwise 
5 volts (note that there is a delay of one 'tstep'). 
 
{E 3 0 'IFTE(CV(2)>2.5,0,5)' 4} 
 
Including nonlinear components as such would make solving the matrix equ- 
ation system a tedious process. It would also make the analysis MUCH slower. 
However, it could be done. 
 
ERROR MESSAGES 
 
These are the only error messages in this program. Note that there are not 
many error checking routines provided, so the user should be careful when 
entering the circuit description. For any strange behaviour or false re- 
sults, please email me directly and explain what occurred. 
 
SYNTAX ERROR - an error occurred in 'Setup' while Csim was loading the 
               matrices. Check the circuit description and the component 
               that is first on stack. See also section on syntax. 
 
NEGATIVE NODE NO. - a negative number was given as a node number. Check the 
               the first component on stack. 
 
BOTH NODES SAME - a component was specified having two nodes that were the 
               same value. To override this, use a short-circuit (S) between 
               these nodes. 
 
ZERO VALUE OR BRANCH - a component with a value of zero was given or its 
               branch number was zero (which is reserved for the ground 
               node). 
 
n2 MUST EQUAL n4 IN T - you have entered a transmission line in the circuit 
               with nodes 2 and 4 not equal. This is not allowed since the 
               equivalent pi-circuit to the transmission line is actually 
               used. 
Im{Cc} \=/ 0 IN DC - you have specified components with complex values in 
               DC analysis. 
 
A good way to avoid errors is to proceed systematically, e.g. in the 
following way: 
 
1) Choose one reference node to be ground (GND) and set its node number 
   to 0. 
 
2) Assign the rest of the nodes a number each, in numerical order: 
   1,2,3,... 
 
3) Find all the components that require a branch and assign each required 
   branch a number starting from the highest node number plus one. 
 
!) The node and the branch numbers should follow eachother in numerical 
   order, with no 'gaps' in between (e.g. 0,1,2 are nodes and 3,4 are 
   branches). 
 
4) Enter the circuit description component by component. Note that the 
   stack should only contain component descriptions! Check your stack 
   with 'View'. 
 
5) Decide what results you need and edit 'outp' if necessary. Also, set 
   'node' to the correct value. 
 
6) Run 'Setup' once and start analyzing! Remember to run 'Setup' whenever 
   you change your circuit or want to start from zero. Sometimes all you 
   need to do is to edit your X vector.  
 
FREQUENTLY ASKED QUESTIONS 
 
Some people have had trouble with the branch currents (the direction...) 
so here's more on that: 
 
In all components (J,E,L etc.) the current is defined to be FROM the first 
node TO the second node. Thus no matter which way you put your source (E) 
The value of the branch current remains the same (i.e. in the direction of 
the U of the source) with respective to the source. In the sample RLC 
circuit, when the first node of E and L is the same, the currents should 
be the opposite. When the second node of E is the first node of L, the 
currents are the same. 
 
For E the situation looks like this: 
 
           --- U=E --> 
 
 node1 +  o->-( E )---o - node2 
 
            I 
 
for L: 
 
           --- U1,2 -> 
 
 node1    o->- Ind ---o   node2 
 
            I 
 
for J: 
 
 node1    o->-( J )---o   node2 
 
            I=J 
 
for S:     
 
           --- U=0 --> 
 
 node1    o----->-----o   node2 
 
                I 
 
This could be defined the other way around too, but in this case it isn't. 
 
For two-ports, the node numbers are defined as 
 
                _________ 
 node1    o->--|         |--<-o node3 
               |         |              
               |         | 
               |         |   
               |         | 
 node2    o----|_________|----o node4 
 
Note that the direction of the currents is always towards the two-port. 
This should be remembered when defining e.g. ideal opamps, controlled 
sources and two-ports with y- or z-parameter representation. 
 
>I can't get the transient analysis to work properly unless I do 
>an entire setup first. If I do a transient plot, and then repeat it, I 
>get different results, unless I run setup. 
> 
 
What happens is that unless you run setup, the transient analysis continues 
from where it stopped (however, this time from the beginning of the screen). 
Thus the new beginning should match with the previous end. As you might 
have noticed, the transient analysis should always start from time=0. This 
is due to the fact that solving this problem is an iterative process. 
 
>It would be nice to be able to specify initial values for capacitors and 
>inductors. 
> 
 
This can be done. The X vector contains the starting values, and is zeroed 
at setup. However, nothing stops you from running a dc-analysis and then 
running a tran analysis without a setup in between, thereby giving the re- 
sults from the dc-analysis as beginning values for the tran analysis. The 
X vector can also be manually edited. To do this, run setup, then press 
enter for analysis?, which stops the program. Edit the X, and run tran 
analysis without setup. The execution of setup can be avoided by answering 
something else than 'Y' at 'Setup?'. 
 
>I'm interested in any references you used, for algorithms for circuit 
>solving, this is something I've never really looked into before. 
> 
 
A good place to start is to look at a book called 
 
Computer Methods for Circuit Analysis and Design 
 
by Jiri Vlach and Kilshore Singhal (Van Nostrand Reinhold Company 1983, 
ISBN 0-442-28108-0). Check out chapter 4 and 9. For transient analysis, 
(which is normally done by Laplace tranforms when working manually) the 
trapezoidal rule is pretty powerful. Also, for all the theory needed for 
Csim, I have written a report called 
 
A Tutorial on Developing a Simple Circuit Simulating Program 
 
which I can email (ps-file format) to anybody interested upon request. It 
is about 30 pages + 30 pages including this manual and the commented source 
code for Csim. 
 
FINAL REMARK 
 
This simulator is not necessarily completely bug-free, so please report 
to me for any strange behaviour. Note also that the transient analysis 
methods are not necessarily stable for all values of time steps. Try an- 
other time range or time step if this happens. If you get the system error 
   INV Error: 
   Infinite Result 
in any analysis mode, this usually indicates that the component matrix 
cannot be inverted. This error can sometimes be avoided by assigning the 
nodes the values 0...n and the branches the values n+1...m. If this does 
not help, please send me the circuit description you used. 
 
I am happy to provide any further information on this program. Please 
send also some comments on its appearance, suggestions on improvement 
etc. Note that very little syntax checking is done (e.g. no node or 
branch number checks!). I hope this short manual is sufficient, if not 
please ask me directly via email. 
 
copyright Per Stenius, Helsinki University of Technology. 
          email perre@aplac.hut.fi or pstenius@otax.tky.hut.fi 
 
END_DOC