Author: hpfcso.FC.HP.COM [Ray Depew] 
  Date: Thu Dec 19 1991 
 
In comp.sys.hp48, robf@mcs213g.cs.umr.edu (Rob Fugina) writes: 
 
> I just bought the serial interface kit, and I can't get anything to work! 
> I set the right port, speed, and parity on the computer, and I set the 
> 48 to wire, ascii, and the same baud and parity as the computer.  Nothing 
> seems to happen!  The only thing that I can get to happen (sometimes) is 
> when the computer is in terminal mode and I put the 48 in server mode, 
> the computer will receive 4-6 characters (that I recognize as the 48  
> telling the computer it's in server mode).  Is there any way to test the 
> connection?  Does the computer's com port need to be set for DCE or  
> something???  HELP!!!!!!!!!! 
>  
> Rob   robf@cs.umr.edu 
 
1) To test the connection without Kermit getting in the way, type "connect" 
   at the 'Kermit >' prompt on your computer, or use a dumb terminal. 
 
   a) To test the computer->48 connection: 
      - press OPENIO on the 48. 
      - type HELLO on the computer and press RETURN/ENTER/whatever. 
      - press BUFLEN on the 48 (last pg. of the I/O menu). 
      - you should see two numbers on the stack.   
        Level 1 is a flag:  1 := data transferred o.k. 
                            2 := framing error or UART overrun 
        Level 2 is the number of characters received from the computer. 
      - press DROP to remove the flag and put the # of char's into Level 1. 
      - press SRECV on the 48 (last pg. of the I/O menu). 
      - you should see two numbers on the stack. 
        Level 1 is a flag:  1 := data transferred o.k. 
                            2 := unsuccessful receive.  (press ERRM for 
                                 more detail) 
        Level 2 should be the string received from the computer. 
     
    b) To test the 48->computer connection: 
       - (Assuming you already pressed OPENIO) 
       - put a string like "HI BACK" on Level 1 of the 48. 
       - press XMIT on the 48 (last pg. of the I/O menu). 
       - if data transfer is successful, you will see a 1 on Level 1. 
       - if part of the string failed to transmit, you will see a 0 on 
         Level 1 and the unsent portion of the string on Level 2. 
 
2) Remember to press CLOSEIO when you've finished. 
 
Regards 
Ray Depew 
Hewlett Packard Co, Fort Collins, Colorado 
rrd@hpfitst1.fc.hp.com