£ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨ 
                       3 HP48G/GX -- LIBEVAL 3 
                       …ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ— 
                             by Joe Horn 
 
The G/GX has a new command: LIBEVAL.  It's sort of like SYSEVAL, but 
instead of taking a memory address (which could be ambiguous due to 
the G/GX's massive need for bank switching), it takes XLIB numbers. 
It's a "back door" for us hackers.  Unlike the ELSYSEVAL command in 
the HP Solve Equations Library Card, which only worked for the 
libraries in that card, LIBEVAL works for *any* library, including the 
hidden ones in the operating system. 
 
      CAUTION: LIBEVAL, like SYSEVAL, is both powerful and 
      dangerous. If used with incorrect input(s) and/or in 
      the wrong environment, it can nuke your memory. 
 
LIBEVAL takes a single user binary integer of the form #LLLFFFh, where 
LLL is the library ID (hex), and FFF is the three-digit function 
number (hex, with leading zeros if necessary). 
 
For example, the R->B command is XLIB 2 9.  So you can perform a R->B 
by executing #2009h LIBEVAL.  Try it: 10 #2009h LIBEVAL ŽŽ  #Ah. 
 
Using it for named commands is unnecessary, but the G/GX is highly 
XLIB oriented (again, due to the need for bank switching), and there 
are many useful and interesting features accessible only thru LIBEVAL. 
 
A prime example is the G/GX's inability to programmatically launch the 
new "dialog boxes".  Suppose a program needs to print things; it would 
be awfully nice to be able to throw the I/O PRINT dialog box onto the 
screen.  The User's Guide is no help here, and in fact it would seem 
impossible to do. But #B4197 LIBEVAL is all it takes!  Try it.  Cool, 
huh? 
 
Here's a table of a few useful LIBEVAL magic numbers that I've been 
able to nail down.  Be sure to type them in correctly! 
 
# hex  LIBEVAL result 
ŽŽŽŽŽ  ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ 
 
B2000 *CMD (Last Command window) 
 
B2001  CHARS Application 
 
B41C1  MODES Application input form 
B41CF *Flag Browser (returns TRUE or FALSE to level 1; just DROP it) 
B41D7 *MEMORY Application (aka Variable Browser) 
 
B4000 *SOLVE Application choose box 
B4001  Solve Equation input form 
B4017  Solve Differential Equation input form 
B402C  Solve Polynomial input form 
B4033  Solve Linear System of Equations input form 
B4038  Solve Financial Equation (TVM) input form 
 
B4045  PLOT input form 
 
B4113 *SYMBOLIC Application choose box 
B4114  Integrate input form 
B4122  Differentiate input form 
B412B  Taylor Polynomial Expansion input form 
B412D  Isolate A Variable input form 
B4130  Solve Quadratic input form 
B4131  Manipulate Expression input form 
 
B4137 *TIME Application choose box 
B4138  Set Alarm input form 
B415B  Set Time and Date input form 
B416E *Alarm Browser (aka Alarm Catalog) 
 
B4175 *STAT Application choose box 
B4176  Single-Variable Statistics input form 
B417D  Frequencies input form 
B417F  Fit Data input form 
B418F  Summary Statistics input form 
 
B4192 *I/O Application choose box 
B4193  Send to HP 48 input form 
B4197  Print input form 
B41A8  Transfer input form 
B50FF *Get from HP 48 (immediate) 
 
E4012 *recalls the contents of the reserved variable 'Mpar' 
 
      * ŽŽ  see note below 
ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ 
 
Note: Ray Depew figured out that if you run a program that looks like: 
 
                   <<  #B2001h  LIBEVAL  LCD->  >> 
 
and exit the input form by pressing the ON key, you'll grab a snapshot 
of the screen into a grob on the stack!  Excellent for printing 
examples of input forms (see PCLPRINT.LIB and EPSPRINT.LIB). 
 
  * ŽŽ   This method does *not* work with the LIBEVAL's listed with an 
asterisk above; it only seems to work for input forms and the CHARS 
application.