NAME
	spline - interpolate using splines under tension

SYNOPSIS
	spline [file] [options]

DESCRIPTION
	Without options, SPLINE reads pairs of numbers (x- and y-values) from
	the standard input (or the given file), generates a smooth curve
	through the points, and writes to the standard output points from the
	smooth curve.  The curve is a spline under tension (see references),
	which is somewhat "tighter" than a cubic spline, and less
	likely to have spurious inflection points.  As with GRAPH, each
	pair of points may optionally be followed by a comment.  If the
	comment is surrounded by quotes "...", the comment may contain
	spaces.  The given points, and their comments if any, will be
	included in the output.  The interpolation may optionally be
	restarted after each label, so that a family of curves may be
	processed together (see the -b switch).

	Input lines starting with ";" are copied to the beginning of
	the output file but are otherwise ignored.  Blank lines are
	ignored.

	If the -c switch is not used, the input points must be from a function
	- that is, the x values must be strictly increasing.  The
	output points will also be from a function.  (If the -b switch
	is used, this restriction applies only within each segment.)

	If the -c switch is used (indicating a general curve), the
	input points need not be from a function, but each pair of
	points must be separated from the previous pair by a finite
	distance.  (If the -b switch is used, this restriction applies
	only within each segment.)
	
options are:
  -a  [step [start]] Input data contains only y values - generate automatic
  		abscissas at intervals of step (default 1) starting at start
  		(default 0).

  -b 		break the interpolation at each label.  That is, the input
		curve is divided into sections with the last point in
		each section marked by a label (which may be empty:
		"").  A separate interpolating curve is to be found for
		each section.  In this case, the requirements on the
		number of intervals (specified by the -n switch or
		defaulted) and the interpolation range (specified by the 
		-x switch) are applied to each section independently.

  -c            general curve rather than function.  In this case, the curve is
  		parameterized on the polygonal arclength from the first
  		to the last given point, with the whole length scaled
  		to be 1.  Thus, the values min and max for the -x
  		switch should satisfy 0 <= min < max <= 1.  The -s and
  		-c switches cannot be used together.

  -n  num       interpolate over num intervals (default is 100)

  -q            Quadruple: increase the number of intervals fourfold.

  -s [num [num]]
  		Specify slopes at beginning and end of curve.  Slopes
  		not given are assumed to be zero.  Without the -s 
  		switch, slopes are determined from other information.  
  		The -s and -c switches cannot be used together.

  -t num	Specify tension in interpolating curve.  Tension of 50 gives
		almost polygonal line, tension of .01 gives almost cubic
		spline.  Tension must be positive.  Default is 1.

  -x [min [max]]
  		Interpolate from min to max only.  min and max should
  		be in the range of the given x values, except that if
  		the -c switch is used they should satisfy 0 <= min <
  		max <= 1.

  -xl		take log of x values before interpolating, take exponential
   		afterwards (probably necessary if -xl switch is needed for
   		GRAPH)

  -yl		take log of y values before interpolating, take exponential
   		afterwards (probably necessary if -yl switch is needed for
   		GRAPH)

NOTES
	Similar to the Unix routine, except using splines under tension,
	passing labels through, performing multiple interpolations from
	one file and allowing general curves.

REFERENCES

	A.  K.  Cline, "Scalar- and Planar- Valued Curve Fitting Using
	Splines Under Tension", Communications of the ACM v 17 n 4 p
	218-223 (Apr 74).

	Schweikert, D.  G.  "An interpolation curve using a spline in
	tension", J.  Math.  and Physics v 45 p 312-317 (1966).

AUTHOR
	Copyright (c) 1985  James R. Van Zandt

	Resale forbidden, copying for personal use encouraged.