BASIC WINDOWING TOOLBOX
                            ----- --------- -------

                Windowing for IBM Personal Computers using BASIC
                                  Version 2.0

 
              (C)Copyright Image Computer Systems 1985, 1986, 1987












































                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


   CONTENTS

        What is BASIC WINDOWING TOOLBOX? .....................  1
        Technical overview of BASIC WINDOWING TOOLBOX ........  1
        BASIC WINDOWING TOOLBOX files ........................  2
        Compatibility with BASIC .............................  4
        Using with a standard BASIC interpreter ..............  4
        Using with compiled BASIC ............................  6
        Overview of functions ................................  7
        Function parameters ..................................  7
        Text display .........................................  8
        Character attributes .................................  8
        Window border types .................................. 10
        BASIC WINDOWING TOOLBOX functions
          Initializing windowing ............................. 11
          Defining a window .................................. 11
          Opening a window ................................... 12
          Closing a window ................................... 13
          Deallocating window buffer space ................... 14
          Scrolling contents of window ....................... 14
          Displaying a string in a window .................... 15
          Displaying a character ............................. 16
          Get cursor X position .............................. 16
          Get cursor Y position .............................. 17
          Go to X, Y position ................................ 17
          Setting foreground color ........................... 18
          Setting background color ........................... 18
          Drawing a border ................................... 19
          Enabling error window display ...................... 20
          Disabling error window display ..................... 20
        Miscellaneous functions
          Accessing software interrupts ...................... 21
          Changing which printer is "LPT1:" .................. 22
          Altering printer time-out .......................... 23
        Error handling ....................................... 24
        Error messages ....................................... 24
        REGISTERING BASIC WINDOWING TOOLBOX .................. 26
        ImagePrint ........................................... 26
        Restrictions ......................................... 27
        Disclaimer ........................................... 27
        INDEX .................................................28
        ORDER FORM ........................................... 29






        IBM, PC-DOS are trademarks of International Business Machines.
        Compaq is a trademark of Compaq Computer Corp.
        QuickBASIC, Microsoft, MS-DOS are trademarks of Microsoft Corp.











                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


   WHAT IS BASIC WINDOWING TOOLBOX?

        BASIC WINDOWING TOOLBOX (B-WINDOW) is a collection of functions 
        that give windowing capability to a BASIC programmer using an IBM 
        Personal Computer or compatible. With B-WINDOW you can write 
        BASIC programs that look much more visually exciting and profes-
        sional.  Windows can be opened over sections of the screen and 
        when the windows are closed, the original contents of the screen 
        reappears.  Special windowing cursor control, string and character 
        display and border drawing are included.  And everything happens 
        at top speed because B-WINDOW was written in the C language, 
        converted to assembler, and hand optimized.  
        
        In addition to windowing functions, B-WINDOW also gives you easy 
        access to the interrupt structure of an IBM Personal Computer and 
        also allows you to reassign printer ports.  

        B-WINDOW is User-Supported Software. Feel free to make copies of 
        the distribution version of B-WINDOW and give them to your 
        friends. Registering for the full windowing package, which allows 
        B-WINDOW to be used with BASIC compilers, only costs $20 and you 
        can pay by MasterCard or Visa. See the Section "REGISTERING BASIC 
        WINDOWING TOOLBOX" for details.  

        Software developers - if you meet one simple requirement, there 
        is no restriction on using B-WINDOW in a product of your own. See 
        the Section "RESTRICTIONS" for details.  


   TECHNICAL OVERVIEW OF BASIC WINDOWING TOOLBOX 

        Both interpreted BASIC and compiled BASIC are supported by either 
        BLOADing a windowing support file if you are using an interpreter,
        or linking to it if you are using a BASIC compiler.  The 
        BLOADable windowing support files have file name extensions of 
        ".BIN", and the linkable B-WINDOW files have an extension of 
        ".OBJ".  

        An array of bytes, in each windowing support file, called the 
        window buffer, is used to store each defined window, plus the 
        section of the screen that each window overlays. The window 
        buffer size varies from 5000 bytes to 20000 bytes, depending on 
        which B-WINDOW file you bload/link. A larger window buffer allows 
        more active window definitions; smaller means a smaller program. 
        When a window is defined, storage is allocated in the window 
        buffer.  

        The standard IBM Personal Computer screen, in 80 column alpha-
        numeric mode, which is the mode B-WINDOW works in, uses 4000 
        bytes (80 x 25 x 2) of video RAM. Each character on the screen 
        has a trailing attribute byte that indicates if the character is 
        bright or dark, blinking, etc. For example, a 10000 byte window 
        buffer (B-WIN10I.BIN or BWIN10BC.OBJ) is enough to create a 
        window the size of the screen (4000 bytes to save old screen, 


                                                                         1





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


        4000 for window), plus another little window. Or several medium 
        sized windows.  

        A window's width and height is specified when it is defined. When 
        it is opened, it can be located at any location on the screen, as 
        long as it doesn't stray outside of the screen's boundaries. If 
        you have specified a border for a window, the writable area of 
        the window is reduced to fit inside the border. For example, if 
        you defined a window that had a width of 20 and a height of 10, 
        and had a border, the writable coordinates would be 0..17 in the 
        horizontal direction and 0..7 in the vertical direction. The 
        upper left corner of the writable area of a window is at 
        horizontal (X) coordinate 0 and vertical (Y) coordinate 0.  

        B-WINDOW allows deallocation of window storage so you can have as 
        many windows as you like by deallocating and redefining them as 
        needed. The only restriction is that only as many windows as can 
        be defined in the window buffer can be visible at any one time.  

        If no windows are open, the windowing functions WSCROLL, WWRITE, 
        WDSP1, WGETCX, WGETCY and WGOTOXY are relative to the standard 
        80x25 screen.

        No more than one version of a defined window can be open at any 
        one time, irregardless of screen placement. This is because each 
        window's storage contains information about the section of screen 
        it overlaid and opening a second version of the same window would 
        overwrite that information.

        When a window is closed, the cursor will return to the location 
        it occupied before the window was opened. If a window is 
        reopened, the cursor will move to the position it occupied when 
        the window was previously open.  


   BASIC WINDOWING TOOLBOX FILES

        Be sure to make a backup of the B-WINDOW files before running or 
        altering any of the diskette files.

        All B-WINDOW ".BAS" files are in ASCII format so you can copy 
        them to a printer or view them with an ordinary text editor.  

        The files on the B-WINDOW distribution diskette are:

          B-WREAD.ME

            Contains latest changes, notes. Lists B-WINDOW upgrade
            history.
            
          B-WINDOW.DOC

            The B-WINDOW documentation file. It has been pre-formatted 
            for 9x11 paper, 66 lines per page.


                                                                         2





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------



          B-WINI.MRG 

            Use BASIC's MERGE command to add this file to your program if 
            you are using B-WINDOW with standard interpreted BASIC. e.g.:
        
                MERGE "B-WINI.MRG"
        
            It contains BASIC program code to set up the correct entry 
            offsets for the B-WINDOW functions, BLOADs the B-WINDOW 
            support file (".BIN" file name extension), and calls WINIT to 
            initialize the windowing functions. Line numbers start at 
            60000, so if your program already uses line numbers in this 
            range, be sure to renumber your program's lines before the 
            MERGE. To execute the BASIC program code contained in B-
            WINI.MRG, add the lines:
        
                CLEAR,&h8000
                GOSUB 60060

            to the very beginning of your program. See the demonstration 
            programs BWDEMO1.BAS and BWDEMO2.BAS for examples of how this 
            is done.  

          B-WIN5I.BIN

            BLOADable B-WINDOW support file used with standard 
            interpreted BASIC. It has a 5000 byte window buffer. The two 
            demonstration programs BWDEMO1.BAS and BWDEMO2.BAS make use 
            of it.  

          B-WIN10I.BIN 

            BLOADable windowing support file, 10000 byte buffer. Used 
            with standard interpreted BASIC.

          B-WIN20I.BIN 

            BLOADable windowing support file, 20000 byte buffer. Used 
            with standard interpreted BASIC.

          BWDEMO1.BAS

            B-WINDOW demonstration program that BLOADs B-WIN5I.BIN.
            B-WINI.MRG has already been merged into it. Before running 
            it make sure the file B-WIN5I.BIN is on the default drive.

          BWDEMO2.BAS

            B-WINDOW demonstration program that BLOADs B-WIN5I.BIN. 
            B-WINI.MRG has already been merged into it. Shows how to use 
            WKILL to display more windows than the 5000 byte window 
            buffer in B-WIN5I.BIN can hold at one time. Before running it 
            make sure the file B-WIN5I.BIN is on the default drive.


                                                                         3





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


          BWDEMOC.EXE

            Compiled B-WINDOW demonstration. The BASIC source file is 
            BWDEMOC.BAS, which was linked to BWIN20QB.OBJ. Just type 
            "BWDEMOC" to run it.

        The files on a B-WINDOW REGISTERED diskette include all of the 
        files on a distribution diskette, plus: 

          BWDEMOC.BAS

            BASIC source for BWDEMOC.EXE.

          BWIN5BC.OBJ   - 5000 byte windowing buffer
          BWIN10BC.OBJ  - 10000 byte windowing buffer
          BWIN20BC.OBJ  - 20000 byte windowing buffer
                           
            Linkable windowing support files for use with earlier BASIC
            compilers that are limited to 64K for all code and data, as
            well as QuickBASIC version 1.

          BWIN5QB.OBJ   - 5000 byte windowing buffer
          BWIN10QB.OBJ  - 10000 byte windowing buffer
          BWIN20QB.OBJ  - 20000 byte windowing buffer
                                       
            Linkable windowing support files for use with the QuickBASIC 
            version 2 compiler. The BWDEMOC.EXE file was compiled with 
            QuickBASIC version 2 and linked with BWIN20QB.OBJ.  


   COMPATIBILITY WITH BASIC

        B-WINDOW is compatible with standard interpreted BASIC as 
        supplied for an IBM Personal Computer or close compatible, such 
        as a Compaq.  
        
        The B-WINDOW linkable object files are compatible with the 
        standard IBM or Microsoft BASIC compilers, versions 1.00 and up. 
        They are also compatible with the Microsoft QuickBASIC compiler 
        versions 1 and 2.  


   USING WITH A STANDARD BASIC INTERPRETER

        The files BWDEMO1.BAS and BWDEMO2.BAS are examples of windowing 
        with interpreted BASIC.
        
        To use the B-WINDOW functions in your interpreted BASIC program 
        you must: 

         (1) Have approximately 55-60K of available string space. When 
             you first enter BASIC, a message stating how much free RAM 
             you have will appear.  The message should say something like 
             "55000 BYTES FREE" or "60000 BYTES FREE".  


                                                                         4





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------



         (2) Merge the file B-WINI.MRG with your BASIC program. e.g.
        
                MERGE "B-WINI.MRG"
        
             The BASIC program code in B-WINI.MRG automatically BLOADs 
             the windowing support file into BASIC's string space.  

             B-WINI.MRG'es line numbers start at 60000, so if your 
             program already uses line numbers in this range be sure to 
             renumber your program's lines before the MERGE.

         (3) Add the lines:

                CLEAR,&H8000
                GOSUB 60060

             to the very beginning of your program to initialize B-
             WINDOW. DO NOT NEGLECT TO DO THIS.  The CLEAR command limits 
             BASIC to the lower half of the available string space.  The 
             subroutine call executes the code in B-WINI.MRG.

         (4) Alter the BLOAD command (contained in B-WINI.MRG) to load a 
             B-WINDOW support file with a sufficiently large window buffer 
             for your requirements. Window buffer sizes range from 5000 
             bytes (B-WIN5I.BIN) to 20000 bytes (B-WIN20I.BIN). Make sure 
             the support file is on the drive you specify in the BLOAD 
             command.

        You can now run your BASIC program.

        Because BASIC initializes all variables when a new variable is 
        created, you must never alter your BASIC program and then jump 
        directly to a line number that by-passes the B-WINDOW initiali-
        zation "GOSUB 60060" line. If you do this, all of the B-WINDOW 
        function entry point offsets will have been set to zero, so you 
        will jump to offset zero and probably crash your computer.  

      For experimenters:

        If you wish to have all of BASIC's string space available for 
        BASIC variables by BLOADING the B-WINDOW windowing support file 
        beyond BASIC's 64K range: 
        
          Note - The technique of BLOADing the B_WINDOW file just outside 
          of BASIC's range is risky. You may be overwriting something 
          important, so proceed with caution.  
        
                1) In your BASIC program, remove the "CLEAR,&h8000" line 
                   that immediately precedes the line "GOSUB 60060" 

                2) In B-WINI.MRG, the line "W.SEGBASE = DS% + &h800" 
                   should be changed to "W.SEGBASE = DS% + &h1000".



                                                                         5





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


        If you look at the code in B-WINI.MRG, you can see what is 
        happening. &h1000 = 64K = the memory segment address just beyond 
        BASIC's string space. &h800 = 32K, or half of BASIC's string 
        space.

   USING WITH COMPILED BASIC

        The process for using B-WINDOW functions with compiled BASIC 
        programs is quite simple:

         (1) If you are converting a windowing program that was developed 
             with a BASIC interpreter, remove the lines added to your 
             program from the B-WINI.MRG file by deleting all lines 
             numbered 60000 and above. Also remove the "CLEAR,&H8000" and 
             "GOSUB 60060" lines from the beginning of your program.  

         (2) Place the line "CALL WINIT (STATUS%)" at the very beginning 
             of your program. This sets up some windowing data pointers 
             and must NOT be omitted.

         (3) Compile your BASIC source:

                   BASCOM TESTPROG /O           - std. BASIC compiler
                        or
                   QB TESTPROG /O;              - QuickBASIC V2 compiler

         (4) Link the resulting ".OBJ" file with the appropriate B-WINDOW 
             ".OBJ" file. For example, to link to the 20000 byte window 
             buffer version of B-WINDOW if you are using QuickBASIC 
             version 2:
         
                   LINK TESTPROG + BWIN20QB;

        IMPORTANT - There are 2 types of ".OBJ" files; those with "QB"
        in their name (e.g. BWIN5QB.OBJ) and those with "BC" in their
        name (e.g. BWIN10BC.OBJ). If you are using QuickBASIC version 
        2, link to the "QB" object files. If you are using another BASIC 
        compiler, including QuickBASIC version 1, then link to the "BC" 
        object files.

        The "QB" type object files link to your QuickBASIC version 2 
        ".OBJ" files as two classes: 'CODE' and 'DATA'. The windowing 
        subroutines are in the 'CODE' class, and the data used by the 
        windowing subroutines is in the 'DATA' class.  
        
        The "BC" type object files link to your BASIC ".OBJ" files as one 
        class: 'CODE'. Both the windowing code and data are addressed off 
        the code segment register.  
        
        If you have Microsoft QuickBASIC Version 2, use the "separate 
        compilation method." Don't use BUILDLIB to create a user library 
        of any of the B_WINDOW .OBJ files.  




                                                                         6





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


  OVERVIEW OF FUNCTIONS

        YOU MUST ALWAYS CALL THE WINDOWING FUNCTION "WINIT" BEFORE USING 
        ANY OF B-WINDOW's FUNCTIONS. Do NOT neglect to do this, as 
        several important data pointers are initialized. The merge file 
        B-WINI.MRG, used with standard interpreted BASIC, does this for 
        you.
        B-WINDOW automatically selects 80 column alphanumeric screen mode.

        When using a BASIC interpreter, because variables have global 
        scope, you must be careful when you name variables, arrays, 
        strings, etc not to use a name already assigned to a B-WINDOW 
        function. All B-WINDOW function names defined in B-WINI.MRG are 
        preceded by "W", so if you never create a variable beginning with 
        the letter "W", you will be safe.  

        The four major windowing functions are:

          (1) Defining a window with WDEF.
          (2) Opening a window with WOPEN.
          (3) Closing the most recently opened window with WCLOSE. 
          (4) Deallocating window(s) and releasing window buffer 
              space with WKILL.


   FUNCTION PARAMETERS

        A function's parameters are the variables contained between the 
        parentheses immediately following the name of the function being 
        called. For example, in the statement "CALL ABC (X, Y)", the
        parameters are X and Y. Most of the B-WINDOW function parameters 
        are values being sent from your BASIC program, but a few B-WINDOW 
        functions return a value through one of the parameters.

        ALL PARAMETERS USED BY B-WINDOW FUNCTIONS MUST EITHER BE A 
        STRING, OR AN INTEGER. STRING NAMES ARE FOLLOWED BY A DOLLAR SIGN 
        ("$") AND INTEGER NAMES ARE FOLLOWED BY A PERCENT SIGN ("%"). The 
        B-WINDOW functions assume they are being sent integers for all 
        numeric values and, as the internal data storage format of other 
        BASIC numeric variable types vary considerably, using anything 
        other than integers results in erratic program behavior.  

        BASIC will not accept constants or complex expressions as numeric 
        function parameters:

          100 CALL FUNCT (12)     'Wrong - a constant
          110 CALL FUNCT (X%+Y%)  'Wrong - a complex expression
          120 CALL FUNCT (X%)     'OK 

        All function calls must include all parameters, even if they are 
        only dummy place-holders. For example, if a window has been 
        defined without a border, the window opening function WOPEN must 
        include all 9 parameters, even though the border type speci-
        fications are ignored. SPECIFYING TOO MANY OR TOO FEW FUNCTION 


                                                                         7





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


        PARAMETERS IS A SERIOUS ERROR AND WILL CAUSE YOUR PROGRAM TO 
        CRASH. BASIC pushes function parameters onto the stack before 
        calling a function and the called function must clear the 
        parameters from the stack before it returns to BASIC. For 
        example, if a function expects 4 parameters and only gets 3, then 
        the stack will be unbalanced when 4 parameters are cleared from 
        it.  


   TEXT DISPLAY

        WWRITE is the B-WINDOW screen writing function. It does not 
        attempt to interpret and act on any characters, including carriage 
        returns and line feeds. The only action taken is to wrap-around in 
        the active window if the cursor is at the right side of the window 
        and to scroll up if the bottom of the window is reached. Any extra 
        text handling will have to be added by you. The advantage is that 
        you can write any character to a window with WWRITE.

        Any standard BASIC output functions that involve outputting 
        carriage returns or line feeds to the screen MUST be avoided when 
        a window is open. The standard BASIC output functions know 
        nothing about the windowing environment and can easily write 
        across a window's border. Functions like PRINT can be used with 
        care, providing the user (1) first positions the cursor in a 
        window with WGOTOXY (2) never sends a carriage return or line 
        feed to the screen and (3) avoids writing across a window's 
        border.


   CHARACTER ATTRIBUTES

        The windowing functions WFGCOLOR and WBGCOLOR select the 
        foreground and background character attribute values for text 
        display. In 80 column alphanumeric mode, which is the mode 
        B-WINDOW works in, each character visible on your screen has 
        another attribute byte associated with it that determines whether 
        the visible character will blink, what color it is, etc. The 
        following table explains the different values of the character 
        attribute byte for both WFGCOLOR and WBGCOLOR.  

      IF YOU HAVE A MONOCHROME ADAPTER:

            There are two foreground display modes that can be selected 
            by WFGCOLOR -

              Attribute byte value:          Result:
                        0                 black foreground
                        7                 white foreground

              If you add 16 to either of the above, the character(s) 
              will blink. If you add 8 to either of the above, the 
              character(s) will be high intensity (if your monitor 
              recognizes the intensity signal).


                                                                         8





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------



            There are two background display modes that can be selected 
            by WBGCOLOR -

              Attribute byte value:          Result:
                        0                 black background
                        7                 white background
            Monochrome adapter attribute examples:

              100 ATTRIB%=7 : CALL WFGCOLOR (ATTRIB%) 'white foreground
              110 ATTRIB%=0 : CALL WBGCOLOR (ATTRIB%) 'black background

              100 ATTRIB%=7+8+16 'white foreground, bright, blinking
              110 CALL WFGCOLOR (ATTRIB%)

      IF YOU HAVE A COLOR GRAPHICS ADAPTER:

            There are 16 possible foreground colors that can be selected 
            by WFGCOLOR.

              Attribute byte value:     Result:
                        0                Black
                        1                Blue
                        2                Green
                        3                Cyan 
                        4                Red
                        5                Magenta
                        6                Brown
                        7                White
                        8                Gray
                        9                Light Blue
                       10                Light Green
                       11                Light Cyan
                       12                Light Red
                       13                Light Magenta
                       14                Yellow
                       15                Bright white

            Add 16 to the any of the above foreground color values to 
            make the character blink.

            There are 8 possible background colors that can be
            selected by WBGCOLOR. The background is the area around a 
            character.  

              Attribute byte value:          Result:
                        0                Black background
                        1                Blue background
                        2                Green background
                        3                Cyan background
                        4                Red background
                        5                Magenta background
                        6                Brown background
                        7                White background


                                                                         9





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------



            Color Graphics Adapter attribute examples:

              100 ATTRIB% = 0
              110 CALL WBGCOLOR (ATTRIB%) 'black background
              100 ATTRIB%=6 : CALL WBGCOLOR (ATTRIB%) 'brown background
              110 ATTRIB%=14 : CALL WFGCOLOR (ATTRIB%) 'yellow foreground

              100 ATTRIB%= 8+16
              110 CALL WFGCOLOR (ATTRIB%) 'Gray, blinking foreground

        To select standard white-on-black (B-WINDOW default) for either a 
        monochrome or color screen, specify 7 as the character foreground 
        attribute and 0 as the background attribute.  


   WINDOW BORDER TYPES

        If you defined a window as having a border, when you open that 
        window you can select one of six types of borders. The six types 
        of borders are:

            (a) type = 0   The border is not visible because it is made 
                           up of spaces. You cannot write on a border, 
                           even one that is blank, using WWRITE or WDSP1.

            (b) type = 1   Both the top, bottom and sides of the border 
                           are made up of single lines.

            (c) type = 2   Both the top, bottom and sides of the border 
                           are made up of double lines.

            (d) type = 3   The top and bottom edges of the border are 
                           made up of double lines, and the sides are 
                           made up of single lines.

            (e) type = 4   The top and bottom edges of the border are 
                           made up of single lines, and the sides are 
                           made up of double lines.

            (f) type = 5   Both the top, bottom and sides of the border 
                           are made up of solid block shapes.

        Another type of border is available if you have a color monitor 
        or a monochrome monitor that recognizes the color intensity 
        signal. If you select the same color for both the background and 
        foreground of a window's border, then a thick border will 
        surround the window.








                                                                        10





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


   BASIC WINDOWING TOOLBOX FUNCTIONS
        
    WINIT - Initialize B-WINDOW
    
        Usage: 

          CALL WINIT (STATUS%)

        Called with:
            Nothing
        Returns:
            STATUS% = 1 if success, 0 if error 

        Example:

            100 CALL WINIT (STATUS%)
            110 IF STATUS% = 0 THEN PRINT "Windowing initialization error"

        WINIT sets up pointers to the window buffer, detects the type of 
        monitor (color or monochrome) and selects 80 column alphanumeric 
        mode.

        YOU MUST CALL WINIT BEFORE CALLING ANY OTHER B-WINDOW FUNCTIONS. 
        Failure to do this can cause random sections of memory to be 
        overwritten.
        
        If you are using standard interpreted BASIC, you don't have to 
        call WINIT because the merge file B-WINI.MRG does it for you.  


    WDEF - Define a window 

        Usage: 

          CALL WDEF (WNUM%, WID%, HGT%, BORDER%)

        Called with:
            WID%     = Width of window, including optional border.
            HGT%     = Height of window, including optional border.
            BORDER%  = Set this equal to 1 if a border is desired, 0 for 
                       no border.
        Returns:
            WNUM%    = 0 if error, window access number otherwise.

        Example:

            100 WID% = 40 : HGT% = 15 : BORDER% = 1
            110 CALL WDEF (WNUM%, WID%, HGT%, BORDER%)
            120 IF WNUM% = 0 THEN PRINT "Error defining window"
            130 REM Use WNUM% to open window later

        Define a window and reserve storage for it in the window buffer.
        A window must be defined before it can be opened.



                                                                        11





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


        The window's width and height include a border, if a border is 
        specified. If the window has a border, then the writable area of 
        the window is reduced to fit inside the border. For example, a 
        bordered window that has a width of 30 and a height of 8 has 
        writable coordinates of 0..27 in the horizontal (X) direction 
        and 0..5 in the vertical (Y) direction. If the window didn't 
        have a border, the X and Y ranges would be 0..29 and 0..7
        respectively.

        You cannot define a window larger than the standard screen. Also, 
        a window must be big enough so that at least one writable 
        character position is on the window. In other words, the window 
        must not be smaller than three columns by three rows if a border 
        is specified and one column by one row if no border is specified.

        If you have called WERRDISPLAYOFF, be sure to check the returned
        status for 0, the error condition. Errors occur if the window is 
        too small, too big, or if there is not enough room for the window 
        in the window buffer.


    WOPEN - Open a window previously defined by WDEF

        Usage:

          CALL WOPEN (STATUS%, WNUM%, X%, Y%, CLR%, WBGC%,
                      BTYPE%, BFGC%, BBGC%))

        Called with:
            WNUM%    = Window access number returned by a previous WDEF
            X%       = Horizontal coordinate of upper left corner
            Y%       = Vertical coordinate of upper left corner
            CLR%     = Pre-clear window if set to 1, retain 
                       previous contents if set to 0
            WBGC%    = Window background color
            BTYPE%   = Border type
            BFGC%    = Border foreground color
            BBGC%    = Border background color
        Returns:
            STATUS%  = 1 if success, 0 if error

        Example:

            100 X% = 3          'upper left corner of window is 4th
            101 '                column from far left of std. screen
            110 Y% = 4          'upper left corner of window is 5th
            111 '                row down from top of std. screen
            120 CLR% = 0        'don't clear previous text from window
            130 WBGC% = 2       'window background color is green
            140 BTYPE% = 1      'single lines
            150 BFGC% = 4       'red border foreground
            160 BBGC% = 1       'blue border background
            170 CALL WOPEN (STATUS%, WNUM%, X%, Y%, CLR%, WBGC%,
                            BTYPE%, BFGC%, BBGC%))


                                                                        12





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


            180 IF STATUS% = 0 THEN PRINT "Window open error"

        (line 170 wrapped for purpose of documentation formatting only)

        Open a window that has been previously defined by a call to WDEF. 
        If a window is being opened for the first time, then the contents 
        of the window are initialized to spaces. If the window is being 
        opened again, the previous contents of the window will be erased, 
        unless "CLR%" is set to 0.  

        "X%" and "Y%" are absolute locations on the standard 80x25 screen 
        and specify the location of the upper left corner of the window 
        to be opened.

        See the Section "WINDOW BORDER TYPES" for a listing of the 
        six border types.

        If you have called WERRDISPLAYOFF, be sure to check the returned 
        status for 0, the error condition. Errors occur if wnum is too 
        small or big, if the window is already open, or if the window 
        won't fit on the screen at the X,Y location specified.


    WCLOSE - Close a window 

        Usage: 

          CALL WCLOSE 

        Called with:
            Nothing
        Returns:
            Nothing

        Example:

            100 CALL WCLOSE

        Close the most recently opened window and restore the previously 
        overwritten section of screen. Windows close in the reverse order 
        in which they were opened.

        When a window is closed, the cursor will return to the location 
        it previously occupied before the window was opened.

        If all windows are already closed, WCLOSE will simply return.
        Extra WCLOSE calls are ignored and do not generate an error.









                                                                        13





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


    WKILL - Deallocate window buffer space

        Usage:

          CALL WKILL (STATUS%, WNUM%)

        Called with:
            WNUM%   = Number of window to kill
        Returns:
            STATUS% = 1 if success, 0 if error

        Example:

            100 'Define 3 windows
            110 WID% = 48 : HGT% = 5 : BDR% = 1
            120 CALL WDEF (WNUM1%, WID%, HGT%, BDR%)
            130 WID% = 30 : HGT% = 10 : BDR% = 0
            140 CALL WDEF (WNUM2%, WID%, HGT%, BDR%)
            150 WID% = 35 : HGT% = 20 : BDR% = 1
            160 CALL WDEF (WNUM3%, WID%, HGT%, BDR%)
            170 'Deallocate WNUM2%. Also de-allocate WNUM3%
            180 'because it was defined after WNUM2%, but not
            190 'WNUM1%, because it was defined before WNUM2%
            200 CALL WKILL (STATUS%, WNUM2%)
            210 IF STATUS% = 0 THEN PRINT "Deallocation error"

        Deallocate a window, and all subsequently defined windows, 
        freeing up window buffer space. The window definition, and all 
        subsequent definitions, will no longer exist. Using WKILL allows 
        you to display an unlimited number of windows because the window 
        buffer can be cleared and reused.

        When WKILL is called, all of the open windows on the screen are 
        automatically closed. This is done because the deallocated 
        window(s) may be partially or fully hidden under a window that is 
        not being deallocated. The windows defined before the deallocated 
        window will still be in the window buffer, however.

        If you have called WERRDISPLAYOFF, be sure to check the returned
        status for 0, the error condition. Errors occur if wnum is too 
        small or too big or if no window is associated with wnum.


    WSCROLL - Scroll contents of window

        Usage:

          CALL WSCROLL (DIR%, NUM%)

        Called with:
            DIR% = Direction of scroll; 0 = up, 1 = down
            NUM% = Number of lines to scroll
        Returns:
            Nothing


                                                                        14





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------



        Example:

            100 'Scroll current window down 3 lines
            110 DIR% = 1
            120 NUM% = 3
            130 CALL WSCROLL (DIR%, NUM%)

        The current window is scrolled in "DIR%" direction for "NUM%" 
        lines. If no windows are open, the standard 80x25 screen will 
        scroll. The current window's background color (set by WOPEN) will 
        be the attribute of the blanked area.


    WWRITE - Display a string in a window

        Usage:

          CALL WWRITE (STR$)

        Called with:
            STR$    = String to be displayed
        Returns:
            Nothing

        Example:

            100 STR$ = "String to be displayed"
            110 CALL WWRITE (STR$)

        Display string in current window at location set by WGOTOXY. If 
        the right hand side of a window is reached, the cursor will wrap-
        around to the next line. If the cursor reaches the bottom of the 
        current window, the contents of the window will scroll up 1 line. 
        WWRITE leaves the cursor 1 character position to the right of the 
        last character in the string.
        
        If no windows are open, WWRITE writes to the standard 80x25 
        screen.

        No control characters are recognized, so any character can be 
        displayed. The length of the string cannot exceed 255 characters.
        
        Previous calls to WFGCOLOR (foreground) and WBGCOLOR (background) 
        determine the attributes of the text displayed by WWRITE.  











                                                                        15





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


    WDSP1 - Display 1 character

        Usage:

          CALL WDSP1 (X%, Y%, CH%)

        Called with:
            X%      = X position within current window
            Y%      = Y position within current window
            CH%     = ASCII value of character to display
        Returns:
            Nothing

        Example:

            100 REM display "Q" on screen at 40,10
            110 X% = 40 : Y% = 10 : CH% = ASC ("Q")
            120 CALL WDSP1 (X%, Y%, CH%)

        Display a single character at an X, Y location relative to the 
        currently open window. WDSP1 leaves the cursor at the same X, Y 
        location as the displayed character. If no windows are open, the
        X and Y coordinates correspond to absolute locations on the
        standard 80x25 screen.

        Previous calls to WFGCOLOR (foreground) and WBGCOLOR (background) 
        determine the attributes of the text displayed by WWRITE.  

        Though WDSP1 doesn't return a status to your BASIC code, if "X%" 
        or "Y%" are outside of the current window and WERRDISPLAYOFF has 
        not been called, an error window will open and an error message 
        will display.  


    WGETCX - Get cursor horizontal (X) position

        Usage:

          CALL WGETCX (XPOS%)

        Called with:
            Nothing
        Returns:
            XPOS% = cursor X position

        Example:

            100 CALL WGETCX (XPOS%)
            110 PRINT "The cursor X position is: ";XPOS%

        This function returns the current X position of the cursor, 
        relative to the upper left corner (0, 0) of the writable part of 
        the current window. If no windows are open, the X position is 
        relative to the upper left corner of the standard 80x25 screen.


                                                                        16





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


    WGETCY - Get cursor vertical (Y) position

        Usage:

          CALL WGETCY (YPOS%)

        Called with:
            Nothing
        Returns:
            YPOS% = cursor Y position

        Example:

            100 CALL WGETCY (YPOS%)
            110 PRINT "The cursor Y position is: ";YPOS%

        This function returns the current Y position of the cursor, 
        relative to the upper left corner (0, 0) of the writable part of 
        the current window. If no windows are open, the Y position is 
        relative to the upper left corner of the standard 80x25 screen.


    WGOTOXY - Go to X, Y position

        Usage:

          CALL WGOTOXY (X%, Y%)

        Called with:
            X% = Horizontal position (column)
            Y% = Vertical position (row)
        Returns with:
            Nothing

        Example:

            100 X% = 20 : Y% = 15
            110 CALL WGOTOXY (X%, Y%)

        Go to specified X, Y location on the writable part of the 
        current window. If you specified a border when you defined and 
        opened the window, the writable part of the window is reduced to 
        fit inside the border. For example, if you specified a window 
        that was 10 x 10, and it had a border, then the allowable 
        horizontal (X) and vertical (Y) coordinates for WGOTOXY would be 
        between 0..7.

        If there are no windows open, the X, Y coordinates refer to the 
        standard 80x25 screen.

        Though WGOTOXY doesn't return a status to your BASIC code, if 
        "X%" or "Y%" are outside of the current window and WERRDISPLAYOFF 
        has not been called, an error window will open and an error 
        message will display.


                                                                        17





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


    WFGCOLOR - Set text foreground color

        Usage:

          CALL WFGCOLOR (ATTRIB%)

        Called with:
            ATTRIB% = foreground display attribute
        Returns with:
            Nothing

        Example:

            100 ATTRIB% = 6+16 'blinking brown
            110 CALL WFGCOLOR (ATTRIB%)

        Set the foreground color for text displayed by WWRITE, WDSP1 and 
        WBORDER. See the Section "CHARACTER ATTRIBUTES" for a listing of 
        the display attributes available.  

        Though WFGCOLOR doesn't return a status to your BASIC code, if 
        "ATTRIB%" is outside of the range of allowable foreground values 
        (0..31) and WERRDISPLAYOFF has not been called, an error window 
        will open and an error message will display.  


    WBGCOLOR - Set text background color

        Usage:

          CALL WBGCOLOR (ATTRIB%)

        Called with:
            ATTRIB% = background display attribute
        Returns with:
            Nothing

        Example:

            100 ATTRIB% = 5 'magenta
            110 CALL WBGCOLOR (ATTRIB%)

        Set the background color for text displayed by WWRITE, WDSP1 and 
        WBORDER. See the Section "CHARACTER ATTRIBUTES" for a listing of 
        the display attributes available.  

        Though WBGCOLOR doesn't return a status to your BASIC code, if 
        "ATTRIB%" is outside of the range of allowable background values 
        (0..7) and WERRDISPLAYOFF has not been called, an error window 
        will open and an error message will display.  






                                                                        18





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


    WBORDER - Draw border on screen

        Usage:

          CALL WBORDER (STATUS%, X%, Y%, WID%, HGT%, BTYPE%)

        Called with:
            X%    = Horizontal position
            Y%    = Vertical position
            WID%  = Width of border
            HGT%  = Height of border
            BTYPE% = Type of border
        Returns with:
            STATUS% = 1 if success, 0 if error

        Example:

            100 X% = 10: Y% = 5 : WID% = 40 : HGT% = 8 : BTYPE% = 5
            110 CALL WBORDER (STATUS%, X%, Y%, WID%, HGT%, BTYPE%)
            120 IF STATUS% = 0 THEN PRINT "Error drawing border"

        Draw a border around an area of the screen. X and Y are absolute 
        coordinates, relative to the standard 80x25 screen. The upper 
        leftmost coordinate of the standard screen is (0, 0) and the 
        lower rightmost coordinate of the standard screen is (79, 24).

        Borders created by WBORDER are not windows. You can close a 
        window, which may or may not have a window border, but you cannot 
        close a WBORDER border because it is written onto the standard 
        80x25 screen.

        See the Section "WINDOW BORDER TYPES" for a listing of the six 
        border types.

        The foreground and background colors of the border's characters 
        are determined by previous calls to WFGCOLOR and WBGCOLOR. If you 
        set both the background and foreground colors to the same value, 
        then the border will appear quite thick.  

        If you have called WERRDISPLAYOFF, be sure to check the returned
        status for 0, the error condition. An error occurs if the border 
        type is not one of the types specified or if the border will not 
        fit on the standard 80x25 screen.













                                                                        19





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


    WERRDISPLAYON - Enable error window display

        Usage:

          CALL WERRDISPLAYON

        Called with:
            Nothing
        Returns with:
            Nothing

        Example:

            100 CALL WERRDISPLAYON

        Turn on the display of windowing errors. If an error is detected 
        by a B-WINDOW function, an error window will open and an error 
        message will be displayed. Re-edit your BASIC program and remove 
        the cause of the windowing error.

        Note that the functions WLPTSELECT and WLPTIMOUT return a status 
        flag only. They never generate a visible error message.

        The display of windowing errors is the default state. You have to 
        call WERRDISPLAYON only if you had previously called 
        WERRDISPLAYOFF.  


    WERRDISPLAYOFF - Disable error window display

        Usage:

          CALL WERRDISPLAYOFF

        Called with:
          Nothing
        Returns with:
          Nothing

        Example:

            100 CALL WERRDISPLAYOFF

        Turn off the display of windowing errors. If you call 
        WERRDISPLAYOFF, the only way to check for windowing errors is to 
        check the returned status.










                                                                        20





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


    WINT86 - Access software interrupts

        Usage:

          CALL WINT86 (INTTYPE%, ARRAYPTR)

        Called with:
            INTTYPE% = Interrupt type
            ARRAYPTR = Pointer to register array
        Returns with:
            Upper 8 bytes of register array = returned registers

        Example:

            100 'Send "Q" to LPT1: - example for BASIC interpreter
            110 ' (See ROM BIOS listing...)
            120 ' The register AH determines what action the BIOS
            130 ' interrupt 17H takes when it is called. If AH = 0, then
            140 ' AL contains the character to print, and DX selects the
            150 ' printer, which in this case is LPT1:
            160 ' 
            170 DEF SEG 'Set base pointer for POKEs to BASIC storage
            180 DIM REGARRAY%(8) '16 bytes
            190 REGPTR = VARPTR(REGARRAY%(0)) 'First element in array
            200 IF REGPTR < 0 THEN REGPTR = REGPTR + 65536
            210 POKE REGPTR, asc("Q") 'Register AL = "Q"
            220 POKE REGPTR+1, 0 'Register AH = 0
            230 POKE REGPTR+6, 0 : POKE REGPTR+7, 0 'Register DX = 0
            240 'Alter base pointer for CALL to windowing program
            250 DEF SEG = W.SEGBASE 'W.SEGBASE is defined in B-WINI.MRG
            260 INTTYPE% = &H17 'Printer BIOS call
            270 CALL WINT86(INTTYPE%, REGARRAY%(0))
            280 ' AH returns equal to 1 if printer timed-out (not ready)
            290 DEF SEG 'Base pointer back to BASIC storage for PEEK
            300 IF PEEK(REGPTR+9) = 1 THEN PRINT "Printer time-out"
            310 DEF SEG = W.SEGBASE 'And back to windowing program

        Directly access the software interrupt structure of an IBM 
        Personal Computer. BIOS functions and low-level DOS functions are 
        accessed by execution of software interrupts. For a detailed 
        explanation of the various interrupts we refer you to the IBM 
        Technical Reference Manual and the PC-DOS Reference Guide.

        The above example is for use with standard interpreted BASIC. 
        Notice how you have to use the "DEF SEG" command to alternate 
        between the windowing support file (for the CALL instruction), 
        and BASIC's array storage (for the POKE and PEEK instructions). 

        Before calling WINT86, you must reserve a section of memory 16 
        bytes in size. You must fill the first 8 bytes with the initial 
        register values before the software interrupt and the last 8 
        bytes will contain the register values returned after the 
        interrupt. In the above example, 16 bytes was reserved by 
        declaring an 8 element integer array. Each element of an integer 


                                                                        21





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


        array takes up 2 bytes. In line 190 above, "REGPTR" is set to
        point at the first element of the array and the 16 bytes map to
        the registers according to the following table:

          Initial register values before interrupt:

            REGPTR    = AL      REGPTR+1  = AH
            REGPTR+2  = BL      REGPTR+3  = BH
            REGPTR+4  = CL      REGPTR+5  = CH
            REGPTR+6  = DL      REGPTR+7  = DH

          Returned register values after interrupt:

            REGPTR+8  = AL      REGPTR+9  = AH
            REGPTR+10 = BL      REGPTR+11 = BH
            REGPTR+12 = CL      REGPTR+13 = CH
            REGPTR+14 = DL      REGPTR+15 = DH

        To send WINT86 a pointer to the first byte of the register table, 
        send the address of the first element of the table. e.g.
        REGARRAY%(0).

        Users of QuickBASIC V2 should use the interrupt access routines 
        provided with the compiler, not the B-WINDOW function.


    WLPTSELECT - Change which printer corresponds to "LPT1:"

        Usage:

          CALL WLPTSELECT (STATUS%, PRTR%)

        Called with:
            PRTR% = The new printer port to correspond to "LPT1:"
        Returns with:
            STATUS% = 1 if success, 0 if error

        Example:

            100 LPRINT "This will come out on LPT1"
            110 PRTR% = 2
            120 CALL WLPTSELECT (STATUS%, PRTR%)
            130 LPRINT "This will come out on LPT2"
            140 'Back to original port mapping..
            150 PRTR% = 1
            160 CALL WLPTSELECT (STATUS%, PRTR%)
            170 LPRINT "Back to LPT1 again"

        The standard BASIC commands LLIST and LPRINT send all output to 
        the first line printer LPT1. If you have more than one printer, 
        using WLPTSELECT you can direct all of the output normally sent 
        to LPT1 to the other printer(s).




                                                                        22





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


        Be sure to change the physical port address that LPT1 maps to 
        back to its original value before exiting a program that uses 
        WLPTSELECT, unless you want the port reassignment to persist 
        until you reboot your computer. If you don't restore the original 
        port address of LPT1, the next time your windowing program runs 
        WINIT will read your modified version of the port address table 
        and you will not be able to select the original port 
        corresponding to LPT1 because the port address will have been 
        overwritten.  

        Be sure to check the returned status for 0, the error condition. 
        An error occurs if "PRTR%" is not in the range 1..3 or if there 
        is no physical port installed on your computer corresponding to 
        your port selection. WLPTIMOUT does NOT generate an error message 
        window. Checking the returned status is the only way to check for 
        errors.


    WLPTIMOUT - Alter printer time-out

        Usage:

          CALL WLPTIMOUT (STATUS%, PRTR%, TVAL%)

        Called with:
            PRTR% = Printer port to alter
            TVAL% = New timer value for this printer
        Returns with:
            STATUS% = 1 if success, 0 if error

        An IBM Personal Computer use a software time-out value when 
        waiting for a printer to come on-line and start accepting data.  
        This time-out value can be altered to increase or decrease the 
        amount of time your computer will wait before giving up on 
        sending to a printer. A standard IBM Personal Computer has a 
        time-out value of 20. The allowable range for "TVAL%" is 
        1..255. The allowable range for "PRTR%" is from 1 (LPT1) to 3 
        (LPT3).  

        If you have a very slow printer and it keeps timing out when you 
        are printing from your word processor, etc., then you can use 
        this facility of B-WINDOW to increase the printer time-out value.
        The new time-out value will persist until you reboot your 
        computer, or you call WLPTIMOUT again.

        Note that some clones of IBM Personal Computers do not use the 
        same memory location as the Personal Computer for the printer 
        time-out count. This function will not work on these computers.

        Be sure to check the returned status for 0, the error condition. 
        An error occurs if "PRTR%" is not in the range 1..3, or if 
        "TVAL%" is not in the range 1..255. WLPTIMOUT does NOT generate 
        an error message window. Checking the returned status is the only 
        way to check for errors.


                                                                        23





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


   ERROR HANDLING

        You can control the action taken when a windowing error occurs 
        through calls to WERRDISPLAYOFF and WERRDISPLAYON. If you call 
        WERRDISPLAYON (the default state) then, if an error occurs, the  
        program will display an error message window. The name of the 
        windowing function and what is wrong with what you are asking the 
        function to do will be indicated in the window. Your program will 
        then pause, waiting for you to press a key. When you press a key, 
        your program will continue. Break out (CTRL+BREAK) of your 
        program as soon as possible and correct the error. Often the 
        problem is as simple as mixing the X and Y coordinates up, or 
        using a non-integer numeric variable.

        If you call WERRDISPLAYOFF, for all B-WINDOW windowing functions 
        that return a status value (1 = success, 0 = error), be sure to 
        check that no error has occurred. If a windowing function returns 
        an error value, do not ignore it. Terminate your program and 
        check for the cause of the error.

        WLPTIMOUT and WLPTSELECT return a status value only. They are not 
        windowing functions, and will not display an error message 
        window.


   ERROR MESSAGES

        If a windowing error occurs and you haven't called 
        WERRDISPLAYOFF, B-WINDOW will usually display an error message 
        window. It contains an error message consisting of the name of 
        the B-WINDOW function where the error occurred, followed by a 
        brief description of the error. The following is a listing of all 
        error messages and their meanings: 

      "BORDER - Incorrect border type"

        The border types range from 0 (spaces) to 5 (block characters).
        You have specified a border type value outside of this range. See 
        the Section "WINDOW BORDER TYPES" for a description of the 
        borders available.

      "BORDER - Won't fit on screen"

        There is no virtual screen extending beyond the visible portion 
        of your computer's screen, so a border must be entirely visible. 

      "WDEF - Window too small"

        A window must be large enough to have at least one writable 
        character position. Note that if you define a window with a 
        border, then the minimum window size is 3 columns by 3 rows 
        because the border will take up 2 character positions vertically 
        and horizontally.



                                                                        24





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


      "WDEF - Window too large"

        As with borders, a window must be entirely visible when opened.
        Therefore, the largest window possible is as large as the 
        standard 80x25 screen.

      "WDEF - Too many windows"

        The maximum number of windows that can be defined is 30.

      "WDEF - No window buffer freespace"

        You have used up all of the window buffer with your window 
        definitions. You must choose a larger window buffer version of 
        B-WINDOW or use WKILL to free up window buffer space.

      "WOPEN - Window number out of range"

        You have tried to open a window using a window access number 
        outside of the range 1..30. The window access number is the value 
        returned by WDEF.

      "WOPEN - Window already open"

        Only one copy of a defined window can be open at any one time.
        You can however, close a window and then immediately reopen it at 
        a different location.

      "WOPEN - Window not defined"

        You have forgotten to use WDEF to define the window you wish to 
        open or the window access number sent to WOPEN is incorrect.

      "WOPEN - Window won't fit on screen"

        The window won't fit on the screen where you want to put it and 
        still be entirely visible.

      "WGOTOXY - Cursor out of range"
                  or
      "WDSP1 - Cursor out of range"

        You have specified coordinates outside of the currently active 
        area when locating the cursor. Remember that all coordinates 
        start with zero and that a window defined with a border has 2 
        less writable positions in both the horizontal and vertical 
        directions than a window defined without a border.

      "WFGCOLOR - Color out of range"
                   or
      "WBGCOLOR - Color out of range"

        You have specified a character attribute that is not in the range 
        0..31 for foreground colors, or 0..7 for background colors.


                                                                        25





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


   REGISTERING BASIC WINDOWING TOOLBOX

        The distribution version of B-WINDOW has three interpreted BASIC 
        windowing support files. Registered users of B-WINDOW get
        windowing support files (5000, 10,000 and 20,000 byte window 
        buffers) in ".OBJ" format for linking with compiled BASIC 
        programs.

        If you use B-WINDOW, please register and show your support for 
        our efforts. $20 is a small price to pay for all that B-WINDOW 
        offers. And please don't give anyone a registered copy of 
        B-WINDOW.

        There are two places to register for the full B-WINDOW package:
        

          In the USA for $20 US:        In Europe for 17 English pounds:

            Image Computer Systems        Image Computer Systems
            P. O. Box 647                 27 Cobham Road
            Avon, Connecticut  06001      Ferndown Industrial Estate
            Ph: (203) 678-8771            Wimborne, Dorset, England
                                          Ph: 0202-876064

        The above prices include domestic postage. Add $3/3 pounds for 
        overseas postage. No surcharge for USA orders shipped to Canada 
        or Mexico. Connecticut residents must pay 7 1/2% sales tax, and 
        United Kingdom residents must pay 15% VAT.  We accept MasterCard 
        and Visa. Use the order form at the end of this documentation, or 
        order by phone.  

        B-WINDOW is sent on a DOS 2.0 formatted double-sided floppy 
        diskette.  


   IMAGEPRINT

        Another Image Computer Systems User-Supported product is 
        ImagePrint, a software package that allows your IBM Graphics 
        Printer or IBM Proprinter or Epson printer or compatible printer 
        to produce print quality comparable to that of a daisy wheel 
        printer.
        
        Most print quality enhancing programs and so-called letter 
        quality printers only make two print-head passes to form 
        characters, and the results show it. Our sophisticated font 
        design process, combined with three print-head passes, gives a 
        print quality nothing else matches.
        
        Text can be formatted and individual characters can be bold, 
        italic, double width, half-high, 17.1 or 12 or 10 cpi, 
        superscripted or subscripted, and underlined. Fonts can be 
        dynamically switched during printing and each font contains an 
        entire IBM Graphics Printer's character set, so you don't need an 


                                                                        26





                                                   BASIC WINDOWING TOOLBOX
   -----------------------------------------------------------------------


        IBM Graphics Printer to print ASCII characters 128-255. Both 80 
        and 136 column versions of ImagePrint are included on a 
        REGISTRATION diskette.  

        The distribution version of ImagePrint, with 1 font (Cubic) and 
        support for 80 column printers only, is available for $10 or 9 
        English pounds. The registered version of ImagePrint, with a 
        total of 6 fonts and support for both 80 and 136 column printers, 
        is available for $20 or 17 English pounds. The above prices 
        include postage. Connecticut residents must pay 7 1/2% sales tax, 
        and United Kingdom residents must pay 15% VAT. We accept 
        MasterCard and Visa. Use the order form at the end of this 
        documentation, or order by phone.  


   RESTRICTIONS

        The BASIC WINDOWING TOOLBOX (B-WINDOW) software package is 
        Copyright (C) Image Computer Systems 1985, 1986, 1987.  

        The distribution version of B-WINDOW has three windowing support
        files for interpreted BASIC. You may freely copy the distribution 
        version of B-WINDOW and give it to your friends or acquaintances.  
        You must not charge more than $7 for this service, to cover the 
        cost of reproducing a diskette.  

        The distribution version of B-WINDOW is a single entity. No files 
        may be deleted or modified, whether B-WINDOW is copied onto 
        another diskette, transmitted by a telecommunications link, or 
        any other means of transfer.

        The ONLY source of REGISTERED B-WINDOW, with windowing support 
        files for compiled BASIC, is Image Computer Systems.  
        
        Non-commercial users of B-WINDOW may use B-WINDOW without any 
        other restrictions.  

        No-one may sell or represent B-WINDOW, or a derivative of
        B-WINDOW that uses any or all of the B-WINDOW code, as their own 
        "windowing toolbox" product.

        Commercial users of B-WINDOW, i.e. individuals or companies using 
        or planning to use B-WINDOW in support of their own commercial  
        product, must include a B-WINDOW and Image Computer Systems 
        credit in their documentation, or on the computer's screen if 
        their product has no documentation.  


   DISCLAIMER

        Users of B-WINDOW do so at their own risk. No representations as 
        to B-WINDOW's suitability for any purpose are made. Users of 
        B-WINDOW are entirely responsible for loss or damage of any kind 
        caused by B-WINDOW.


                                                                        27





                                                          B-WINDOW TOOLBOX
   -----------------------------------------------------------------------


   INDEX

         ASCII, 2, 16, 27
         Attribute, 1, 8, 9, 10, 15, 16, 18, 25
         B-WINI.MRG, 3, 5, 6, 7, 11, 21
         Background, 8, 9, 10, 12, 15, 16, 18, 19, 25
         BLOAD, 1, 3, 5
         BORDER, 1, 2, 7, 8, 10, 11, 12, 13, 17, 18, 19, 24, 25
         Buffer, 1, 2, 3, 4, 5, 6, 7, 11, 12, 14, 25, 26
         Color, 8, 9, 10, 11, 12, 15, 16, 18, 19, 25
         Compatibility, 4
         Compile, 1, 4, 6, 22, 26, 27
         Cursor, 1, 2, 8, 13, 15, 16, 17, 25
         Disclaimer, 27
         Error, 8, 11, 12, 13, 14, 16, 17, 18, 19, 20, 22, 23, 24
         Foreground, 8, 9, 10, 12, 15, 16, 18, 19, 25
         Height, 2, 11, 12, 19
         Initialize, 3, 5, 7, 11, 13
         INT86, 21, 22
         Interrupt, 1, 21, 22
         Link, 1, 4, 6, 8, 9, 10, 18, 26, 27
         Monochrome, 8, 9, 10, 11
         PEEK, 21
         POKE, 21
         Printer, 1, 2, 21, 22, 23, 26, 27
         Restrictions, 1, 27
         Source, 4, 6, 27
         String, 1, 4, 5, 6, 7, 15
         WBGCOLOR, 8, 9, 10, 15, 16, 18, 19, 25
         WBORDER, 18, 19
         WCLOSE, 7, 13
         WDEF, 7, 11, 12, 13, 14, 24, 25
         WDSP1, 2, 10, 16, 18, 25
         WERRDISPLAYOFF, 12, 13, 14, 16, 17, 18, 19, 20, 24
         WERRDISPLAYON, 20, 24
         WFGCOLOR, 8, 9, 10, 15, 16, 18, 19, 25
         WGETCX, 2, 16
         WGETCY, 2, 17
         WGOTOXY, 2, 8, 15, 17, 25
         Width, 2, 11, 12, 19, 26
         WINIT, 3, 6, 7, 11, 23
         WINT86, 21, 22
         WKILL, 3, 7, 14, 25
         WLPTIMOUT, 20, 23, 24
         WLPTSELECT, 20, 22, 23, 24
         WOPEN, 7, 12, 15, 25
         WSCROLL, 2, 14, 15
         WWRITE, 2, 8, 10, 15, 16, 18

        






                                                                        28





                     B-WINDOW REGISTRATION/ORDER FORM
                               (IMAGE V2.0)

     __________________________________________________________________

     USA:  Image Computer Systems     Europe:  Image Computer Systems
           P. O. Box 647                       27 Cobham Road
           Avon, Connecticut 06001             Ferndown Industrial Estate
           Ph: (203) 678-8771                  Wimborne, Dorset, England
                                               Ph: 0202-876064
     ------------------------------------------------------------------



       Company                     ___________________________________

       Name                        ___________________________________

       Address                     ___________________________________

       Address                     ___________________________________

       City, State (Town, County)  ___________________________________

       Zip Code (Postal code)                              ___________


               (Prices are in US dollars and English pounds)


       __ B_WINDOW REGISTRATION diskette                 $20/17 pounds
          (Latest version, compiler support files)


       __ ImagePrint REGISTRATION diskette               $20/17 pounds
          (Latest version, 80 & 136 column printers,
           total of 6 fonts) 

       __ Surcharge if Purchase Order                      $5/4 pounds

       __ Overseas Postage (air mail)                      $3/3 pounds

               Connecticut residents add 7 1/2% sales tax   __________

                     United Kingdom residents add 15% VAT   __________

                                                    Total   __________


    Payment is by:

       __ Check           __Purchase Order

       __ MasterCard      __Visa


    Card number _______________________________ Expiration date ________

    Card Holder Signature ______________________________________________
    
    Card Holder Name (Please Print) ____________________________________