NAME
	contour - draw contours for a tabulated function of two variables

SYNOPSIS
	contour [file][options]

USAGE
	The input data for CONTOUR is normally a file written by 
	LAPLACE.  The output is a file suitable for GRAPH.  Since 
	LAPLACE only reports the potentials at grid points, and the 
	boundaries in general don't fall on grid points, the actual 
	boundaries probably won't appear in the data.  In that case, it
	may be helpful to append the input file for LAPLACE (which
	specifies the boundaries) to the output file from CONTOUR, so
	the boundaries may be seen as well as the other equipotentials.
	
OPTIONS

	-n  num
		Approximate number of contours desired (default 6). 
		The contour levels are always chosen at "reasonable"
		values: a small integer times some power of ten.

	-o  name
		Specify name of output file.  The default name is the
		same as the input file, but with extension ".CNT".

	-z  [min [max]]
		Specify range of contours.  Use this to get contours
		for only a part of the z range of the data.  The values
		default to the minimum and maximum z values in the
		data.

	-?	print a help message, such as:

		contour   version 0.2
		usage: contour  [file]  [options]
		options are:
		  -n  num            approximate number of contours (default 6) 
		  -o  name           specify name of output file 
		  -v  voltage        calculate capacitance assuming this 
		                     voltage between the two boundaries
		  -z  [min [max]]    specify range of contours

INPUT FILE

	The input data file has a two line header such as the following:

0.  3.  10      minimum and maximum y values, width of grid
0.  3.   6      minimum and maximum y values, height of grid

	On each line, any text after the first three numbers is discarded.

	The header is followed by the (width*height) data points separated
	by spaces and/or newlines.  For the sample header above, the points 
	would appear in the following order:

	ymax -> 50 51 52 53 54 55 56 57 58 59
	        40 41 42 43 44 45 46 47 48 49
	        30 31 32 33 34 35 36 37 38 39
	        20 21 22 23 24 25 26 27 28 29
	        10 11 12 13 14 15 16 17 18 19
	ymin ->  0  1  2  3  4  5  6  7  8  9
	         ^ xmin                     ^ xmax

	The data file output by LAPLACE is acceptable to CONTOUR.  Note 
	that CONTOUR is slightly more general in that LAPLACE always 
	uses a square grid (x and y spacing equal) while CONTOUR allows 
	a rectangular grid.

OUTPUT FILE
	CONTOUR writes to its output file X and Y values of points on 
	the contours, with one point per line.  The last point on each 
	contour is followed by the potential on that contour in 
	quotation marks.  This data file is appropriate for GRAPH.

AUTHOR
	Copyright (c) 1986 James R. Van Zandt (jrv@mitre-bedford)
	Resale forbidden, copying for personal use encouraged, comments
	welcome.