The following procedure can be used to prepare a hard

disk system so that it is not necessary to have a floppy disk

inserted for operations except for the initial power on booting.

	The assumptions are that the maker of your disk system

has included a DOS2.x compatible device driver which is installed

during the boot procedure from the CONFIG.SYS file.

	The root directory on the hard disk should have the

following at a minimum:

	AUTOEXEC.BAT
	COMMAND.COM

	The AUTOEXEC.BAT on the hard disk should set up the path

and do those things that you are probably doing in the autoexec

you are presently using on your floppy disk.

My AUTOEXEC.BAT has the following:

	path=c:;c:\dos;c:\usr;c:\user1
	pwrupclk	(sets clock from quadram card)
	mode com1:24,,,,p	(sets the async port parameters)
	qspool 2	(sets a printer spooler)
	prompt	$p$g	(I like a different prompt)
	chkdsk		(I check the disk each time I power up)


	To get going you must boot from the floppy disk,  this

disk must contain the driver for the hard disk at a minimum.

Include any other drivers you use.  The CONFIG.SYS must be

included to select the driver and an AUTOEXEC.BAT.  The

AUTOEXEC.BAT of the floppy is different from that on the hard

disk.

	My floppy disk boot has the following:

	ANSI.SYS	(DISPLAY/KEYBOARD DRIVER)
	TECDRIVE.SYS	(HARD DISK DRIVER FOR TECHMAR UNIT)
	SPEEDISK.SYS	(DRIVER FOR RAM-DISK)
	CONFIG.SYS	(REQUIRED BY DOS TO SELECT THE DRIVERS)
	AUTOEXEC.BAT	(NOTE: NOT THE SAME AS ON THE HARD DISK)

	The CONFIG.SYS has the following:

	device=tecdrive.sys -p3 (install the hard disk driver)
	device=speedisk.sys -k128 (install 128k of ram disk)
	device=ansi.sys 	(install keyboard/display driver)
	buffers=5		(set number of dos buffers)
	break=off		(or other config.sys commands you use)
	shell=c:\command.com c:\ /p

	The shell command is the one that is important to allow

you to remove the floppy disk and not get the 'load disk with

command.com' message.

	Notice that the floppy disk does not even contain the

command.com file.

	The AUTOEXEC.BAT file on the floppy is very simple:

	c:		(change to the hard disk)
	autoexec.bat	(execute the AUTOEXEC.BAT file on the hard disk)

	The sequence of actions for the booting is as follows.

	system does a power on reset, testing the hardware and memory.

	DOS2.x is loaded from the floppy in drive A:, this

consists of two files not normally seen by the user, DOS itself

and an interface to the PROM BIOS in the machine.

	The floppy disk is checked for a CONFIG.SYS file, which

is found and then acted on.  This file causes, at a minimum, a

device driver for the hard disk to be installed and a shell to be

installed.  If there is no shell command then the COMMAND.COM

file fill be used as the shell.  In our case the shell comes from

the hard disk (driver previously attached).  The second part of

the shell command informs the COMMAND.COM program that it can

find itself on the C: root directory and that it is to remain in
memory permantly.

	Then the floppy drive is checked for an AUTOEXEC.BAT

file, which is found and acted on.  This AUTOEXEC.BAT simply

passes control to the hard disk (C:) and executes that

AUTOEXEC.BAT file found on the hard disk. The commands in the

hard disk AUTOEXEC.BAT file would be those you normally use.

	The system will now be logged into the hard disk at the

root directory and ready for the user.	The floppy is no longer

necessary.

	I have been using this set of commands for the past few

months without problems and hope this example will help you set

up your system.

		Michael E. Walraven
(revised 84/6/30, set comspec= not required on autoexec.bat in

hard disk)