CHAPTER 9   DIRECTIVES IN A86                             9-1


Segments in A86

The following discussion applies when A86 is assembling a .COM 
program.  See the next chapter for the discussion of segmentation 
for .OBJ files.

A86 views the 86 computer's memory space as having two parts: The 
first part is the program, whose contents are the object bytes 
generated by A86 during its assembly of the source.   A86 calls 
this area the CODE SEGMENT.  The second part is the data area, 
whose contents are generated by the program after it starts 
running.  A86 calls this area the DATA SEGMENT.  

Please note well that the only difference between the CODE and 
DATA segments is whether the contents are generated by the 
program or the assembler.  The names CODE and DATA suggest that 
program code is placed in the CODE segment, and data structures 
go in the DATA segment.  This is mostly true, but there are 
exceptions.  For example, there are many data structures whose 
contents are determined by the assembler: pointer tables, arrays 
of pre-defined constants, etc.  These tables are assembled in the 
CODE segment.  

In general, you will want to begin your program with the 
directive DATA SEGMENT, followed by an ORG statement giving the 
address of the start of your data area.  You then list all your 
program variables and uninitialized data structures, using the 
directives DB, DW, and STRUC.  A86 will allocate space starting 
at the address given in the ORG statement, but it will not 
generate any object bytes in that space.  After your data segment 
declarations, you provide a CODE SEGMENT directive, following by 
an ORG giving the address of the start of your program.  You 
follow this with the program itself, together with any assembler-
generated data structures.  A short program illustrating this 
suggested usage follows: 

DATA SEGMENT
ORG 08000
  ANSWER_BYTE  DB ?
  CALL_COUNT   DW ?

CODE SEGMENT
  JMP MAIN

TRAN_TABLE:
  DB 16,3,56,23,0,9,12,7

MAIN:
  MOV BX,TRAN_TABLE
  XLATB
  MOV ANSWER_BYTE,AL
  INC CALL_COUNT
  RET

                                                          9-2
A86 allows you to intersperse CODE SEGMENTs and DATA SEGMENTs 
throughout your program; but in general it is best to put all 
your DATA SEGMENT declarations at the top of your program, to 
avoid problems with forward-referencing.  


CODE ENDS and DATA ENDS Statements

For compatibility with Intel/IBM assemblers, A86 provides the 
CODE ENDS and DATA ENDS statements.  The CODE ENDS statement is 
ignored; we assume that you have not nested a CODE segment inside 
a DATA segment.  The DATA ENDS statement is equivalent to a CODE 
SEGMENT statement.  



The ORG Directive

Syntax: ORG address

ORG moves the output pointer for the segment currently being 
assembled to the value of the operand, which should be an 
absolute constant, or an expression evaluating to an absolute, 
non-forward-referenced constant.  

ORG is most often used in a DATA segment, to control the location 
of the data area within the segment.  For example, in programs 
that fit entirely into 64K, you provide an ORG directive as the 
first line within your DATA segment at the top of your program.  
The location given by the ORG is some location that you are sure 
will be beyond the end of your program.  If you are sure that 
your program will not go beyond 8K (02000 hex), your program can 
look like this: 

DATA SEGMENT
ORG 02000       ; data goes here, beyond the end of the program

(your data segment variable and buffer declarations go here)

DATA ENDS

(your program goes here)


There is a special side-effect to ORG when it is used in the CODE 
segment.  If you begin your code segment with ORG 0, then A86 
knows that you are not assembling a .COM program; but are instead 
assembling a code segment to be used in some other context 
(examples: programming a ROM, or assembling a procedure for Turbo 
Pascal).  The output file will start at 0, not 0100 as in a .COM 
file; and the default extension for the output file will be .BIN, 
not .COM.  

                                                          9-3
Other than in the above example, you should not in general issue 
an ORG within the CODE segment that would lower the value of the 
output pointer.  This is because you thereby put yourself in 
danger of losing part of your assembled program.  If you re-
assemble over space you have already assembled, you will clobber 
the previously-assembled code.  Also, be aware that the size of 
the output program file is determined by the value of the code 
segment output pointer when the program stops.  If you ORG to a 
lower value at the end of your program, the output program file 
will be truncated to the lower-value address.  

Again, almost no program producing a .COM file will need any ORG 
directive in the code segment.  There is an implied ORG 0100 at 
the start of the program.  You just start coding instructions, and 
the assembler will put them in the right place.  


The EVEN Directive

Syntax: EVEN

The EVEN directive coerces the current output pointer to an even 
value.  It does so by adding 1 to the pointer is the pointer was 
odd; doing nothing if the pointer was already even.  EVEN is most 
often used in data segments, before a sequence of DW directives.  
The 16-bit machines of the 86 family fetch words more quickly 
when they are aligned onto even addresses; so the EVEN directive 
insures that your program will have the faster access to those 
DW's that follow it.  (This speed improvement will not be seen on 
the 8-bit machines, most notably the 8088 of the original IBM-
PC.) 


Data Allocation Using DB, DW, DD, DQ, and DT

The 86 computer family supports the three fundamental data types 
BYTE, WORD, and DOUBLEWORD. A byte is eight bits, a word is 16 
bits (2 bytes), and a doubleword is 32 bits (4 bytes).   In 
addition, the 87 floating-point processor manipulates 8-byte 
quantities, which we call Q-words, and 10-byte quantities, which 
we call T-words. The A86 data allocation statement is used to 
specify the bytes, words, doublewords, Q-words, and T-words which 
your program will use as data. The syntax for the data allocation 
statement is as follows: 

(optional var-name)  DB  (list of values)
(optional var-name)  DW  (list of values)
(optional var-name)  DD  (list of values)
(optional var-name)  DQ  (list of values)
(optional var-name)  DT  (list of values)

                                                          9-4
The variable name, if present, causes that name to be entered 
into the symbol table as a memory variable with type BYTE (for 
DB), WORD (for DW), DWORD (for DD), QWORD (for DQ), or TBYTE (for 
DT). The variable name should NOT have a colon after it, unless 
you wish the name to be a label (instructions referring to it 
will interpret the label as the constant pointer to the memory 
location, not its contents).  

The DB statement is used to reserve bytes of storage; DW is used 
to reserve words.  The list of values to the right of the DB or 
DW serves two purposes.  It specifies how many bytes or words are 
allocated by the statement, as well as what their initial values 
should be.  The list of values may contain a single value or more 
than one, separated by commas.  The list can even be missing; 
meaning that we wish to define a byte or word variable at the 
same location as the next variable.  

If the data initialization is in the DATA segment, the values 
given are ignored, except as place-markers to reserve the 
appropriate number of units of storage.  The use of "?", which 
in .COM mode is a synonym for zero, is recommended in this 
context to emphasize the lack of actual memory initialization.  
When A86 is assembling .OBJ files, the ?-initialization will 
cause a break in the segment (unless ? is embedded in a nested 
DUP containing non-? terms, in which case it is a synonym for 
zero).
                 
A special value which can be used in data initializations is the 
DUP construct, which allows the allocation and/or initialization 
of blocks of data.  The expression  n DUP x  is equivalent to a 
list with x repeated n times.  "x" can be either a single value, 
a list of values, or another DUP construct nested inside the 
first one.  The nested DUP construct needs to be surrounded by 
parentheses.  All other assemblers, and earlier versions of A86, 
require parentheses around all right-operands to DUP, even simple 
ones; but this requirement has been removed for simple operands 
in the current A86.

Here are some examples of data initialization statements, with 
and without DUP constructs: 

CODE SEGMENT
  DW 5                    ; allocate one word, init. to 5
  DB 0,3,0                ; allocate three bytes, init. to 0,3,0
  DB 5 DUP 0              ; equivalent to DB 0,0,0,0,0
  DW 2 DUP (0,4 DUP 7)    ; equivalent to DW 0,7,7,7,7,0,7,7,7,7

DATA SEGMENT
XX      DW ?      ; define a word variable XX
YYLOW   DB        ; no init value: YYLOW is low byte of word var YY
YY      DW ?
X_ARRAY DB  100 DUP ?     ; X_ARRAY is a 100-byte array
D_REAL  DQ ?              ; double-precision floating variable
EX_REAL DT ?              ; extended precision floating variable

                                                          9-5
A character string value may be used to initialize consecutive 
bytes in a DB statement.  Each character will be represented by 
its ASCII code.  The characters are stored in the order that they 
appear in the string, with the first character assigned to the 
lowest-addressed byte.  In the DB statement that follows, five 
bytes are initialized with the ASCII representation of the 
characters in the string 'HELLO': 

DB 'HELLO'

Note that the DB directive is the only place in your program that 
strings of length greater than 2 may occur.  In all other 
contexts (including DW), a string is treated as the constant 
number represent the ASCII value of the string; for example, CMP 
AL,'@' is the instruction comparing the AL-register with the 
ASCII value of the at-sign.  Note further that 2-character string 
constants, like all constants in the 8086, have their bytes 
reversed.  Thus, while DB 'AB' will produce hex 41 followed by 
hex 42, the similar-looking DW 'AB' reverses the bytes: hex 42 
followed by hex 41.  

For compatibility, A86 now accepts double-quotes, as well as 
single-quotes, for strings in DB directives.


The DD directive is used to initialize 32-bit doubleword pointers 
to locations in arbitrary segments of the 86's memory space.  
Values for such pointers are given by two numbers separated by a 
colon.  The segment register value appears to the left of the 
colon; and the offset appears to the right of the colon.  In 
keeping with the reversed-bytes nature of memory storage in the 
86 family, the offset comes first in memory.  For example, the 
statement 

   DD 01234:05678

appearing in a CODE segment will cause the hex bytes 78 56 34 12 
to be generated, which is a long pointer to segment 01234, offset 
05678.  

DD, DQ, and DT can also be used to initialize large integers and 
floating-point numbers.  Examples:

  DD 500000   ; half-million, too big for most 86 instructions
  DD 3.5      ; single-precision floating-point number
  DQ 3.5      ; the same number in a double-precision format
  DT 3.5      ; the same number in an extended-precision format

                                                          9-6
The STRUC Directive

The STRUC directive is used to define a template of data to be 
addressed by one of the 8086's base and/or index registers.  The 
syntax of STRUC is as follows: 

(optional strucname)  STRUC  (optional effective address)

The optional structure name given at the beginning of the line 
can appear in subsequent expressions in the program, with the 
operator TYPE applied to it, to yield the number of bytes in the 
structure template.  

The STRUC directive causes the assembler to enter a mode similar 
to DATA SEGMENT, with the optional addition of indexing: if an 
effective address, which can include base registers [BX] or [BP] 
and/or index registers [SI] or [DI], is given at the end of the 
STRUC line, all variables declared between STRUC and ENDS will be 
indexed by the effective address.  For example: 

LINE STRUC [BP]
       DB 80 DUP (?)
LSIZE  DB ?
LPROT  DB ?
     ENDS

The above STRUC defines the variables LSIZE, equivalent to 
[BP+80], and LPROT, equivalent to [BP+81].  You can now issue 
instructions such as MOV AL,LSIZE; which automatically generates 
the correct indexing for you.  

The mode entered by STRUC is terminated by the ENDS directive, 
which returns the assembler to whatever segment (CODE or DATA) it 
was in before the STRUC.  



Forward References

A86 allows names for a variety of program elements to be forward 
referenced.  This means that you may use a symbol in one 
statement and define it later with another statement.  For 
example: 

  JNZ TARGET
   .
   .
TARGET:
  ADD AX,10

In this example, a conditional jump is made to TARGET, a label 
farther down in the code.  When JNZ TARGET is seen, TARGET is 
undefined, so this is a forward reference.  

                                                          9-7
Earlier versions of A86 were much more restricted in the kinds of 
forward references allowed.  Most of the restrictions have now 
been eased, for convenience as well as compatibility with other 
assemblers.  In particular, you may now make forward references 
to variable names.  You just need to see to it that A86 has 
enough information about the type of the operand to generate the 
correct instruction.  For example, MOV FOO,AL will cause A86 to 
correctly deduce that FOO is a byte variable.  You can even code 
a subsequent MOV FOO,1 and A86 will remember that FOO was assumed 
to be a byte variable.  But if you code MOV FOO,1 first, A86 
won't know whether to issue a byte or a word MOV instruction; and 
will thus issue an error message.  You then specify the type by
MOV FOO B,1.

In general, A86's compatibility with That Other assembler has 
improved dramatically for forward references.  Now, for most 
programs, you need only sprinkle a very few B's and W's into your 
references.  And you'll be rewarded: in many cases the word-form 
is longer than the byte form, so that the other assembler winds 
up inserting a wasted NOP in your program.  You'll wind up with 
tighter code by using A86!


Forward References in Expressions

A86 now allows you to add or subtract a constant number from a 
forward-reference symbol; and to append indexing registers to a 
forward-reference symbol.  This covers a vast majority of 
expressions formerly disallowed.  For the remaining, more 
complicated expressions, there is a trick you can use to work 
your way around almost any case where you might run into a
forward-reference restriction.  The trick is to move the 
expression evaluation down in your program so that it no longer 
contains a forward reference; and forward-reference the 
evaluation answer.  For example, suppose you wish to advance the 
ES segment register to point immediately beyond your program.  
If PROG_SIZE is the number of bytes in your program, then you
add (PROGSIZE+15)/16 to the program's segment register value.  
This value is known at assembly-time; but it isn't known until 
the end of the program.  You do the following:

     MOV AX,CS        ; fetch the program's segment value
     ADD AX,SEG_SIZE  ; use a simple forward reference
     MOV ES,AX        ; ES is now loaded as desired

Then at the end of the program you evaluate the expression:

     PROG_SIZE EQU $
     SEG_SIZE EQU (PROG_SIZE+15)/16


                                                          9-8
The EQU Directive

Syntax: symbol-name EQU expression
        symbol-name EQU built-in-symbol
        symbol-name EQU INT n

The expression field may specify an operand of any type that 
could appear as an operand to an instruction.  

As a simple example, suppose you are writing a program that 
manipulates a table containing 100 names and that you want to 
refer to the maximum number of names throughout the source file.  
You can, of course, use the number 100 to refer to this maximum 
each time, as in MOV CX,100, but this approach suffers from two 
weaknesses.  First of all, 100 can mean a lot of things; in the 
absence of comments, it is not obvious that a particular use of 
100 refers to the maximum number of names.  Secondly, if you 
extend the table to allow 200 names, you will have to locate each 
100 and change it to a 200.  Suppose, instead, that you define a 
symbol to represent the maximum number of names with the 
following statement: 

MAX_NAMES EQU 100

Now when you use the symbol MAX_NAMES instead of the number 100 
(for example, MOV CX,MAX_NAMES), it will be obvious that you are 
referring to the maximum number of names in the table.  Also, if 
you decide to extend the table, you need only change the 100 in 
the EQU directive to a 200 and every reference to MAX_NAMES will 
reflect the change.  

You could also take advantage of A86's strong-typing, by changing 
MAX_NAMES to a variable: 

MAX_NAMES  DB ?

or even an indexed quantity:

MAX_NAMES EQU [BX+1]

Because the A86 language is strongly-typed, the instruction for 
loading MAX_NAMES into the CX-register remains exactly the same 
in all cases: simply MOV CX,MAX_NAMES.  

                                                          9-9

Equates to Built-In Symbols

A86 allows you to define synonyms for any of the assembler 
reserved-symbols, by EQUating an alternate name of your choosing, 
to that symbol.  For example, suppose you were coding a source 
module that is to be incorporated into several different 
programs.  In some programs, a certain variable will exist in the 
code segment.  In others, it will exist in the stack segment.  
You want to address the variable in the common source module, but 
you don't know which segment-override to use.  The solution is to 
declare a synonym, QS, for the segment register.  QS will be 
defined by each program: the code-segment program will have a QS 
EQU CS at the top of it; the stack-segment program will have QS 
EQU SS.  The source module can use QS as an override, just as if 
it were CS or SS.  The code would be, for example, QS MOV 
AL,VARNAME.  

The NIL Prefix

A86 provides a mnemonic, NIL, that generates no code.  NIL can be 
used as a prefix to another instruction (which will have no 
effect on that instruction), or it can appear by itself on a 
line.  NIL is provided to extend the example in the previous 
section, to cover the possibility of no-overrides.  If your 
source module goes into a program that fits into 64K, so that all 
the segment registers have the same value, then code QS EQU NIL 
at the top of that program.  


Interrupt Equates

A86 allows you to equate your own name to an INT-instruction with 
a specific interrupt-number.  For example, if you place  TRAP EQU 
INT 3  at the top of your program, you can use the name TRAP as a 
synonym for INT 3  (the debugger trap on the 8086).  


                                                          9-10
Duplicate Definitions

A86 contains the unique feature of duplicate definitions.   We 
have already discussed local symbols, which can be redefined to 
different values without restriction.  Local symbols are the only 
symbols that can be redefined.  However, any symbol can be 
defined more than once, as long as the symbol is defined to be 
the same value and type in each definition.  

This feature has two uses.  First, it eases modular program 
development.  For example, if two independently-developed source 
files both use the symbol ESC to stand for the ASCII code for 
ESCAPE, they can both contain the declaration ESC EQU 01B, with 
no problems if they are combined into the same program.  

The second use for this feature is assertion-checking.  Your 
deliberate redeclaration of a symbol name is an assertion that 
the value of the symbol has not changed; and you want the 
assembler to issue you an error message if it has changed.  
Example: suppose you have declared a table of options in your 
DATA segment; and you have another table of initial values for 
those options in your CODE segment.  If you come back months 
later and add an option to your tables, you want to be reminded 
to update both tables in the same way.  You should declare your 
tables as follows: 

DATA SEGMENT
  OPTIONS:
    .
    .
  OPT_COUNT EQU $-OPTIONS    ; OPT_COUNT is the size of the table

CODE SEGMENT
  OPT_INITS:
    .
    .
  OPT_COUNT EQU $-OPT_INITS  ; second OPT_COUNT had better be the same!



The = Directive

Syntax: symbol-name = expression
        symbol-name = built-in-symbol
        symbol-name = INT n

The equals-sign directive is provided for compatiblity with That 
Other assembler.  It is identical to the EQU directive, with one 
exception: if the first time a symbol appears in a program is in 
an = directive, that symbol will be taken as a local symbol.  It 
can be redefined to other values, just like the generic local 
symbols (letter followed by digits) that A86 supports.  This 
facility is most often used to define "assembler variables", that 
change value as the assembly progresses.

                                                          9-11
The PROC Directive

Syntax:  name  PROC NEAR
         name  PROC FAR
         name  PROC

PROC is a directive provided for compatibility with Intel/IBM 
assemblers.  I don't like PROC; and I recommend that you do not 
use it, even if you are programming for those assemblers.  

The idea behind PROC is to give the assembler a mechanism whereby 
it can decide for you what kind of RET instruction you should be 
providing.  If you specify NEAR in your PROC directive, then the 
assembler will generate a near (same segment) return when it sees 
RET.  If you specify FAR in your PROC directive, the assembler 
will generate a far RETF return (which will cause both IP and CS 
to be popped from the stack).  If you simply leave well enough 
alone, and never code a PROC in your program, then RET will mean 
near-return throughout your program.  

The reason I don't like PROC is because it is yet another attempt 
by the assembler to do things "behind your back".  This goes 
against the reason why you are programming in assembly language 
in the first place, which is to have complete control over the 
code generated by your source program.  It leads to nothing but 
trouble and confusion.  

Another problem with PROC is its verbosity.  It replaces a simple 
colon, given right after the label it defines.  This creates a 
visual clutter in the program, that makes the program harder to 
read.  

Even if you are programming in that other assembler, and you need 
to code a far-return, I recommend that you create a RETF macro 
(it would have the single line DB 0CBH), and stay away from PROCs 
entirely.  

                                                          9-12

The ENDP Directive

Syntax:   [name] ENDP

The only action A86 takes when it sees an ENDP directive is to 
return the assembler to its (sane) default state, in which RET is 
a near-return.  

NOTE that this means that A86 does not support nested PROCs, in 
which anything but the innermost PROC has the FAR attribute.  I'm 
sorry if I am blunt, but anybody who would subject their program 
to that level of syntactic clutter has rocks in their head.  


The LABEL Directive

Syntax:  name LABEL NEAR
         name LABEL FAR
         name LABEL BYTE
         name LABEL WORD

LABEL is another directive provided for compatibility with 
Intel/IBM assemblers.  A86 provides less verbose ways of 
specifying all the above LABEL forms, except for LABEL FAR.  

LABEL defines "name" to have the type given, and a value equal to 
the current output pointer.  Thus, LABEL NEAR is synonymous with 
a simple colon following the name; and LABEL BYTE and LABEL WORD 
are synonymous with DB and DW, respectively, with no operands.  

LABEL FAR does have a unique functionality, not found in other 
assemblers.  It identifies "name" as a procedure that can be 
called from outside this program's code segment.  Such procedures 
should have RETFs instead of RETs. Furthermore, I have provided 
the following feature, unique to A86: if you CALL the procedure 
from within your program, A86 will generate a PUSH CS instruction 
followed by a NEAR call to the procedure.  Other assemblers will 
generate a FAR call, having the same functional effect; but the 
FAR call consumes more program space, and takes more time to 
execute.  

WARNING: you cannot use the above CALL feature as a forward-
reference; the LABEL FAR definition must precede any CALLs to it.  
This is unavoidable, since the assembler must assume that a CALL 
to an undefined symbol takes 3 program bytes.  All assemblers 
will issue an error in this situation.