~››››››››››››››››                                Documentation for›››                                  850 Express!›››                                 1030 Express!›››                                      and›››                                  MPP Express!›››                                  versions 3.0x›››››››               All Versions Copyright (c) 1986 by Keith Ledbetter›››››››››  This program is a 'shareware' program, and may be freely distributed as›long as this copyright notice remains.  This program may in no means be sold›by itself, or packaged with another product, without the expressed written›consent of the author.›››  All donations will be graciously accepted, and can be sent to:››                         Keith Ledbetter›                         2919 Ennismore Court›                         Richmond, VA  23224››››››››››››                               Table Of Contents›››››››        Subject                                                Page›        -------                                                ----››     Introduction..............................................  1››     The XModem Routines.......................................  3››     The Buffering System......................................  4››     RTime-8 Cartridge Support.................................  5››     The Edit Window...........................................  6››     Filename Entry............................................  7››     Word Wrap.................................................  8››     The BOOTUP.EXP File.......................................  9››     The Dialing Menu.......................................... 10››     That's All, Folks!........................................ 11››››››››››››››››››››››››››››››››››››850/1030/MPP Express!                                                  Page 1›››                          Introduction To Version 3.0›››››   Since the original release of 1030 Express! back in September, 1985,›there have been many good improvements suggested by Express! users.  Earlier›upgrade releases have addressed most of those suggestions; now version 3.0›includes some of the more major (maybe the correct word is big) changes.›››   As you have probably noticed, the version number has been rolled up to 3.0›for this version.  This is due to the fact that the latest version numbers for›the 850 was 1.1, for the 1030 was 2.1, and for the MPP was 1.1.  Of course,›having so many versions of the program out has caused me some considerable›headaches (did I mention 850 version 1.1S or 1030 version 2.1R??).  Hopefully›with the release of the version 3.0 family of software, the programs will be›normalized across modem types.  In other words, a person using a 1030 version›will "see" the same thing a person using an MPP or an 850 will see.  This may›be a little aggressive on my part; due to extra features on Hayes-compatible›modems, the 850 version is always going to have one or two extra features.›But overall, the programs will be virtually identical.›››  Here is a quick overview of the new features in version 3.0 of Express!.  If›you have been using Express! for quite some time and feel very comfortable with›it, then this is probably all you will need to read of this documentation.›››  *  16-bit Cyclic Redundancy Count (CRC) Xmodem routines.››  *  Much looser Xmodem timing, allowing use of services like PC Pursuit.››  *  The ability to download .BIN files on Compuserve using XModem protocol.››  *  Intelligent buffering system.  The smaller the DOS you use, the larger›     your "capture buffer" will be.››  *  An Edit Window in terminal mode.  Great for keying in messages, or when›     in "conference mode" on large time-sharing systems.››  *  RTime-8 Cartridge support.››  *  Vidtex mode for Compuserve cursor positioning.››  *  Longer filename entry for sub-directory support.››  *  Ability to enter a directory mask on catalog commands.››  *  Word Wrap while in terminal mode.  Any word crossing the rightmost›     boundary of your screen will be erased and wrapped to the next line.››  *  A File called BOOTUP.EXP, if present, will be read at bootup time.  The›     contents of this file will be sent directly to the modem.  Great for doing›     AT commands to set your modem's dialing speed, etc. (850 version only).››  *  Pressing 1-9 from the "Dialing Menu" will now load in the phone list›     named PHONEx.LST (PHONE1.LST thru PHONE9.LST).›››››››850/1030/MPP Express!                                                  Page 2›››                          Introduction To Version 3.0›››››  As you can see, there weren't tons of changes made to this version.  But the›changes are major, and address the couple of major deficiencies that earlier›versions of the program had.›››  Probably two are the most important.  First is the CRC XModem routines, which›gives you even more error-free uploads and downloads than before.  CRC xmodem›is said to be 99.997% error free (on "line bursts" up to 18 characters long),›and that's just about as good as you are going to get!  The second is the›edit window.  There have been MANY requests for this feature, so there should›be a lot of happy people now!›››  One I am also excited about is the ability to download all of the .BIN files›on Compuserve.  Never again will you have to log off and boot up TScope to›download a file!  I would like to thank Dan Moore, co-author of BackTalk, for›the guidance in adding this feature to Express!.›Thanks Dan! (The check's in the mail!).››››››››››››››››››››››››››››››››››››››››››850/1030/MPP Express!                                                  Page 3›››                              The XModem Routines›››››  Even though Express! has much more complex XModem routines now, you will only›notice one change.  When Receiving a file, the program will prompt you with:››                          [S]tandard Cksum or [C]RC? _›››  If you are communicating with an Atari BBS System, then choose "S" since no›8-bit Atari BBS's that I am aware of support CRC at this time.  The next›versions of BBS Express! will support CRC Xmodem.›››  If you are transferring from either another Express! user or a large system›like CompuServe, then choose CRC.  If you are not sure if the system you are›talking to supports CRC or not, then go ahead and choose CRC once and see what›happens.  The worst that will happen is that the XModem will abort with›"Checksum Errors" on the first block.  If the system you are calling does not›support CRC, but DOES handle the "ignoring" of the CRC like it should, then›Express! will detect this and switch from CRC to Standard checksum mode.›››  When you are Sending a file, you will not be prompted for the type of›transfer to do.  Express! will determine whether to use or not use CRC›depending upon the actions of the receiver.›››  The XModem routines will now download all of the .BIN files on CompuServe›with the same dependability as it does .XMO files.  Simply tell CompuServe›that you want to download the file using XModem-7, and then proceed just as›you would if you were downloading an .XMO file.  You do not need to tell›Express! anything special to let it know that you are downloading a .BIN file.›It will figure this out on its own, and will process the file accordingly.›››  Express! is now much more forgiving of timing errors when processing XModem›transfers.  The older versions of Express! were written "by the book", which is›fine if you are talking PC to PC.  But, when you start throwing multi-user›mainframe systems in, XModem delays can be fairly long.  I am sure many of you›have tried to download using Express! and PC Pursuit, only to be bombarded with›"Bad CMA Byte" messages.›››  On the average, Express! will now allow roughly 10 times longer delays than›earlier versions would.  It has been tested thoroughly with dial-up services›such as PC Pursuit, and transfers now work like a charm!››››››››››››››››850/1030/MPP Express!                                                  Page 4›››                              The Buffering System›››››  Where the old Express! versions had a "set" buffer size for everyone, this›new version is intelligent enough to determine the available memory in your›machine.  The process is a very simple one, and is directly dependent upon the›size of the DOS that you are using.›››  At bootup, Express! will round the value of LOMEM up to the next 128-byte›boundary and then subtract this figure from its ORGed location.  This becomes›the size of your buffer, and it can change dramatically by simply using a›different DOS.›››  Your best bet is still to use SpartaDOS 2.3x because of its extremely small›size.  If you are currently using 850 Express! 1.1S (a special 850 version›used only with SpartaDOS 2.3x), your buffer will be a little smaller with›version 3.0 (due to the added program features).  But, the difference is not›really that much, and for what you gain it is buffer space well spent.›››››››››››››››››››››››››››››››››››››››››››850/1030/MPP Express!                                                  Page 5›››                           RTime-8 Cartridge Support›››››  Version 3.0 of Express! will support the RTime 8 cartridge.  Express! itself›does nothing with the RTime cartridge; rather, it simply allows you to use the›time/date display line in SpartaDOS with Express!.›››  All you have to do is to run the corresponding Time/Date command before›booting Express!.  If you are using 3.2d, then use the TDLINE command.  If you›are using 2.3, use the TIME command.›››  You DO NOT have to have an RTime 8 cartridge to use the time/date display.›If you use the TIME and DATE commands to set SpartaDOS's internal (software)›clock, this will work, too!  For example, let's set up a batch file to boot›Express! (this one assumes that you are using SpartaDOS 3.2x):›››                                TDLINE›                                DATE›                                TIME›                                EXPRESS›››  Now, when you execute this batch file, the Time/Date line will be installed›and then you will be prompted for the system date and time.›››  Since SpartaDOS "hooks" its Time/Date line into the current display list to›add another line to the display, I have removed one line from the display of›Express!.  What used to be 1 status line and 24 terminal mode lines is now›1 status line and 23 terminal mode lines.  This was probably good anyway,›since I have had some complaints from people (using televisions) that the 25›line display caused overscan at the bottom of their display.›››  The only disadvantage to using the Time/Date line with Express! is that there›will be times when the display will "jerk".  This is due to the nature of the›way SpartaDOS sets his "hooks".  Each vertical blank, SpartaDOS checks to see›if the display list has changed locations, and if it has, it will re-install›the time/date line.  With Express!, this will only occur in two places:›(1) when you toggle the edit window on/off, and (2) when you go to/from the›main menu with the edit window on.  All in all, the 1/2 second screen jerk is›a small annoyance that you will rarely run into.››››››››››››››››››850/1030/MPP Express!                                                  Page 6›››                                The Edit Window›››››  While in terminal mode, pressing the SELECT key will toggle the edit window›on and off.  Anything that is typed in the edit window will not be sent to the›host system until the RETURN or the ESCAPE key is pressed.›››  Pressing RETURN will send the line with a carriage return on the end of the›data.  Pressing ESCAPE will send the line without a carriage return at the›end.  This is useful for BBS's (such as BBS Express!) that use 1-key commands›with no RETURN.  If you are in VIDTEX mode, pressing ESCAPE will send the line›with an actual ESCAPE character appended to the end.  This is really only›useful if you are using the filge editor on Compu-Serve.›››  The edit-window processor is a fairly intelligent one;  while keying in text›you have access to the following special keys:›››  Cursor Left   -    Moves the cursor one character to the left.›  Cursor Right  -    Moves the cursor one character to the right.›  Cursor Up     -    Moves the cursor to position 1 in the edit window.›  Cursor Down   -    Moves the cursor to the END of the line in the window.›  Shift/Delete  -    Deletes text from the current cursor position to the›                     end of the line.›  Shift/Clear   -    Clears the entire edit window and places the cursor›                     in position one of the window.›  Ctrl/Insert   -    Inserts a space in the window at the current cursor›                     position, and moves text to the right of the cursor›                     one position to the right.›  Ctrl/Delete   -    Deletes the character UNDER the cursor and moves the›                     entire line from the current position one character›                     to the left.›  Delete        -    Moves the cursor one position to the left, and replaces›                     the character there with a space.›  Tab Key       -    Moves the cursor five characters to the right (with a›                     maximum of the length of the window text).››››  Any CONTROL keys that you press will be "passed through" the edit window to›the host system.  In other words, you can be keying into the edit window and›still send Ctrl-S's, Ctrl-Q's, etc. to the host system.›››››››››››››››››››850/1030/MPP Express!                                                  Page 7›››                                 Filename Entry›››››   You now have a much larger area for entering in filenames on all of the›file-specific commands.  This was done to allow you to enter subdirectory›paths such as "D2:UPLOADS>GAME1.OBJ".›››   Also, when you do a directory command now (by hitting 1-8), you will be›prompted ("Mask> ") for a directory mask to search by.  If you just press›RETURN, the mask will default to "*.*" (which would be identical to the old›Express! versions).  But, especially for hard-disk users, this allows you to›do directory listings of subdirectories other than the current one.›››  For example, you could respond with:  Mask> D3:DOWNLOAD>*.OBJ›to see a listing of all of the files in the subdirectory DOWNLOAD that have an›extender of .OBJ.›››  If you are using SpartaDOS, the "1-8" directory listing will be the SpartaDOS›LONG directory listing.  If, for some reason, you want to see the short,›DOS 2.0-type listing (perfect if you need to know the sector size of a file),›then do a SHIFT/1-8 command.  The Shift/1-8 command functions identically to›the 1-8 except that it will show the short form.  If you are not using›SpartaDOS, then both the 1-8 and the Shift/1-8 commands will yield the exact›same results.›››  Because of the Shift/1-8 keys now being used for a short directory, some of›the commands that were previously executed with these keypresses have been›moved to other keys (such as the save config, load config, etc).›››››››››››››››››››››››››››››››850/1030/MPP Express!                                                  Page 8›››                                   Word Wrap›››››››  While in terminal mode, pressing Shift/Control/W will toggle word wrap on›and off.  A short message will be displayed showing you the current status of›word wrap.   At bootup time word wrap defaults to OFF, but once you turn it›on, it will remain on until (1) you turn it off or (2) you exit the program.›If word wrap is on, any word that extends to the right margin of your terminal›screen will be erased and rewritten on the next display line.  So, there will›never be "wraparound" (or broken) words on your screen.›››››››››››››››››››››››››››››››››››››››››››››››››››850/1030/MPP Express!                                                  Page 9›››                     The BOOTUP.EXP file (850 version only)›››››  When Express! boots up it will now look for a file called D1:BOOTUP.EXP.›This file, if present, is just a pure text file that contains modem commands›that you want executed (sent to the modem).  For example, here is a BOOTUP.EXP›file you Hayes or Hayes-compatible owners can use to speed up your dialing:››                                ATZ›                                AT S11=50›››  There is no limit on the number of lines you can have in the BOOTUP.EXP file.›But, all of the lines in the BOOTUP.EXP file MUST be less than 30 characters›in length.››››››››››››››››››››››››››››››››››››››››››››››››850/1030/MPP Express!                                                  Page 10›››                                The Dialing Menu›››››  There are only a few new features in the dialing menu section of the program,›and most are very minor changes.  First, the program now does pure block I/O›when loading/saving a phone list which makes both much quicker.  Also, the›MARKED status of the boards is now saved along with the phone list.  This is›convenient if you always mark the same boards each time you boot Express!.›Just mark the numbers that you want, then SAVE the phone list.   Unfortunately,›because of this change, your old phone list files are not compatible with›version 3.0.  Joe Lesko, one of the BETA testers of the program, solved this›problem by writing a program to convert old Express! phone lists to the new›format.  Look for it under the name EXPCONV when you download the new version›of Express!.›››  The third change is that pressing "1-9" from the dialing menu will load in›the file PHONE#.LST.  What this means is that you virtually now have 9 "pages"›of 18 files each.  Of course, this can get a little confusing if you add a new›entry and want to save the phone list (was this PHONE4.LST or PHONE5.LST??).›A little trick I use is this:  on each of your phone lists, use the first›entry in the list to denote the page number, as in "  Page 1 ".  This will›cost you one phone number per list, but your sanity is worth it!  Also,›whereas the old Express! programs loaded in PHONE.LST at bootup, version 3.0›now loads in PHONE1.LST at bootup.›››  The last change in the dialing menu is that there is now a VIDTEX mode to›supplement the ATASCII and ASCII modes.  VIDTEX mode is used on Compu-Serve›and allows various cursor positioning commands.  Express! DOES NOT allow you›to view on-line graphics on Compu-Serve;  but, with VIDTEX mode and the ability›to now download .BIN files, that is about all that is missing.›››››››››››››››››››››››››››››››850/1030/MPP Express!                                                  Page 11›››                               That's All, Folks!››››››  That concludes the changes to this version of Express!.  The scheduled›release dates for each version of Express! 3.0 are:›››                                850  -  9/24/86›››                                1030 -  11/1/86›››                                MPP  -  12/1/86››››    Thanks for your support, and enjoy the program!›››                                     Keith Ledbetter››/////////////////////////////////////////////////////////////////////////////////