----------------------------------
			  unPACKIT: for the IBM PC
		     ----------------------------------
			    PACKIT file unpacker
		     ----------------------------------







unPACKIT is distributed freely and may be copied by anyone for any number
of machines.  The author considers unPACKIT to be "shareware" or "freeware".
unPACKIT is a part of the shareware package PC-VCO.  If you have subscribed
to PC-VCO, unPACKIT is released for your use.  If you wish to use unPACKIT
without subscription to PC-VCO, please support its development and main-
tenance with a subscription of 10.00 dollars.  The author may be reached at:


		     R. (Scott) McGinnis
		     P.O. Box 3607 Mdse Mart
		     Chicago, IL 60654-0607

		     PLINK id: TARTAN




							    Version 1.0: 861021
							    R.McGinnis; Chicago


unPACKIT: PACKIT file extractor
Version 1.0: 861021


			     Table of Contents
			     -----------------



I.	Introduction  ................................................. page  1

II.	Running the program  .......................................... page  3

III.	unPACKIT Command Summary ...................................... page  4

IV.	unPACKIT Switches ............................................. page  5

V.	VCOLIB usage .................................................. page  6

VI.	Batch extraction .............................................. page  7

VII.	Program Requirements .......................................... page  7

VIII.	Program and Author Information	............................... page  8




				Appendices
				----------


A.	MacBinary Header .............................................. page  9

B.	PACKIT File structure ......................................... page 10

C.	PACKIT Subfile structure ...................................... page 11

D.	unPACKIT Error messages ....................................... page 12





unPACKIT: PACKIT file extractor 					 Page  1
Version 1.0: 861021


I.	Introduction


	unPACKIT for the IBM PC is a utility that extracts files packed together
	on a MacIntosh computer with the PACKIT utility.  PACKIT on the Mac-
	Intosh will pack multiple files together (optionally compressing
	and encoding them) into one file.  unPACKIT on the IBM PC allows
	the extraction of individual files from the PACKIT envelope.  Many
	files maintained as '.PIT' (the usual PACKIT extension) on Mac BBS's,
	Clubs, and SIG's are now accessible to users of the IBM PC.


	PACKIT was developed and has been extended by Harry Chesley.  PACKIT I
	(the original version) simply stored files together, with error checks
	designed into the construction.  PACKIT II added compression to the
	PIT file.  PACKIT III added data encryption - simple encryption and
	DES encryption - as options.  PACKIT versions I/II/III is available as
	shareware from Harry Chesley.


	unPACKIT is compatible with PACKIT I and II.  Data encryption is not
	supported.  unPACKIT was developed to support the shareware package
	PC-VCO for the IBM PC.	 Face files created on MacIntosh computers
	are frequently packed together on the various boards: PLINK, CIS,
	Delphi, and GEnie.  Now packed face files are available to PC-VCO
	users.	A packed file may be downloaded to an IBM PC and unPACKIT
	used to extract individual face files.



	unPACKIT may be copied freely and distributed to anyone for any number
	of machines.  The author considers this to be "shareware" or "freeware"
	unPACKIT is a part of the shareware package PC-VCO.  If you have sub-
	scribed to PC-VCO, unPACKIT is released for your use.  If you wish to
	use unPACKIT without subscription to PC-VCO, a contribution is asked.
	unPACKIT (and PC-VCO/unPACKIT) will be extended and enhanced if response
	warrants.



unPACKIT: PACKIT file extractor 					 Page  2
Version 1.0: 861021


I.	Introduction (continued)


	What is PC-VCO, by-the-way?

	PC-VCO is a communications program for the IBM PC with two sides.
	On the one hand, it provides standard comm program functions: a
	dialing directory, macros, disc logging, XMODEM and ASCII file
	transfer, and so on.  However, used with network conferencing
	services such as People/Link's PARTY, CompuServe's CB and Delphi's
	conference area, PC-VCO provides a way to 'see' and 'hear' people
	talking.


	The idea for PC-VCO was derived from the VCO system, and its
	predecessor VMCO, developed for the MacIntosh computer.  The VCO
	programs (PC and MacIntosh) allow you to see the people you
	communicate with on-line, using the graphic capabilities of the
	personal computer and to hear conversation with speech synthesis.



	VCO was originally developed by Harry Chesley. It was followed by
	VMCO (which is CIS specific), written by Bob Perez independant to
	the development of VCO.  The current (MacIntosh) version of VCO is
	almost an exact duplicate of Harry Chesley's original - the original
	source code was converted by Mike Cohen and made to accept multiple
	service formats.  [Note: Mike Cohen's VCO uses VMCO formated files.
	Harry Chesley's VCO files differ.  VCOLIB can accomodate either.
	PC-VCO in VCO mode can talk to either, according to your choice.]


	The MacIntosh VCO allows the user to see the people talking on-line
	through graphic Icons.	The Icons are provided to the VCO program
	as 'Resource files' and are built using a 'Resource Editor'.  Each
	VCO user must have a resource file for every potential other speaker.
	Charlie Brown and Snoopy Icons are used if no 'Faces' are available.
	A range of expressions, from 'normal' to bored to surprised make
	VCO conferences lively.  Each participant controls the expression
	displayed to all other participants.


	On most large systems, the face files for 20 or more people have
	been packed (and compressed) together with the shareware product
	PACKIT.  The files will be found in the library areas with the
	extension of '.PIT'.  And thus unPACKIT for the IBM PC !


unPACKIT: PACKIT file extractor 					 Page 3
Version 1.0: 861021


II.	Running the program


	unPACKIT is invoked at the DOS prompt with the command:

	------------------------------------------------------
	"d>" unPACKIT <option>

	Where "d>" is the DOS prompt, and

	      <option> is: (<switch> or <cmd> <PIT-File> (<parm> (,<parm> ...)))

	      where <switch>   is one of the following: /+, /-, /B, /D, /R
		    <parm>     is a subfile name,
		    <PIT-file> is the PACKIT file name to be used,
	      and <cmd>        is one of the following: E,X,L,V

	Note: Specifying no commands at all will provide an abbreviated
	      HELP display summarizing available commands.
	------------------------------------------------------

	unPACKIT commands and switches are summarized on the next pages.



unPACKIT: PACKIT file extractor 					 Page 4
Version 1.0: 861021


III.	unPACKIT Command Summary.


	Command    Parameter Description
	---------  --------- --------------------------------------------------
	(E)xtract  subfile   Extract the specified subfile.  Subfile names are
		   name      listed with the 'L' or 'V' commands.  Subfile names
			     are up to 63 bytes in length, and may not contain a
			     comma or a semi-colon.  Case is not significant.

	(X)tract   subfile   Extract the specified subfile.  This is simply a
		   name      synonym for the 'E' command discussed above for
			     those of us who spell phonetically.

	(L)ist		     List the subfiles of the specified PIT file.  If a
			     parameter is given it will be ignored.  The list
			     command gives the following information:

			     Subfile name (1-63 characters in length)
			     File Type (4 characters)
			     File creator (4 characters)
			     Compression.  Compression types are:

				PMag - simple compression (PACKIT I)
				PMa4 - huffman compressed (PACKIT II)
				PMa5 - compressed and encrypted (PACKIT III)
				PMa6 - compressed and DES encrypted (PACKIT III)

				Note: unPACKIT can only deal usefully with
				      compression types "PMag" and "PMa4".

	(V)erbose	     List the subfiles of the specified PIT file.  If a
			     parameter is given it will be ignored.  The verbose
			     list give the information above and the following:

				Data Fork size:     Byte count in the
						    subfile's Data fork.
				Resource Fork size: Byte count in the subfile's
						    Resource fork.
				Creation date:	    Date the file was created.
				Modification date:  Date the file was last
						    modified.


unPACKIT: PACKIT file extractor 					 Page 5
Version 1.0: 861021


IV.	unPACKIT Switches.


	unPACKIT uses switches to control its output format.  In order to
	explain these switches, some preliminary explanation is required.
	Bear with me if you already understand the following points:

	.  Files uploaded by a MacIntosh and downloaded by an IBM PC will have
	   a header called 'MacBinary'.  The MacBinary header gives specifics
	   about the file's name, type/creator, etc.  The PIT file used by
	   unPACKIT must have a MacBinary header, with a type of "PIT " and a
	   creator of "PIT ".  VCOLIB (the face file librarian for PC-VCO)
	   expects face files offered it for ingestion to have a MacBinary
	   header.

	.  MacIntosh files are implemented as 'forks'... each file has a
	   'Data' and a 'Resource' fork.  The Data fork is what we who use
	   IBM PC's understand to be a file - it is object code, data, a data
	   base, what-have-you.  The Resource fork contains O/S information
	   such as the ICON to be displayed to represent the file.  Again
	   using VCOLIB as an example:	VCOLIB uses only the resource fork of
	   a face file.

	   And I don't know why the whole construction isn't referred to as
	   a fork, and the elements 'tines'.


	With this understood, unPACKIT offers the following switches (which
	must be entered prior to the command(s) effected):

	Switch	Description
	------- ------------------------------------------------------------
	/+	Default condition.  A MacBinary header is created for each
		file extracted (with the appropriate name, type and creator).

	/-	No MacBinary header will be output with extracted files.  This
		would be appropriate if, for example, an encrypted file were
		being uncompressed and encryption performed separately.

	/B	Default condition.  Both the Data and Resource forks are to be
		extracted (if present).  Each will be output as a separate file
		on the IBM PC (the name for each file will be queried).

	/D	Only the Data fork is to be extracted.	The Resource fork will
		be skipped if present.

	/R	Only the Resource fork is to be extracted.  The Data fork will
		be skipped if present.



unPACKIT: PACKIT file extractor 					 Page 6
Version 1.0: 861021


V.	VCOLIB usage.


	Face files packed together into one PIT file will have certain
	characteristics.  First of all, the Data fork for each subfile
	will be empty (size is 0 bytes).  Only the Resource fork is
	used.  VCOLIB will only accept resource files with one of the
	following type/creator values:

		Type Creator Usage
		---- ------- --------------------------------------------
		FACE VCO!    File created for use with Mike Cohen's VCO
			     (this version is mostly used on PLINK)
		FACE VMCO    File created for use with Bob Perez's VMCO
			     (this version is mostly used on CIS)
		HRC1 HRC1    File created for use with Harry Chesley's VCO
			     (this version is mostly used on GEnie and Delphi)


	For example:  you can easily find the file FACES1.PIT in the CIS
	MacIntosh Users Group (MAUG) library (DL).  Download the file using
	an error free binary protocol.	It will be seen to conform to the
	above description (0 size data forks, and type/creator of "FACEVMCO".


	List the file's contents with the command:

	   "d>" unPACKIT L FACES1.PIT    (assuming that is the name you gave it)


	Extract an individual face with the command:

	   "d>" unPACKIT X FACES1.PIT <somebody's name from the listing>

	You will be queried for the file name for the extracted subfile.
	Choose any name (the face file itself contains the original name,
	so the name you use for the file is relatively unimportant) that
	does not conflict with a file already on your diskette/subdirectory.


	Add the extracted file to PC-VCO's face library with the command:

	   "d>" VCOLIB A <your library file> <the extracted file's name>

	Normally, the library file would be PC-VCO.FLB.  You may view the
	entry with the command:

	   "d>" VCOLIB V <your library file> <the name as it was originally>




unPACKIT: PACKIT file extractor 					 Page 7
Version 1.0: 861021


VI.	Program Requirements


	Version 1.0 of unPACKIT allows redirection of the output (e.g. of the
	'L' command to the printer.  However, redirection of input is not
	supported.  Although it may appear obvious to build a contents list
	of a PIT file with the command:

	d> unPACKIT >TEMP.TXT L JAPANART.PIT	       ; This works just nicely

	and then edit the result - providing blank (empty) lines for files to
	be skipped - it won't work.  When the edited file is presented to be
	processed, e.g. with the command:

	d> unPACKIT <TEMP.TXT X JAPANART.PIT	       ; It doesn't work!

	the program terminates abnormally.  If this program is extended, this
	feature will be one of the first addressed.


	unPACKIT will accept the 'X' command with no operand and unpack the
	entire contents of the PIT file.  The command above (without the
	redirection of input, of course) is an example.  Simply enter:

	d> unPACKIT X <PIT file name>

	and every file within the PIT file will be unpacked.  You can skip a
	subfile with a null entry - a carriage return) at the file name prompt.
	And its faster than a selective extraction.  Another matter to be
	addressed if response warrants.


VII.	Program Requirements


	This program can only function on an IBM PC or DOS compatible machine.
	It uses 'Handle' oriented I/O routines added with DOS 2.0.  Therefore
	DOS 2.0 is also a requirement.


	The current version's memory requirements are modest.  unPACKIT will
	run in 64K.



unPACKIT: PACKIT file extractor 					 Page 8
Version 1.0: 861021


VIII.	Program and Author Information


	This program was written using Microsoft Macro-Assembler.  The author
	likes assembler.  Assembly language is an entirely appropriate vehicle
	for the program.


	unPACKIT, VCOLIB and PC-VCO were written by R. Scott McGinnis of Chicago
	Illinois.  [PLINK ID is TARTAN].  Comment and suggestions are welcomed.

		     R. (Scott) McGinnis
		     P.O. Box 3607 Mdse Mart
		     Chicago, IL 60654-0607


	Credit for information on the MacIntosh must be given to Kelly Major
	and Mike Cohen.  Both Kelly and Mike helped me make unPACKIT and PC-VCO
	possible.  I must also thank my wife, Elizabeth, who has helped me at
	every step, and smiled upon my vagaries.


	unPACKIT (Version 1.1) may be distributed freely, with the caveat that
	the Author information displayed at program termination is not removed.
	The author considers this to be "shareware" or "freeware".  unPACKIT is
	a part of the shareware package PC-VCO.  If you have subscribed to
	PC-VCO, unPACKIT is released for your use.  If you wish to use unPACKIT
	without subscription to PC-VCO, a contribution of $10.00 is requested.
	unPACKIT (and PC-VCO/unPACKIT) will be extended and enhanced if response
	(measured by contribution) warrants.


	Most of the hardware names and software names (and products not hardware
	or software) mentioned in this document are trademarks or trade names of
	specific manufacturers.



unPACKIT: PACKIT file extractor 					 Page 9
Version 1.0: 861021						     Appendices


A.	MacBinary header.

	The MacBinary header is 128 bytes in length, and structured:


	0      1      2      3	    4	   5	  6	 7	       65
	+------+------+------+------+------+------+------+-----/ /-----+->
	! Ver  ! FLN  ! File Name			       ...     !
	+------+------+------+------+------+------+------+-----/ /-----+->

	       65     66     67     68	   69	  70	 71	72     73
	    >--+------+------+------+------+------+------+------+------+->
	       ! Type			   ! Creator		       !
	    >--+------+------+------+------+------+------+------+------+->

	       73     74    ...     126    127
	    >--+------+-----/ /-----+------+
	       ! Unused by us		   !
	    >--+------+-----/ /-----+------+

	Where: Ver -------> MacBinary Version Number
	       FLN -------> Len of following File name (value 0-63)
	       File Name -> File Name; Used here as Creator ID.
	       Type ------> Type of file field.  We expect "PIT ".
	       Creator ---> Creator of file field.  We expect "PIT ".




unPACKIT: PACKIT file extractor 					 Page 10
Version 1.0: 861021						      Appendices


B.	PACKIT file structure.


	The PACKIT file is a concatenated series of subfiles, with
	a MacBinary Header.  After the MacBinary header, a PACKIT
	file looks like:

	+------+------+------+------+--//
	! Type (4 bytes)	    !			Subfile 1
	+------+------+------+------+--//

	       +------+------+------+------+------+------+--//
	       ! 1st subfile contents (variable length)  !
	       +------+------+------+------+------+------+--//

	+------+------+------+------+--//
	! Type (4 bytes)	    !			Subfile 2
	+------+------+------+------+--//

	       +------+------+------+------+------+------+--//
	       ! 2nd subfile contents (variable length)  !
	       +------+------+------+------+------+------+--//

	... And so on.	Lastly, there is:

	+------+------+------+------+--//
	! EOF Type (4 bytes)	    !
	+------+------+------+------+--//

	Type	Contents
	----	---------------------------------------------------
       "PMag"   Simple packed file
       "PMa4"   Compressed subfile (huffman encoded)
       "PMa5"   Compressed subfile (huffman) and simple encryption
       "PMa5"   Compressed subfile (huffman) and DES encrypted
       "PEnd"   EOF indicator




unPACKIT: PACKIT file extractor 					 Page 11
Version 1.0: 861021						      Appendices


C.	PACKIT Subfile structure.


	Each subfile is structured:

	+------+------+------+------+
	!      Header		    !
	+------+------+------+------+
	!			    !
       / /     Data fork	   / /
	!			    !
	+------+------+------+------+
	!			    !
       / /     Resource fork	   / /
	!			    !
	+------+------+------+------+
	!      Data/Resource CRC    !
	+------+------+------+------+

	------------------------------------------------------------

	The header has the following structure:

	Field	Length	Contents
	------- ------- --------------------------------------------
	NameLen 1	Length of NAME field in bytes (1-63)
	Name	63	Name of subfile
	Type	4	File type (as type above in MacBinary header)
	Creator 4	File creator (as creator above)
	Flags	1	Finder flags
		1	one byte of filler to preserve word alignment
	Locked	2	File locked if non-zero
	DSize	4	32 bit count of bytes in data fork
	RSize	4	32 bit count of bytes in resource fork
	CrDate	4	file creation date  !  Count in seconds since
	ModDate 4	file last modified  !	     Jan 1, 1904
	CRC	2	CRC for above header

	------------------------------------------------------------
	Note: If the subfile type indicates compression, the header
	as described above is compressed along with the data and the
	resource forks.  The DSize and RSize fields refer to the un-
	compressed file size... therefore the entire subfile must be
	uncompressed in order to get to the next subfile!
	------------------------------------------------------------


unPACKIT: PACKIT file extractor 					 Page 12
Version 1.0: 861021						      Appendices


D.	unPACKIT Error messages.


	------------------------------------------------------------
	... Parameter error

	The command line, as entered after the invocation of unPACKIT could
	not be interpreted.  Re-type the command line.
	------------------------------------------------------------
	... File name syntax error

	unPACKIT follows the SEA/ARC convention of placing the file name of the
	file to be manipulated after the first command and before the parameters
	of that first command.	unPACKIT could not interpret the expected name.
	------------------------------------------------------------
	... File is not PACKIT format

	The file specified is not identified as a PACKIT file in its MacBinary
	header (the first 128 bytes).  Type must be "PIT " and creator "PIT ".
	------------------------------------------------------------
	Short read reading subfile header

	The PACKIT file has been truncated - only part of its contents are
	available for extraction.
	------------------------------------------------------------
	Warning: Subfile header CRC does not match computed CRC.

	The PACKIT file has been corrupted.  Or the author has a bug.  If
	the file is downloaded a second time, and the error persists, its
	probably a bug.  Please contact the author.
	------------------------------------------------------------
	Subfile type unrecognized.

	The PACKIT file has been corrupted, or a PACKIT IV has been released.
	------------------------------------------------------------
	Position past EOF requested.

	The PACKIT file has been truncated - only part of its contents are
	available for extraction.
	------------------------------------------------------------
	Huffman tree is corrupt. I can not use it.

	Decoding information could not be loaded from a compressed file.  The
	file could be corrupt, or the author (again) may have a bug.
	------------------------------------------------------------
	Warning: Subfile contentual CRC does not match computed CRC.

	The PACKIT file has been corrupted.  Or the author has a bug.  If
	the file is downloaded a second time, and the error persists, its
	probably a bug.  Please contact the author.