INSTRUCTIONS FOR INSTALLING AND RUNNING PROGRAM.

1. REMOVE U-30 AND INSTALL SOCKET

2. REMOVE U-7 BY REMOVING EPOXY,CUTTING PINS AND SOLDERING
SOCKET TO PINS IN PC BOARD OR BY REMOVING  U-7 COMPLETLY
FROM THE BOARD  AND INSTALLING A SOCKET.

3. RUN JUMPER WIRE FROM U-19 PIN 9 TO PIN 35 OF NEW U-7

4. INSTALL LOADER CHIP IN U-30 SOCKET, TURN ON POWER. VC-2
LIGHT SHOULD COME ON AND DISPLAY A SCREEN. NOW PRESS "ENTER"
AS THE SCREEN SAYS. A NEW SCREEN SHOULD NOW BE DISPLAYED
TELLING YOU THAT RAM HAS BEEN LOADED.

5. WIDGET_WIZ.RUN
INSTALL RUN CHIP IN U-30 SOCKET AND TURN POWER ON. WHEN
UNIT TURNS  ON PRESS SETUP AND 7 AND SELECT THE
APPROPRIATE BANK FOR THE CODES THAT YOU WILL RUNNING ON.
THIS CHIP WILL TAKE HITS AND CALCULATE THE WORKING KEY FOR
THE DATA STREAM IT IS RUNNING ON. IF YOU LOOK AT SETUP-1 YOU
WILL SEE THE MONTHS CODES. WHEN THE BOX TAKES A HIT IT WILL BE
DISPLAYED HERE AND SHOW WHICH MONTH CODE IS LOADED.
NOW PRESS SETUP 5 TO BUILD BANK 1 AND SETUP 6 TO BUILD BANK 2.
LOOK AT SETUP 7, BANKS 1 AND 2 SHOULD HAVE THE WORKING KEYS
STORED IN THEM. NOW ALL YOU HAVE TO DO EACH MONTH IS PRESS
SETUP 5 OR SETUP 6 TO CALCULATE THE WORKING KEY AND THEN PRESS
SETUP 7 AND SELECT BANK 1 OR 2 WHICHEVER HAS THE RIGHT KEY
FOR THE MONTH.
TO ENTER NEW CODES PRESS SETUP AND 8, SELECT THE BANK
THAT YOU WISH TO ENTER THEM INTO AND PRESS THAT NUMBER
[3-8].THEN TYPE THE WORKING KEY IN AS PROMPTED BY
THE SCREEN.
THE WORKING KEYS CAN BE ENTERED USING THE STANDARD WIZZARD CONVERSION
FORMAT, 01=1  91=A...ECT.

6. WIDGET_CLN.RUN
INSTALL RUN CHIP IN U30 AND POWER UP. THIS IS A PRETTY STRAIGHT
FORWARD CLONE CHIP. IT ROLLS OVER AUTOMATICALLY EACH MONTH.
LOOK AT SETUP-1 AND SEE WHICH MONTHS HITS HAVE BEEN RECIEVED.

7.WIDGET.RUN INSTALL RUN CHIP IN U30 AND POWER UP. THIS CHIP HAS AN AUTOMATICCLONE MODE AND AN AUTOMATIC UPDATING WIZZARD MODE WITH 15 BANKS FOR CODES.THIS CHIP IS SIMULAR TO THE G.I. BUSTER BUT BETTER.
SETUP 5 WILL SWITCH BETWEEN AUTO AND SEMI-AUTO MODE. IN AUTO MODE IT
WILL RUN LIKE A CLONE, IN SEMI-AUTO MODE IT IS A AUTO-UPDATING WIZZARD.          WHEN ENTERING CODES SUCH AS "WORKING KEYS" OR "PUBLIC DATA"
OR EVEN SELECTING ANOTHER BANK OF CODES THAT HAVE BEEN ENTERED EARLIER.
YOU DO NOT HAVE TO CONVERT NUMBERS BECAUSE AN "A" IS AN A, AND A "9" IS
A 9, NOT A"91" AND A "09".
FOLLOWING IS A TABLE OF THE KEYS...
VIEW =  A
HELP =  B
SETUP = C
NEXT =  D
TEXT =  E
MESS =  F
0 THROUGH 9 = 0 THROUGH 9
THE ARROW KEYS ARE USED TO EXIT!!! IF YOU PRESS "VIEW" TO EXIT YOU
WILL HAVE SELECTED AN "A".
AFTER YOU PRESS AN ARROW KEY TO EXIT THEN THE KEYPAD WILL RETURN TO
ITS NORMAL OPERATION.

8. TO UPDATE THE "WIDGETLDR.UTL" CHIP ENTER AS FOLLOWS:
PUBLIC DATA #1: 3E00
PUBLIC DATA #2: 3E80
UNIT NUMBER   : 3F00 - ENTER THIS IN REVERSE [03 20 AB XX] = [XX AB 20 03].
U7 KEYS       : 3F04 - FOLLOWING UNIT # FOR 28 BYTES
WORKING KEYS  : 3F40 - 8 BYTES + MONTH POINTER



THIS CHIP SET WILL RUN ALL CODES AVAILABLE IN A 4* AND ALL BUT C4
AND 77 IF IN A  5* BOARD. AT THIS TIME ONLY 77 CODES WILL
WORK IN A 7* BOARD.
********************************************************************************                 ORDERING INFO SOON SO STAY TUNED
     ORDERING INFO SOON TO COME.........STAY TUNED

                    W I D G E T - C O









 
Downloaded From P-80 International Information Systems 304-744-2253