compiler/compiler					    compiler/compiler
compiler/COMPILER					    compiler/COMPILER

				DICE SYSTEM

			      Matthew Dillon
			      891 Regal Rd.
			      Berkeley, Ca. 94708
			      USA

			      dillon@overload.Berkeley.CA.US
			      uunet.uu.net!overload!dillon

			      BIX: mdillon

		    COMPILER FEATURES LIST AND ORGANIZATION

		    NOTE: net distributed releases will not contain
			  commodore includes or amiga*.lib

    (1) Organization of includes and libraries, default:

	DINCLUDE:	    location of top level includes such as stdio.h
	DINCLUDE:Amiga/     location of amiga includes (e.g. amiga/exec/types.h)
				(amiga includes not included)

	NOTE !!! Amiga includes should be placed in the subdirectory
	dinclude:Amiga, that is, dinclude:Amiga/Exec/*.h,
	dinclude:Amiga/graphics/*.h, etc...

	DCC references startup and libraries to DLIB:

	DLIB:amigas.lib     A small-data model version of AMIGA.LIB
	DLIB:c.lib	    The main C library for which you have source code
	DLIB:m.lib	    The math library
	DLIB:auto.lib	    The auto library-open library
	DLIB:c.o	    The startup module
	DLIB:x.o	    The terminator module

    (2) Organization of includes and libraries, -2.0 option (usually
	set in the DCCOPTS enviroment variable)

	DINCLUDE:AMIGA20/   instead of DINCLUDE:AMIGA
	DLIB:amigas20.lib   instead of DLIB:amigas.lib


    (3) DCC generated link lines

    If you give DICE the following line:

	1> DCC foo.o -o foo

    It will run DLink with the following options:

	DLink dlib:c.o foo.o dlib:c.lib dlib:amigas.lib dlib:auto.lib dlib:x.o -o foo

    DLIB:C.O		DICE startup code
    FOO.O		your object module(s)
    DLIB:C.LIB		DICE C.LIB
    DLIB:AMIGAS.LIB	small data model version of commodore amiga.lib
    DLIB:AUTO.LIB	DICE AUTO.LIB
    DLIB:X.O		DICE section terminator code


	Some explanation is in order.  AUTO.LIB catches any references
	to common library base variables when no storage has been
	declared and imports code to automatically open said libraries
	on startup and close them on exit.  DICE uses this feature to
	import code to open and close "dos.library" when DOSBase is
	referenced, and also for the floating point libraries.

	X.O is used to supply an RTS at the end of the special autoinit
	and autoexit sections.	Any module between C.O and X.O may
	declare these special sections to handle run-time relocations and
	other DICE features, and do so such that when the base of the
	section is JSR'd all the various module's code is sequenced
	through until the RTS in X.O is hit for the sections in
	question.


    (4) SMALL DATA AMIGA.LIB

	DICE uses a small-data model version of Commodore's AMIGA.LIB
	to allow it to generate residentable executables (-r option to
	DCC).  The small data amiga.lib, called AMIGAS.LIB (note the 's')
	is generated from the large modem amiga.lib with the LIBTOS
	program.

	LIBTOS, including source, is included.	The source is available
	to allow developers using DICE to add new base variables to
	LIBTOS's search list when new operating systems come out without
	having to wait for my update.


    ----------------------------------------------------------------------

			    COMPILER FEATURES LIST

    (0) ANSI.  Pretty much ansi.  Please report non-ansism problems.  Check
	out the doc/KnownBugs list before reporting a problem.

    (1) autos are placed in registers based on weighted usage.  A0,A1,D0,D1
	will be used as register variables whenever possible, which usually
	reduces the number of registers that must be saved/restored in
	critical low level routines.  The 'register' keyword is
	essentially ignored (use 'volatile' to force a variable to NOT
	be in a register).

    (2) LINK/UNLK is removed from low level routines that do not reference
	A5 and do not make any subroutine calls.

    (3) MOVEM is converted to MOVE or deleted entirely when possible.

    (4) Various obvious optimizations:  use of BSET, BCLR, BTST as short
	cuts to logic operations, CMP/TST, etc...

    (5) Switch() statements are optimized as follows:

	    * if the range of values is less than double the number of cases
	      a lookup table will be used

	    * if a small number of cases exists a sub[q]/beq sequence
	      will be used

	    * for a sufficiently large set of cases that cannot be made
	      into a jump table, a binary subdivision method is used.

    (6) Branch optimization.  Bxx to BRAs are optimized (up to 20 hops) by
	DAS, and massive optimization is done to multi-level conditionals
	by the main compiler pass.

    (7) Workbench support.  The standard startup module supports the workbench.
	Specifically, the low level _main() in c.o does this.

	When a program is run from the workbench, a different entry point is
	called:     wbmain(wbmsg)

	If you do not supply a wbmain() then the one from the c.lib library
	is used which immediately return(-1)s, exiting the program.

	The standard return from wbmain() or using exit() automatically
	ReplyMsg()s the workbench message for you.

    (8) _main() shortcut for extremely low level programs.

	You may overide c.lib's _main with your own.  If you do so you may
	not use any c.lib memory allocation, stdio, or fd (open,close...)
	related routines.  The startup module (c.o) will still run
	autoinits, autoexits, setup resident programs, and initialize your
	BSS space.

	_main(len, arg)     (as passed to the program on startup)
	long len;
	char *arg;
	{
	}

	If running from the workbench, you must GetMsg() and process the
	workbench startup message yourself, as well return the message
	when you exit.

	_exit exists in c.o and cannot be overridden.  If you use the _main
	override you may NOT call exit() unless you also override it.
	Calling exit() will generate references to stdio library code and
	bring it in from the library, making your executable larger
	unnecessarily.

	i.e. if you use _main() you should either fall through or use
	_exit() to exit.

    (9) AutoInit support.  You may qualify a subroutine with the __autoinit
	keyword that will cause it to be automatically called by the
	startup code rather than having to explicitly call it from main.

	This feature is more useful to bring code in indirectly.  For
	example, to automatically OpenLibrary() (& CloseLibrary()) floating
	point libraries if their base variables are referenced.

	Refer to the auto.lib source code for examples.

	__autoexit works the same way.	Note that __autoinit routines are
	called BEFORE _main, just after autoinit libraries are openned,
	and __autoexit routines are called in __exit just before autoinit
	libraries are closed.

    (10) DCC runs fast.  Make everything resident and watch it fly.  Most
	 of this speed comes from loading entire files into memory at once.
	 This might present a memory problem, but in general DICE's memory
	 usage is comparable to Lattice and Aztec.

    (11) CODE SIZE is comparable with Lattice and Aztec, even better in
	 many cases.  The minimum program sizes are as follows:

	_main() { }          448    no stdio/fd
	 main() { }         2736    some stdio
	 main() { printf..} 5492    most of stdio

    (12) EXTENSIONS , see EXTENSIONS.DOC.  DICE provides many extensions
	 to C to support various AMIGAisms and ROM based code, including
	 special treatment of the 'const' storage qualifier.

    (13) The preprocessor is able to handle arbitrarily sized macros.  There
	 are no limits to symbol or macro length.  The preprocessor is able to
	 handle up to 64 levels of includes / macro recursions with arbitrary
	 use of the string-ize (#) and token pasting (##) operators.

	 The preprocessor implements the __BASE_FILE__ macro as well as all
	 standard ANSI macros (__FILE__, __LINE__, __DATE__, __TIME__, ...)

    (14) DICE supports the creation of residentable executables in nearly
	 all cases (exception: using the __geta4 procedure qualifier
	 precludes being able to make an executable resident, also non
	 const __chip data).

	 Not only is residentability supported, but it is supported
	 without requiring the programmer to #include all sorts of
	 prototype/pragma files.

    (15) DICE supports the small-data model, large data model, small and
	 large code models, and special data models (word absolute,
	 absolute known address) for supporting ROMable code.  The linker
	 automatically generates JMP tables when the small-code model is
	 used in large executables.

    (16) REGISTERED user's DICE supports __chip, __near, and __far keywords,
	 as well as others.

    (17) Simplified library and startup module design.  There are no multiple
	 versions of a single library for different memory models and the
	 frontend, DCC, makes all library and startup module interaction
	 except m.lib invisible.  The same c.o handles both resident and
	 non-resident startup.	c.lib and m.lib may be used with programs
	 that declare more than 64KBytes of BSS (though not with programs
	 that declare more than 64KBytes of __near initialized storage).

	 There is no large-data-model version of c.lib and m.lib,
	 although you can easily recompile the libraries into a large-data
	 model version if you wish.  I suggest that instead of doing that
	 you stick with the small-data model and use the __geta4 type
	 qualifier to procedures which are called out of context.

    (18) Optimization of args to prototyped routines


    --------------------------------------------------------------------------
				    GOALS

    In writing DICE my goals are as follows:

    - reasonably fast compilation.  Modular executables for ease of use,
      reliability, and testability.

    - concentrate more on reliability and less on optimizations.  Remember that
      this is only the third major distribution of DICE, I expect some bugs
      to show up.  I expect to become more reliable than the two other
      commercial C compilers in the Amiga market within a year.

    - but do not forget optimizations... put in relatively easy to implement
      optimizations that do not destroy the reliability of DICE.  DICE does
      no common sub-expression or loop unrolling optimizations, but does do
      relatively smart register allocation and multi-level history to
      propogate conditional expressions.

    - provide comprehensive support of the Amiga, especially for new
      versions of the OS that come out.

    - I have always torn my hair out at not being able to easily fix bugs in
      the support libraries for commercial compilers.  DICE includes full
      source for its support libraries (c.lib, m.lib, auto.lib) and a means
      to remake the library.  DICE also includes full source to some of
      its own utilities, namely LIBTOS and the DCC frontend which are the
      most likely candidates for programmer hair loss.

    ------------------------------------------------------------------------
				   COMMENTS

    Registerized parameters are not implemented.  While such a feature
    would make an executable somewhat smaller and a little faster, a few
    percent of gain is not worth the complexity of the implementation (and
    thus the possibility of introduced bugs).  The difference in execution
    speed is generally so miniscule that it isn't noticable, and where it
    is noticable it is usually due to a badly implemented algorithm in
    the first place.

    So, cute, but not as much of a boost as you might think.

    Inline library calls are not implemented either.  Inline library calls
    are actually useful and when properly implemented increase efficiency
    to low level calls such as AddHead() and GetMsg().  Other calls such as
    Move() and Draw() do not increase noticably in efficiency. #pragma's
    must be used to define inline calls and this makes the compiler
    enviroment less portable.  Lattice made a big mistake *requiring* the
    use of inline library calls with residentable programs.  My solution
    was to write a program to convert AMIGA.LIB into a small-data version
    of same called AMIGAS.LIB.

    In general, I refuse to implement a thousand nearly useless features
    that will only introduce more bugs into the compiler.

    ------------------------------------------------------------------------
				COMPATIBILITY

				   ANSI C

    DICE is getting closer to being ANSI C compliant, there are only a
    few things missing.

    I spent a great deal of time ensuring that STDIO routines run relatively
    fast.  I decided to write nearly all of the support library in C instead
    of falling back to optimized assembly to keep the system uniform and
    portable.  One does not notice much of a difference between the C
    strcpy() and an assembly strcpy() relative to the run time of their
    program.

				    AMIGA

    As said in feature (7), if you wish your program to be runnable from
    the workbench you must supply a wbmain() entry point.  If you do not
    then running the program from the workbench will result in its
    immediate termination (e.g. nothing happens).  On return from wbmain()
    or exit() the workbench message is automatically ReplyMsg()d by the
    exit code.

    DICE separates workbench startup and puts it in the hands of the user
    to simplify the user's code.  Since there are two entry points,
    main() for CLI run programs and wbmain() for WORKBENCH-run programs,
    the programmer can more easily modularize his code.

    The Registered release of DICE supports the __near, __far, and __chip
    keywords.

			      UNBUFFERED CONSOLE IO

    You may set a console to RAW mode using the setbuf() and setvbuf() calls.
    You may set a console back to COOKED mode using the same calls.

    ------------------------------------------------------------------------

				Your first program

    1> cd examples
    1> dcc hello.c -o ram:hello
    1> ram:hello
    hello world
    1>

				Your first residentable program

    1> cd examples
    1> dcc hello.c -o ram:hello -r
    1> ram:hello
    hello world
    1> resident ram:hello
    1> hello	    ; instantanious execution
    hello world
    1>

    * NOTE, a common problem is that users have removed various floating
    point libraries from LIBS: and this will prevent DC1 from running.
    Make sure you have the full complement of floating point libraries
    in LIBS: