06601030305800
F0110030
9[...................................................]011
€
-----------------------AIM-:-ANOTHER-IMAGE-MANAGER

The-image-processing-program-AIM-was-originally-developed-for-the-
ATARI-ST-by-Frans-Groen-and-Robert-de-Vries.-Since-the-first-
version-of-AIM-the-extension-of-this-public-domain-image-
processing-package-has-become-a-joint-effort-of-a-number-of-
people-from-the-Delft-University-of-Technology-and-the-University-
of-Amsterdam.-Especially-Piet-Verbeek-supplied-many-linear-and-
non-linear-filtering-routines,-Lucas-van-Vliet-and-Ben-Verwer-
developed-the-fast-morphological-operations.-Also-Gert-van-
Antwerpen,-Damir-Sudar-and-Igor-Weber-supplied-a-number-of-
routines-to-AIM.

AIM-runs-in-high-resolution-and-low-resolution-mode.-The-medium-
resolution-mode-is-not-supported.-AIM-has-been-written-in-the-C-
language-using.-The-purpose-of-the-program-is-to-experiment-with-
digital-image-processing.

-
User-interface

The-user-interface-of-AIM-consists-of:

-GEM-interface.-Operations-and-parameters-can-be-selected-by-
means-of-dialog-boxes-and-drop-down-menus.-A-choice-from-a-menu-
results-in-a-command-which-is-passed-to-the-command-interpreter.-
Image-displays-can-be-moved-and-sized.

-Command-interpreter.-Sequences-of-commands-can-be-put-together-
in-a-command-file.-When-the-logging-is-on,-commands-which-are-
entered-are-also-stored-in-a-log-command-file.-A-command-file-may-
be-called-within-another-command-file-up-to-16-levels-deep.

The-command-interpreter-has-a-history-handler-with-some-editing-
facilities.

Images-in-AIM

Four-image-memories-are-available-in-AIM.-The-image-memories-are-
8-bit-wide-and-have-a-maximum-size-of-65536-pixels.-Standard-aim-
images-have-a-the-size-of-256-x-256-pixels.-These-image-memories-
are-displayed-at-the-ATARI-screen.-The-windows-are-designated-
with-'A',-'B',-'C'-and-'D'.-The-position-of-the-windows-is-
obtained-from-a-setup-file.-Image-windows-can-be-moved-and-sized.

A-colour-image-consists-of-4-memories-with-a-maximum-of-16384-
pixels-respectively-for-the-intensity,-red,-green-and-blue-sub-
images.-This-maximum-size-is-the-result-from-the-current-1M-byte-
memory-restriction-of-the-Atari-ST.-When-the-memory-increases,-
larger-colour-images-could-be-supported.-Standard-aim-colour-
images-have-a-size-of-4-times-128-x-128-pixels.-They-occupy-the-
same-area-as-an-grey-value-image-of-size-256-x-256.-Most-of-the-
(colour)-image-operations-are-applied-to-all-sub-images-of-a-
€colour-image.-Some-image-operations-(gradx,-grady,-equal-)-are-
performed-on-the-intensity-sub-image-of-a-colour-image.-After-
such-an-operation-the-red,-green-and-blue-colour-values-are-
updated-according-to-the-new-intensity-value.

The-8-bitplanes-of-the-grey-value-images-can-also-be-used-as-8-
binary-images.-Binary-and-Cellular-Logic-operations-can-be-
performed-on-these-bitplanes.-The-bitplanes-are-numbered-from-1-
to-8.

When-an-image-is-read-from-disk-all-8-bitplanes-are-read-
simultaneously.-The-same-holds-when-an-image-is-written-to-disk.
An-image-is-displayed-in-the-grey-value-mode-when-the-extension-
is-.IM-and-in-color-mode-when-the-extension-is-.COL.-The-display-
of-color-images-is-only-supported-in-the-low-resolution-mode.

Also-DEGAS-and-Neochrome-images-can-be-read-or-written.-With-the-
read-command-these-pictures-are-converted-to-320-x-200-grey-value-
images.-With-the-cread-command-they-are-converted-to-colour-
images-of-size-160-x-100.-When-the-extension-is-.PI1-or-.PI3-a-
DEGAS-file-is-read-or-written,-when-the-extension-is-.NEO-a-
neochrome-file-is-read-or-written.-Examples-are-given-in-@democ4.

Great-care-should-be-taken-by-storing-images-in-degas-or-
neochrome-format.-In-these-formats-a-limited-number-of-grey-
values-or-colours-is-used-(palette),-so-a-drastic-reduction-of-
information-takes-place,-which-limits-the-possibility-of-further-
image-processing.-Images-are-stored-in-full-grey-or-colour-
resolution-in-the-AIM-format.

In-the-high-resolution-mode-a-standard-grey-value-image-is-
represented-by-256-x-256-black-and-white-dots.-(there-are-only-2-
grey-values-possible:-white-and-black).-A-sigma-delta-technique-
is-used-to-obtain-a-local-density-of-the-dots-representing-as-
good-as-possible-the-grey-values-in-the-image.-In-a-binary-
display-0-gives-a-black-dot-and-1-a-white-dot.

In-the-low-resolution-mode-a-standard-grey-value-image-is-
represented-by-128-x-128-pixels-in-8-grey-values.-Again-a-sigma-
delta-technique-is-used-to-represent-as-good-as-possible-the-
original-256-grey-values.-As-the-standard-images-have-a-size-of-
256-x-256-pixels,-in-the-low-resolution-mode-only-1-pixel-out-of-
each-2x2-pixel-neighbourhood-is-displayed.-In-the-default-binary-
low-resolution-mode-(don-1)-a-black-dot-is-displayed-when-all-
pixels-of-a-2x2-neighbourhood-are-'0'-and-a-white-dot-is-
displayed-when-all-pixels-in-a-2x2-neighbourhood-are-'1'.-In-all-
other-cases-a-grey-dot-is-displayed.

A-standard-color-image-is-displayed-in-128-x-128-pixels-with-16-
different-colors.-An-optimum-palette-is-chosen-for-the-currently-
displayed-image.-So-the-palettes-of-other-images-are-no-longer-
correct.-The-palette-of-the-image-which-is-on-top-is-displayed.-
Clicking-on-another-window-brings-it-on-top-with-the-correct-
palette.
€
Standard-grey-value-images-on-disk-(extension-.IM)-consist-of-256-
lines-of-256-pixels-(unsigned-characters)-of-1-byte.-So-an-image-
consists-of-65536-bytes-in-total.-The-sequence-is-line-by-line-
from-top-left-to-bottom-right.

Standard-color-images-on-disk-(extension-.COL)-consist-of-a-
sequence-of-4-sub-images-of-128-lines-of-128-pixels-(unsigned-
characters)-of-1-byte.-The-sub-images-are-intensity,-red,-green-
and-blue-respectively.

When-an-image-does-not-have-a-standard-format-a-header-is-needed-
(extension-.HD),-describing-the-image-width-and-height.-The-
header-used-is-the-header-of-the-Centre-for-Image-Processing-
Delft-and-is-given-in-the-Appendix.-When-an-image-is-written-in-
the-AIM-format-always-a-header-is-written.

Command-interpreter

It-is-not-necessary-to-give-the-complete-command-name.-The-
smallest-number-of-letters-which-gives-no-ambiguity-is-suffi
cient.

It-is-possible-to-edit-your-commands-in-a-simple-way.-The-delete--
or-backspace-key-delete-the-last-character.-CONTROL-X-deletes-the-
whole-line.-A-sequence-of-commands-which-perform-a-certain-
operation-may-be-grouped-to-a-command-file-and-stored-on-disk.-
The-extension-of-command-files-is-.AIM.-When-the-logging-is-on-
all-the-entered-commands-are-stored.-When-the-logging-is-switched-
off-a-log-command-file-is-written-to-disc.


Command-files-are-executed-by-typing-@name-(without-the-exten
sion).-A-new-command-file-can-be-called-from-a-command-file-and-
may-be-nested-up-to-16-levels-deep.-So-typing-@command-file-name-
instead-of-a-command-executes-the-command-file.-ESC-stops-the-
execution-of-a-commandfile-and-asks-the-user-to-go-on-or-not.-
Default-values-are-used-when-a-parameter-is-not-given.-When-an-
erroneous-value-of-a-parameter-is-given,-the-command-interpreter-
asks-for-a-correct-value.-ESC-stops-this-procedure-and-returns-to-
the-command-interpreter-(AIM-prompt).-If-in-this-case-a-return-is-
given,-the-default-value-is-used.-This-gives-the-possibility-to-
ask-for-a-parameter-value-when-a-command-file-is-executed,-
instead-of-using-a-fixed-value.-In-the-commandfile-for-instance-a-
question-mark-(?)-can-be-used-instead-of-the-parameter-value-to-
obtain-this-feature.

A-question-mark-(?)-instead-of-a-command-gives-a-list-of-all-
available-commands.

A-star-(*)-indicates-that-the-remainder-of-the-commandline-
consists-of-comments.

9[....................................................]001
History
€
The-history-mechanism-in-AIM-is-intended-to-resemble-as-much-as-
possible-the-UNIX-mechanism.-Except-for-the-'history'-command-most-
important-features-have-been-included.
!!-:-repeat-last-command.-It-is-possible-to-type-extra-characters-
after-the-!!.-These-are-appended-after-the-previous-line.
!{chars}-:-repeat-the-command-that-started-with-{chars}.
!<n>-:-repeat-the-n-th-command-with-n-is-an-integer.-In-case-the-number-
is-negative-the-n-th-previous-command-is-repeated.-If-some-
characters-follow-the-integer-number,-these-are-appended.
^<string1>^<string2>^<string3>-:-replace-<string1>-in-the-previous-
command-with-<string2>,-append-<string3>--and-repeat-the-changed-
command.

Examples:
In-the-examples-the-prompt-has-the-form-of-'aim'-followed-by-an-
integer-number-followed-by-'>'.
The-first-command-is-a-sample.
---aim1>-readf-trui-
Now-let's-repeat-it.
---aim2>-!!
---readf-trui
Another-way-to-repeat-it.
---aim3>-!rea
---readf-trui
You-can-also-append-text-after-the-previous-command.
---aim4>-!!.im
---readf-trui.im
Repeat-first-command.
---aim5>-!1
---readf-trui
Repeat-the-command-of-aim4>
---aim6>-!-2
   readf-trui.im
Change-trui-into-cermet.
---aim7>-^trui^cermet
   readf-cermet.im
Change-cermet-into-ketel-and-put-image-in-B.
   aim8>-^cermet^ketel^,B
   readf-ketel.im,B

GEM-INTERFACE

Operations-marked-with-a-star-(*)-are-only-available-in-the-
command-interpreter.

Dialog-boxes

Parameters-are-entered-in-the-dialog-boxes-by-first-pushing-the-
ESC-button-to-delete-the-default-value-and-to-go-to-the-first-
position.-Only-at-the-first-position-minus-signs-are-allowed.
There-are-two-special-dialog-boxes.-One-is-for-the-threshold-
command.-The-default-threshold-value-is-computed-each-time-a-new-
input-image-is-selected.
€The-other-special-box-is-for-the-palette.-If-a-color-is-chosen-
the-color-coefficients-are-shown-in-the-editable-text-line-
underneath.-If-the-coefficients-are-changed-and-any-other-color-
box-is-clicked-the-effect-of-the-changes-are-visible.-The-three-
coefficients-represent-the-red,-green-and-blue,-and-may-vary-from-
0-to-7.-Higher-values-are-cast-to-7.

Printer-driver

Printer-output-can-only-be-done-in-monochrome-mode.-This-is-
because-the-actual-screen-image-is-printed.-The-printer-driver-
supports-8-pin-and-24-pin-graphics.-In-the-file-AIM.INF-after-
'printer'-the-printer-definition-is-placed.-First-the-name-of-the-
printer-is-given-on-a-single-line.-After-that-the-number-of-dots-
and-finally-the-printer-codes-to-reset-the-printer,-to-set-the-
linedistance-and-finally-to-start-graphics-printing.
To-make-a-printerdriver-for-your-own-printer-you-only-need-a-text
editor-to-create-it.-The-first-line-contains-the-name-of-your-
printer.-The-second-line-gives-the-number-of-vertical-dots-per-
line.-It-looks-like-:-
dpl-8
"dpl"-is-a-keyword-for-"dots-per-line"-and-it-is-separated-by-the-
value-by-a-space.-The-only-values-supported-at-this-moment-are-8-
and-24.
The-third-line-gives-the-reset-code-for-your-printer.-It-looks-
like:
reset-1B-40
"reset"-is-a-keyword-for-the-reset-code.-The-characters-in-the-
reset-code-are-given-in-hexadecimal-seperated-by-a-space.-The-
maximum-number-of-characters-in-the-control-sequence-is-20.
The-fourth-line-gives-the-control-sequence-to-set-the-linedistance-
between-two-lines-of-graphical-output.-It-looks-like-:
linedist-1B-41-08
"linedist"-is-the-keyword-for-the-linedistance-control-sequence.-
It-can-be-20-characters-long.
The-last-line-gives-the-control-sequence-to-start-graphical-
output.-It-looks-like:
graphics-1B-4B
"graphics"-is-again-a-keyword.-The-sequence-to-start-printing-
graphics-is-always-followed-by-the-number-of-columns-of-dots-to-be-
printed.-In-most-printers-this-is-done-by-sending-first-the-low-
byte-followed-by-the-high-byte-of-the-word-that-contains-this-
number.-Other-printers-send-the-number-in-BCD-format.-In-AIM-only-
the-first-way-is-supported.


------------------------�OPERATIONS-IN-AIM€
FILE-OPERATIONS


readf[ile]:-reads-an-image-from-disk.

The-first-command-parameter-is-the-image-name,-the-second-
optional-parameter-is-the-image-memory-(A,B,C,D).-Default-is-
€image-memory-A.-The-extension-of-an-grey-value-image-file-is-.IM.-
Available-standard-images-are-:-TRUI.IM,-CERMET.IM,-TUD.IM-and-
ASBEST.IM.-When-no-extension-is-given-.IM-is-assumed.
(When-the-extension-is-.COL-a-colour-image-is-read-in).

When-no-header-file-is-present-a-standard-image-size-is-assumed,-
otherwise-the-description-from-the-header-file-is-used.
When-the-extension-is-.PI1-or-.PI3-a-DEGAS-file-is-converted-to-a-
grey-value-image-of-320-x-200-pixels.-When-the-extension-is-.NEO-
a-neochrome-file-is-converted-to-a-grey-value-image-of-320-x-200-
pixels.

command-:-readf-image-file,-image
default-:-readf---trui----,---A
range---:-----------------,-<A-D>

creadf[ile]:-reads-a-colour-image-from-disk.

The-first-command-parameter-is-the-image-name,-the-second-
optional-parameter-is-the-image-memory-(A,B,C,D).-Default-is-
image-memory-A.

The-extension-of-a-color-image-is-.COL.-Available-color-images-
are-:-MANDRIL.COL,-MAID.COL,-GIRL.COL-and-ARLES.COL.
When-no-extension-is-given-.COL-is-assumed.
(When-the-extension-is-.IM-a-grey-value-image-is-read-in).

When-no-header-file-is-present-a-standard-image-size-is-assumed.-
otherwise-the-description-from-the-header-file-is-used.

When-the-extension-is-.PI1-a-DEGAS-file-is-converted-to-a-colour-
image-of-160-x-100-pixels.-When-the-extension-is-.NEO-a-neochrome-
file-is-converted-to-a-colour-image-of-160-x-100-pixels.

command-:-creadf-image-file,-image
default-:-creadf-mandril---,---A
range---:------------------,-<A-D>


writf[ile]:-writes-an-image-to-disk.

The-first-command-parameter-is-the-image-memory-(A,B,C,D).-The-
second-parameter-is-the-name-of-the-image-file.-When-no-extension-
is-given-.IM-is-assumed.-Besides-the-image-file-also-a-header-
file-is-written-(extension-.HD).-The-header-structure-is-given-in-
the-Appendix.

When-the-extension-is-.PI1-or-.PI3-a-DEGAS-file-is-written.-When-
the-extension-is-.NEO-a-neochrome-file-is-written.

command-:-writf-image,-image-file
default-:-writf---A--,---dummy
range---:-------<A-D>,-<anything>

€load-setup

This-command-loads-a-setup-file.-The-setup-file-describes-the-
path-of-the-image-files-(read/write),-the-commandfiles,-the-
helpfiles,-the-aspect-and-align-flags-and-the-position-of-the-
windows.

save-setup

This-command-saves-the-current-settings-(paths-and-window-
positions)-in-a-setup-files.

Macro-:-selects-and-starts-a-commandfile.

@filename-is-a-command-file.-An-@-starts-the-command-file.-
Command-files-may-be-nested-up-to-16-levels.-An-example-is-given-
in-@demo.-The-extension-of-command-files-is-.AIM.-These-exten
sions-are-added-to-the-command-file-name-by-AIM.

When-infinite-=--1-the-commandfile-is-infinitely-repeated.

command-:-@name.AIM,infinite
default-:----------,----0
range---:----------,-<-1,0>

Logging

When-the-logging-is-on-all-entered-commands-are-stored.-When-the-
logging-is-switched-off,-the-stored-commands-are-written-in-a-log-
file.-In-this-way-automatically-command-files-can-be-created.

printpic-:-prints-a-picture.

This-command-prints-the-contents-of-a-window.-It-only-works-in-
highres.-If-a-histogram-or-numbers-are-displayed-in-a-window-it-is-
also-printed.-The-second-parameter-is-the-magnification-factor.-
When-a-24-dot-matrix-printer-is-installed-the-result-looks-better-
with-magnification-factor-2.

command-:-printpic-im---,-factor
default-:-printpic-A-  -,-1
range---:----------<A-D>,-<1,5>

exit-:-ends-the-program.-This-action-can-also-be-obtained-by-
typing-Control-C-or-by-clicking-the-close-box-of-the-command-
window.

command-:-exit

TEST-IMAGE-GENERATION
ÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿ
shad-:-shading-image-generator


€Shad generates a shadinglike grey image.-The-grey-value-is-the-
sum-of-the-bilinear-interpolation of the corner points b a 
                                                       c d 
and the quadratic (e*x*(1-x) + f*y*(1-y))*N/128 
if-e+f>0,-N = (255-(a+b+c+d)/4),  
such that e=f=-256 -> 255-(a+b+c+d)/4 as maximum-output 
if-e+f<0,-N = (    (a+b+c+d)/4), 
such that e=f=-256 -> ----(a+b+c+d)/4 as minimum-output


command:-shad-out_im,-a-,  b-,--c-,--d-,--e-,--f
default:-shad-   B  ,255   0 ,  0 ,  0 ,  0-, -0    
range--:-------<A-D>,-<0-----,----255>-,<-255,255>


GEOMETRIC-AND-ARITHMETIC-GREY-VALUE-OPERATIONS
ÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿ
GEOMETRIC-GREY-VALUE-OPERATIONS

copy-:-copies-or-samples-an-image.

The-first-command-parameter-is-the-input-image,-the-second-is-
the-output-image-(A,B,C,D).-Extra-parameters-allow-sampling-the-
input-image-which-is-virtually-repeated-in-all-directions-
(periodic).-The-third-and-fourth-parameter-are-the-sampling-
starting-position-X,Y-and-allow-wrapping-(X-with--sign-enforces-
the-inverse-operation,-Y-also-with--sign-enforces-write-without-
clear-(stamping));--the-fifth-and-six-give-the-2D-sampling-step-
dx,dy-taken-in-the-input-image-when-writing-a-line-in-the-output-
image;-the-seventh-and-eighth-are-the-2D-sampling-step-DX,DY-
taken-when-feeding-a-line-in-the-output-image.-Inverse sampling-
(-X)-at-2**k-stepsize-multiply overwrites-all-copying-results-but-
that-of-the lower right block,-which-is-thus-blown-to-dots.
Different-parameter-choices:
                 |
type-of-sampling |  X    Y    dx   dy   DX   DY
copy               (1)  (1)   (1)  (0)  (0)  (1)-(default)
smear-line-31       1   31    -1   -0   -0-  -0
smear-column-17    17   -0    -0   -0   -0   -1
wrap 17,31->1,1 -- 17   31    (1)  (0)  (0)  (1)
reduce 2x hor--     1    1    -2    0    0 -  1
reduce 3x ver--     1    1    -1    0    0    3
reduce 2x-hor&ver   1    1     2    0    0    2
skew up             1    1     1    1    0    1
skew left           1    1     1    0    1    1
skew right          1    1     1    0   -1    1
reflect hor--     256    1    -1    0    0    1
reflect ver--      -1- 256     1    0    0   -1
upside down    -- 256- 256    -1    0    0   -1
transpose           1    1     0    1    1    0
symmetr. ri half -256    1    -1    0    0    1   out=in
symmetr. lo half    1 -256     1    0    0   -1   out=in
pointsym-lo half  256- 256    -1    0    0   -1   out=in
tilt atan 1 = 45  127 -127    -1    1   -1    1 
€tilt atan-1 =-45- 127 -127     1   -1    1    1
tilt atan-2    -- 127- 127    -1   -2    2    1
tilt atan-1/2     127 -127     2   -1    1    2
inverse of-this- -127 -127     2   -1    1    2
blow-to-dots--     -1    1     4    0    0    4

command:-copy-input_image,-out_im,-X,-  Y,--dx,--dy,--DX,--DY
default:-copy---    A----,-   B  , 1    1    1    0    0   -1    
range--:----------<A-D>--,--<A-D>,-<----256----,-----256---->

ARITHMETIC-GREY-VALUE-OPERATIONS

Standard-and-signed-grey-values.
The-standard-arithmetic-grey-value-operations-have-been-built-for-
grey-values-in-the-range-of-0-to-255.-Some-interesting-image-
processing-results-such-as-gradients-may-be-negative.-In-AIM-such-
results-are-represented-by-silently-adding-127-(integer-255/2).-
In-effect-a-new-kind-of-grey-values,-"signed-grey-values",-with-a-
range-of--127-to-128-is-so-defined.-Arithmetic-with-signed-grey-
values-asks-for-a-separate-set-of-signed-arithmetic-commands.-
They-are-similar-to-the-normal-commands-but-for-a-prefix-"s"-and-
will-not-be-separately-described.-"sadd"-does-not-exist-as-it-is-
identical-to-"add",-"sginv-a"-is-identical-to-"scmul-a--1".

MONADIC-GREY-VALUE-ARITHMETIC

cadd-:-adds-a-constant-to-an-image.

The-first-command-parameter-is-the-input-image.-The-second-
parameter-is-the-constant-which-is-added.-The-third-parameter-is-
the-output-image.-If-no-output-image-is-specified-the-output-
overwrites-the-input.

output_image-=-input_image-+-constant

command-:-cadd-input_image-,---constant-,-output_image
default-:-cadd------A------,------0 -- -, input_image
range---:---------<A-D>----,-<-255,255>-,----<A-D>-----


ginv-:-subtracts-the-image-from-255

The-first-command-parameter-is-the-input-image.-The-second-
parameter-is-the-output-image.-If-no-output-image-is-specified-
the-output-overwrites-the-input.

output_image-=-255---input_image

command-:-ginv-input_image-,-output_image
default-:-ginv------A------, input_image
range---:---------<A-D>----,----<A-D>-----


cabs-:-determines-absolute-difference-with-a-constant
€
The-first-command-parameter-is-the-input-image.-The-second-
parameter-is-the-constant.-The-third-parameter-is-the-output-
image.-The-result-is-clipped-above-255.-If-no-output-image-is-
specified-the-output-overwrites-the-input.

output_image-=-|-input_image---constant-|

command-:-cabs-input_image-,---constant-,-output_image
default-:-cabs-------A-----,------0 -- -, input_image
range---:----------<A-D>---,-<-255,255>-,----<A-D>-----


cmul-:-multiplies-an-image-by-a-constant.

The-first-command-parameter-is-the-input-image.-The-second-
parameter-is-the-multiplication-constant.-The-third-parameter-is-
the-output-image.-If-no-output-image-is-specified-the-output-
overwrites-the-input.

output_image-=-input_image-*-constant

command-:-cmul-input_image-,---constant-,-output_image
default-:-cmul-------A-----,------1 -- -, input_image
range---:----------<A-D>---,---<0,255>--,----<A-D>-----


cdiv-:-divides-an-image-by-a-constant.

The-first-command-parameter-is-the-input-image.-The-second-
parameter-is-the-division-constant.-The-third-parameter-is-the-
output-image.-If-no-output-image-is-specified-the-output-
overwrites-the-input.

output_image-=-input_image-/-constant

command-:-cdiv-input_image-,---constant-,-output_image
default-:-cdiv-------A-----,------1 -- -, input_image
range---:----------<A-D>---,---<1,255>--,----<A-D>-----


(*)clear:-clears-an-image.

Clear-sets-each-pixel-value-in-the-image-to-0.

command-:-clear---image----default-:-clear-----A------range---:---------
<A-D>-(*)assign:-assigns-a-constant-to-each-pixel-in-an-image.

command-:-assign--image----,-constant
default-:-assign----A------,-----0
range---:---------<A-D>----,--<0,255>


DYADIC-GREY-VALUE-ARITHMETIC
€
add-:-adds-two-images.

The-first-command-parameter-is-the-first-input-image,-the-second-
parameter-is-the-second-input-image,-the-third-parameter-is-the-
output-image.-If-no-output-image-is-specified-the-output-
overwrites-the-second-input.

output_image-=-(input1_image-+-input2_image-)/2

command-:-add-input1_image-,-input2_image-,-output_image
default-:-add-------A------,-------B    --, input2_image
range---:---------<A-D>----,-----<A-D>----,-----<A-D>


sub-:-subtracts-two-images.

The-first-parameter-is-the-first-input-image,-the-second-
parameter-is-the-second-input-image.-The-third-parameter-is-a-
constant-which-can-be-added-to-the-difference.-The-fourth-
parameter-is-the-output-image.-As-the-image-cannot-become-
negative,-the-resulting-value-is-clipped-below-0-and-above-255.-
If-no-output-image-is-specified-the-output-overwrites-the-second-
input.

output-image-=-(input1_image---input2_image-)-+-constant

command-:-sub-input1_image-,-input2_image,-constant-,-output-image-
default-:-sub-------A------,------B------,----0-----,-input2_image-
range---:---------<A-D>----,----<A-D>----,<-255,255>,  ---<A-D>


abs-:-gives-absolute-difference-of-two-images.

The-first-parameter-is-the-first-input-image,-the-second-
parameter-is-the-second-input-image.-The-third-parameter-is-a-
constant-which-can-be-added-to-the-difference.-The-fourth-
parameter-is-the-output-image.-The-resulting-value-is-clipped--
above-255.-If-no-output-image-is-specified-the-output-overwrites-
the-second-input.

output-image-=-|-input1_image---input2_image-+-constant-|

command-:-abs-input1_image-,-input2_image,-constant-,-output-image-
default-:-abs-------A------,------B------,----0-----,-input2_image-
range---:---------<A-D>----,----<A-D>----,<-255,255>,  ---<A-D>


mul-:-multiplies-two-images.

The-first-parameter-is-the-first-input-image,-the-second-
parameter-is-the-second-input-image.-The-third-parameter-is-a-
constant-by-which-the-product-can-be-divided.-The-fourth-
parameter-is-the-output-image.-The-resulting-value-is-clipped-
€above-255.-If-no-output-image-is-specified-the-output-overwrites-
the-second-input.

output-image-=-(input1_image-*-input2_image-)/constant

command-:-mul-input1_image-,-input2_image,-constant,-output-image-
default-:-mul-------A------,------B------,---256---,-input2_image-
range---:---------<A-D>----,----<A-D>----,<1,32767>,  ---<A-D>


div-:-divides-two-images.

The-first-parameter-is-the-first-input-image,-the-second-
parameter-is-the-second-input-image.-The-third-parameter-is-a-
constant-by-which-the-quotient-can-multiplied.-The-fourth-
parameter-is-the-output-image.-The-resulting-value-is-clipped-
above-255.-If-no-output-image-is-specified-the-output-overwrites-
the-second-input.

output-image-=-(input1_image-/-input2_image-)-*-constant

command-:-div-input1_image-,-input2_image,-constant-,-output-image-
default-:-div-------A------,------B------,----1-----,-input2_image-
range---:---------<A-D>----,----<A-D>----,-<0,32767>,  ---<A-D>


TRIADIC-GREY-VALUE-ARITHMETIC

mud-:-multiplies-two-images-and-divides-by-a-third-image.

The-first-parameter-is-the-first-input-image,-the-second-
parameter-is-the-second-input-image.-The-third-parameter-is-the-
third-input-image-by-which-the-product-is-divided.-The-fourth-
parameter-is-the-output-image.-The-resulting-value-is-given-
modulo-255.-If-no-output-image-is-specified-the-output-overwrites-
the-second-input.

output-image-=-(input1_image-*-input2_image-)-/-input3_image

command-:-div-input1_image,input2_image,input3_image,output-image-
default-:-div-------A-----,------B-----,------C-----,input3_image-
range---:---------<A-D>---,----<A-D>---,----<A-D>---,----<A-D>



DYADIC-GREY-VALUE-NON-ARITHMETIC


(*)-minimum-:-minimum-of-two-images.

The-first-command-parameter-is-the-first-input-image,-the-second-
parameter-is-the-second-input-image,-the-third-parameter-is-the-
output-image.-If-no-output-image-is-specified-the-output-
overwrites-the-second-input.

€output_image-=-minimum(input1_image-,-input2_image-)

command-:-minimum-input1_image-,-input2_image-,-output_image
default-:-minimum-------A------,-------B    --, input2_image
range---:-------------<A-D>----,-----<A-D>----,-----<A-D>


(*)-maximum-:-maximum-of-two-images.

The-first-command-parameter-is-the-first-input-image,-the-second-
parameter-is-the-second-input-image,-the-third-parameter-is-the-
output-image.-If-no-output-image-is-specified-the-output-
overwrites-the-second-input.

output_image-=-maximum(input1_image-,-input2_image-)

command-:-maximum-input1_image-,-input2_image-,-output_image
default-:-maximum-------A------,-------B    --, input2_image
range---:-------------<A-D>----,-----<A-D>----,-----<A-D>



(*)-sminimum-:-signed-minimum-of-two-standard-images.-

This-operation-is-applicable-to-standard,-not-to-signed-grey-
values.-The-output-is-signed.-The-first-command-parameter-is-the-
first-input-image,-the-second-parameter-is-the-second-input-
image,-the-third-parameter-is-the-output-image.-The-resulting-
value-is-clipped-below-0-and-above-255.--If-no-output-image-is-
specified-the-output-overwrites-the-second-input.

if(input1_image<input2_image)
---output_image-=-127-+-input1_image
else
---output_image-=-127---input2_image-

command-:-sminimum-input1_image-,-input2_image-,-output_image
default-:-sminimum-------A------,-------B   ---, input2_image
range---:--------------<A-D>----,-----<A-D>----,-----<A-D>


(*)-ssminimum-:-signed-minimum-of-two-images.

This-operation-is-applicable-to-signed,-not-to-standard-grey-values.-
The-output-is-signed-to-indicate-.-The-first-command-parameter-is-the-first-
input-image,-the-second-parameter-is-the-second-input-image,-the-
third-parameter-is-the-output-image.-The-resulting-value-is-
clipped-below-0-and-above-255.--If-no-output-image-is-specified-
the-output-overwrites-the-second-input.

if(input1_image<input2_image)
---output_image-=-input1_image
else
---output_image-=-254---input2_image-
€

command-:-ssmaximum-input1_image-,-input2_image-,-output_image
default-:-ssmaximum-------A------,-------B  - --, input2_image
range---:---------------<A-D>----,-----<A-D>----,-----<A-D>


TRIADIC-GREY-VALUE-NON-ARITHMETIC

(*)-mindev-:-take-input-value-with-minimum-deviation.

The-output-pixel-value-is-that-value-of-the-input1-or-input2-
images,-that-differs-the-least-from-the-input3-pixel-value.-If-no-
output-image-is-specified-the-output-overwrites-input3.

if-|input3-value---input1-value|-<-|input3-value---input2-value|
----output-=-input1
else
----output-=-input2


command:-mindev-input1_im,input2_im,input3_im,output-im-
default:-mindev-----A----,----B----,----C----,input3_im-
range--:----------<A-D>--,--<A-D>--,--<A-D>--,--<A-D>


GREY-VALUE-FILTERS
ÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿ
A-pixel-value-in-the-output-image-is-determined-by-the-value-of-
the-pixel-in-the-input-image-together-with-the-pixel-values-in-a-
local-neighbourhood-around-the-pixel.-Both-linear-and-non-linear-
operations-can-be-applied-to-such-a-neighbourhood.-In-AIM-the-
neighbourhoods-are-either-fixed-size-and-fixed-shape:-3x3-
square,or-variable-size-and-shape.
Indicating-horizontal-by--,-vertical-by-|-and-the-diagonals-by-/-
and-\-a-variable-filter-of-size-s-can-have-different-shapes:-
size--x-1|-(shape-=-0-or-4),-size/-x-1\-(shape-=-1-or-5),-size|-x-
1--(shape-=-2-or-6),-size\-x-1/-(shape-=-3-or-7),-size--x-size|-
(square,-shape-=-8),-size/-x-size\-(diamond,-shape-=-9),-and-in-
some-cases-approximately-round-rings-with-diameter-s-(shapes-10-
17).

APPLICATIONS

Different-tasks-in-image-processing-can-be-defined.-Each-task-can-
be-performed-by-different-filters.-The-main-tasks-are
1.-make-the-image-less-sharp-("smoothing")-
2.-represent-slope-strength-("gradient")-
3.-extract-detail-("detail")
4.-enhance-detail-("crispening")
5.-extract-edges-or-high-contrast-areas-("edge")-
6.-find-local-extrema-("min",-"max")

SURVEY-GREY-FILTERS-----------------------------------------
€ÿÿÿÿÿÿÿÿ|ÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿ|
--------|-------------non-adaptive---------------------adaptive-|------------------
        |      linear              non-linear               ----|
size----|-------------------------------------------------------|
&-shape-|-fixed------variable---fixed------variable-------------|
--------|-------------------------------------------------------|
smooth--|-gauss------uniform----median-----dyt-tet-----kuwahara-|
--------|------------lgauss-------------------------------------|
--------|------------adne,adre----------------------------------|
--------|-------------------------------------------------------|
gradient|-gradx,y----lgradient----x---------x---x---x--kugradien*
--------|------------ggradient----------------------------------|
--------|------------sune,sure----------------------------------|
--------|-------------------------------------------------------|
detail--|-laplace----parabola---peak-------dyg-teg-rag-vanefilte*
--------|-dog--------ori-smooth-ori-smooth-dys-tes-ras----------|
--------|-------------------------------------------------------|-------------------
crisp---|-filter(df)-ori+detail-have-------dyf-tef-raf-ori+detail
--------|-ori+detail--------------------------------------------|
--------|-------------------------------------------------------|
contrast|-roberts----lgradient8------------dyr-ter-rar----------|
/-edge--|-----------------------hara-------dyl-tel-ral----------|
--------|-------------------------------------------------------|
min-----|---contrast-detail-----------------lmin-low------------|
max-----|---contrast+detail-----------------lmax-upp------------|
--------|-------------------------------------------------------|
general-|-filter-----separable----x--------------------edgps----|
purpose-|------------(+recurs)----------------------------------|--
ÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿÿ-
*-not-yet-implemented;-df-default;-x-impossible;---absent.

IMPLEMENTATION

--Separable-filters.-Filters-that-can-be-replaced-by-a-one-
dimensional-filtering-of-each-image-line-followed-by-a-one-
dimensional-filtering-of-each-(resulting)-column-are-called-
separable.-They-work-on-a-rectangular-or-square-neighbourhood.-
Examples-are-the-linear-'uniform'-filter-and-the-non-linear-
'l(ocal)maximum'-filter.-In-AIM-this-separation-has-been-exploi
ted-to-speed-up-variable-size-filtering.-The-one-dimensional-
filters-used-can-also-be-applied-one-by-one-along-horizontal,-
vertical-and-both-diagonal-directions.-Combining-diagonal-direc
tions-yields-a-diamond-neighbourhood.
--Sum-of-separable-filters.-The-sum-of-two-separable-filters-
without-a-common-one-dimensional-component-belong-to-a-special-
class-of-non-separable-filters.-In-AIM-their-construction-from-
one-dimensional-filters-is-sometimes-but-not-always-used.-Exam
ples-are-the-non-linear-'dyt'-(dynamic-threshold)-and-the-linear-
'laplace',-respectively.-In-AIM-a-not-separated-filter-is-always
a-fixed-size-3x3-filter-or-its-repeated-version-(e.g.-'dog',-
difference-of-gaussians).-In-principle-any-linear-filter-is-a-sum-
of-separable-filters,-to-be-found-by-singular-value-decomposi
tion.-This-has-not-been-implemented-in-AIM.-Also-other-functions-
of-linear-filters-may-occur,-like-the-maximum-of-absolute-values-
€in-the-2-D-l(ocal)gradient-(a-la-Roberts).---Non-separable-
filters.-Some-non-linear-filters-are-not-known-to-be-reducible-to-
one-dimensional-filters.-An-example-is-the-'median'-filter.

LINEAR,-FIXED-SIZE&SHAPE

A-linear-filter-can-be-realized-by-multiplying-a-pixel-and-its-
neighbourhood-by-coefficients.-The-result-is-the-sum-of-these-
multiplica-tions-and-is-called-a-convolution.-Examples-of-linear-
filters-are-the-'gauss',-'gradient'-and-'laplace'-filters.

In-AIM-the-size-of-linear-filters-is-limited-to-a-3x3-neighbour
hood.-'Filter'-is-a-rotation-symmetrical-3x3-filter-of-which-the-
coefficients-can-be-specified-by-the-user.-In-the-'gauss',-
'gradient'-and-'laplace'-filters-the-coefficients-are-fixed.

The-coefficients-are-:

1---2----1---------1---0---1--------1---2---1-------0---1---0---------
2---4---2--------2---0---2--------0---0---0-------1---4---1---------
1---2---1--------1---0---1--------1---2---1-------0---1---0-----------
gauss---------x-gradient-------y-gradient--------laplace
----------
cd--chv-cd----0--1--0----0--0--1----0--1--0----1--0--0---1--0--0
chv-cc--chv---1--5--1----0--0--0----1--0--0----0--0--0---0--1--0
cd--chv-cd----0--1--0----1--0--0----0--0--0----0--0--1---0--0--0
---filter----(default)---grad/-3----grad/-2----grad\-3---grad\2-
                          ---------------roberts-----------------
 
   
gauss-:-linear-filter-for-smoothing.

-The-first-parameter-is-the-input-image-(default-A)-and-the-
second-parameter-is-the-output-image-(default-B).-The-filtering-
can-be-repeated-(size-1)/2-1-more-times-and-then-emulates-a-size-
x-size-binomial-filter,-an-approximation-of-the-actual-gauss-
filter.
The-third-parameter-is-the-size-(2n+2=2n+1,-default-3).

output-image-=-gauss(gauss(gauss...(gauss(input-image-))...))-
command-:-gauss--input-image-,-output-image-,-size
default-:-gauss--------A-----,-----B--------,--3
range---:------------<A-D>---,---<A-D>------,-<3-255>


gradx-:-horizontal-"Sobel"-gradient-filter.

The-first-parameter-is-the-input-image-(default-A)-and-the-second-
parameter-is-the-output-image-(default-B).-The-output-image-may-
be-multiplied-by-a-factor-(multiply/1024)-and-a-constant-(add)-
may-be-added-to-the-result.
output-image-=-gradx(input-image-)-*-(multiply-/-1024)-+-add

command-:-gradx--input-image-,-output-image-,-multiply,---add
€default-:-gradx--------A-----,-----B--------,---1024--,---128
range---:------------<A-D>---,---<A-D>------,<1-10000>,<-255-255>


grady-:-vertical-"Sobel"-gradient-filter.

The-first-parameter-is-the-input-image-(default-A)-and-the-second-
parameter-is-the-output-image-(default-B).-The-output-image-may-
be-multiplied-by-a-factor-(multiply/1024)-and-a-constant-(add)-
may-be-added-to-the-result.

output-image-=-grady(input-image-)-*-(multiply-/-1024)-+-add

command-:-grady--input-image-,-output-image-,-multiply,---add
default-:-grady--------A-----,-----B--------,---1024--,---128
range---:------------<A-D>---,---<A-D>------,<1-10000>,<-255-255>

enhance-:-linear-filter-for-image-detail-enhancement.

This-is-the-previous-laplace-operation.-The-first-command-
parameter-is-the-input-image-and-the-second-parameter-is-the-
output-image.-Defaults-are:-A-for-the-input-image-and-B-for-the-
output-image.

command-:-enhance-input-image-,-output-image
default-:-enhance------A------,-----B
range---:------------<A-D>----,---<A-D>

nlaplace-:-linear-filter-for-image-detail-extraction.

The-first-command-parameter-is-the-input-image-and-the-second-
parameter-is-the-output-image.-Defaults-are:-A-for-the-input-image-
and-B-for-the-output-image.

command-:-nlaplace-input-image-,-output-image
default-:-nlaplace------A------,-----B
range---:------------<A-D>----,---<A-D>

dog-:-difference-of-gaussians,-linear-filter-for-image-detail-
extraction.

The-first-command-parameter-is-the-input-image-and-the-second-
parameter-is-the-output-image.-Defaults-are:-A-for-the-input-
image-and-B-for-the-output-image.-The-third-and-fourth-parameters-
the-are-sizes-of-the-largest-and-smallest-gauss-(binomial)-filter-
(2s+2=2s+1,-defts.-3,1).

output-image-=-gauss(input-image,s)---gauss(input-image,l)-+127
-
command-:-dog-input-image-,-output-image-,-large-l,---small-s
default-:-dog------A-----,-----B-------,---3--,--1(original)
range---:--------<A-D>---,----<A-D>-----,-<3,255>,-<1,sl-1>


€roberts:-3x3-or-2x2-Roberts-gradient-filter.

The-first-parameter-is-the-input-image-(default-A)-and-the-second-
parameter-is-the-output-image-(default-B).-The-third-parameter-
indicates-size-3x3-(3,-default)-or-2x2-(2).

output-image-=-pointmaximum(abs(grad/),abs(grad\))
command-:-gradx--input-image-,-output-image-,-size
default-:-gradx--------A-----,-----B--------,---3
range---:------------<A-D>---,---<A-D>------,-<2-3>


filter-:-general-purpose-3x3-rotation-symmetrical-filter.

This-filter-performs-a-general-3x3-rotation-symmetrical-convolu
tion.-Parameters-are-the-input-image,-the-output-image-and-the-3-
different-coefficients-in-a-3x3-neighbourhood.-The-coefficient-of-
the-central-pixel-is-cc,-the-coefficients-of-the-horizontal-and-
vertical-neighbours-are-chv-and-the-coefficients-of-the-diagonal-
neighbours-are-cd.-The-defaults-(5,--1,-0)-are-chosen-so-as-to-
give-the-crisp-sum-'original+laplace'.
The-result-may-be-multiplied-by-a-factor-(multiply-/-1024)-and-a-
constant-(add)-may-be-added-to-the-result.

output-image-=-filter(input-image-)-*-(multiply/1024)-+-add

command-:-filter-input-image,output-image,cd,chv,cc,multiply,add
default-:-filter------A-----,----B----,-0,--1,-5,----2048,----0
range---:-----------<A-D>---,---<A-D>-,<-/+1000>,-<10000>,<-+255>


LINEAR,-VARIABLE-SIZE&SHAPE

For-even-size-the-result-is-shifted-over-1/2-pixel-with-respect-
to-the-filter-center.


unif-:-linear-filter-for-smoothing.

This-filter-determines-for-each-pixel-the-average-of-a-local-
neighbour-hood-in-the-input-image.-This-average-becomes-the-pixel-
value-in-the-output-image.
The-first-parameter-is-the-input-image,-the-second-parameter-is-
the-output-image.-The-third-parameter-is-the-size-of-the-local-
neighbourhood.-This-size-is-a-value-between-1-and-127.-The-fourth-
parameter-is-the-shape:-0,4=-;-1,5=/;-2,6=|;-3,7=\;-8=+,-9=X.-
Round-shapes-have-not-yet-been-implemented.


command-:-unif-input-image,output-image,neighbourhood-size,shape
default-:-unif------A-----,-----B------,-------3----------,--8
range---:---------<A-D>---,---<A-D>----,-----<1,63>-------,<0,9>

lgau-:-linear-filter-for-smoothing.
€
This-filter-determines-for-each-pixel-the-weighted-average-of-a-
local-neighbourhood-in-the-input-image.-The-binomial-coefficients-
are-used-as-weights.-This-average-becomes-the-pixel-value-in-the-
output-image.
The-square-version-is-far-better-isotropic-than-square-unif.
The-first-parameter-is-the-input-image,-the-second-parameter-is-
the-output-image.-The-third-parameter-is-the-size-of-the-local-
neighbour-hood.-This-size-is-a-value-between-1-and-63.-The-fourth-
parameter-is-the-shape.-Round-shapes-are-not-needed-and-have-not-
been-implemented.


command-:-lgau-input-image,output-image,neighbourhood-size,shape
default-:-lgau------A------,-----B-----,--------3---------,--8
range---:---------<A-D>----,---<A-D>---,------<1,63>------,<0,9>


adne-:-linear-filter-for-smoothing.

This-filter-adds-to-each-pixel-in-the-input-image-the-value-(or-
half-or-a-quarter-etc.)-of-its-left-neighbour-(if-shape=0)-in-the-
input-image.-The-sum-(or-in-case-of-overflow-sum-256)-becomes-the-
pixel-value-in-the-output-image.-The-first-pixel-of-each-line-(if-
shape=0)-is-copied-unprocessed.-The-first-parameter-is-the-input-
image,-the-second-parameter-is-the-output-image.-The-third-
parameter-indicates-which-part-of-the-neighbour-is-added:-0->
full,-1->half,-2->quarter,-k->-1/(2**k),-7->-1/128.-The-fourth-
parameter-is-the-shape-and-also-the-Freeman-direction.-0->E(ast),-
1->NE,-2->N,-3->NW,-4->W,-5->SW,-6->S,-7->SE.
2-D-filters-are-combined-from-these:-8->0,2,4,6;-9->1,3,5,7.-
No-round-shapes.-"adne"-is-the-exact-inverse-of-"sure".


command-:-adne-input-image,output-image,neighbour-part,shape
default-:-adne------A------,----B-----,------0-------,--0
range---:---------<A-D>----,--<A-D>----,----<0,7>-----,<0,9>

adre-:-recursive-linear-filter-for-smoothing.

This-filter-adds-to-each-pixel-in-the-input-image-the-value-(or-
half-or-a-quarter-etc.)-of-its-left-neighbour-(if-shape=0)-in-the-
output-image.-The-sum-(or-in-case-of-overflow-sum-256)-becomes-
the-pixel-value-in-the-output-image.-The-first-pixel-of-each-line-
(if-shape=0)-is-copied-unprocessed.-The-first-parameter-is-the-
input-image,-the-second-parameter-is-the-output-image.-The-third-
parameter-indicates-which-part-of-the-neighbour-is-added:-0->
full,-1->half,-2->quarter,-k->-1/(2**k),-7->-1/128.-The-fourth-
parameter-is-the-shape-and-also-the-Freeman-direction.-0->E(ast),-
1->NE,-2->N,-3->NW,-4->W,-5->SW,-6->S,-7->SE.-2-D-filters-are-
combined-from-these:-8->6,4,2,0;-9->7,5,3,1.-No-round-shapes.-
"adre"-is-the-exact-inverse-of-"sune".

command-:-adre-input-image,output-image,neighbour-part,shape
€default-:-adre------A-----,----B------,------0-------,--0
range---:---------<A-D>---,--<A-D>----,----<0,7>-----,<0,9>

lgra-:-linear-gradient-filter.

This-filter-determines-for-each-pixel-the-slope-a-of-the-best-fit-
first-degree-polynomial-(ax+b)-over-a-local-neighbourhood-in-the-
input-image.-This-slope-becomes-the-pixel-value-in-the-output-
image;-normally-it-is-scaled-so-that-the-largest-step-up-(0-0-0-0-
255-255-255-255)-produces-output-127+127,-the-largest-step-down-
127-127.-The-first-parameter-is-the-input-image,-the-second-
parameter-is-the-output-image.-The-third-parameter-is-the-size-of-
the-local-neighbour-hood.-This-size-is-a-value-between-1-and-127.-
A--sign-enforces-exact-slope-scaling.-The-fourth-parameter-is-the-
shape.-2-D-shapes-(square-8,-diamond-9)-give-maximum-of-absolute-
slopes-a-la-Roberts-(8->0,2;-9->1,3).-No-round-shapes.-

command-:-lgra-input-image,output-image,neighbourhood-size,shape
default-:-lgra------A------,-----B-----,--------3---------,--8
range---:---------<A-D>----,---<A-D>---,------<1,127>-----,<0,9>

ggra:-linear-gradient-filter.

This-filter-is-equivalent-to-lgau-followed-by-sune-(full-
subtraction).-The-first-parameter-is-the-input-image,-the-second-
parameter-is-the-output-image.-The-third-parameter-is-the-size-of-
the-local-neighbour-hood.-This-size-is-a-value-between-1-and-127.-
The-fourth-parameter-is-the-shape.-2-D-shapes-(square-8,-diamond-
9)-give-maximum-of-absolute-slopes-a-la-Roberts-(8->0,2;-9->1,3).-
No-round-shapes.-

command-:-ggra-input-image,output-image,neighbourhood-size,shape
default-:-ggra------A------,-----B-----,--------3---------,--8
range---:---------<A-D>----,---<A-D>---,------<1,127>-----,<0,9>




sune-:-linear-gradient-filter.

This-filter-subtracts-from-each-pixel-in-the-input-image-the-
value-(or-half-or-a-quarter-etc.)-of-its-left-neighbour-(if-
shape=0)-in-the-input-image.-The-sum-(or-in-case-of-underflow-sum-
+256)-becomes-the-pixel-value-in-the-output-image.-The-first-
pixel-of-each-line-(if-shape=0)-is-copied-unprocessed.-The-first-
parameter-is-the-input-image,-the-second-parameter-is-the-output-
image.-The-third-parameter-indicates-which-part-of-the-neighbour-
is-subtracted:-0->full,-1->half,-2->quarter,-k->-1/(2**k),-7->-
1/128.-The-fourth-parameter-is-the-shape-and-also-the-Freeman-
direction.-0->E(ast),-1->NE,-2->N,-3->NW,-4->W,-5->SW,-6->S,-7-
>SE.-2-D-filters-are-combined-from-these:-8->0,2,4,6;-9->1,3,5,7.-
No-round-shapes.-"sune"-is-the-exact-inverse-of-"adre"-and-even-
compensates-its-overflow-effects.

€command-:-sune-input-image,output-image,neighbour-part,shape
default-:-sune------A------,-----B-----,------0-------,--0
range---:---------<A-D>----,--<A-D>---,----<0,7>-----,<0,9>

sure-:-recursive-linear-gradient-filter.

This-filter-subtracts-from-each-pixel-in-the-input-image-the-
value-(or-half-or-a-quarter-etc.)-of-its-left-neighbour-(if-
shape=0)-in-the-output-image.-The-sum-(or-in-case-of-underflow-
sum+256)-becomes-the-pixel-value-in-the-output-image.-The-first-
pixel-of-each-line-(if-shape=0)-is-copied-unprocessed.-The-first-
parameter-is-the-input-image,-the-second-parameter-is-the-output-
image.-The-third-parameter-indicates-which-part-of-the-neighbour-
is-subtracted:-0->full,-1->half,-2->quarter,-k->-1/(2**k),-7->-
1/128.-The-fourth-parameter-is-the-shape-and-also-the-Freeman-
direction.-0->E(ast),-1->NE,-2->N,-3->NW,-4->W,-5->SW,-6->S,-7-
>SE.-2-D-filters-are-combined-from-these:-8->6,4,2,0;-9->7,5,3,1.-
No-round-shapes.-"sure"-is-the-exact-inverse-of-"adne"-and-even-
compensates-its-overflow-effects.

command-:-sure-input-image,output-image,neighbour-part,shape
default-:-sure------A------,-----B-----,------0-------,--0
range---:---------<A-D>----,--<A-D>---,----<0,7>-----,<0,9>


para-:-linear-detail-extracting-filter.

This-filter-determines-for-each-pixel-the-coefficient-a-of-the-
best-fit-second-degree-polynomial-(ax2+b)-over-a-local-neighbour
hood-in-the-input-image.-This-coefficient-becomes-the-pixel-value-
in-the-output-image;-normally-it-is-scaled-so-that-the-largest-
trough-(255-255-255-0-...-0-255-255-255-255)-produces-output-
127+127,-the-largest-ridge-127-127.-The-first-parameter-is-the-
input-image,-the-second-parameter-is-the-output-image.-The-third-
parameter-is-the-size-of-the-local-neighbourhood.-This-size-is-a-
value-between-1-and-127.-A--sign-enforces-exact-coefficient-
scaling.-The-fourth-parameter-is-the-shape.-2-D-shapes-(square-8,-
diamond-9)-give-maximum-of-absolute-slopes-a-la-Roberts-(8->0,2;-
9->1,3).-No-round-shapes.

command-:--lgra-input-image,output-image,neighbourhood-size,shape
default-:-lgra------A------,-----B-----,--------3---------,--8
range---:---------<A-D>----,---<A-D>---,------<1,127>-----,<0,9>

sepa:-general-purpose-linear-filter

This routine performs a one-dimensional filtering; the-first-
parameter-(filter)type can be min=0,-max=1,-unif=2,-
lgau(=binom)=4,-adne(=add neighb)=10,--adre(=recursive adne)=12,-
lgra(=linfit)=6,-sune(=sub neighb)=11,-sure(=recursive sune)=13,-
para(=quadfit)=8,-recu(=3point recursive filtering)=14,-defined-
as  out-=-b0*in-+b1*in_1-+b2*in_2--a1*out_1--a2*out_2--a3*out_3.
The-second-and-third-parameter-are-input-and-output-image.-The-
fourth-parameter-is f(ilter)size, even size gives 1/2 pixel-wrap-
€ped output-in the f(ilter)dir(ection) indicated by the-fifth-pa-
rameter; fdir can be 0=E(astwd),1=NE,2=N,3=NW,4=W,5=SW,6=S,7=SE;-
the-sixth-through-eleventh-parameters-are-b0,b1,b2,a1,a2,a3.

diagonal scanning goes as follows:                 
             SE scan  xsize = 10, ysize = 8         
                              11   *      7 = 77    
                                                    
     1  8 15 22 29 36 43 50 57 64                   
    71  2                      58                  
    65 72  3                   52                   
    59    73  4                46                   
    53       74  5             40                   
    47          75  6       27 34                   
    41             76  7 14 21 28                   
    35 42 49 56 63 70 77 -  -  -                    

             SW scan  xsize = 10, ysize = 8         
                               9   *      9 = 81    
                                                    
-   18  9 18 55 46 37 28 19 10  1                   
     -                       2 11                   
    66                    3    52                   
    58                 4       46                   
    50              5          40                   
    42           6          27 34                   
-   34        7                                     
    26 17  8 17             -  -                    

command:-sepa-type,in-im,outim,---fsize--,-fdir,a1,a2,a3,b0,b1,b2
default:-sepa--2--,--A--,--B--,-----3----,--0--,-0,-0,-0,-0,-0,-0
range--:----<0,14>,<A-D>,<A-D>,<-127,127>,<0,7>,-<---127-,-127-->



   out-=-b0*in-+b1*in_1-+b2*in_2--a1*out_1--a2*out_2--a3*out_3 



NON-LINEAR-FILTERS

Non-linear-filters-perform-image-operations-which-are-impossible-
with-linear-filters.-Noise-can-be-suppressed-with-a-non-linear-
filter-without-deteriorating-edges-in-an-image.-The-median-
filter,-Schlag's-peak-filter,-the-local-minimum-and-maximum-
filters-and-their-relatives-(the-max/min-family-including-the-
PAPS-dynamic-threshold-"dyt"-and-the-Lee-Haralick-edge-filter-
"dyl"-and-"hara")-are-implemented-in-AIM.

NON-LINEAR-FIXED-SIZE&SHAPE

medi-:-median-filter.

The-median-filter-determines-for-each-pixel-the-median-(the-
€middle)-value-of-a-local-(3x3)-neighbourhood-in-the-input-image.-
This-median-value-becomes-the-pixel-value-in-the-output-image.
This-filter-suppresses-noise.

The-first-parameter-is-the-input-image,-the-second-parameter-is-
the-output-image.

command-:-medi-input-image-,output-image
default-:-medi------A------,-----B--
range---:----------<A-D>----,---<A-D>-


peak-:-ridge-finding-filter.

The-peak-filter-(John-Schlag)-determines-for-each-pixel-if-it-is-
a-1-D-maximum-along-the--,-/,-|-and-\-direction.-If-this-is-true-
for-"num"-or-more-directions-and-if-the-pixel-value-is-above-
"thresh"-the-output-pixel-is-given-the-value-"val"-else-0.

The-first-parameter-is-the-input-image,-the-second-parameter-is-
the-output-image,-the-third-parameter-is-the-number-of-directions-
in-which-the-pixel-must-be-max-in-order-that-it-may-be-peak,-the-
fourth-parameter-is-the-threshold-above-which-the-pixel-can-be-
peak,-the-fifth-parameter-is-the-value-written-at-peak-positions.

command-:-peak-input-image,-output-image,-number,-thresh,-value
default-:-peak------A-----,------B--    ,----2  ,---0---,--255
range---:---------<A-D>---,----<A-D>----,--<0,4>,<0,255>,<0,255>


(*)hara-:-non-linear-edge-filter.

The-filter-hara-performs-a-variant-(Lucas-van-Vliet)-of-the-3x3-
Lee--Haralick-edge-filter-(Patt.-Rec.-Conf.,-Paris-'86).
This-filter-is-based-upon-the-weighted-difference-between-the-
original-image-and-the-local-minimum-and-local-maximum-filtered-
images.

The-first-command-parameter-is-the-input-image-and-the-second-
parameter-is-the-output-image.-Defaults-are:-A-for-the-input-
image-and-B-for-the-output-image.

command-:-hara-input-image-,-output-image
default-:-hara------A------,-----B
range---:---------<A-D>----,---<A-D>

(*)have-:-non-linear-laplace-like-filter.

The-filter-have-performs-a-non-linear-laplace-like-like-operation-
inspired-by-the-3x3-Lee--Haralick-edge-filter-(Patt.-Rec.-Conf.,-
Paris-'86).
Adding-the-have-result-to-the-original-gives-sharpening-as-in-the-
linear-laplace-filter.
This-filter-is-based-upon-the-weighted-difference-between-the-
€original-image-and-the-local-minimum-and-local-maximum-filtered-
images.

The-first-command-parameter-is-the-input-image-and-the-second-
parameter-is-the-output-image.-Defaults-are:-A-for-the-input-
image-and-B-for-the-output-image.

command-:-have-input-image-,-output-image
default-:-have------A------,-----B
range---:---------<A-D>----,---<A-D>


NON-LINEAR,-VARIABLE-SIZE&SHAPE

lmin:-local-minimum-filter.

The-minimum-filter-determines-for-each-pixel-the-minimum-of-a-
local-neighbourhood-in-the-input-image.-This-minimum-becomes-the-
pixel-value-in-the-output-image.-This-operation-results-in-an-
extension-of-the-dark-parts-in-an-image.-This-operation-is-also-
called-grey-value-erosion.
The-first-parameter-is-the-input-image,-the-second-parameter-is-
the-output-image.-The-third-parameter-is-the-size-of-the-local-
neighbourhood.-This-size-is-a-value-between-1-and-127.-This-size-
is-a-value-between-1-and-127.-The-fourth-parameter-is-the-shape:-
0,4=-;-1,5=/;-2,6=|;-3,-7=\;-8=+;-9=X;-10=sparse-circular-cordon;-
11=10+centre;12=10stamping;13=11stamping;14=circular-ring;-15=14+-
centre;-16=14stamping;17=15stamping.-The-operation-is-illustrated-
in-@demo5-and-@demo7.

command-:-lmin-input-image-,output-image,neighb-size,-shape
default-:-lmin------A------,-----B------,-----3   --,---8
range---:---------<A-D>----,---<A-D>----,--<1,127>  , <0,17>

lmax-:-local-maximum-filter.

The-maximum-filter-determines-for-each-pixel-the-maximum-of-a-
local-neighbourhood-in-the-input-image.-This-maximum-becomes-the-
pixel-value-in-the-output-image.-This-operation-results-in-an-
extension-of-the-bright-parts-of-an-image.-This-operation-is-also-
called-grey-value-dilation.
The-first-parameter-is-the-input-image,-the-second-parameter-is-
the-output-image.-The-third-parameter-is-the-size-of-the-local-
neighbourhood.-This-size-is-a-value-between-1-and-127.-The-fourth-
parameter-is-the-shape:-0,4=-;-1,5=/;-2,6=|;-3,7=\;-8=+,-9=X;-
10=sparsecircularcordon;11=10+centre;12=10stamping;13=11stamping;-
14=circular-ring;-15=14+centre;-16=14stamping;-17=15stamping.

command-:-lmax-input-image-,output-image,neighb-size,-shape
default-:-lmax------A------,-----B------,-----3   --,---8
range---:---------<A-D>----,---<A-D>----,--<1,127>  , <0,17>

MAX/MIN-FAMILY
All-filters-in-the-max/min-family-are-combinations-of-lmax-and-
€lmin-filters,-the-size-and-shape-of-which-can-be-specified.-The-
input-image-is-always-A,-the-output-image-always-B.-
Intermediate-results-are-stored-in-C-(most-cases)-and-in-D-(many-
cases).-Due-to-the-concatenation-of-filter-steps-the-effective-
size-of-the-total-filter-will-be-correspondingly-larger.
-
low:-lower-envelope-filter

The-lower-envelope-filter-removes-small-peaks-and-follows-smooth-
ramps.-It-consists-of-lmin-followed-by-lmax:-low-=-lmax(lmin).

command-:-low--input-image-,output-image,neighb-size,-shape
default-:-low-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

upp:-upper-envelope-filter

The-upper-envelope-filter-removes-small-dips-and-follows-smooth-
ramps.-It-consists-of-lmax-followed-by-lmin:-upp-=-lmin(lmax).

command-:-upp--input-image-,output-image,neighb-size,-shape
default-:-upp-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

dyt:-dynamic-threshold-filter

The-dynamic-threshold-filter-(Bernsen,-Philips-PAPS)-is-a-non-
linear-smoothing-filter-that-provides-a-local-threshold-in-shaded-
images.-Applying-it-as-a-threshold-brings-out-detail.-It-consists-
of-the-average-of-lmin-and-lmax:-dyt-=-(lmin-+-lmax)/2.

command-:-dyt--input-image-,output-image,neighb-size,-shape
default-:-dyt-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

tet:-texture-threshold-filter

The-texture-threshold-filter-is-a-non-linear-smoothing-filter-
that-provides-a-local-threshold-in-shaded-images-while-following-
ramps.-Applying-it-as-a-threshold-brings-out-texture-detail-but-
no-ramp-detail.-There-is-no-linear-equivalent-for-this.-The-
filter-consists-of-the-average-of-low-and-upp:
tet-=-(low-+-upp)/2.-Noise-is-handled-as-texture:-reduced-by-tet.

command-:-tet--input-image-,output-image,neighb-size,-shape
default-:-tet-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

dyg:-dynamic-gist-filter

The-dynamic-gist-(=essence)-filter-is-a-non-linear-detail-
extracting-filter.-It-subtracts-the-dynamic-threshold-from-the-
original.-While-PAPS-dynamic-thresholding-gives-the-sign-of-the-
difference-as-a-binary-output,-dyg-gives-the-difference-as-grey-
€value-output:-dyg-=-ori---dyt.

command-:-dyg--input-image-,output-image,neighb-size,-shape
default-:-dyg-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

teg:-texture-gist-filter

The-texture-gist-(=essence)-filter-is-a-non-linear-texture-detail-
extracting-filter-that-ignores-ramp-detail.-There-is-no-linear-
equivalent-for-this.-The-filter-subtracts-the-texture-threshold-
from-the-original:-teg-=-ori---tet.-Noise-is-handled-as-texture:-
extracted-by-teg.

command-:-teg--input-image-,output-image,neighb-size,-shape
default-:-teg-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

rag:-ramp-gist-filter

The-ramp-gist-(=essence)-filter-is-a-non-linear-ramp-detail-
extracting-filter-that-ignores-texture-detail.-There-is-no-linear-
equivalent-for-this.-The-filter-subtracts-the-texture-gist-from-
the-total-dynamic-gist-:-rag-=-dyg---teg.-Noise-is-handled-as-
texture:-reduced-by-rag.-For-noisy-images-rag-is-better-than-dyg.

command-:-rag--input-image-,output-image,neighb-size,-shape
default-:-rag-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>


dyl:-dynamic-Lee-edge-filter

The-Lee-Haralick-Shapiro-filter-is-a-non-linear-edge-filter.-It-
gives-the-absolute-difference-of-the-original-with-the-local-
minimum-or-the-local-maximum,-whichever-is-smallest:-
dyl-=-pmin(lmax-ori,ori-lmin).-

command-:-dyl--input-image-,output-image,neighb-size,-shape
default-:-dyl-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

tel:-texture-Lee-edge-filter

This-variant-of-the-Lee-Haralick-Shapiro-filter-is-a-non-linear-
texture-edge-filter.-It-gives-the-absolute-difference-of-the-
original-with-the-lower-or-upper-envelope,-whichever-is-smallest:-
tel-=-pmin(upp-ori,ori-low).-At-ramps-these-differences-are-both-
small.-Noise-is-handled-like-texture:-extracted-by-tel.

command-:-tel--input-image-,output-image,neighb-size,-shape
default-:-tel-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

€ral:-ramp-Lee-edge-filter

This-variant-of-the-Lee-Haralick-Shapiro-filter-is-a-non-linear-
ramp-edge-filter.-It-gives-the-absolute-difference-of-the-local-
minimum-with-the-lower-envelope-or-the-absolute-difference-of-the-
local-maximum-with-the-upper-envelope,-whichever-is-smallest:
ral-=-pmin(lmax-upp,low-lmin).-At-ramps-these-differences-are-
both-small.-Noise-is-handled-like-texture:-reduced-by-ral.-In-
noisy-images-ral-is-better-than-dyl.

command-:-ral--input-image-,output-image,neighb-size,-shape
default-:-ral-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

dys:-dynamic-signed-Lee-filter
his-variant-of-the-Lee-Haralick-Shapiro-filter-is-a-non-linear-
detail-extracting-filter.-Unlike-dyg-(and-linear-laplace)-it-
represents-detail-by-very-sharp-extremes.-Starting-out-from-dyl-
one-gets-dys-by-adding-the-sign:-+-if-original-nearer-to-local-
maximum,---if-nearer-to-minimum:-dys-=-smin(lmax-ori,ori-lmin).-

command-:-dys--input-image-,output-image,neighb-size,-shape
default-:-dys-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

tes:-texture-signed-Lee-filter

This-variant-of-the-Lee-Haralick-Shapiro-filter-is-a-non-linear-
texture-detail-extracting-filter.-There-is-no-linear-equivalent-
for-this.-Unlike-teg-it-represents-detail-by-very-sharp-extremes.-
Starting-out-from-tel-one-gets-tes-by-adding-the-sign:-+-if-
original-nearer-to-upper-envelope,---if-nearer-to-lower-envelope:-
tes-=-smin(upp-ori,ori-low).-At-ramps-these-differences-are-both-
small.-Noise-is-handled-like-texture:-extracted-by-tes.

command-:-tes--input-image-,output-image,neighb-size,-shape
default-:-tes-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

ras:-ramp-signed-Lee-filter

This-variant-of-the-Lee-Haralick-Shapiro-filter-is-a-non-linear-
ramp-detail-extracting-filter.-There-is-no-linear-equivalent-for-
this.-Unlike-rag-it-represents-detail-by-very-sharp-extremes.-
Starting-out-from-ral-one-gets-tes-by-adding-the-sign:-+-if-local-
maximum-nearer-to-upper-envelope,---if-local-minimum-nearer-to-
lower-envelope:-ras-=-smin(lmax-upp,low-lmin).-At-texture-these-
differences-are-both-small.-Noise-is-handled-like-texture:-
reduced-by-ras.-In-noisy-images-ras-is-better-than-dys.

command-:-ras--input-image-,output-image,neighb-size,-shape
default-:-ras-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

€dyf:-dynamic-front-Lee-filter

This-variant-of-the-Lee-Haralick-Shapiro-filter-is-a-non-linear-
crispening-filter.-Edges-are-shaped-into-steps.-Like-adding-
linear-laplace-here-non-linear-dys-is-added-to-the-original:-
dyf-=-ori-+-dys.-

command-:-dyf--input-image-,output-image,neighb-size,-shape
default-:-dyf-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

tef:-texture-front-Lee-filter

This-variant-of-the-Lee-Haralick-Shapiro-filter-is-a-non-linear-
texture-crispening-filter.-Texture-edges-are-shaped-into-steps.-
There-is-no-linear-equivalent-for-this.-Like-adding-dys-here-tes-
is-added-to-the-original:
tef-=-ori-+-tes.-At-ramps-tes-is-small.-Noise-is-handled-like-
texture:-extracted-by-tef.

command-:-tef--input-image-,output-image,neighb-size,-shape
default-:-tef-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

raf:-ramp-front-Lee-filter

This-variant-of-the-Lee-Haralick-Shapiro-filter-is-a-non-linear-
ramp-crispening-filter.-Texture-edges-are-shaped-into-steps.-
There-is-no-linear-equivalent-for-this.-Like-adding-dys-here-ras-
is-added-to-the-original:
raf-=-ori-+-ras.-At-texture-ras-is-small.-Noise-is-handled-like-
texture:-reduced-by-raf.-In-noisy-images-raf-is-better-than-dyf.

command-:-raf--input-image-,output-image,neighb-size,-shape
default-:-raf-------A------,-----B------,-----3   --,---8
range---:----------<A>-----,----<B>-----,--<1,127>  , <0,17>

ADAPTIVE-FILTERS

Typically,-adaptive-filters-are--composites-of-simple-linear-or-
non-linear-filters.-Their-effect-is-usually-non-linear.-A-simple-
example-would-be-an-X-ray-enhancer-that-applies-crispening-in-
light-areas-only:-one-smoothing-filter-"tastes"-the-grey-value-of-
areas,-the-result-is-used-to-control-a-steerable-crispening-
filter.-More-in-general,-several-tasting-filters-may-collect-
information-transformed-by-a-control-rule-into-a-control-signal-
vector-that-steers-a-steerable-acting-filter,-(e.g.-a-weighted-
filter-bank).-

edgps:-flipping-neighbourhood-mechanism

Van-Antwerpen-introduced-this-mechanism-as-pivotal-part-of-his-
version-of-Kuwahara-edge-preserving-smoothing-(kuwa-in-AIM).-It-
can-be-used-to-generalize-the-kuwa-filter.-The-first-parameter-is-
€a-filtered-image.-The-second-parameter-is-an-image-that-contains-
the-tasted-information.-The-third-parameter-is-the-output-image.-
For-each-output-pixel-the-mechanism-inspects-the-corners-of-a-nxn-
square-(n-is-the-fourth-parameter,-usually-equal-to-the--size-of-
the-filters-used-to-produce-the-input-images)-around-it-(giving-
the-fifth-parameter-(c)-a-non-zero-value-enforces-additional-
inspection-of-the-center-position)-and-selects-the-one-with-least-
tasted-value.-The-value-of-the-filtered-image-at-the-selected-
position-is-written-as-the-output-result.-The-mechanism-mimicks-
the-choice-between-the-results-of-four-(five-if-c!=0)-acting-
filters-(with-as-neighbourhoods-the-upper-left,-upper-right,-
lower-left-and-lower-right-quadrant-with-respect-to-the-output-
pixel,-and-also-a-centered-square-if-c!=0).-This-choice-may-
change-from-one-position-to-the-next:-a-flipping-neighbourhood.-
For-even-n-the-output-position-has-an-1/2,1/2-offset-that-will-
compensate-the-offsets-of-the-filters-used,-if-they-are-South-and-
East-oriented-(as-is-default-in-AIM).
-
command:-edgps-filt'd-im,tasted-im,-output-im,-size--,-center-on
default:-edgps-----A----,----B----,-filt'd-im,---3  -,-----0
range--:---------<A-D>--,--<A-D>--,---<A-D>--,<2,255>,-<-255,255>

kuwa:-edge-preserving-smoothing-filter

Hachimura-&-Kuwahara-proposed-the-flipping-neighbourhood-in-
combination-with-a-variance-filter-as-tasting-filter-and-with-
uniform-smoothing-as-acting-filter.-Areas-that-contain-an-edge-
having-larger-variance-than-others-are-avoided-in-the-smoothing.
Hence-edges-are-preserved.-In-AIM-(according-to-Van-Antwerpen)-
the-dynamic-range-(lmax---lmin)-is-tasted-rather-than-variance.
The-first-parameter-is-the-input-image,-the-second-is-a-
temporary-image-used-as-scratch,-the-third-is-the-output-image.-
The-fourth-parameter-is-the-size-of-the-smoothing-and-tasting-
filters-(even-sizes-allowed).-The-fifth-parameter-if-non-zero-
extends-the-four-quadrants-choice-by-a-center-square-(see-edgps).--

command:-kuwa-input-im,temp-im,output-im,quadrant-size,-center-on
default:-kuwa-----A---,---B---,----C----,------3  ----,-----0
range--:--------<A-D>-,-<A-D>-,--<A-D>--,----<2,15>---,<-255,255>



GREY-VALUE-POINT-OPERATIONS

equal(ization)-:-histogram-equalization.

This-operation-reassigns-the-grey-values-in-an-image-and-results-
in-an-"optimum"-use-of-the-available-grey-values.-The-grey-value-
histogram-of-the-output-image-is-as-flat-as-possible-(given-the-
necessary-requantization).-An-example-is-given-in-@demo1.

command-:-equal-input-image-,-output-image
default-:-equal------A------,-----B
range---:----------<A-D>----,---<A-D>
€
table:-transforms-a-grey-value-image-using-a-look-up-table.

The-grey-value-g-from-the-input-image-(first-parameter)-is-used-
as-table-address,-the-content-found-there-becomes-the-grey-value-
h-in-the-output-image-(second-parameter).-Several-tables-can-be-
generated-(third-parameter,-t;-examples-are-given-in-@demtable):
t=0:-h=g**(j/k);-------------------t=2:-h=(k/g)**j;
t=1:-h=(j/k)**g;---j=0-->-j/k=e;---t=-1:-h=log(g)/log(j/k);-
t=3:-h=atan(k*(g-gj));-------------t=-3:-h=tan(g-j)/k+gj;
t=4:-g=(x+8)+16*(y+8)->h=phi*16/2pi+16*r;--t=-4:-inverse-of-t=4;
t=5:-h=cos(g**j-*k*2pi);-----------t=-5:-h=sin(g**j-*k*2pi);-
t=6:-j=lower,-k=higher-threshold;--t=-6:-8-thresholds-j,j+1,,j+7;
t=7:-h=log(g+1)-log(256-g);--------t=-7:-h=-1+257/(1+exp(-g)); 
t=8:-h=((j/k)**g+(j/k)**-g)/2 -1;|-t=-8:-h=(log(g+1+sqrt((g+1)**2-1)))
               -  j=0 -> j/k=e  ;|-----    /log(j/k);   j=0 -> j/k=e.
t=-8: inverse cosh-1, sqrt at low g,h but log at high g,h:
      pseudo Weber-Fechner law of human visual sensitivity
Fourth-para.(r)-reflects-table:-r=1:-normal;-r=2:-g->-g;-r=3:-h->-
-h;-r=4:-g->-g,-h->-h;-r=5:-g->|g|;-r=6:-g->|g|,-h->-|h|*sgn(g).

thresh[olding]:-transforms-a-grey-value-image-in-a-binary-image.

The-binary-image-is-obtained-by-thresholding-the-input-image.-
After-thresholding-binary-image-operations-may-be-applied.-Pixels-
with-a-grey-value-above-the-threshold-get-the-binary-value-'1'-
and-thus-become-white.-Pixels-with-a-grey-value-below-the-
threshold-get-the-binary-value-'0'-and-become-black.-The-default-
value-of-the-threshold-is-obtained-from-the-grey-value-histogram-
with-the-method-of-Ridler-&-Calvert.

command-:-thresh-input-image-,-output-image-,-bitplane,-threshold
default-:-thresh------A------,------B-------,-----1---,-automatic
range---:-----------<A-D>----,----<A-D>-----,---<1,8>-,--<0,255>-

mcop:-transforms-a-binary-image-into-a-grey-value-image.

mcop-allows-a-binary-image-wanted-to-take-part-in-grey-operations-
to-be-copied-to-all-bitplanes-of-a-grey-image-(1->255).-A-mask-
word-may-restrict-"all"-to-some:-e.g.-255->all,-37->-only-1,3,6.-
Note-that-the-remaining-bitplanes-will-not-be-reset.--

command-:-mcop-input-image-,-output-image-,-input-bitplane,-mask
default-:-mcop------A------,------B-------,--------1------,-255
range---:---------<A-D>----,----<A-D>-----,------<1,8>--,<0,255>-



CELLULAR-LOGIC-(BINARY)-OPERATIONS

These-operations-can-be-applied-to-the-8-bitplanes-of-an-image.-
The-bitplanes-are-numbered-from-1-to-8.-A-black-pixel-has-the-
value-'0',-a-white-pixel-has-the-value-'1'.
The-edge-value-of-the-image-can-be-set-to-'0'-or-'1'-in-all-
€operations.-The-default-value-of-the-image-edge-is-black-(0).-The-
given-number-of-iterations-is-a-maximum.-The-iterations-stop-when-
no-changes-in-the-pixel-values-occur-anymore.
The-number-of-iterations-is-shown-in-that-case.

erosion-:-erodes-white-objects.

One-layer-of-the-white-objects-is-peeled-off-in-each-iteration.-
White-objects-which-are-smaller-than-the-number-of-iterations-*-2-
will-disappear.-The-connectivity-determines-which-white-pixels-
belong-to-a-layer-to-be-peeled-off.-When-the-connectivity-is-4-
this-layer-consists-of-those-white-pixels-that-have-a-horizontal-
or-vertical-black-neighbour.-When-the-connectivity-is-8-a-layer-
consists-of-those-white-pixels-that-have-a-horizontal,-vertical-
or-diagonal-black-neighbour.-When-the-connectivity-is-6-for-the-
odd-iterations-a-4-connectivity-is-used-and-for-the-even-
iterations-an-8-connectivity-is-used.-The-erosion-is-illustrated-
in-@demo6.

command-:-erosion-#iterations,bitplane,connectivity,-edge-,image
default-:-erosion-------1----,----1---,------6-----,---0--,--B
range---:----------<1,512>---,--<1,8>-,--<4,6,8>---,-<0,1>,<A-D>

dilation-:-extends-white-objects.

One-layer-is-added-to-the-white-objects-in-each-iteration.-Black-
parts-such-as-holes-which-are-smaller-than-the-number-of-
iterations-*-2-will-disappear.-The-connectivity-determines-which-
black-pixels-belong-to-a-layer-to-be-added.-When-the-connectivity-
is-4-this-layer-consists-of-those-white-pixels-that-have-a-
horizontal-or-vertical-white-neighbour.-When-the-connectivity-is-
8-a-layer-consists-of-those-black-pixels-that-have-a-horizontal,-
vertical-or-diagonal-white-neighbour.-When-the-connectivity-is-6-
for-the-odd-iterations-a-4-connectivity-is-used-and-for-the-even-
iterations-an-8-connectivity-is-used.

command-:-dilation-#iterations,bitplane,connectivity,edge,image
default-:-dilation-------1----,----1---,-----6------,--0-,--B
range---:-----------<1,512>---,--<1,8>-,--<4,6,8>---,<0,1>,<A-D>

propag[ation]:-dilates-a-bitplane-under-a-mask.

The-propagation-strongly-resembles-the-dilation.-However,-the-
black-pixels-are-only-added-when-they-are-white-(1)-in-the-mask-
bitplane.-The-propagation-can-be-used-to-find-the-original-shapes-
of-objects-which-remained-after-a-number-of-erosion-iterations.-
This-application-is-also-shown-in-@demo6.
The-first-parameter-is-the-number-of-iterations.-The-second-
parameter-is-the-bitplane-of-which-the-dilation-takes-place-(seed-
bitplane).-The-third-parameter-is-the-mask-bitplane.-The-other-
parameters-are-again-the-connectivity-and-the-image-edge-value.-
When-the-edge-value-is-0-only-the-seed-bitplane-is-propagated.-
When-the-edge-value-is-1-only-the-edge-is-propagated-and-when-the-
edge-value-is-2-both-the-edge-and-the-seed-bitplane-are-
€propagated.

command-:-propag-#iterations,bitplane,maskbitplane,connectiv,-
edge,image
default-:-propag-------1----,----1---,------2-----,-----6---,--0--
,--A
range---:---------<1,512>---,--<1,8>-,----<1,8>---,-<4,6,8>-
,<0,2>,<A-D>

skelet-:-skeleton-with-endpixels.

The-skeleton-is-an-1-pixel-thick-line-in-the-middle-of-white-
objects.-The-skeleton-operation-resembles-the-erosion,-but-in-
this-case-pixels-of-a-layer-are-only-deleted,-when-their-deletion-
does-not-change-the-topology-of-the-image.-(They-are-not-break-
pixels).-An-additional-restriction-is-that-a-pixel-may-not-be-
deleted-at-the-end-of-a-skeleton(line).-The-number-of-iterations-
must-be-sufficiently-large-to-find-the-complete-skeleton-(the-
biggest-diameter-of-the-white-objects-divided-by-2).
The-operation-stops-when-the-number-of-iterations-is-reached-or-
when-no-pixels-change-anymore.-An-example-is-given-in-@demo3.

command-:-skelet--#iterations-,-bitplane,-edge-value,-image
default-:-skelet-------100----,----1----,------0----,---B
range---:-----------<1,512>---,--<1,8>--,----<0,1>--,-<A-D>

-skelet-:-skeleton-without-endpixels

The-skeleton-without-endpixels-is-the-same-as-the-previous-
skeleton-operation,-but-endpixels-may-be-deleted-in-this-case.-
Solid-objects-will-result-in-single-pixels-and-holes-in-objects-
will-result-in-rings.-This-is-illustrated-by-the-skeleton-of-the-
background-(exo-skeleton)-in-@demo4.

command-:--skelet-#iterations-,-bitplane,-edge-value,-image
default-:--skelet------100----,----1----,-----0-----,---B
range---:-----------<1,512>---,--<1,8>--,---<0,1>---,-<A-D>

contour-:-determines-the-contours-of-objects.

The-result-is-the-edges-of-white-objects.-This-means-all-white-
pixels-with-one-or-more-black-neighbours.

command-:-contour-bitplane,-edge-value,-image
default-:-contour----1----,----0------,---B
range---:----------<1,8>--,--<0,1>----,-<A-D>

majority-:-performs-a-majority-voting.

The-central-pixel-of-a-3x3-neighbourhood-becomes-black-or-white-
depending-upon-the-majority-of-the-neighbourhood.

command-:-majority-bitplane,-edge-value,-image
default-:-majority----1----,----0------,---B
€range---:-----------<1,8>--,--<0,1>----,-<A-D>

remove[noise]:-removes-pepper-and-salt-noise.

A-white-pixel-in-a-complete-black-3x3-neighbourhood-becomes-
black.-A-black-pixel-in-a-complete-white-3x3-neighbourhood-
becomes-white.

command-:-remove-bitplane,-edge-value,-image
default-:-remove----1----,----0------,---B
range---:---------<1,8>--,--<0,1>----,-<A-D>

life-:-game-of-life

The-well-known-game-of-life-is-also-a-cellular-logic-operation-!

command-:-life-#iterations-,-bitplane,-edge-value,-image
default-:-life------1------,-----1---,-----0-----,---B
range---:---------<1,512>--,---<1,8>-,--<0,1>----,-<A-D>



SPECIAL-LINEFIGURE-PIXELS

sinpix[els]-:-determines-isolated-white-pixels

These-white-pixels-have-no-white-neighbour-in-a-3x3-neighbour
hood.

command-:-sinpix-bitplane,-edge-value,-image
default-:-sinpix----1----,----0------,---B
range---:---------<1,8>--,--<0,1>----,-<A-D>

endpix[els]:-determines-endpixels-of-a-linefigure.

These-white-pixels-have-only-one-white-neighbour-in-a-3x3-
neighbourhood.

command-:-endpix-bitplane,-edge-value,-image
default-:-endpix----1----,----0------,---B
range---:---------<1,8>--,--<0,1>----,-<A-D>

linkpix[els]:-determines-white-pixels-with-two-white-neighbours.

These-white-pixels-have-two-white-neighbours-in-a-3x3-neighbour
hood.

command-:-linkpix-bitplane,-edge-value,-image
default-:-linkpix----1----,----0------,---B
range---:----------<1,8>--,--<0,1>----,-<A-D>

vertices:-determines-the-vertices-in-a-linefigure.

These-white-pixels-have-more-than-two-white-neighbours-in-a-3x3-
€neighbourhood.

command-:-vertices-bitplane,-edge-value,-image
default-:-vertices----1----,----0------,---B
range---:-----------<1,8>--,--<0,1>----,-<A-D>


BIT-OPERATIONS


bcopy-:-copies-a-bitplane.

The-command-parameters-are-the-input-bitplane-and-the-output-
bitplane.

command-:-bcopy-bitplane-in,-bitplane-out,-image-in,-image-out
default-:-bcopy-------1----,-----3-----,--B----,----B
range---:----------<1,8>--,---<1,8>---,--<A-D>-,--<A-D>

and-:-AND-function-of-two-bitplanes.

The-command-parameters-are-the-input-bitplanes-of-which-the-AND--
function-is-taken-and-the-output-bitplane.

command-:-and-bitplane-in-1-,-bitplane-in-2-,-bitplane-out,-image
default-:-and------1--------,--------2------,--------2----,---B
range---:--------<1,8>------,------<1,8>----,------<1,8>--,-<A-D>

or-:-OR-function-of-two-bitplanes

The-command-parameters-are-the-input-bitplanes-of-which-the-OR--
function-is-taken-and-the-output-bitplane.

command-:-or-bitplane-in-1-,-bitplane-in-2-,-bitplane-out,-image
default-:-or-------1-------,-------2-------,------2------,---B
range---:--------<1,8>-----,-----<1,8>-----,----<1,8>----,-<A-D>

exor-:-EXOR-function-of-two-bitplanes

The-command-parameters-are-the-input-bitplanes-of-which-the-EXOR-
function-is-taken-and-the-output-bitplane.

command-:-exor-bitplane-in-1,bitplane-in-2,bitplane-out,image
default-:-exor-------1------,-----2-------,------2-----,---B
range---:----------<1,8>---,---<1,8>-----,-----<1,8>--,-<A-D>

invert-:-inverts-a-bitplane

The-first-command-parameter-is-the-bitplane.-The-second-command-
parameter-is-the-image.

command-:-invert-bitplane,-image
default-:-invert-----1---,---B
range---:----------<1,8>-,-<A-D>
€
set-:-sets-a-bitplane,-so-makes-it-white-(1).

The-first-command-parameter-is-the-bitplane.-The-second-command-
parameter-is-the-image

command-:-set-bitplane,-image
default-:-set-----1---,---B
range---:-------<1,8>-,-<A-D>

reset-:-resets-a-bitplane,-so-makes-it-black-(0).

The-first-command-parameter-is-the-bitplane.-The-second-command-
parameter-is-the-image.

command-:-reset-bitplane,-image
default-:-reset-----1---,---B
range---:---------<1,8>-,-<A-D>


label-:-labels-connected-components.

This-command-labels-the-connected-components-within-a-binary-
image.-The-maximum-number-of-labels-is-255.-(In-low-resolution-
the-best-display-is-obtained-by:-don,3-followed-by-bdisp.)

command-:-input-image,-output-image,-input-bitplane,-connectivity
default-:------B-----,-------A-----,--------1------,------8
range---:---<A-D>----,-----<A-D>---,------<1-8>----,---<4,6,8>

UTILITIES

(*)don-:-Automatic-display-on

When-the-automatic-display-is-on,-after-each-operation-the-result-
is-shown.
An-optional-parameter-gives-the-type-of-display-in-the-low-
resolution-mode.-An-example-is-given-in-@democ5.

0-:-display-off-(same-as-doff)

1-:-When-all-pixels-of-a-2x2-neighbourhood-in-the-original-
bitplane-are-'0'-a-black-dot-is-displayed.-When-all-pixels-of-a-
2x2-neighbourhood-in-the-bitplane-are-'1'-a-white-dot-is-
displayed.-In-all-other-cases-a-grey-dot-is-displayed.

2-:-The-bitplane-is-sampled-depending-upon-the-GEM-window-size.-
When-the-first-pixel-of-a-sample-region-is-'0'-a-black-dot-is-
displayed.-When-the-first-pixel-is-'1'-a-white-dot-is-displayed.

3-:-Multiple-bitplane-display.-Bitplanes-are-sampled-depending-
upon-the-GEM-windowsize.-Bitplane-1-is-displayed-in-red,-bitplane-
2-in-blue-and-bitplane-3-in-green.-When-all-three-lowest-
bitplanes-are-'0',-the-3-highest-bitplanes-are-shown-as-grey-
€value.

4-:-Multiple-bitplane-display.-Bitplanes-are-sampled-depending-
upon-the-GEM-windowsize.-Bitplane-8-is-displayed-in-red,-bitplane-
7-is-displayed-in-blue-and-bitplane-6-is-displayed-in-green.

command-:-don,-display_type
default-:-don,-1
range---:-don,-<-0,4>

(*)doff-:-Automatic-display-off

When-the-automatic-display-is-off,-only-an-image-is-displayed-
after-a-gdisp-or-bdisp-command.

command-:-doff

(*)ton-:-Timer-on

The-execution-time-of-each-command-is-displayed-when-the-timer-is-
on.

command-:-ton

(*)toff-:-Timer-off

Sets-timer-off.

command-:-toff

gdisp-:-Grey-value-/-color-display-of-an-image.

This-routine-displays-a-grey-value-image-as-256x256-black-or-
white-dots-in-high-resolution.-In-low-resolution-128-x-128-pixels-
of-8-grey-values-are-displayed.-Images-are-always-displayed-with-
maximum-contrast.-The-contrast-is-computed-from-the-0.1-*-promille-
percentile-of-the-histogram.
When-the-image-is-a--color-image-it-is-displayed-in-color-in-the-
low-resolution-mode.-When-the-cdisp_type-parameter-is-0-an-optimal-
palette-is-computed.-When-the-parameter-is-2-a-sigma/delta-
technique-for-red-green-and-blue-dots-is-used.-When-the-parameter-
is-1,-red-and-blue-are-displayed-with-dots,-green-is-displayed-in-
4-values.
-The-first-parameter-is-the-image-(A-to-D).

command-:-gdisp-image,-promille,-cdisp_type
default-:-gdisp---A--,-previous,------0-
range---:-------<A-D>,-<0-100>-,---<0-2>

bdisp-:-Displays-one-of-the-8-bitplanes-of-an-image.

First-command-parameter-is-the-image-(default-A).-Second-parame
ter-is-the-bitplane-(default-1).-In-high-resolution-black-or-
white-pixels-are-displayed.-The-type-of-display-in-low-resolution-
€is-determined-by-the-(optional)-don-parameter.

command-:-bdisp-image,bitplane
default-:-bdisp---A--,---1
range---:-------<A-D>,-<1,8>

hist-:-calculates-the-histogram-of-an-image.

The-histogram-is-displayed-in-overlay-in-the-appropriate-image-
window-(A-to-D).-A-threshold-is-calculated-from-the-histogram-to-
segment-the-image-(-for-the-thresh-command).-The-command-
parameter-is-the-image-(default-A).

command-:-hist-image
default-:-hist---A
range---:------<A-D>
Palette-:-Change-the-palette-interactively.

This-option-is-only-supported-in-the-low-resolution-mode.

Preferences:-Change-preferences.

When-the-image-windows-are-sized,-the-aspects-ratio-can-be-
preserved-or-not.
The-images-can-be-aligned-to-byte-boundaries-or-not.

help-:-gives-help-information.

command-:-help-command

APPENDIX-:-File-header-structure


/*-call-the-headerfile-*.hd,-this-file-contains-the-structure-
with-all-parameters-of-the-corresponding-image-file-*.im.-*/

typedef-struct
--------{
--------short-*address;--------/*-image_address-in-memory--*/
--------char--name[16];--------/*-name-of-the-image-file---*/
--------short-format;----------/*-format-------------------*/
--------short-sizex;-----------/*-dimension-1--------------*/
--------short-sizey;-----------/*-dimension-2--------------*/
--------short-sizez;-----------/*-dimension-3--------------*/
--------unsigned-short-commsz;-/*-size-of-comment-in-bytes-*/
--------short-data[16];--------/*-user-image-dependent-data*/
--------}
--------HEADER;

#define-F_WORDS-0--/*-format-words-in-the-image-*/
#define-F_BYTES-1--/*-format-bytes-in-the-image-*/
#define-F_FOBIT-2--/*-four-bits-image,-packed-in-4pix/word-*/
#define-F_TWBIT-3--/*-two-bits-image,-packed-in-8-pix/word-*/
#define-F_SBITS-4--/*-format-single-bits-in-the-image-*/
€

ACKNOWLEDGEMENT

The-following-people-contributed-to-AIM:
Frans-Groen-(UVA/VU)-----:-some-image-processing.
Robert-de-Vries-(TUD)----:-GEM--interface.
Igor-Weber-(University-of-Zagreb,-YU):-low-resolution-and-colour-
                                        display.
Gert-van-Antwerpen-(CBD)-:-lmin,-lmax,-unif,-label
Piet-Verbeek-(TUD):-gaus,dog,robe,lgau,adne,adre,lgra,ggra,-
sune,sure,para,sepa,-peak,hara,have,-low,upp,dyt,tet,dyg,teg,rag,-
dyr,ter,rar,dyl,tel,ral,dys,tes,ras,dyf,tef,raf,-kuwa,edgps,-copy
Lucas-van-Vliet-and------:-erosion,-dilation,-propagation,
Ben-Verwer-(TUD)-----------skeleton
Tom-Hoeksma-(TUD)--------:-tests-and-evaluation.
Ad-Herweijer-(TUD)

------------------------------------------Frans-Groen
------------------------------------------Piet-Verbeek
------------------------------------------Robert-de-Vries

------------------------------------------March-1988


Please-send-remarks-and-comments-to-:
Frans-Groen
Faculty-of-Mathematics-and-Computer-Science
University-of-Amsterdam
Kruislaan-409
1098-SJ-Amsterdam
The-Netherlands
email:-groen@uva.uucp---(....!mcvax!uva!groen)

or-to:
Piet-Verbeek
Applied-Physics-Department
Delft-University-of-Technology
Lorentzweg-1
2628-CJ-Delft
The-Netherlands
tel-(31)-15-781416