A SYNC SIGNAL SWITCH BOX FOR THE MIDI HOME STUDIO.

     Files in this .lzh file include..........

     SYNC_SWT.DOC  What you are reading.
     SYNC_SWT.PI2  Med. rez (degas) wiring diagram.
     SYNC_SWT.PI3  High rez (degas) wiring diagram.

     Note...  The  PI3  and PI2 files must be viewed with degas, degas
elite or some kind of degas picture viewing program. One public domain
program that works well is DCSHW11.ARC file# 14572.

INTRODUCTION.......

     This  is  a  handy  MIDI  sync signal switcher for home recording
studios  with  multi  track  tape  decks.  If  you've got a 4,8, or 16
channel  setup, and you hate to repatch RCA cables every time you want
to  use  a  sync  box,  you  too  can  benefit  from  this  simple and
inexpensive  project.  You  will  never have to repatch the RCA cables
from  the  in  and  out on your sync box, or unplug them from the tape
deck  input  and  output  if your not using the sync box. And the same
goes for your mixer input and output.

PARTS..............

     The  parts  are  easy to come by. you'll need (6) RCA panel mount
female  jacks, (1) project box, (just about any size will do). (2 feet
at  the  most) of 20 gauge hookup wire, (1) 3 position wafer switch. A
wafer  switch unfortunately can't be bought at radio shack. However it
can  be  found  at  any electronic supply house or just about any well
stocked  music store. You see, this switch is also the pickup selector
for  a  Fender Stratacaster guitar. (In the degas drawing is a section
called  "signal path". I originally did this to further understand how
the switch actually worked and to help in the design. I left it in the
drawing  as an aid to those who might know of another switch that will
do the same job.) And if you want to install the optional test switch,
you'll need (1) normally open momentary push button switch. You should
be able to set yourself up with everything for around $10.

CONSTRUCTION.......

     The hardest part of constructing this project is cutting the slot
for the wafer switch. It requires a slot (1 inch long) and (1/16 of an
inch  wide).  I've  included  a  section in the drawing called "switch
slot".  This  shows  the  exact measurements of the slot. There's many
ways  to  cut this, more then I shall discuss. But here are three. The
best  and  easiest  way  is if you have access to a bridgeport milling
machine  and  1/16"  bit,  like  I  did.   But  a  DREMEL tool with an
adjustable  fence  and a tiny carving bit is a more realistic approach
to  the  job. And if a DREMEL tool is beyond your means. Alot of 1/16"
holes  in  a  line and some time with a small rat tail file will serve
the  purpose. The RCA jacks require drilling 1/4 inch holes. I suggest
you  label the switch, RECORD - BYPASS - PLAY  for convenience. And it
wouldn't  hurt  to  label  the  jacks  either.  There's  not much more
explanation of the assembly necessary. The degas drawings say it all.

SETUP PATCHING.....

     This  part might get a little confusing because there are so many
different  systems  and setups. I'll try to make it plain as possible.
Just for example, lets say you have an 8 channel deck and an 8 channel
mixer setup. And you always put your sync signal on track#8. Jack#1 is
labeled  TO  MIXER.  It  goes to channel #8 line or tape input on your
mixer.  Jack#2  is  labeled  FROM DECK. Connect a cord from channel #8
output  on your tape deck to this jack. Jack#3 is labeled TO DECK. You
want  to  connect a cord from here to the channel #8 input on you tape
deck.  Jack#4  is labeled FROM MIXER. A cord from channel #8 output on
your  mixer  goes  here.  Jack#5  is  labeled TO SYNC IN and jack#6 is
labeled  FROM  SYNC OUT these are self explanatory. This box will work
with  many different setups. If you have a 4 channel setup just change
the #8 to #4 etc.

OPERATION..........

     The  operation  of  this  box  is pretty simple. When you wish to
record  the  sync  signal  on the tape, place the switch in the RECORD
position.  If  you  want your recorded signal to trigger your sequence
program  or sequencer, place the switch in the PLAY position. And when
you want to return to normal operation with no sync, set the switch in
the  BYPASS  position.  If  you've  installed  the  test  switch, when
pressed,  you can hear the sync tone. The tone is sent to the mixer. I
installed  the  test  switch  to  troubleshoot  the  system.  It's not
necessary for operation.

OTHER STUFF........

    As  simple  as  this box is, and if you were able to buy it, you'd
probably  pay  somewhere  in  the  neighborhood of $40 to $50 or more.
Sickening, isn't it? Well, the point I'm getting at is, this box is my
own  invention, and if it makes your MIDI setup more efficient, my job
is complete. But still any contributions would be greatly appreciated,
no matter how small.

     There's  not much more to say, except I hope you'll be doing more
music and less repatching.

     Another D.I.Y. project from Flying Monkey Studios.

                               Mark Bombard
                               74 Loveland Rd.
                               North Granby, Ct. 06060
                               (203) 653-3134