This is an amateur radio RTTY program for the Atari ST.

Capabilities:
	1.	BAUDOT (60,	75, & 100 WPM)
		ASCII (110 & 300 Baud)
	 
	2.  Variable size split Screen 
		Drag the MOVE bar on the transmit window to change size
		Type ahead to transmit window during receive.

	3.  Write Sessions to disk 
		Received and transmitted characters are written to disk
		in the order they occur on the air.

	4.  Read disk files into transmit buffer.

	5.  Desk accessory support.  
		NOTE--received characters are written to receive window 
		even while desk accessory is active.  This works OK as
		long as the desk accessory is running in a GEM window because
		RTTY uses GEM to determine if its window is obscured by
		another window.  However, GEM forms (e.g. the standard file
		selector form) are not windows and are not protected from
		being overwritten on the screen by the RTTY program.

	6.  Limited line editing for transmitting.
		(delete back to	beginning of current line)

	7.  Drop down menus are used for all functions except:
		F1 switches unconditionally and immediately to
			receive mode, and sets RTS off.
		F2 switches unconditionally and immediately to
			transmit mode, sets RTS on, and starts
			transmitting characters from the transmit
			buffer.  When there are none, it holds the
			modem in the MARK state (no diddling).
		F3 inserts a character in the transmit buffer 
			(displayed as a greek letter phi) that is
			not transmitted, but switches back to receive
			mode when it is reached.  Any characters following
			the F3 character remain in the transmit buffer
			and will be sent when F2 is selected again.
		F4 allows deletion of all characters in the transmit
			buffer (after a confirmation).  The deleted
			characters remain in the transmit window in
			the display, however.

NOTES:
	RTTY.PRG and RTTY.RSC must reside in the same folder.  The
	program exits immediately if the resource file is missing.

	The ASCII/Baudot conversion is from the 1982 ARRL Radio
	Amateur's Handbook, the chapter on Specialized Communications
	Systems.  The FIGS code used is the US Figures (versus the
	CCITT No 2 Figures).  The Bell character (FIGS 5) does not
	ring a bell, but prints a diamond character.  When transmitting
	Baudot, the conversion from ASCII is done as characters are
	removed from the type ahead buffer.  Characters that do not
	translate into Baudot are simply discarded at that time, even
	though they appear on the transmit half of  the screen.

	I use the NOTEPAD desk accessory from COMPUTE!  April, 1987
	Atari ST disk if I need a real text editor to compose for
	transmission, which makes up somewhat for the limited
	editing capability of the RTTY program itself.  This is
	the main purpose of the "SWITCH RECORDING..." menu entry.
	It allows you to close the file currently being recorded,
	open a new one for recording, and then NOTEPAD can open
	the old one for inspection, or retransmitting text if you like.

	I used Megamax C compiler and resource editor to develop
	this program (but you don't need a C compiler to run it).

	This program was written and tested on an Atari 1040ST
	with single disk drive and monochrome monitor.  My RTTY modem
	is a Heathkit HD3030 and my rig is a Kenwood TS-440S.
	I don't know whether this program will work on any other
	hardware although I think it should.  Specifically, the
	color monitor could be a problem. I'd like to hear from anyone that 
	tries this program on a color monitor, as well as from anyone that
	finds this program useful at all.  Please send me a QSL at:

	1805 Mayfield
	Round Rock, Texas 78681