Howard Chu
								10-10-90

tip - ("terminal interface program") This is a small, stupid terminal
program modeled after the BSD 4.3 Unix program of the same name. It is
meant to be used with MiNT, though can easily be changed to work fully
with MicroRTX or plain old TOS as well. I wrote it to tide me over until
I have some better tools working with MGR. (Like KA9Q and a Unix-Windows
look alike, for example...)

Synopsis
	tip [speed]

Description
	Tip establishes a full-duplex connection to another machine
	through the ST serial port. Typed characters are normally
	transmitted directly to the remote machine (which does the
	echoing as well). A tilde (`~') appearing as the first
	character of a line is an escape signal for introducing
	commands; the following are recognized:

	~^D ~.	Exit the program (the connection is left intact).

	~!	Escape to a shell (exiting the shell will return
		you to tip).

	~#	Send a BREAK to the remote system.

	~s	Set a variable (see below).

	~^Z	Stop tip (only available with job control).

	~?	Get a summary of the tilde escapes.

	Tip uses a default baud rate of 9600 bps, which may be changed
	by specifying the desired speed on the command line.

	When tip prompts for an argument (e.g. when setting a variable)
	the input line may be edited with the usual erase and line-kill
	characters. A null line in response to a prompt will abort the
	operation. Typing an interrupt character (e.g. `^C') at this
	point will cause tip to crash.

	Variables

	Tip maintains a set of variables which control its operation.
	Variables may be displayed and set through the `s'' escape.
	Supplying ``all'' as an argument to the set command displays
	all variables and their current values. Variables are numeric,
	string, character, or boolean values. Values are assigned by
	typing the name, followed by either `=' or ` ' (space), then
	the value. (For boolean variables, the value is either ``on''
	or ``off''.) Variable names may be abbreviated to any length,
	one character or greater. The following is a list of currently
	implemented variables and their default values.

	baudrate
	    (num) The current baud rate setting. Any ST supported
	    speeds may be specified. Default is 9600.

	flowcontrol
	    (str) The current flow control method. Accepted values are
	    ``none'', ``xon/xoff'', and ``rts/cts''. Default is none.

	localecho
	    (bool) Echo keypresses locally, for half-duplex sessions.
	    Default is off.

	parity
	    (str) The parity and word size to use. Accepted values are
	    ``none'', ``odd'', and ```even''. The word size is set to
	    8 bits when parity=none, and 7 bits otherwise. Default is
	    none.

	escape
	    (char) The command prefix (escape) character. Default
	    value is `~'.

	shell
	    (str) The name of the shell to use for the ~! command. The
	    default value is taken from the environment. If no setting
	    is found from the environment, no default value is set.

Bugs
	You tell me... I think it works fine, for an evening's hack.
	Feel free to improve it, and please notify me of your changes.
		hyc@math.lsa.umich.edu