*      ETERNAL2 - A reset survivable ramdisk for the Atari ST
*		  which can be resized and removed
*
*	authors - There seem to have been many contributors to
*		  the development of this and other reset-survivable
*		  ramdisks.  It is belived that John Harris originated
*		  the idea and others added some embellishments.  This
*		  particular ramdisk is different from most in that it
*		  can be resized or removed.
*
*	    use - The ramdisk can be sized the following three ways: 
*		    
*		    a) By a ramdisk spec found in \auto\ramdisk.dat
*		    b) By entering a ramdisk spec through the console
*		    c) By not doing a) or b) to get the default spec
*
*		  The ramdisk spec has the form yxxx where y is a drive
*		  letter [a-p] and x is a digit [0-9].  A successfully
*		  created ramdisk will have a number of clusters equal
*		  to the number xxx and be installed on drive y
*		  (note that number of clusters is number of kbytes).
*		  The default ramdisk spec is h100 (100k ramdisk on
*		  drive h).  To install a ramdisk you must put eternal2.prg
*		  into an AUTO folder.  You may also create and put a
*		  ramdisk.dat file (containing a ramdisk spec) into the AUTO 
*		  folder but it is not necessary to do so.  To install for 
*		  the first time, put the disk with the AUTO folder into
*		  drive A and press reset (or switch on the computer).
*		  A ramdisk will be set up according to the spec in the
*		  .dat file, if it exists, or according to the default spec
*		  unless you press either the "caps lock" or the "alternate"
*		  key during boot.  If you press "caps lock" no ramdisk will
*		  be set up (you must keep the key depressed until bootup
*		  is finished or you see that etrnl2.prg has finished
*		  executing).  If you press "alternate" you will be prompted
*		  for a ramdisk spec.  Enter the spec and hit return to
*		  create the ramdisk.  To remove a ramdisk, press reset and
*		  keep a finger on the "caps lock" key.  To resize a ramdisk
*		  press reset and keep a finger on the "alternate" key
*		  until you see the prompt.  Then type in the spec and hit
*		  carriage return.  If a ramdisk is installed, the auto
*		  folder exists on a disk in drive A, reset is pressed and
*		  you keep your fingers off the keys, the ramdisk will still 
*		  be present with all its original files after 
*		  re-initialization.  To prevent a ramdisk from being
*		  created at startup use Q for the ramdisk spec in the
*		  ramdisk.dat file.  The ramdisk.dat file must have four
*		  characters otherwise.  To get a ramdisk of size less than
*		  100k on startup use leading zeros in the size field of
*		  the ramdisk.dat spec.
*
*	  notes - A ramdisk spec with two or one digit(s) is also legal.
*		  If you use a ramdisk spec like m0 you will get a size zero
*		  ramdisk but you will have lost 9k of space to the overhead
*		  used in setting it up.  Therefore, the proper way to
*		  remove a ramdisk is by means of the "caps lock" key.
*		  If you give no ramdisk spec then the default h100 is set
*		  up.  If you give only a device letter, say m, then a RD
*		  with spec m100 is set up.  There is no button to push to 
*		  abort - simply letting the boot process run its course is,
*		  for all practical purposes, an abort.
*
*                                               John Franco
*						Bloomington, IN
*						1/30/87